## Slide 1
SPARC_LAB – EuPRAXIA@SL status
Massimo.Ferrario@LNF.INFN.IT
On behalf of the SPARC_LAB – EuPRAXIA collaboration
LNF Scientific Committee Meeting, May 9, 2017
PWFA
Ext-LWFA
Self-LWFA
TNSA
Thomson
THz
FEL
EOS

## Slide 2: Milestones achieved after last SciCom
31-12-2016
  Systematic study of active plasma lens with different capillary lengths and different discharge circuits
    Better control of emittance growth
  31-03-2017
  Cathode replacement
    Systematic studies of new cathode thermal emittance and QE
30-04-2017
  Installation of PMQs triplet before the capillary to control beam matching at the plasma
  Replacement of photocathode laser chiller to minimize laser temperature fluctuations which spoil the charge stability
2016
2017 (till April 30th)

## Slide 3
FLAME status: roadmap
White room aircon cleaning
28/11/2016 for 1 w
White room floor and walls cleaning
5/12/2016 for 1 w
Optics cleaning
12/12/2016 for 2 w
Starting the laser from oscillator
9/01/2017 for 2 w
Laser transport to the FLAME bunker
23/03/2017 for 2 w
Fire accident
17/10/2016
After the fire accident, we have been following a roadmap to restart the laser as soon as possible. The roadmap has been successfully obeyed with only one week of delay and laser beam has been transported into the FLAME bunker where a strong instability on the focal spot has been observed (beam was moving from shot to shot more than 10 sigmas). The problem has been found on the air conditioning which was giving a flux which was too high. Problem has been fixed only at the end of MARCH 2017.

## Slide 4
Active Plasma Lens

## Slide 6: Active Plasma Lens Experiment: 1 cm long, 0.5 mm radius, 3D-printed capillary
Notes: PMQs characteristics:
Length: 1-2-1 cm
520 T/m

## Slide 7: Active Plasma Lens Experiment: control of emittance growth
Electron beam parameters
- 50 pC (at the cathode)
- 85% transmission through the capillary
- 126 MeV (0.3‰ energy spread)
- 1 ps rms bunch length
Notes: Qual e’ la beam size misurata sulla stessa targhetta, con il capillare ma senza plasma???

## Slide 9
velocity of plasma
Dielectric capillary
Electrode
Plasma discharge
Electrode shadows
e-
In order to understand what happens
to the electron beam outside of the
capillary we have studied the plasma
parameters in such areas:
Plasma density
Velocity of plasma
Inside
capillary
Outside capillary:
Plasma plumes
Image acquired by using
an ICCD camera:
Gate: 10 ns
Delay: 1100 ns
Area: 1000 x 500 pixel
+V
-V
Electrode

## Slide 10
Photocathode side: POSITIVE
velocity of plasma
Undulator side: NEGATIVE
Delay: 20 images separated by 100 ns = 2 µs
Gate: 10 ns
Area: 1000 x 500 pixel

## Slide 11
0 ns
200 ns
400 ns
700 ns
1000 ns
1300 ns
1600 ns
2000 ns
POSITIVE VOLTAGE
by using the camera delay it is possible to take a photo of the plasma plume during its expansion

## Slide 12
700 ns
2000 ns
POSITIVE VOLTAGE
NEGATIVE VOLTAGE
Vf=900 m/s
Vi = 15800 m/s
Ma=1.4
h ≈ 0.9 mm
Vi = 13050 m/s
Ma=1.2
Vf=1350 m/s
2000 ns
500 ns
h ≈ 0.8 mm
velocity of plasma
Electrode
shadow
Electrode
shadow
It could be possible to obtain the plasma temperature by the shock wave moving

## Slide 13
Plasma density
By using the Stark broadening method to measure the plasma density, we obtain the below result: the larger is the Balmer line (Δλ), the higher is the electron density of plasma
Balmer β line (486,1 nm)
Electrode
shadows
Plasma
channel
Plasma plumes
Position (mm)
λ (nm)
Δλ
We have measured the plasma
density outside the capillary,
where the plasma plumes expand

## Slide 14
Photocathode side: POSITIVE
Undulator side: NEGATIVE
Plasma density
channel
electrode
plume
We are looking here
We are looking here

## Slide 15
PWFA – Particle Wake Field Accelerator
Focusing
PMQ
PWFA
module
Capture
PMQ

## Slide 16: PMQ tunable system
Completely motorized PMQ triplet that allows to change the effective focal length of the focusing system
Piezo-actuators with 20nm resolution adopted
Pushing force >40 N
UHV compatible
Tunable distance between PMQ: from 3mm to 12mm
Longitudinal field (simulated & measured)
by V. Lollo and R. Pompili

## Slide 17: PMQ installation in vacuum chamber

## Slide 18
C-Band accelerating structure and PWFA chamber

## Slide 19
New Capacitive Voltage divider (CVD)
Coaxial copper tube for HV connection between the secondary winding of the pulse transformer and klystron cathode
New Current monitor (CT)
Filament (black cable) and HV (red cable) connections to the klystron
C-band ScandiNova Modulator Socket Upgrade
and installation of new diagnostics
Old Capacitive Voltage divider (CVD)
New low Inductance cables installed to increase the modulator pulse performances

## Slide 20
Currents along the new cables
New CT
Old CVD
New CVD
Strange spikes on all the monitored signals of the modulator
Different grounding configurations of the system have been tested
No noise has been detected on the RF pulse

## Slide 21: Up Time in Hours
Operation from Dafne in the night and during the weekends
Conclusion of installations after long shut-down
Cathode replacement

## Slide 22
R. Pompili et al.,
Experimental characterization of active plasma lensing for electron beams
Appl. Phys. Lett. 110, 104101 (2017)
doi: 10.1063/1.4977894
E. Chiadroni et al.,
Beam manipulation for resonant plasma wakefield acceleration
Nucl. Instrum. and Meth. in Phys. Res. A (2017) in press
doi: 10.1016/j.nima.2017.01.017
F. Villa et al.,
Generation and characterization of ultra-short electron beams for single spike infrared FEL radiation at SPARC_LAB
Nucl. Instrum. and Meth. in Phys. Res. A (2017) in press
doi: 10.1016/j.nima.2017.02.042
B. Paroli et al.,
A systematic study of the asymmetric lateral coherence of radiation emitted by ultra-relativistic particles in laser-driven accelerators
Nucl. Instr. and Methods in Physics Research A 839, 1-5 (2016)
doi: 10.1016/j.nima.2016.09.032
F. Filippi et al.,
Spectroscopic measurements of plasma emission light for plasma-based acceleration experiments
Journal of Instrumentation 11, C09015 (2016)
A. Biagioni et al.,
Electron density measurement in gas discharge plasmas by optical and acoustic methods
Journal of Instrumentation 11, C08003 (2016)

## Slide 23
R. Pompili et al.,
Femtosecond timing-jitter between photo-cathode laser and ultra-short electron bunches by means of hybrid compression
New Journal of Physics 18, 083033 (2016)
doi:10.1088/1367-2630/18/8/083033
A. Marocchino et al.,
Efficient modeling of plasma wakefield acceleration in quasi-non-linear-regimes with the hybrid code Architect
Nucl. Instr. and Methods in Physics Research A 829, 386-391 (2016)
F. Giorgianni et al.,
Strong nonlinear terahertz response induced by Dirac surface states in Bi2Se3 topological insulator
Nature Communications 7:11421 (2016)
doi: 10.1038/ncomms11421
F. Giorgianni et al.,
Tailoring of Highly Intense THz Radiation Through High Brightness Electron Beams Longitudinal Manipulation
Appl. Sci. 6, 2 (2016)
doi: 10.3390/app6020056
A. Cianchi et al.,
Observations and diagnostics in high brightness beams
Nucl. Instr. and Methods in Physics Research A 829, 343-347 (2016)
doi: 10.1016/j.nima.2016.03.076
F. Filippi et al.,
Plasma density characterization at SPARC_LAB through Stark broadening of Hydrogen spectral lines
Nucl. Instr. and Methods in Physics Research A 829, 326-329 (2016)
doi: 10.1016/j.nima.2016.02.071
S. Romeo et al.,
Beam dynamics in resonant plasma wakefield acceleration at SPARC_LAB,
Nucl. Instrum. and Meth. in Phys. Res. A 829, 109-112 (2016)
V. Shpakov et al.,
Betatron radiation based diagnostics for plasma wakefield accelerated electron beams at the SPARC_LAB test facility
Nucl. Instr. and Methods in Physics Research A 829, 330-333 (2016)
doi: 10.1016/j.nima.2016.02.074
M. P. Anania et al.,
Plasma production for electron acceleration by resonant plasma wave
Nucl. Instr. and Methods in Physics Research A 829, 254-259 (2016)
doi: 10.1016/j.nima.2016.02.029

## Slide 24
A. R. Rossi et al.,
Stability study for matching in laser driven plasma acceleration
Nucl. Instr. and Methods in Physics Research A 829, 67-72 (2016)
doi: 10.1016/j.nima.2016.02.015
R. Pompili et al.,
Beam manipulation with velocity bunching for PWFA applications
Nucl. Instr. and Methods in Physics Research A 829, 17-23 (2016)
doi: :10.1016/j.nima.2016.01.061
F. Villa et al.,
Laser pulse shaping for high gradient accelerators
Nucl. Instr. and Methods in Physics Research A 829, 446-451 (2016)
doi: 10.1016/j.nima.2016.01.010
A. Cianchi et al.,
Transverse emittance diagnostics for high brightness electron beams
Nucl. Instr. and Methods in Physics Research A in press (2016)
doi: 10.1016/j.nima.2016.11.063
D. Alesini et al.,
Design, realization and test of C-band accelerating structures for the SPARC_LAB linac energy upgrade
Nucl. Instr. and Methods in Physics Research A 837, 161-170 (2016)
doi: 10.1016/j.nima.2016.09.010
F. Massimo et al.,
Electromagnetic self-consistent field initialization and fluid advance techniques for hybrid-kinetic PWFA code Architect
Nucl. Instr. and Methods in Physics Research A 829, 378-389 (2016)
doi: 10.1016/j.nima.2016.02.043
A. Curcio et al.,
Numerical and analytical models to study the laser-driven plasma perturbation in a dielectric gas-filled capillary waveguide
Optics Letters 41, Issue 18, 4233-4236 (2016)
doi: 10.1364/OL.41.004233

## Slide 25: Planning 2017: First Period

## Slide 26: Planning 2017: Second Period

## Slide 28
Ti:Sa FLAME laser

## Slide 29
FLAME status
A fire accident has stopped suddenly FLAME operations…. October 2016

## Slide 30
FLAME status: program
Activity | Start date | End date
YAGs update – first 5 YAGs (upgrade, installation and test) | 09/01/2017 | 10/05/2017
YAGs update – last 5 YAGs (upgrade, installation and test) | 15/05/2017 | 28/07/2017
EOS experiment – phase 2 – set-up | 24/04/2017 | 05/05/2017
1st Amplitude visit for YAG installation | 10/05/2017 | 13/05/2017
2nd Amplitude visit for YAG installation | 26/07/2017 | 28/07/2017
EOS experiment – phase 2 – experiment | 15/05/2017 | 26/07/2017
Installation of the new interaction chamber | 04/09/2017 | 08/09/2017
LWFA experiment – phase 2 – set-up | 11/09/2017 | 22/09/2017
LWFA experiment – phase 2 – experiment | 25/09/2017 | 22/12/2017
BIG DELAY:
Expected 1 month. Real more then 5!!!

## Slide 31
EOS experiment - phase 2.
LWFA – phase 2
The aim of this experimental campaign is to add more diagnostic to the previous experimental campaign. Examples of diagnostic that will be included in this experimental campaign are electron charge and energy.
Moreover, a more comprehensive study of the potential barrier will be carried out.
The goal of the experiment is to accelerate bunches and measure the emittance growth from the plasma to the vacuum.
The emittance will be measured with betraton radiation for inside the plasma and with OTR radiation for outside the vacuum.
Using this two measurement, we will be able to estimate the emittance growth.
FLAME status: what next

## Slide 32
FLAME status: EOS experiment
More diagnostic added:
CR39 films to measure proton energy and charge.
Electron spectrometer to measure electron energy.
Main diagnostic is still EOS crystal.
The goal is to understand the scaling laws that governing particle acceleration from solid targets and the correlation between target shape and proton yield

## Slide 33
LASER–CAPILLARY INTERACTION FOR THE EXIN PROJECT, F.G. Bisesto et al., NIM A (2016)
CHARACTERIZATION OF X-RAY RADIATION FROM SOLID SN TARGET IRRADIATED BY FEMTOSECOND LASER PULSES IN THE PRESENCE OF AIR PLASMA SPARKS, A. Curcio et al. , Laser and particle beams (2016)
THE SPARC_LAB THOMSON SOURCE, C. Vaccarezza et al., NIM A (2016)
FEMTOSECOND DYNAMICS OF ENERGETIC ELECTRONS IN HIGH INTENSITY LASER-MATTER INTERACTIONS, R. Pompili et al., Nature Scientific Reports (2016)
AN ULTRASHORT-PULSE RECONSTRUCTION SOFTWARE: GROG, APPLIED TO THE FLAME LASER SYSTEM, M. Galletti, Il Nuovo Cimento (2016)
SUB-PICOSECOND SNAPSHOTS OF FAST ELECTRONS FROM HIGH INTENSITY LASER-MATTER INTERACTIONS, R. Pompili et al., Optics Express (2016)
TRACE-SPACE RECONSTRUCTION OF LOW-EMITTANCE ELECTRON BEAMS THROUGH BETATRON RADIATION IN LASER-PLASMA ACCELERATORS, A. Curcio et al, Physical Review Special Topics - · January 2017.

## Slide 34
FLAME status: what next
The new interaction chamber has been designed: it guarantees the maximum flexibility and space for diagnostic. With this new design, we will also be able to change parabola’s focal length in order to have higher intensity.
The order for the new interaction chamber will be placed soon and the camera will be installed hopefully after summer.

## Slide 35: EXIN vacuum chamber
Measured arm
Laser tracker
The measurements were carried out in the mechanical workshop of the accelerator division

## Slide 38
130 m
60 m
40 m
8 m
6 m
12 m
8 m
10 m
12 m
6 m
15 m
20 m
13 m
31 m
EuPRAXIA@SPARC_LAB

## Slide 39
EuSPARC => FEL driven by RF Linac only
EuPRAXIA@SPARC_LAB => FEL driven by Plasma module PWFA and/or LWFA

## Slide 40
209 MW
150 ns
46 MV/m
209 MW - 150 ns
65 MV/m
 | Phase I | Phase II
RF gradient | 46 MV/m | 65 MV/m
# of sections | 20 | 
# of modulators | 1 | 2
# of klystrons | 2 | 4
# of SLEDs | 1 | 2
linac length | 20 m (15 m active) | 
section input power | 21 MW | 42 MW
linac energy | 690 MeV | 975 MeV
EUSPARC scenario based on “X-band FEL collaboration” RF module

## Slide 41: Higher Gradient layout (A. Grudiev – CERN)
parameters |  |  | comments |  | 
<a> [mm] | 3.2 |  |  |  | 
d [mm] | 2.5 |  |  |  | 
Ls [mm] | 500 |  |  |  | 
Qe | 21400 |  |  |  | 
vg/c [%] | 2.5 – 0.77 |  |  |  | 
Tp [ns] | 121 |  |  |  | 
R’_PC [MΩ/m] | 350 |  | =G2/(Pkl/L) |  | 
 | Phase 1 | Phase 2 |  | Phase 1 | Phase 2
Energy gain: Vt [MeV] | 850 | 1350 |  | 850 | 1350
N structures | 30 | 30 |  | 32 | 32
Total active length: Lt [m] | 15 | 15 |  | 16 | 16
Total klystron power: Pt [MW] | 138 | 347 | On crest, No losses in WG | 129 | 325
N klystrons | 4 | 8 |  | 4 | 8
Does not fit together
N structures = 32
Lt = 16m
Layout Phase 1:
c
p
kl
x 4
c
p
kl
x 4
Layout Phase 2:
~5m
kl
CPI klystron: 50MW, 1.5us
SLED pulse compressor:
Q0=180000; Qe=21400
1500ns -> 121ns

## Slide 45: Possible CERN-EuSPARC collaboration
Sharing of designs and commercial partners
Training of INFN personnel at CERN
CERN participation to the EuSPARC design study
X-Box installation at LNF
Beam Commissioning Support at LNF
HB injector for CLEAR/AWAKE?
Beam/Plasma interaction studies and capillary development?

## Slide 48: Configuration D: PWFA with external RF beam driver
undulator
hall
~ 15 m
out-of-vacuum undulators
1 plasma stages
one laser beam from level above
~ 30m
X-band structures
RF gun & 3 S-band structures
5 m
PWFA uses electron beam as driver in one plasma stage
RF structures consist of S-band and X-band
Laser needed for pre-ionization of plasma
A = 45 x 5 m2 = 225 m2
~ 90 m
EuPRAXIA
facility
Including
plasma, undulators, and user areas
3D layout by Dariusz Kocoń
and Paul Andreas Walker

## Slide 51
SASE FEL studies
lu = 1.5 cm

## Slide 52
I=2kA,e=0.5,DE/E=0.25E-3
I=2kA,e=0.5,DE/E=0.5E-3
I=2kA,e=0.5,DE/E=1E-3
I=2kA,e=1,DE/E=0.25E-3
I=2kA,e=1,DE/E=0. 5E-3
I=2kA,e=1,DE/E=1E-3
I=1kA,e=1,DE/E=1E-3

## Slide 53: CDR Status Report active collaboration with ENEA, CNR, INFN_Mi, Universities of Roma, HUJI
Machine parameters optimization in good progress
Injector options: S & C band under investigation
Baseline RF Linac Design: X-band at 1 GeV, collaboration with CLIC/CERN group under construction
500 TW FLAME design and upgrade in progress
PWFA and LWFA modules under investigation
First start to end simulation performed
FEL users hall defined, collaboration with FERMI under construction
Secondary particle sources and HEP applications under investigation, collaboration with LNS under construction

## Slide 54
CDR delivery expected by July