## Slide 1: Muon Tomography in Padova (+ Genova)*
M. Benettoni,G. Bettella, G. Calvagno, P. Checchia,G. Cortelazzo, E. Conti, l. Cossutta, M. Furlan, F. Gonella, G. Nebbia , M. Pegoraro, S. Pesente, A. Rigoni Garola, S. Vanini, G. Viesti , G. Zumerle Univ. & INFN Padova, Italy
P. Calvini, S. Squarcia Univ. & INFN Genova, Italy
*+ Bs

## Slide 2: Outline
Scientific activity
Related projects and partners
Future plans

## Slide 3: Experimental Setup (2005)
At the INFN National Laboratory of Legnaro (Padova) an apparatus for the study of muon radiography has been assembled using two spare Muon Chambers Detectors produced for CMS.
Two Drift Chambers 2.5x3.0 m2
Gap between chambers: 160 cm vol. ≈ 11.5 m3
2 extra planes to measure p;
Fe p-filter
Trigger: upper chamber (events “pointing” from upper to lower chamber)
Acquisition rate: 350 Hz

## Slide 4: Experimental Setup
Drift chambers
Drift cell
Chamber layout
- -
- -
- -
- -
Planes of 4 layers of cells (SuperLayers); 2 SL (up to 8 points) measure angle and position in one direction (); 1 SL (4 points) measures the orthogonal direction (Θ)
Given the high lever arm the direction is much better determined in  (>1.2 mrad) than in Θ (>10 mrad)
Data
MC
Data
MC
Good agreement: reliable simulation

## Slide 5: Reconstruction Techniques
Simplest method: Single Scattering Approximation (SSA). In space: Point Of Closest Approach (POCA) of 2 straight lines
It tends to fail in presence of several scattering centers
Detector
Detector
Detector
Detector
Basic (POCA)
See dedicated presentation

## Slide 6: Reconstruction Techniques
Tomographic (Maximum Likelihood Expectation Maximization)*
If the material is not homogeneous the volume can be divided into N cubic voxels and
with an iterative optimization algorithm (MLEM) applied to a Maximum Log-likelihood functional the system can reach reasonably approximate values of k
Define linear scattering density LSD for a material:
with {si2=i2 ; i=1,…M} M measurements.
the average square deviation expected for a particle i crossing L
where {k ; k=1,…N} are N unknowns
Detector
Detector
unknowns
given the Gaussian p.d.f.
=1/X0
* Other algorithms: see ref. list
See dedicated presentation

## Slide 7: Results
Pb (left) and Fe (right) bricks at different height
MLEM
Shape Reconstruction
Pb 10x10x10 cm3
Fe 10x20x10 cm3
POCA
MLEM

## Slide 8: Results
MLEM
Material Discrimination
Blocks of different material
 | density (g/cm3) | X0 (cm) | l0 (cm-1) | sDF (mrad)
Al | 2,7 | 8.9 | 0,11 | 14
Fe | 7,9 | 1,76 | 0,57 | 35
Brass | 8.5 | 1.49 | 0,67 | 38
Cu | 8,9 | 1,43 | 0,70 | 39
Pb | 11,3 | 0,56 | 1.8 | 64
W (sintered) | 18.1 | 0.37 | 2.7 | 79
Clear “saturation effect”

## Slide 9: Results
Material Discrimination
Effect confirmed by simulation!
Effect related to the total thickness rather than to the material scattering density
W
Pb
simulation
real data
W
W
Pb
Pb
known
measured

## Slide 10: Results*
Momentum effect
Traversing the sample material, the low momentum component of the muon spectrum is absorbed, to an extent depending on the sample nature and thickness.
Given the scattering length
without momentum evaluation the basic relation is
simulation
simulation 10 cm
MLEM
~same non linearity (MLEM20% difference for W)
perfectly linear
This effect can be responsible for non-linearities
*NIM A 604 (2009) 738

## Slide 11: Mu Steel
The problem: orphan sources in scrap metal
All over the world, radioactive sources are sometimes present in scrap metal used for steel recycling.
In some cases, when the radiation source is well shielded by its heavy metal transportation cask and by the scrap metal itself, it is not detected by radiation portals and is melt, with serious consequences for the plant and public.
MuSteel project: study and design a portal capable to detect the heavy metal shield of the radiation source. NB: in a short (~ 5 min) time
In conjunction with radiation detectors, this system will be capable to intercept every source

## Slide 12: Cosmic Muon Tomography in transport control
2 l Pb shield
7 min data taking
Results:the program was successfully completed:
Reproducing a similar situation in the Demonstrator
Simulating a real situation in a full scale Portal
M. Benettoni et al2013
JINST 8 P12007 [arXiv:1307.6093].
https://ec.europa.eu/research/industrial_technologies/pdf/rfcs/summaries-rfcs_en.pdf.

## Slide 13: Example of rough momentum estimation
10 GeV muon tracked by drift tube chamber
Momentum Estimation from muon chamber track fit
80 MeV muon tracked by drift tube chamber

## Slide 14: Precision measurements
Iron blocks
Mock-up for normalization
(with known LSD)
Is it possible to make precision measurements with MCS tomography?
Despite several difficulties due to
calibration and saturation effects...

## Slide 15: Precision measurements*
Good correspondence of measured R=l/r with predicted values
Expected precision 7-10% DR=Rmeas/Rpred-1
Measured :
mean DR= -3.1% with r.m.s. of 4.8%
an important output of Mu-Blast project*:
Yes!
Several materials collected from a furnace with a wide
range of LSD or R
*E. Åström et al., 2016 JINST 11 P07010
R predicted
R measured
density

## Slide 16: Industrial application Cosmic Muon Tomography in Blast furnace control
Blast furnace imaging
Mu-Blast: European project to characterize the inner status of a Blast furnace (RFSR-CT-2014-00027)
Monitor the density profile of the materials. The spatial distribution of the three main components ( ore , coke and partially reduced metal) can be monitored profiting of their different densities.
Simple BF model
before sw changes
Simple BF model
after sw changes
Realistic BF model
after sw changes

## Slide 17: Industrial application Cosmic Muon Tomography in Blast furnace control
Mu-Blast:
Study the capability of a realistic (~small) detector: two detectors with 5m x 5m surface
Images obtained using the true momentum value of each muon, as given by the simulation data, averaged over the muon path.

## Slide 18: The muon momentum challenge
Previous results cannot be reproduced without the knowledge of the individual muon momentum. Simulations show that to have good images the momentum value must be known with a precision better than 50%.
It is necessary to design detectors capable of measuring the muon momentum. We base the design on the measurement of the muon scattering through materials of known composition and thickness.
Two of the many schemes explored are the following.

## Slide 19: Results with measured momentum
A detector space resolution of 300 μm (as obtained in Mu-Steel) has been assumed. Using such detectors the density structures in the BF materials are visible, though with long Data Acquisition (DAQ) times and with significant statistical noise.
Comparison with the true momentum results shows that important improvements in image quality could be achieved by improving the detector design, for instance improving the space resolution.

## Slide 20: Spent nuclear fuel control*
Additional information from MCS not included (yet) …
No validated methods to verify the content of storage containers without opening Possibilities: neutron radiography or muon radio/tomography.
Detectors positioned around the container  Absorption, Transmission and MCS
S. Vanini, P. Peerani, A.Rigoni, G. Zumerle, P.C.
Realistic simulation of the detector with one fuel bar removed from the CASTOR
m absorbed m crossing
*ESARDA BULLETIN, No. 54, June 20
https://esarda.jrc.ec.europa.eu/images/Bulletin/Files/B_2017_054.pdf

## Slide 21: Related projects and partners
2006/2008 (UNIPD Progetto d’Ateneo): Muon radiography: the use of cosmic rays in the contrast of the Nuclear Material illicit trafficking.
2009/2011 (Mobilità sostenibile Industria 2015) SLIMPORT Sicurezza, Logistica, Intermodalità Portuale. Sottosistema SLIMCHECK: OTO-MELARA (coord.),CAEN, C.I.E.L.I. INFN
2009/2010 (UNIPD Progetto d’Ateneo): Decision algorithms for the muon tomography
2010/2012 (RFCS: RFSR-CT-2010-00033) Mu-Steel
next step: a prototype portal (no resources)
2014/2016(RFCS: RFSR-CT-2014-00027) Mu-Blast
next step: a “small” detector for
radiographic inspection (no partners)

## Slide 22: Future perspectives
Spent nuclear fuel control: a radioactive environment
How much does radioactivity emitted by nuclear material stored inside Canisters interfere with the detector response?
Is the (low) cosmic-ray intensity (~.1 mSv/h) compatible with the noise induced by radioactivity?
We make just a work hypotheses: 150 mSv/h
From independent (unpublished) measurements that activity corresponds to a hit rate of ~ 40 Hz/cm2 in a drift tube
is that affordable? Does it still allow to see muon tracks?
Our evaluation: Yes (see below) but the best (too many unknowns and approximations) is to prove it with a test…

## Slide 23: A test proposal
Produce a small prototype: 8 layers of 8 tubes
Each Al tube: 50 mm diameter, 1.5 mm thickness, 2 m long, central 100 mm anode wire (+3000 V)
Signal processed by FE electronics (amplification and shaping) and RO chain (time digitization, trigger and remote transmission). Both available from CMS experiment production
Total size: 0.6 m x 0.5m x 2 m, total mass ~100 kg
Easy to move and to handle
~0.60 m
~0.50 m
~2 m

## Slide 24: A test proposal
Example of muon event with radioactivity noise
Expected from previous assumption:
when a muon crosses a tube,
in a 1ms time ( >> drift time)
0.04 hit/tube (at 150 mSv/h)
~ 2.5 hits in total due to noise
But the test will prove definitely if the technique works in a storage environment

## Slide 25: Backup

## Slide 26: Muon detector prototype
Realised for MU-Steel project
Drift tubes technique suitable for industrial production

## Slide 27
A realistic test
Test case:
  Pb block (~10 dm3) buried into scrap metal over a solid iron slab
  Total Fe thickness equivalent to 2.5 m of scrap iron
Time to recostruct a sample of
  500 k-muons
  500 k-voxels
Old package: ~15 min.
Present package: ~30 sec

## Slide 28: Cosmic Muon Tomography in transport control
Evolution with iterations (400).
The realistic case : 250 k μ (~8 min exposure time)
NB: TEST DATA

## Slide 29: Cosmic Muon Tomography in transport control
Full portal
NB:
SIMULATION
Simulation validated by the test data!!

## Slide 30: Reconstruction Techniques
Tomographic (List Mode Iterative Algorithm)
N~0.5·106 voxels of 3 cm side
M~ 20·106 
~ 40 iterations
reconstruct the material distribution with scattering in the F-view alone, the Q-view only to determine the muon trajectory in the orthogonal plane.
no momentum evaluation  assume an average value <1/p2> for (1/pi)2
In our case considering the volume between the chambers
s= and