## Slide 1: Overview of the Geant4-DNA extension of the Geant4 Monte Carlo simulation toolkit
Sébastien INCERTI
CNRS / IN2P3 / CENBG / Bordeaux U.- France
representing the efforts of the Geant4-DNA Collaboration
15th Seminar on Software for Nuclear, Sub-nuclear and Applied Physics Porto Conte, Alghero (Italy), 27 May - 1 June, 2018
http://geant4-dna.org

## Slide 2: Contents
Context of the Geant4-DNA project
Simulation of interactions of radiation with biological targets (e.g. DNA)
  Physical stage
  Physico-chemical & chemical stages
  Geometrical models of biological targets
  Early damage prediction
Where to find more information ?
See Geant4-DNA publication … (link)

## Slide 3
1) CONTEXT

## Slide 4: Modelling biological effects of ionising radiation remains a major scientific challenge
« A major challenge lies in providing a sound mechanistic understanding of low-dose radiation carcinogenesis »
L. Mullenders et al.
Assessing cancer risks of low-dose radiation
Nature Reviews Cancer (2009)
NCC
Mars
Chronic exposure
http://rcwww.kek.jp/norm/index-e.html
Diagnosis
Space exploration
Space missions
Proton & hadrontherapy
ISS
Fukushima
Moon
village

## Slide 5: The Monte Carlo approach
Can « reproduce » with accuracy the stochastic nature of particle-matter interactions
Many Monte Carlo codes are already available today in radiobiology for the simulation of TRACK STRUCTURES at the molecular scale in biological medium
  E.g. PARTRAC, KURBUC, MC4*, RETRACKS/RITRACKS, TRAX, …
  Include physics & physico-chemistry processes, detailed geometrical descriptions of biological targets down to the DNA size, DNA and chromosome damage simulation and even repair mechanisms…
Usually designed for very specific applications
Not always easily accessible
  Is it possible to access the source code or even the executable code ?
  Are they adapted to recent OSs ?
  Are they extendable by the user ?
« To expand accessibility and avoid ‘reinventing the wheel’, track structure codes should be made available to all users via the internet from a central data bank» H. Nikjoo, IJRB 73, 355 (1998)

## Slide 6: Geant4 for radiobiology ?
Can we try to extend Geant4 to model biological effects of radiation ?
LIMITATIONS prevent its usage for the modelling of biological effects of ionising radiation at the sub-cellular & DNA scale
  Condensed-history approach
    No step-by-step transport on small distances, a key requirement for micro/nano-dosimetry
  Low-energy limit applicability of EM physics models is limited
    « Livermore » Low Energy EM models can technically go down to 10 eV but accuracy limited < 250 eV
    100 eV for « Penelope 2008 » Low Energy EM models, accurate down to 1 keV
  No description of target molecular properties
    Liquid water, DNA nucleotides, other ?
  Only physical particle-matter interactions
    At the cellular level, physical interactions are NOT the dominant processes for DNA damage at low LET...
Biomed. Phys. Eng. Express 4 (2018) 024001 (link)
Volume ∅ < track length

## Slide 7: Geant4-DNA timeline
Main objective
Extend the general purpose Geant4 Monte Carlo toolkit for the simulation of interactions of radiation with biological systems at the cellular and DNA level in order to predict early and late DNA damage in the context of manned space exploration missions (« bottom-up » approach).
C++ extension designed to be developed and delivered in a FREE software spirit under the Geant4 license, easy to upgrade and improve.
2001
Initiated at the European Space Agency/ESTEC by Petteri Nieminen
2007
First prototypes of physics models for liquid water added to Geant4 9.1
2008
Development coordinated by CNRS/IN2P3
(physics, chemistry, geometries)
2014
Chemistry stage extension ready for end users in Geant4 10.1
2015-17 New alternative models for electron tracking & geometries
10.2 – 10.4
W. Friedland
D. Emfietzoglou M. Dingfelder

## Slide 8: How Can Geant4-DNA model early DNA damage ?
Physical stage
step-by-step modelling of physical interactions of incoming & secondary ionising radiation with biological medium (liquid water mainly)
Physico-chemical/chemical stages
Radical species production
Diffusion
Mutual chemical interactions
Geometrical models
DNA strands, chromatin fibres, chromosomes, whole cell nucleus, cells…
Excited water molecules
Ionised water molecules
Solvated electrons
DIRECT DNA damage
INDIRECT DNA damage
t=0
t=10-15 s
t=10-6 s
REPAIR

## Slide 9: PHYSICAL STAGE

## Slide 10: Overview of discrete physics models for liquid water
Electrons
  Elastic scattering
    Screened Rutherford and Brenner-Zaider below 200 eV
    Updated alternative version by Uehara
    Independent Atom Method (IAM) by Mott et al. & VLE data in ice from CPA100 TS code
    Partial wave framework model by Champion et al., 3 contributions to the interaction potential
  Ionisation
    5 levels for H2O
    Dielectric formalism & FBA using Heller optical data up to 1 MeV, and low energy corrections, by Emfietzoglou et al.
    Improved alternative version by Emfietzoglou and Kyriakou
    Relativistic Binary Encounter Bethe (RBEB) by Terrissol from CPA100 TS code
  Electronic excitation (*)
    5 levels for H2O
    Dielectric formalism & FBA using Heller optical data and semi-empirical low energy corrections, , derived from the work of Emfietzoglou et al.
    Improved alternative version by Emfietzoglou and Kyriakou
    Dielectric formalism by Dingfelder from CPA100 TS code
  Vibrational excitation (*)
    Michaud et al. xs measurements in amorphous ice
    Factor 2 to account for phase effect
  Dissociative attachment (*)
    Melton xs measurements
Protons & H
  Excitation (*)
    Miller & Green speed scaling of e- excitation at low energies and Born and Bethe theories above 500 keV, from Dingfelder et al.
  Ionisation
    Rudd semi-empirical approach by Dingfelder et al. and Born and Bethe theories & dielectric formalism above 500 keV (relativistic + Fermi density)
  Charge change (*)
    Analytical parametrizations by Dingfelder et al.
  Nuclear scattering
    Classical approach by Everhart et al.
He0, He+, He2+
  Excitation (*) and ionisation
    Speed and effective charge scaling from protons by Dingfelder et al.
  Charge change (*)
    Semi-empirical models from Dingfelder et al.
  Nuclear scattering
    Classical approach by Everhart et al.
Li, Be, B, C, N, O, Si, Fe
  Ionisation
    Speed scaling and global effective charge by Booth and Grant
Photons
  from EM « standard » and « low energy »
    Default: « Livermore » (EPDL97)
Med. Phys. 37 (2010) 4692 (link) Appl. Radiat. Isot. 69 (2011) 220 (link)
Med. Phys. 42 (2015) 3870 (link)
Phys. Med. 31 (2015) 861 (link)
Nucl. Instrum. and Meth. B 343 (2015) 132 (link)
Phys. Med. 32 (2016) 1833 (link)
  (*) only available in Geant4-DNA
Geant4 10.4
December 2017
PhD theses of H. N. Tran (2012), Q. T. Pham (2014), J. Bordes (2017)
Fully included in Geant4

## Slide 11: Cross section models for electrons in liquid water
Phys. Med. 31 (2015) 861 (link)
Elastic
Excitation
Ionization
Sum of inelastic

## Slide 12: Geant4-DNA « physics constructors » for liquid water
Electron thermalization (or killing) performed by the G4DNAElectronSolvation process (3 models)
Include ion nuclear scattering
No production cuts: all secondaries are simulated !
All are located in
$G4INSTALL/source/physics_lists/constructors/electromagnetic
Geant4 constructor name | Electron model content
G4EmDNAPhysics (< 1 MeV) | Default models, first set historically available in Geant4-DNA (9.1) - Inelastic model from Emfietzoglou DRF parameterization (2003) with Coulomb-field & Mott like-exchange corrections, - Elastic model from PW calculations
G4EmDNAPhysics_option1 (beta) | Same as G4EmDNAPhysics but uses multiple scattering model G4LowEWentzelVIModel
G4EmDNAPhysics_option2 (< 1 MeV) | Same as default G4EmDNAPhysics but faster (usage of CDCS for ionisation processes)
G4EmDNAPhysics_option3 (<1 MeV) | Same as G4EmDNAPhysics (historical)
G4EmDNAPhysics_option4 (< 10 keV) | - Inelastic models by Ioannina team: improvement of the parameterization of the DRF and low energy exchange corrections - Elastic model from SR with vapor screening parameter
G4EmDNAPhysics_option5 (<10 keV) (beta) | Same but faster (usage of CDCS)
G4EmDNAPhysics_option6 (<255 keV) | CPA100 models: excitation from the DRF of Dingfelder (1999), ionisation from RBEB, elastic from partial wave calculations (IAM)
3 recommended constructors

## Slide 13: New « Ioannina U. » electron models
Much less diffusive DPKs with the new inelastic model.
Example of verification & validation in liquid water
Dose Point Kernels
W-value (mean energy to create an ion pair)
DPK (MeV/nm)
Med. Phys. 42 (2015) 3870 (link)
J. Appl. Phys. 32 (2016) 119, 194902 (link)
The new Ioannina inelastic models get closer to other reference data
e-
e-
e-

## Slide 14: New « CPA100 » electron models
Integral cross sections for electrons
Differential ionisation cross section
CPA100 excitation model is in better agreement with the only experimental data in the gaseous water
good agreement between data and CPA100 cross sections, especially at low ejected kinetic energies (where the differential cross section is the largest).
main differences between Geant4-DNA default model and the experimental data are observed at ejected electron energy W lower than 10 eV.
Phys. Med. 32 (2016) 1833 (link)
An alternative set of models for electrons (10 eV – 255 keV) from the CPA10 Track Structure code (M. Terrissol, M. C. Bordage, Toulouse U. , France)
Software preservation

## Slide 15: Other bio-materials
Part of the effort to extend Geant4-DNA models to other materials than liquid water
Cross sections for biological materials are proposed since Geant4 10.4, applicable to DNA constituents
  tetrahydrofuran (THF), trimethylphosphate (TMP), pyrimidine (PY) and purine (PU)
  serving as precursors for the deoxyribose and phosphate groups in the DNA backbone as well as for the pyrimidine nucleobases, respectively
For the following incident particles
  electrons (12 eV-1keV, elastic + excitation + ionisation) : from measurements @ PTB, Germany
  protons (70 keV-10 MeV, ionisation) from the HKS approach
More details in
Rad. Phys. Chem. 130 (2017) 459–479
Eg. integral electron
ionisation cross section in THF

## Slide 16: Investigation of radiotherapy sensitization using high-Z nanoparticles
"Hot" topic: high-Z NP internalized in cells could boost energy deposition and increase the efficacy of radiotherapy
Well established for photon beams (photoelectric effect), more investigation needed for proton beams…
Still a challenge to perform mechanistic simulations
  We initiated a specific Geant4-DNA activity on the subject in 2015
  Simulation of physics + physico-chemistry + chemistry around GNP of diam. 50 nm (using Livermore for Gold)
  Eg. Radiolysis Enhancement Factor as a function of distance from GNP compared to WNP
  Underlined the necessity to extend Geant4-DNA models to high-Z metals
Graphic: Sébastien Tribot
Nucl. Instrum. Meth. B 373 (2016) 126 (link)
Coming soon

## Slide 17: High-Z materials : gold
Extension of Geant4-DNA for the modelling of radiosensitization from gold nanoparticles
Activity initiated in 2016 by D. Sakata (Bordeaux U., France)
Discrete processes for electrons: elastic (ELSEPA), ionization (modified RBEBV), electronic (4 channels) and bulk plasmon (Quinn's) excitation
Models will be delivered in the near future (probably Dec. 2018)
Integral cross sections for electrons
Eg. of validation: backscattering from gold plate
J. Appl. Phys. 120 (2016) 244901 (link)
Coming soon

## Slide 18: Geant4-DNA versus Geant4 CH models for gold
GNP irradiated with monoenergetic electrons
Two dimensional absorbed dose in a 1 nm thick sampling plane, around the GNP
3 incident energies: 1 keV, 10 keV and 100 keV
3 physics sets for Gold: Geant4-DNA, Livermore, and Penelope
Med. Phys. (2018) 2230-2242 (link)
Geant4-DNA
Livermore
Penelope
Coming soon
Strong backsc.
Uniformbacksc.
Largest energy deposit

## Slide 19: Multiscale combination of EM processes
Thanks to a unified software design, users can easily combine Geant4-DNA processes and models with existing Geant4 physics such as:
  Geant4 photon processes and models
    Photoelectric effect, Compton sc., Rayleigh sc., pair production
    Livermore (EPDL97) included by default in all Geant4-DNA constructors
  Geant4 alternative electromagnetic processes and models for charged particles
    Ionisation, bremsstrahlung, etc…
    Electrons, positrons, ions, etc…
  Geant4 atomic deexcitation (fluorescence + Auger emission, including cascades)
    EADL97 by default, Bearden
    activated by default in all Geant4-DNA constructors
  …and also Geant4 hadronic physics

## Slide 20: Mixed physics lists in geometrical regions: the « dnaphysics » extended example
Nucl. Instrum. and Meth. B 273 (2012) 95 (link)
Prog. Nucl. Sci. Tec. 2 (2011) 898 (link)
/gps/particle ion
/gps/ion 6 12 6
/gps/energy 240 MeV
Courtesy of V. Stepan (CENBG)
See extended/medical/dna/dnaphysics example

## Slide 21: Overview of verification activities
Quantity | Incident particle | References
Cross sections | electron, proton, alpha particle | Phys. Med. 31, 861 (2015) Med. Phys. 37, 4692 (2010)
Dose Point Kernels | electron | Nuclear Inst. and Methods in Physics Research B 398, 13 (2017) Appl. Radiat. Isot. 83, 137 (2014)
Frequency of energy deposition | electron, proton, alpha particle | Nuclear Inst. and Methods in Physics Research B 306, 158 (2013)
Ionization cluster size | electron | Eur. Phys. J. D 60, 85 (2010)
Lineal energy | proton | Appl. Radiat. Isot. 69, 220 (2011)
Mean energy deposition | proton | Appl. Radiat. Isot. 69, 220 (2011)
Radial doses | proton, alpha particle, ions | Nuclear Inst. and Methods in Physics Research B 333, 92 (2014) Phys. Med. Biol. 59, 3657 (2014)
Range | electron, proton, alpha particle | Nuclear Inst. and Methods in Physics Research B 269, 2307 (2011)
S-values | electron | Nuclear Inst. and Methods in Physics Research B 319, 87 (2014) Med. Phys. 42, 3870 (2015)
Slowing down spectrum | electron | Nuclear Inst. and Methods in Physics Research B 397, 45 (2017) Phys. Med. Biol. 57, 1087 (2012)
Stopping power or stopping cross section | electron, proton, alpha particle, C, O, Si, Fe | Med. Phys. 37, 4692 (2010) Phys. Med. Biol. 57, 209 (2011) Nuclear Inst. and Methods in Physics Research B 269, 2307 (2011) Nuclear Inst. and Methods in Physics Research B 397, 45 (2017)
W-value | electron | Phys. Med. Biol. 57, 1087 (2012) Med. Phys. 42, 3870 (2015)
Phys. Med. 31 (2015) 861 (link)

## Slide 22: Verification (1): stopping power
a reliable test to evaluate the accuracy of the code
Geant4-DNA does not use SP tables
users usually try to simulate SP by dividing energy loss over step length but forget to select stationnary regime
  (alternative analytical calculation is always possible from differential ionisation cross sections)
we provide specific « frozen-velocity » Geant4-DNA physics constructors for liquid water which activate a stationary regime in all inelastic models
See extended/medical/dna/spower example
Nucl. Instrum. Meth. B 397 (2017) 45 (link)
Helium2+
dE/dx
dE/dx
dE/dx
dE/dx

## Slide 23: Verification (2): MFP
another test to evaluate the accuracy of the code compared to other TS codes
the user can simulate MFP activating processes of his/her choice
  inelastic
  full
  with or without sub-excitation processes
See extended/medical/dna/mfp example
Inelastic for electrons
Electron
(Energy E)
mean step length of first interaction

## Slide 24: Verification (3): microdosimetry
we also provide an extended example capable of simulating microdosimetry spectra: lineal energy (y), specific energy (z), frequency-mean lineal energy, dose-mean lineal energy, frequency-mean specific energy, dose-mean specific energy
energy scored in spheres of selected radius
particular care for weighting of energy scoring...
See extended/medical/dna/microyz example
J. Appl. Phys. 122 (2017) 024303 (link)
2 nm
10 nm
30 nm
300 nm

## Slide 25: Verification (4): radial doses
Investigation of Geant4-DNA performance for radial dose distribution around ion tracks
  Protons, alphas, C, O, Fe
  MeV–GeV range
General good agreement of dose profiles with a variety of literature data
Selection of results for 1 MeV protons
Dose profile
Process contribution
Restricted LET
Nucl. Instrum. and Meth. B 333 (2014) 92 (link)

## Slide 26: Verification (5): electron slowing down spectra
a reliable test to evaluate the performance of track structure codes
represent the fluence distribution (differential in energy) of both the primary and all subsequent generations of secondary electrons generated through the full slowing-down process
∅(E)dE is the total distance travelled by electrons while their energy is in the interval E, E+dE (Vassiliev, 2012)
method: we record for each simulation step the kinetic energy of each electron undergoing a Geant4-DNA inelastic process in a log-binned histogram, setting for each record a statistical weight equal to the size of the step.
small influence of sub-excitation processes at low energy; Auger electron production from O should be considered.
1 keV
10 keV
100 keV
1 MeV
See extended/medical/dna/slowing example
Nucl. Instrum. Meth. B 397 (2017) 45 (link)
e-
Notes: Each histogram bin is normalized to its energy width (in eV) and the full histogram was normalized to the number of primary electrons

## Slide 27: Verification (6): S-values
a benchmark of Geant4-DNA models against Committee on Medical Internal Radiation Dose (MIRD) data for S-values for several radionuclides
also investigated cellular morphology dependence
see extended/medical/dna/svalue example
Appl. Radiat. Isot. 104 (2015) 113 (link)
Cell radius: 5 um
Nucleus radius: 4 um

## Slide 28: PHYSICO-CHEMICAL & CHEMICAL STAGE

## Slide 29
http://sphweb.bumc.bu.edu

## Slide 30: Contribution of indirect effects
Survival vs Dose with different DMSO concentrations
Contribution of indirect effects VS LET
Hirayama et al, 2009

## Slide 31: Modelling water radiolysis
Water radiolysis = dissociation of water molecules by ionising radiation
  Creation of oxydative species
  They can interact chemically with one another or with the « biological medium » (« non-direct effects ») and interfere with the normal functioning of cells
Stage 1 : Physico-chemistry stage we start from water molecules which underwent changes in their electronic configuration from physical processes occuring during the « Physical stage »
  Electronic excitation, ionisation
  The electronic rearrangement may lead to their dissociation
    We use branching ratios and positioning of dissociation products, which can be modified by the user
PhD thesis of M. Karamitros (2012)

## Slide 32: Modelling water radiolysis
Stage 2 : Chemistry stage the dissociative products can recombine to form new chemical species
  A new stepping algorithm was developed to handle this recombination and more generally manage collisions between tracks
    Requires the synchronization of tracks during simulation
    All tracks are transported simultaneously during dynamic or fixed « time steps »
  A table of chemical reactions and their reaction rates must be provided
All parameters are provided through a « Chemistry list » as Geant4 users would do with a « Physics list »
  G4EmDNAChemistry
Note that the chemistry can be started as a standalone application
  Input user defined « physics » phase space
Parameters can be changed by the user
PhD thesis of M. Karamitros (2012)

## Slide 33: Physico-chemical stage
t=10-15s
t=10-12s
During this stage, water molecules
  Dissociate if ionized
  Relax or dissociate if excited
Products thermalize down to their energy of diffusion at equilibrium
Electronic state | Dissociation channels | Fraction (%)
All single ionization states | H3O + + •OH | 100
Excitation state A1B1: (1b1) → (4a1/3s) | •OH + H• H2O + ΔE | 65 35
Excitation state B1A1: (3a1) → (4a1/3s) | H3O + + •OH + e-aq (AI) •OH + •OH + H2 H2O + ΔE | 55 15 30
Excitation state: Rydberg, diffusion bands | H3O + + •OH + e-aq (AI) H2O + ΔE | 50 50
Dissociative attachment | •OH + OH- + H2 | 100
J. Comput. Phys. 274 (2014) 841 (link)

## Slide 34: Chemical stage
We propose by default the set of parameters published by the authors of the PARTRAC software (Kreipl et al., REB 2009). However, these parameters can be modified by the user.
t=10-15s
t=10-12s
t=10-6s
Reactions (9) | Reaction rate (107 m3 mol-1 s-1)
H3O+ + OH- → 2 H2O | 14.3
•OH + e-aq → OH- | 2.95
H• + e-aq + H2O→ OH- + H2 | 2.65
H3O+ + e-aq → H• + H2O | 2.11
H• + •OH → H2O | 1.44
H2O2 + e-aq → OH- + •OH | 1.41
H• + H• → H2 | 1.20
e-aq + e-aq + 2 H2O→ 2 OH- + H2 | 0.50
•OH + •OH → H2O2 | 0.44
Species | Diffusion coefficient D (10-9 m2 s-1)
H3O + | 9.0
H• | 7.0
OH- | 5.0
e-aq | 4.9
H2 | 5.0
•OH | 2.8
H2O2 | 1.4
H2O | 2.0
J. Comput. Phys. 274 (2014) 841 (link)

## Slide 35
H3O+
e-aq
°OH
Radicals from excitation states
by M. Karamitros
H2O*→H3O + + •OH + e-aq

## Slide 36: How to use Geant4-DNA for radiation chemistry ?
Four examples are available in Geant4 in the « extended examples/medical/dna » category of Geant4 examples
  chem1: activating chemistry
  chem2: how to set minimum time step limits
  chem3: user interactivity and visualization
  chem4: extraction of radiochemical yields (G) in a range of deposited energy
Note
  Examples can be run in MultiThreading mode
  Chemistry works in with G4_WATER material

## Slide 37: Situation at 1 picosecond
A proton of 50 MeV…
μm

## Slide 38: Situation at 1 microsecond
A proton of 50 MeV…
μm

## Slide 39: Chem3
http://dx.doi.org/10.6084/m9.figshare.978887
Geant4-DNA generated track of 1 keV electron, followed up to 100 ns during chemical stage. Using pre-release Geant4 10.1 code.
First, the physical stage is modeled, using Geant4-DNA physics: the 1 keV electron track is fully slowed down and thermalized in a 150 nm sphere of liquid water. Yellow points correspond to interaction events in liquid water.
Next, the physico-chemical /chemical stage is simulated for the first 100 ns. Individual radical species diffusing in space and reacting with each other are shown as colour trails, the color coding chemical species type.

## Slide 40: Definition of radiochemical yield G
Number of molecules of a given species for 100 eV of deposited energy
Time-dependent radiochemical yield
Number of molecules at time t
Deposited energy scaling to 100 eV
An observable quantity commonly used to evaluate chemistry modeling accuracy…
Precautions for comparisons between codes
  scoring volume
  deposited energy
  species, reaction rates, diffusion constants
  compare all yields, not only one species...

## Slide 41: chem4 : easy simulation of G-values
Settings of chem4
  infinite volume
  two thresholds
    The primary is killed once it has deposited more energy than a selectable minimum threshold, T1
    When the primary particle looses more energy in few interaction steps than a maximum allowed threshold, T2, the event is aborted
    this allows to calculate G-values on the deposited energy range [T1,T2]
    can be set using UI commands : /primaryKiller/eLossMin 1 keV # primary is killed if deposited E is greater than this value
    /primaryKiller/eLossMax 2 keV # event is aborted if deposited E is greated than this value
Can run in MT mode
Results are stored in ROOT format and can me vizualised using a dedicated ROOT interface (plotG)
Eg. : species by 10 incident electrons of 100 keV (beam.in)
10 keV
•OH radicals
e-aq

## Slide 42: GEOMETRICAL MODELS

## Slide 43: Molecules: realistic geometries using an interface to PDB
PDB : Protein Data Bank http://www.rcsb.org/pdb/
  3D structure of molecules
  Proteins
  Nucleic acids
Description of DNA molecules, eg.
  1FZX.pdb
    Dodecamer
    12 DNA base pairs
    (2,8 x 2,3 x 4,01 nm3)
  1ZBB.pdb
    Tetranucleosome
    (9,5 x 15,0 x 25,1 nm3)
1FZX.pdb
1ZBB.pdb
HEADER STRUCTURAL PROTEIN/DNA 08-APR-05 1ZBB
TITLE STRUCTURE OF THE 4_601_167 TETRANUCLEOSOME
...
ATOM 1 O5' DA I 1 70.094 16.969 123.433 0.50238.00 O
ATOM 2 C5' DA I 1 70.682 18.216 123.054 0.50238.00 C
ATOM 3 C4' DA I 1 69.655 19.289 122.776 0.50238.00 C
...
TER 14223 DT J 347
...
HELIX 1 1 GLY A 44 SER A 57 1 14
HELIX 2 2 ARG A 63 ASP A 77 1 15
...
SHEET 1 A 2 ARG A 83 PHE A 84 0
SHEET 2 A 2 THR B 80 VAL B 81 1 O VAL B 81 N ARG A 83
http://pdb4dna.in2p3.fr
http://geant4-dna.org

## Slide 44: « pdb4dna » extended example
1) A C++ library
  Reading of PDB files
  Build bounding box from atom coordinates
  Search for closest atom from a given point
  Geometry and visualization : 3 granularities
    (1) Barycenter of nucleotides only
    (2) Atomistic
    (3) Barycenter of nucleotide components
2) A Geant4-DNA example
  Water box surrounding the molecule
  The output results consists in a ROOT file, containing for each event:
    energy deposit in bounding boxes
    number of single strand breaks (SSB)
    number of double strand breaks (DSB)
Available on-line under Geant4 license
(1)
(2)
(3)
http://pdb4dna.in2p3.fr
http://geant4-dna.org
Comput. Phys. Comm. 192 (2015) 282 (link)

## Slide 45: Bacteria: modeling E. coli...
fulld
PhD thesis of N. Lampe (2017)
"integral approach" :
geometry implementation,simulation & scoring of early damage fully driven by Geant4 UI commands
1.9 mm x 0.8 mm, 4.63 Mbp

## Slide 46
Up to cell: the first relaxed human fibroblast
Alternative approach :
using the « DNAFabric » external software
PhD thesis of S. Meylan (2016)

## Slide 47
PhD thesis of S. Meylan (2016)

## Slide 48: …based on the « DNAFabric » software
Choice of shape (ellipsoid, sphere, elliptical cylinder…) and nucleus size.
Generation of an empty nucleus phantom.
Choice and placement of the genome inside the nucleus in a condensed form.
Relaxation step allowing a modelling of the genome domains in G0/G1 phase of the cell cycle.
Filling step of the genome domains with different voxels containing chromatin fibers with molecular DNA components.
Export of the nucleus geometry towards the simulation chain based on Geant4-DNA
DNAFabric: C++ software : generation, modification and 3D geometries that can be exported to Geant4
Comput. Phys. Comm. 204 (2016) 159 (link)

## Slide 49: More geometries: cellular phantoms
Vulvar squamous carcinoma A-431 cells treated with non-internalizing and internalizing antibodies labelled with Auger emitter I-125
Geant4: Livermore based + Coulomb scattering + « microbeam » adv. example (« cellular phantom »)
Simulation of the distribution of energy deposition in the cell model for non-uniform (A – from fluorescence signal) and uniform (B) emission probabilities from I-125 electrons with 35A7 non-internalizing antibodies (logarithmic colour scale).
Spherical equivalent cell
35A7 non-internalizing (A) or m225 internalizing (rigB)
Nucl. Instrum. and Meth. B 366 (2016) 227 (link)

## Slide 50: More geometries: neurons
National University of Mongolia, Oulan Baator, June 2016
Phys. Med. 32(12) 1510–1520 (2016) (link)
Pr Oidov Lkhagva
A new activity in Geant4-DNA initiated by Dr Oleg Belov, JINR, Dubna, in collaboration with B. Munkhbataar and the National Univ. of Mongolia.
Radiation damage to the central nervous system is an active research domain in relation to brain radiotherapy and radiation protection for astronauts during space travel.
Now it becomes possible to investigate early biological damage induced by ionizing radiations in a simple neural network by means of modelling physico-chemical processes occurring in the medium after exposure, thanks to Geant4-DNA.
« neuron » extended example released in Geant4 10.4 Beta

## Slide 51: EARLY DAMAGE

## Slide 52: 1) E. coli: simulation parameters
A test geometry, consisting of 200,000 randomly oriented rectangular boxes (100 × 30 × 30 nm), each containing a straight 216 bp segment of DNA (inspired from Nikjoo et al., Int J Radiat Biol, 71 (1997), pp. 467–483)
Electrons are randomly shot from an inner sphere of radius 500 nm
Reaction rates for •OH , H• and e-aq with DNA components
P, D, bases
« Best » set
Phys. Med. 48, 135-145 (2018) (link)

## Slide 53: E. coli: DNA damage from proton irradiation
SSB and DSB yields from proton damage simulated using Geant4-DNA, compared to results from the PARTRAC (F03) and the KURBUC (N01) simulation codes.
Experimental DSB yields are indicated by F99 for human fibroblast cells, and B00 for V79 Chinese Hamster cells.
Experimental ratios are for plasmids.
Phys. Med. 48, 146-155 (2018) (link)
Suggests a major influence of scavenging…
Coming soon

## Slide 54: 2) Fibroblast: simulation parameters
Geometry: about 2 millions of voxels for the whole nucleus, using 5 types of voxels: straight, up, down, right, left
Direct effects:
  17.5 eV cumulated in the backbone region to induce a direct SSB
  At least 2 SSBs on opposite strands to form a DSB
Non-direct effects:
  Histone proteins (spheres) absorb radicals
  •OH radicals interacting with DNA induce base damage and 40% of •OH radicals interacting with 2-deoxyribose are registered as indirect SSB
  Chemistry duration of 2.5 ns
Damage:
  the DBSCAN clustering algorithm is used to merge direct and non-direct SSBs for DSB prediction
  only fragments > 104 bp are kept for comparison to pulse electropheresis
Sc. Rep. 7 (2017) 11923 (link)

## Slide 55
Fibroblast: early DNA damage
Sc. Rep. 7 (2017) 11923 (link)
Coming soon

## Slide 56: 3) Where to find more information ?

## Slide 57: Geant4-DNA website
  http://geant4-dna.org

## Slide 58: Geant4-DNA examples included in Geant4 (23)
Example code name | Purpose | Location
dnaphysics | Usage of Geant4-DNA Physics processes Automatic combination of Standard EM with Geant4-DNA Physics processes variable density | $G4INSTALL/examples/extended/medical/dna
microdosimetry | "Hand" combination of Standard EM or Low Energy EM processes with Geant4-DNA Physics processes | $G4INSTALL/examples/extended/medical/dna
range | Range simulation | $G4INSTALL/examples/extended/medical/dna
spower | Calculation of stopping power | $G4INSTALL/examples/extended/medical/dna
mfp | Mean Free Path | $G4INSTALL/examples/extended/medical/dna
wvalue | W values | $G4INSTALL/examples/extended/medical/dna
svalue | S values | $G4INSTALL/examples/extended/medical/dna
microyz | Microdosimetry spectra (y, z) | $G4INSTALL/examples/extended/medical/dna
slowing | Electron slowing down spectra | $G4INSTALL/examples/extended/medical/dna
clustering | Clustering code | $G4INSTALL/examples/extended/medical/dna
icsd | Usage of alternative bio-materials | $G4INSTALL/examples/extended/medical/dna
splitting (*) | Acceleration of processes | $G4INSTALL/examples/extended/medical/dna
chem1, chem2, chem3, chem4 | Usage of Geant4-DNA chemistry | $G4INSTALL/examples/extended/medical/dna
wholeNuclearDNA | Cell nucleus | $G4INSTALL/examples/extended/medical/dna
pdb4dna | Interface to PDB database | $G4INSTALL/examples/extended/medical/dna
neuron | 3D neural network | $G4INSTALL/examples/extended/medical/dna
microbeam | 3D cellular phantom | $G4INSTALL/examples/advanced
TestEm5 | Atomic deexcitation tagging | $G4INSTALL/examples/extended
TestEm12 | DPK | $G4INSTALL/examples/extended
TestEm14 | Extraction of cross sections | $G4INSTALL/examples/extended
G4 10.4
Dec. 2017
Useful to compare Geant4-DNA with literature data...

## Slide 59: Geant4 Virtual Machine
http://geant4.in2p3.fr
A virtual Linux PC with Geant4 and tools fully installed
WindowsTM
MacTM
LinuxTM
Full free access
Follows Geant4 releases
Twitter
@Geant4VM

## Slide 60: « Social » networks
Twitter
@Geant4-DNA
@Geant4VM
Facebook
Geant4-DNA

## Slide 61: Perspectives
Physics
  Inclusion of alternative or improved cross section models for electrons and ions
    Liquid water + DNA-like materials + gas materials for nanodosimeters + metals
Physico-chemistry/chemistry
  Alternative approach for the simulation of radiolysis (IRT)
  Addition of scavenger species and reactions
Biology
  Multi-scale geometrical models of biological targets, including « deformable » geometries, from DNAFabric and Geant4 UI messengers
  Prediction of direct and non-direct DNA simple & complex damages in plasmids and realistic cells
  Time evolution of damage: repair processes for the simulation of late damage
  Comparison to experiments: ion microbeam facilities (eg. @ CENBG)
Computing acceleration: GPU for chemistry
Verification (with other codes) and validation (with experimental data)
All these developments take time – once published, they are delivered publicly in Geant4

## Slide 62: Thank you for your attention …and a special thank you to
Theory & MC experts
Michael Dingfelder (ECU, USA) Dimitris Emfietzoglou (Ioannina U., Greece) Werner Friedland (Helmholtz Z., Germany)
Francesc Salvat (Barcelona U., Spain)
Our main developers
Marie-Claude Bordage (INSERM, France)
Ziad Francis (St Joseph U., Lebanon)
Susanna Guatelli (Wollongong U., Australia)
Vladimir Ivantchenko (G4AI Ltd, UK)
Mathieu Karamitros (Bordeaux, France)
Ioanna Kyriakou (Ioannina U., Greece)
Nathanael Lampe (Melbourne, Australia)
Sylvain Meylan (Paris, France)
Shogo Okada (Kobe U., Japan) Dosatsu Sakata (Wollongong U., Australia) Wook-Geun Shin (Bordeaux U., France) – PhD on-going
Nicolas Tang (IRSN, France) – PhD on-going
Hoang N. Tran (CEA, Saclay & Ton Duc Thang U., Vietnam)
Carmen Villagrasa (IRSN, France)
Alumni
J. Bordes, CRCT/INSERM/UPS, Toulouse, France
M. Bug, PTB, Germany
E. Delage, LPC Clermont/IN2P3/CNRS, France
M. Dos Santos, IRSN, France
A. Ivantchenko, G4AI Ltd., UK
A. Mantero, SwHaRD srl, Italy
H. Payno, LPC Clermont/IN2P3/CNRS, France
Y. Perrot, LPC Clermont/IN2P3/CNRS, France
  http://geant4-dna.org
Our users !
If you use Geant4-DNA, please be kind to cite in your work our two collaboration papers
Phys. Med. 31 (2015) 861-874 (link)
Med. Phys. 37 (2010) 4692-4708 (link)

## Slide 63
2018 Geant4 International User Conference
at the Physics - Medicine - Biology frontier
29-31 October 2018, Bordeaux, France
Topics
  imaging, classical radiotherapy, including brachytherapy and targeted radioimmunotherapy, protontherapy, hadrontherapy, radiobiology (Geant4-DNA), detector development, computing
under the auspices of the Geant4 Collaboration
peer reviewed regular papers in EJMP / Physica Medica (Elsevier) in open access
Registration is open
http://geant4.in2p3.fr/2018