## Slide 1: Recent Development in photosensing for astroparticle applications
F. Giordano
University and INFN Bari

## Slide 2
Big Size – PMTs 20’’
Intermediate Size – PMTs 2’’
Small Size – SiPM ¼’’

## Slide 3: Let’s start from our host

## Slide 6
The DCR
The dark counts are random noise pulses that can be measured at the anode of a PMT even in total
darkness.
The most significant source of random noise for a PMT is the spontaneous thermionic
emission of electrons by the photocathode (spe).
The rate at which these pulses are observed is proportional to the photocathode area and
varies considerably depending on the photocathode material. Bialkali photocathodes (as those used
in KM3NeT PMTs) have the lowest ratio per unit area. Another source of dark pulses is the natural
radioactivity in the structure of the PMT itself.
The most important components are usually 40K contained in the glass envelope.
Once the PMTs are fed with the tuned HV, dark count rates are monitored for 9 hours. During
this time, the PMT recover from the initial exposure to the light and the dark count rate becomes
stable. The measured rate is the average over the last 100 s of the run for each PMT. The results are
shown in figure 9. The average dark count rate is about 1300 cps, while the fraction of PMTs above
2000 cps is 7.1%. These PMTs were tested again after a longer darkening (48 hours) reducing the
fraction of PMTs not to be integrated in the KM3NeT DOMs to 3.5%. The average dark count rate
of good PMTs is about 700 cps.

## Slide 7: Timing

## Slide 8
Notes: PhotoDetector development for Hyper-Kamiokande (20' + 5')
https://indico.hep.anl.gov/indico/contributionDisplay.py?contribId=146&confId=1017

## Slide 9: 50 cm Photo-Detectors
Development of large aperture photo-detectors is a key to explore neutrino physics.
Hamamatsu R1449
For Kamiokande
1k PMTs
/ 3 kton water
(1983-1996)
→ IEEE milestone (2014)
First 20-inch (50 cm) Photomultiplier Tube (PMT)
For Super-Kamiokande (Super-K, SK)
11k PMTs
/ 50 kton water
(1996- )
R3600
(Venetian blind dynode, improved)
R7250
For KamLAND
R12850-HQE
50 cm Hybrid Photo-Detector (HPD)
R12860-HQE
50 cm Box&Line PMT
(Venetian blind dynode)
(Box&Line dynode)
(Avalanche diode)
For JUNO
50 cm MCP PMT
42 cm (17”) Box&Line PMT
By NNVC, IHEP
Recently developed in China
Two types of new 50 cm photo-detectors have been developed since 2011 with much improvement for Hyper-Kamiokande.
(Box&Line dynode)
For Hyper-Kamiokande (Hyper-K, HK)
For other experiments
Developed
→ Photo-detector
in Hyper-K baseline design
Under development
→ Possible further improvement of Hyper-K
(Micro-Channel Plate)
Supernova ν observation!
ν oscillation discovery!
with 50 cm bulb of R3600

## Slide 10: Hyper - Kamiokande
→
Hyper-Kamiokande (HK)
60 m
260 kton
74m φ
40%
photo- coverage
Large aperture photo-detectors are essential for physics sensitivities.
×40,000
New high-QE 50 cm Box&Line PMT
×2 high detection efficiency
and half time&charge resolutions
×2 high pressure bearing for 60 m height
compared to Super-K PMT (up to ~40m depth)
And 6,700 of 20 cm (8”) PMTs for Outer Veto Detector
(190 kton Fiducial Mass)
→ High time&charge resolutions, high detection efficiency, ..
low background
→ Wide dynamic range
→ High rate tolerance
→ Clear photon counting,
→ ~nsec time resolution,
Requirements
Water Cherenkov detector in Kamioka, Japan
for 1 tank
×2 tanks

## Slide 11: Principle of Amplification
Performance evaluation
Validation for a long operation in water
Electron might miss dynodes → less collection efficiency
Ambiguity of drift path limits charge and time response.
Photomultiplier tube (PMT)
Hybrid photodetector (HPD)
Venetian blind dynode
Box & Line dynode
Avalanche diode (AD)
(Super-K)
+2kV, 107gain
+2kV, 107gain
+8kV, 105gain
AD
×1600
×100
+ preamp
Venetian blind
Box & Line
New
New
High collection efficiency (CE)
Uniform drift path
→ High charge&time resolutions
Low cost,
high resolutions
50 cm Φ
Reliability
Low cost,
High performance
20mmΦ
are required.
high QE
high QE
Box
Line
e-
Simple inside

## Slide 13: Detection Efficiency
Super-K 67% (61%)
Box&Line PMT 95% (85%)
HPD 97% (80%)
High Quantum Efficiency (QE)
Total Detection Efficiency of 1 PE
HPD → 36%
Super-K
Measured at Hamamatsu by point source injection
×2
22%
at peak
Box&Line PMT
Super-K
→ 30%
(-2016yr)
Collection Efficiency (CE)
By simulation
In 46cmΦ (50cmΦ)
Measured
Measured
Detection efficiency was doubled in both new photo-detectors.
1m
PMT
light
pulse
Relative comparison of single PE counting compared with SK PMT
by a uniform light injection
Box&Line PMT : 1.91 of SK PMT
HPD : 1.76 of SK PMT
Confirmation in relative hit counting
(1ch 20mmΦAD)
(2ch 20mmΦAD)
(Low due to higher threshold for 1 PE)
Box&Line PMTs

## Slide 14
https://www.cta-observatory.org
Imaging
Air Cherenkov
Telescopes (IACTs)
~

## Slide 15: v
https://www.cta-observatory.org
Imaging
Air Cherenkov
Telescopes (IACTs)
~

## Slide 16
© 2017 MAGIC Group
https://www.cta-observatory.org
Imaging
Air Cherenkov
Telescopes (IACTs)
~

## Slide 21: The Schwarzschild-Couder Telescope for CTA
Schwarzschild-Couder dual mirror optics Medium Size Telescope
  Dual mirror optics designed to cancel aberration and de-magnify images, to be compatible with compact high-resolution SiPM camera
  Improved angular resolution
  Mechanical stability and mirror alignment are the main challenges.
First Prototype will be installed at the Veritas site in Arizona in 2018!
http://cta-psct.physics.ucla.edu/

## Slide 22: The SCT: Showers Measured Better
Dual-Mirror
SCT
Images
8° field of view
0.067° pixels
11,328 channels
Single-Mirror
MST
Images
8° field of view
0.18° pixels
1,570 channels
Signal:
γ-ray Shower
Energy: 1 TeV
Background:
Proton Shower
Energy: 3.2 TeV

## Slide 23: The SCT prototype for CTA
The pSCT Camera
25 modules
Module area: 54x54 mm2, divided into 4 matrices composed by 16 SiPMs with an area of 6 x 6 mm2
First module being assembled:
  16 modules equipped with Hamamatsu MPPC S12642-0404PA-50(X)
  9 modules equipped with FBK HD-3 SiPMs (assembled and tested by INFN)
Readout directly behind the focal plane with TARGET 7 (1 GSa/s, 10 bits effective )
University of Wisconsin – Madison
Hamamatsu
FBK
40 matrices produced and tested by INFN

## Slide 24
What is a SiPM?
A marix of N p-n junctions in parallel reversed biased
The working point is set beyond the breakdoiwn voltage
Each cell works in Geiger-Mode.

## Slide 25
SiPM: The model
N = total number of cells
Rq = quenching resistor
Cq = quenching Capacitance
Cd = single diode capacitance
Cg = Strain Capacitanceof the entire device
(N-1)Gq , Rq/(N-1) e (N-1)Cd = N-1 cells contribution
Iav = Current source (avalance event)

## Slide 26: SiPM 3mmx3mm: THE SIMULATION MODEL
N = 3600
Rq = 3.87 MΩ
Cq = 7 fF
Cd = 121 fF
Cg = 10.55 pF
(N-1)Cq = 25.19 pF
Rq/(N-1) = 1.075 KΩ
(N-1)Cd = 453.48 pF
I1 = Current spike 10 ps wide, Rise Time = Fall Time = 1 ps

## Slide 27: SiPM 3mmx3mm: Sipm & Electronics

## Slide 28: SiPM 3mmx3mm: Cancellazione polo-zero (2)

## Slide 29: FBK NUV high-density (HD) SiPM sensors
For a full characterization: we tested devices with different active areas read out with different front-end electronics circuits
  1 x 1 mm2
    Study of gain in terms of charge of the single SiPM microcell and dark rate
  6 x 6 mm2
    Study of correlated noise and of signal-to-noise ratio (SNR)
LED light @380 nm Room temperature HV = 28 – 40 V
Tail filtering!

## Slide 30: FBK NUV high-density (HD) SiPM sensors
400
Compound Poisson distribution

## Slide 31: Gain depends on SiPM thecnology
Gain
Dark count rate
Photon Detection Efficiency
FBK devices extensively characterized at INFN laboratories
High-density Near Ultra-Violet devices (NUV-HD) were chosen
The devices produced in 2016 (NUV-HD3) with 40 x 40 mm2 cell size, have improved optical isolation aimed to reduce direct crosstalk and to further increase the fill factor
Ambrosi et al., SPIE 2017 Proceedings Vol. 10392 https://spie.org/Publications/Proceedings/Paper/10.1117/12.2272982

## Slide 32: Hamamatsu solutions for cta

## Slide 34: Production details
672 SiPMs on 42 matrices
Two different substrates used (8 HD3-2 and 34 HD3-3)
  Same performances in terms of gain and PDE
  The breakdown voltage is approximately 1 V lower for HD3-2
  The DCR is lower for HD3-3
All matrices covered with epoxy
PCB bonding pad
500 μm
SiPM bonding pad
27x27mm2 PCBs are equipped with 16 SiPMs to cover uniformly the exposed area

## Slide 36: IV measurements
IV measured on all channels after assembly
Breakdown voltage evaluated
Uniform Vbd for each of the two SiPM types
  s/m = 0.1% for HD3-2
  s/m = 0.25% for HD3-3
IV characteristics for matrix R46
Vbd distribution for HD3-2 and HD3-3 types

## Slide 37: DCR & Test with flasher
Each matrix was illuminated and read-out through a 16-channel amplifier
Caen V792 QDC used to acquire charge signals
Output signal integrated in 30 ns
Matrices tested at Vbias between 31 V and 36 V
Gain and signal-to-noise ratio studied from the charge distribution
Charge distribution for matrix R46 at Vbias=33 V

## Slide 38: Gain and Signal-to-noise ratio
Gain and signal-to-noise ratio studied from the charge distribution for each matrix
Good uniformity found in general on the matrices
Channels with a not-resolved charge distribution classified as ‘noisy’
Gain (ADC channel/p.e.)
Signal-to-noise ratio

## Slide 39: SMART Specifications
Dimensions: 2.1 x 3.9 mm2
Technology node: 0.35um SiGe
16 analog channels
Digital control and readout: LVDS SPI 1Mbps
6 global configuration bits + 8 local bits for each channel
Chip power consumption: from 290mW to 420mW
64 pin CQFP package

## Slide 40: SMART measurements: output pulses
Single p.e for different gain adj.: Gain ≈ 2-3 mV/p.e.
Single p.e for different shaping adj.: LSB ≈ 0.8ns
Gain lower than expected:
- 50 Ohm load
- SiPM different from simulation
Setup:
4x4 NUV-HD3 matrix
  Vbias = 33V (Over Voltage = 6V)
  All channels active; light only on channel 7; channel 7 read.
  50ps FWHM laser pulser

## Slide 41: SMART measurements: Charge Finger Plots
Highest Input Z
Lowest gain
Fastest Shaping
Highest Input Z
Highest gain
Slowest Shaping
Lowest Input Z
Lowest gain
Fastest Shaping
Lowest Input Z
Highest gain
Slowest Shaping

## Slide 42
Camera Assembly

## Slide 43: What’s in the future for SiPM?
A sipm LST
Herd
LST