## Slide 1: Smart phones as particle detectors: the Distributed Electronic Cosmic-ray Observatory (DECO)
Justin Vandenbroucke (University of Wisconsin)
CRIS 2018, Portopalo di Capo Passero
June 21, 2018
Notes: Questions received:
What is the battery consumption?
How are the countries ranked? Normalized by population?
What about detecting air showers with coincidence?
Do you run it just face down on a table?

## Slide 2: Digital cameras are designed to be particle detectors
Usually the particles are visible photons
Light hits the sensor, knocking loose electrons (charge): photoelectric effect
Charge is collected by (CCD or CMOS) camera image sensor
Notes: Einstein Nobel, 1921 for 1905 paper

## Slide 3: Other particles can also knock loose electrons
High energy photons (gamma rays)
Charged particles (electrons, muons, protons, …)
Digital camera image sensors can therefore detect any of these high energy particles (ionizing radiation)
Camera sensors can detect both
  Cosmic rays
  Background (terrestrial) radiation

## Slide 4: DECO: the idea
Ionizing radiation (high energy particles) passing through a camera image sensor (CCD or CMOS) result in track-like images
True for cameras of all sizes, from telescopes to cell phones
A nuisance for telescopes
Interesting as a handheld detector for education, outreach, science: cover lens with tape and analyze dark images for tracks
The ionizing radiation can be created by cosmic rays, radioactivity in the environment, or a radioactive source
Can be used to teach cosmic rays, particle physics, nuclear physics, astrophysics, radiation
Similar detection principle to huge detectors built by hundreds of physicists (e.g. at LHC, Fermi), but in a handheld ubiquitous device
Single-classroom projects
Multi-classroom projects enabled by a central database
2013: Number of mobile devices in world exceeded number of toilets
2014: Number of mobile devices surpassed number of people

## Slide 5: The app
DECO: Distributed Electronic Cosmic-ray Observatory
App for Android publicly available; iOS in beta testing
App automatically uploads/syncs data to central database
Database aggregates images and associated data (timestamp, geolocation, magnetic field measurements, …)
Database can be queried/analyzed by users
DECO can be used in the classroom and by interested public
Can also be used with radioactive sources
Download at http://wipac.wisc.edu/deco
Data automatically synced to a central repository
Users/public can browse and analyze repository

## Slide 6: The App
Android
iOS

## Slide 7: The app algorithm
Expose sensor as long as possible (depends on cell phone model and Android version, typically ~50 ms)
Analyze to see if a particle was detected (can take up to 1 sec)
Repeat
Every 5 minutes, keep an image, whether it passed the selection or not (“minimum bias” data set: a control for comparison to images with particle events)
How do we determine if a particle was detected?
  When app first starts, calibrate the sensor noise level to choose brightness thresholds; then for each image:
  First check a low resolution version: did at least Nlow pixels have brightness above threshold Tlow?
  If so, check a high resolution version: did at least Nhigh pixels have brightness above threshold Thigh?
Notes: low resolution (fast): 1 to 20 bright pixels passes
high resolution (slow): 5 to 100 bright pixels passes

## Slide 8: The Sun never sets on DECO
As of June 19, 2018
https://wipac.wisc.edu/deco/data

## Slide 9: DECO in Italia

## Slide 10: DECO users in 80 countries
1) USA | 21) Australia | 41) Slovakia | 61) Morocco
2) Italy | 22) China | 42) Indonesia | 62) Venezuela
3) Germany | 23) Andorra | 43) Ireland | 63) Bolivia
4) Mexico | 24) Norway | 44) United Arab Emirates | 64) Panama
5) Poland | 25) Chile | 45) Thailand | 65) Estonia
6) Russia | 26) India | 46) Armenia | 66) Antigua
7) Spain | 27) Taiwan | 47) Hungary | 67) Bangladesh
8) United Kingdom | 28) Austria | 48) Nepal | 68) South Korea
9) France | 29) Ukraine | 49) Czechia | 69) Latvia
10) Greece | 30) Luxembourg | 50) Lithuania | 70) Iceland
11) Netherlands | 31) Malaysia | 51) Peru | 71) Angola
12) Canada | 32) Belgium | 52) Iran | 72) Jordan
13) Finland | 33) Colombia | 53) Cybrus | 73) Pakistan
14) Sweden | 34) Argentina | 54) Syria | 74) Kenya
15) Turkey | 35) Bulgaria | 55) Portugal | 75) Serbia
16) Brazil | 36) Israel | 56) Croatia | 76) Kyrgyzstan
17) Algeria | 37) Uruguay | 57) New Zealand | 77) Ecuador
18) Switzerland | 38) Egypt | 58) Ethiopia | 78) Afghanistan
19) Slovenia | 39) Philippines | 59) Tunisia | 79) Albania
20) Denmark | 40) Antarctica | 60) Romania | 80) Cameroon

## Slide 11: Web-based public data browser
Publicly accessible: part of main DECO page
Events available within a couple hours of detection
Query database based on device ID, time, latitude/longitude, altitude, device model, and particle identity
First 50 events returned by query displayed on web table
All events returned by query can be downloaded to .csv (metadata)
Zoomed, processed (for privacy) image available for each event
Link to google map location of each event, with resolution degraded to 0.01°(~1 km) for privacy

## Slide 12: Astronomers are familiar with identifying charged particles in camera images
Don Groom, “(Unwanted) radiation events in astronomical CCD images”, SPIE 2002
from (GeV) cosmic rays
electrons from Compton scattering of gamma rays from MeV radioactive days
National Optical Astronomy Observatory

## Slide 13: DECO image stack (sum of 379 images from one day)
Notes: One day of data: February 21, 2013

## Slide 14: Example DECO signals: 3 categories
(2) worm
low-energy electron
multiple scattering
(1) track
track
cosmic-ray muon
(3) spot
very low energy electron
from Compton scatter
Notes: 101765957

## Slide 15: Example DECO backgrounds: 3 categories
track
worm
track
spot
(4) hot spot
(5) (thermal) noise
(6) camera artifacts
Notes: 101765957

## Slide 16: Cell phone camera image sensor sizes (= particle collection area)
Sensor format | Area (mm2) | Phone models
1/4.0” | 7.68 | Galaxy Nexus, Nexus 4
1/3.6” | 12.00 | Nokia Lumia 720
1/3.2” | 15.50 | iPhone 5, Nexus 5
1/3” | 17.30 | iPhone 5S, iPhone 6
Notes: http://en.wikipedia.org/wiki/Image_sensor_format
http://www.anandtech.com/show/7517/google-nexus-5-review/6

## Slide 17: Larger camera image sensors also available
Tablets (most have same sensor size as cell phones, but could increase in future)
  If running Android, can run DECO
  iPads: iOS will be available in future
Compact and SLR (factor 10-100 greater sensor size than cell phones) digital cameras: beginning to run Android, or images could be acquired and analyzed by hand
cell phones
DSLR
compact digital
cameras
Area (mm2)
Notes: http://en.wikipedia.org/wiki/Image_sensor_format
1/1.7”: Pentax Q7 compact digital
http://www.dpreview.com/articles/2681655989/pentax-announces-q7-with-larger-1-over-1-point-seven-inch-12mp-bsi-cmos-sensor
4/3” (Four-thirds): DSLR
http://en.wikipedia.org/wiki/Four_Thirds_system

## Slide 18: Cosmic ray rate vs. altitude
30,000 ft: airplanes
17,000 ft: Victor Hess
8,000 ft: high mountain towns
Notes: 8 kft = 2.4 km
5.3 km Victor Hess
30,000 kft = 9.1 km
5.3 km
Figure 27.4: Vertical fluxes of cosmic rays in the atmosphere with E > 1 GeV estimated from the nucleon flux of Eq. (27.2). The points show measurements of negative muons with Eμ > 1 GeV [39–43].s

## Slide 19: A modern take on Victor Hess: now with airplanes and cell phones
Low rate, mostly secondary muons
High rate, mostly protons

## Slide 20: Stratospheric (near-space) balloon flight in Madison, Wisconsin
0.5 hr flight time
Maximum altitude: 100 thousand feet (30 km): 3x airplane altitude

## Slide 21: Different models have different range of exposure times (especially short in Android versions <5)
These exposure times are from image header (EXIF) data, not measured
Some models provide this data and some do not

## Slide 22: University of Wisconsin QuarkNet High school interns building an Arduino LED array to measure DECO exposure time

## Slide 23: Individual sensor areas and event rates are small
Cosmic-ray muon rate at sea level: 1 per minute per cm2
Camera image sensors have area ~0.16 cm2
Therefore expect 230 muons passing through sensor per 24 hrs
If sensor is only exposed 50 ms every 1 sec, livetime is 5%
Only 230 * 0.05 = 12 muons per 24 hrs pass through sensor while it is exposed
Additional efficiency factor: what fraction of muons passing through sensor, during exposure, deposit enough charge and pass selection algorithm?
Efficiency depends on phone model (camera image sensor and noise cleaning)

## Slide 24: Worldwide sensor area in cell phones
Smart phones: 2 x 109
Sensor area per phone: 10 mm2 = 10-5 m2
Total: 2 x 104 m2 = 2 x 10-2 km2
(rough estimate) plus non-smart phones, front facing cameras, compact and SLR cameras, tablets, laptops, webcams, …

## Slide 25: Comparison to silicon trackers used by professional physicists
Fermi LAT •
Worldwide smartphones •
Notes: Moore’s law published 1965 based on few years of silicon transistors
ATLAS:
61 m^2 of microscrips (Semi-Conductor Tracker) plus Pixel Detector
1.7 m^2 of pixel detector area
http://www.atlas.ch/pixel-detector.html

## Slide 26: Measurement of image sensor depletion thickness
J. Vandenbroucke et al., J. Inst. 11 P04019 (2016), 1511.00660
7 dof
p=0.008
7 dof
p=0.45
26.6 ± 1.4 µm

## Slide 27: Distinguishing tracks, worms, and spots

## Slide 28: Classifying images with computer vision (convolutional neural network optimized with deep learning)
M. Winter et al., 1803.04493
“Particle Identification In Camera Image Sensors Using Computer Vision”

## Slide 29: Classifying images with computer vision (convolutional neural network optimized with deep learning)
M. Winter et al., 1803.04493
“Particle Identification In Camera Image Sensors Using Computer Vision”
Column-normalized confusion matrix

## Slide 30: Advertisement: ICRC 2019 in Madison, Wisconsin July 25 – August 1, 2019

## Slide 31: DECO article in INFN’s Asimmetrie magazine (October 2017)
Delia Tosi & Justin Vandenbroucke
https://www.asimmetrie.it/as-illuminazioni-raggi-cosmici-in-tasca

## Slide 32: More information
Public site http://wipac.wisc.edu/deco
Paper #1 https://arxiv.org/abs/1510.07665
Paper #2 https://arxiv.org/abs/1511.00660
Paper #3 https://arxiv.org/abs/1708.01281
Paper #4 https://arxiv.org/abs/1803.04493
Public Google Group “deco-users” https://groups.google.com/forum/#!forum/deco-users
Physics World: http://live.iop-pp01.agh.sleek.net/2014/12/17/dialling-up-the-cosmos/
Symmetry: http://www.symmetrymagazine.org/article/reading-the-heavens-with-your-phone
UW Madison news: http://news.wisc.edu/23166
Kurzweil AI: http://www.kurzweilai.net/how-to-turn-your-android-phone-into-a-cosmic-ray-detector
Universe Today: http://www.universetoday.com/115066/how-to-turn-your-phone-into-a-cosmic-ray-detector/
Discovery: http://news.discovery.com/tech/gear-and-gadgets/turn-your-smartphone-into-a-cosmic-ray-detector-141009.htm
Huffington Post: http://www.huffingtonpost.com/2014/10/11/phone-cosmic-ray-detector_n_5958630.html
CERN Courier: http://cerncourier.com/cws/article/cern/69889
INFN’s Asimmetrie: https://www.asimmetrie.it/as-illuminazioni-raggi-cosmici-in-tasca

## Slide 33: Thank you to my DECO collaborators
Segev BenZvi
James Bourbeau
Silvia Bravo
Felipe Campos
Kenny Jensen
Peter Karn
Matt Meehan
Jeffrey Peacock
Graduate students
Undergraduates
Matthew Plewa
Tyler Ruggles
Marcos Santander
Cassidy Schneider
David Schultz
Ariel Levi Simons
Delia Tosi
Miles Winter

## Slide 34: Thank you to the supporters of DECO
University of Wisconsin
Knight Foundation
QuarkNet
National Science Foundation
American Physical Society
Simon-Strauss Foundation
Wisconsin IceCube Particle Astrophysics Center
Opportunities for collaboration at many levels: Contact me if interested!
justin.vandenbroucke@wisc.edu

## Slide 35: Additional slides

## Slide 36: Power consumption
Running the camera (and image analysis) continuously is battery intensive
In normal use, should be plugged in to wall power
Typically lasts a few hours on battery
An external battery pack can boost this to 10-20 hrs (e.g. on a long plane flight)
In 24 hours, consumes ~100 Watt-hours (costs ~1¢ on electricity bill)