## Slide 1: Diagnostic of fast-ion energy spectra and densities in magnetized plasmas
Mirko Salewski
Technical University of Denmark
Department of Physics
M. Nocente, B. Madsen, I. Abramovic, G. Gorini, A.S. Jacobsen, V.G. Kiptily, S.B. Korsholm, D. Moseev, J. Rasmussen, M. Tardocchi, B. Geiger, J. Eriksson, the JET Contributors, the ASDEX Upgrade Team, and the EUROfusion MST1 Team
5th International Conference on Frontiers in Diagnostic Technologies, Frascati, Rome, 3-5 October 2018

## Slide 2
ITER measurement requirements
High-resolution fast-ion measurements
Velocity-space coverage of fast-ion measurements
Velocity-space tomography at JET and ASDEX Upgrade
Prospects for alpha diagnostic at ITER: Velocity-space tomography, energy spectrum inference, model fitting
Conclusions
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Outline
Alpha particle density and energy spectrum measurements at ITER will be possible by solution of inverse problems: velocity-space tomography, energy spectrum inference, model fitting
Main message of this talk

## Slide 3: ITER measurement requirements
Title | Range Value Coverage | Condition | Time Res. | Spatial Res. | Accuracy
30. Confined alphas and fast ions - alpha density profile | (0.1 - 2) E18 m-3 | (blank) | 100ms | a/10 | 20%
30. Confined alphas and fast ions - alpha energy spectrum | 0.1 - 3.5 MeV, | Energy res. 10 % | 100ms | a/10 | 20%
30. Confined alphas and fast ions - D, T, H, He3 energy spectrum | 0.1 - 1 MeV | Energy res. 10 % | 100ms | a/20 | 20%
Donne et al. (2007) NF. Progress in the ITER Physics Base, Ch.7: Diagnostics
Now in the ITER measurement requirements database

## Slide 4
ITER measurement requirements
High-resolution fast-ion measurements
Velocity-space coverage of fast-ion measurements
Velocity-space tomography at JET and ASDEX Upgrade
Prospects for alpha diagnostic at ITER: Velocity-space tomography, energy spectrum inference, model fitting
Conclusions
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Outline

## Slide 5: Neutron emission and gamma-ray spectrometry at JET
Perpendicular view
Φ=90°(LOS, B)
Oblique view Φ=47°(LOS, B)
Eriksson et al (2015) NF

## Slide 6: NES measurements
3 simultaneously measured spectra in JET #86459
4.5 MW NBI + 3 MW 3rd harmonic ICRF-heating
Yellow: Used for inversion
Measure spectra of various quantities
Salewski et al (2017) NF

## Slide 7: GRS measurements
2 GRS spectra in JET #86459
High-resolution High-purity Germanium detector (1keV over 10 MeV)
Two competing reactions
Measure gamma-ray energies
Salewski et al (2017) NF

## Slide 8: Collective Thomson scattering measurement at ASDEX Upgrade
Rasmussen et al. (2015) PPCF
Data
− Sim
CTS measures velocities projected along a resolved direction u.

## Slide 9: Fast-ion D-alpha spectroscopy at ASDEX Upgrade
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Weiland et al (2016) PPCF

## Slide 10
ITER measurement requirements
High-resolution fast-ion measurements
Velocity-space coverage of fast-ion measurements
Velocity-space tomography at JET and ASDEX Upgrade
Prospects for alpha diagnostic at ITER: Velocity-space tomography, energy spectrum inference, model fitting
Conclusions
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Outline

## Slide 11: Velocity-space origin of the CTS signal
Salewski et al. (2011) NF
Shape of w is implied by energy and momentum conservation

## Slide 12: Alpha densities and energy spectrum
no direct energy resolution
Signal from E>Emin for given u
no direct densities
Signal/ion varies
f(E,p) is incompletely diagnosed
Weight function suggests incomplete velocity-space coverage and no energy resolution.

## Slide 13: Alpha energy spectra and densities cannot be determined directly by CTS, GRS or NES

## Slide 14: Options for alpha-particle energy spectrum and density measurements
Measure 2D velocity distribution function by velocity-space tomography
  Integrate to get energy spectrum
  Integrate again to get density
Measure 1D energy spectrum by velocity-space tomography with prior: isotropy
  - Integrate to get density
Fit a model, e.g. slowing-down distributions
  - Spectrum is assumed, not measured.

## Slide 15
ITER measurement requirements
High-resolution fast-ion measurements
Velocity-space coverage of fast-ion measurements
Velocity-space tomography at JET and ASDEX Upgrade
Prospects for alpha diagnostic at ITER: Velocity-space tomography, energy spectrum inference, model fitting
Conclusions
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Outline

## Slide 16: Introduction to velocity-space tomography
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Forward problem
Salewski et al
(2011,12,13,14,15,16,17,18) NF
Inverse problem
Distribution function F
Measurements S
Matrix W

## Slide 17: Velocity-space tomography vs. Simulation at JET
4.5 MW NBI + 3 MW 3rd harmonic ICRF measured by GRS/NES
Basic features agree: Tail length, tail width.
Barrier region suggests low densities above 2 MeV.
Velocity-space tomography confirms the barrier experimentally.
[a.u.]
[a.u.]
[a.u.]
Salewski et al (2017) NF

## Slide 18: Velocity-space tomography vs. simulation at ASDEX Upgrade
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Simulation
Salewski et al (2016b) NF
Measurement
2.5 MW NBI measured by 5-view fast-ion D-alpha spectroscopy

## Slide 19: Tomography movie of a sawtooth crash
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Salewski et al (2016b) NF
Upper panel: Measurement of fast ion density
Lower panel: tomographic inversion movie
fit to 50.000 data points
  100 frames
  5 spectra per frame
  100 data points per spectrum

## Slide 20: Sawteeth: FIDA tomography vs. TRANSP
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
TRANSP
FIDA
Fairly good agreement
Measured crashes smaller than simulated crashes.
No measured crashes for |p|<0.25 in agreement with Kolesnichenko (1996) NF and disagreement with TRANSP.
Salewski et al (2016b) NF
AUG #32323

## Slide 21: Energy spectrum measurements at JET and ASDEX Upgrade
ASDEX Upgrade
JET
Fast-ion density and energy spectrum measurements are now demonstrated at current machines.

## Slide 22
ITER measurement requirements
High-resolution fast-ion measurements
Velocity-space coverage of fast-ion measurements
Velocity-space tomography at JET and ASDEX Upgrade
Prospects for alpha diagnostic at ITER: Velocity-space tomography, energy spectrum inference, model fitting
Conclusions
Add Presentation Title in Footer via ”Insert”; ”Header & Footer”
Outline

## Slide 23: Alpha velocity-space diagnostic at ITER
2 gamma-ray views and 1 CTS view in the center
All lines-of-sight almost perpendicular to B.
GRS: 90°, CTS: 97°
Shevelev et al. (2013) NF
Nocente et al. (2017) NF
Salewski et al. (2016) ITPA-EP

## Slide 24
Ground truth
Tomography
E>1.7 MeV: Velocity-space tomography
Alpha slowing-down
Co- and counter-passing ejected, but not trapped
Co-passing ejected, but not trapped and counter-passing
Can’t tell co- and counter-going ions apart!
(E,|p|)-coordinates

## Slide 25
Ground truth
GRS 2x90+ CTS
Oblique views tell co-/counter-going ions apart
Inversion with an additional 30°GRS detector
Anisotropy could then be tracked.

## Slide 26
E<1.7 MeV: Energy spectrum inference assuming isotropy
Combined gamma-ray spectroscopy and collective Thomson scattering (>1.7 MeV)
Collective Thomson scattering only (>0.5 MeV)

## Slide 27: Alpha densities by fitting a model to the data
Compute expected spectrum for various alpha densities of an alpha-particle slowing down distribution

## Slide 28: Conclusions
ITER measurement requirements on alpha energy spectra and densities can be fulfilled by solving inverse problems.
2D velocity-distribution functions by velocity-space tomography
  E>1.7 MeV in (E,|p|), requires oblique GRS detector to get (E,p)
Energy spectra
  Integrate 2D velocity distribution function over pitch
  Velocity-space tomography assuming isotropy
Alpha densities
  Integration of energy spectra above
  Fit a model to the measurements, e.g. isotropic slowing-down distribution
Velocity-space tomography experimentally demonstrated on JET and ASDEX Upgrade.
Thank you for your attention!