## Slide 1
SiPM workshop
Bari
3/10/2019
SiPM on board the International Space Station:
from Lazio-Sirad to Mini-EUSO and SPB2
M. Casolino,
M. Bertaina, F. Cafagna, O. Catalano, R. Caruso, G. Osteria, M. Ricci
on behalf of the Sirad and JEM-EUSO collaborations

## Slide 2
Cosmic ray and radiation studies in space

## Slide 3
LAZIO-SIRAD
Italian Mission Eneide on ISS, 2005

## Slide 4: Lazio-Sirad detector
Silicon-Scintillator Tracking Calorimeter
Study of nuclear (>40MeV/n) and electron components inside ISS.
Study of spatial, angular dependence and (in long term) of magnetic perturbations
40cm^2 sr
3 scintillators
4 double sided microstrip detectors 16*7 cm
16 Silicon Photomultiplies Tiles
One-axis magnetometer (EGLE)
PC-104 acquisition with PCMCIA cards
CSES-LIMADOU
(2018)

## Slide 5
Lazio-Sirad

## Slide 6
Lazio -MEB

## Slide 7
SiPM on Lazio
16 detectors with plastic tiles placed in two layers of the detector
(original Dolgoshein-Mephi SiPM)

## Slide 8
Alteino & Lazio, PIRS module
To Soyuz
To main body of ISS
LAZIO and Alteino detectors on ISS (2005)
Grounding
28V power
supply
PCMCIA
card

## Slide 9
Figure 2: Alteino & Lazio detectors inside PIRS module of ISS
To Soyuz
To ISS

## Slide 10: SiPM performance
First (probably) operation of SI-PM in space
Detector size: 1*1 mm^2
0.5 ns, in this case >3 ns due to wavelenght shifter
Excellent agreement with PMTs
No specific problems (inside)

## Slide 11: MINI-EUSO Multiwavelenght Imaging new Instrument Extreme Universe Space Observatory

## Slide 12
EUSO-TA: Ground detector installed in 2013 at Telescope Array site: currently operational
EUSO-BALLOONS:
2014, Timmins, Canada
2017 NASA Ultra long duration flight. EUSO-SPB
3. TUS (2016): free-flyer
4. MINI-EUSO (2019): Detector from International Space Station (ISS): 40 kg total.
5. 2022 NASA
EUSO-SPB-2
6. K-EUSO (2022): ISS Approved by Russian Space Agency
7. POEMMA (2025+): NASA twin free-Flyer
The EUSO program
MINI-EUSO
(2019)
400 km
EUSO-TA (2013-)
EUSO-TA
(>2013)
EUSO-BALLOON (2014)
EUSO-SPB (2017)
EUSO-SPB2 (2022)
30-40 km
(2022)
POEMMA
TUS (2016)

## Slide 13: MINI-EUSO
Multi-band,
Multi-Wavelenght telescope inside ISS
Ultraviolet, with Fresnel lenses
Near Infrared camera
Visible camera
SiPM
30kg telescope
10kg ancillary material
60 W
62*37*37 cm
Multiwavelength Imaging New Instrument for the Extreme Universe Space Observatory
Night observations
From inside UV-transparent window of Zvezda

## Slide 14: Uv transparent window, Zvezda module
Field of view from window

## Slide 15: Science Objectives

## Slide 16: Search for UHECRs
Data of the PDM of the SuperPressureBalloon EUSO-SPB, ground tests at EUSO-TA
Laser is at 20km from detector
Each frame is 2.5microsecond
Laser beam moves from bottom (ground) to top (toward sky)
Threshold ≈7E20 eV
FPGA Trigger
TUS-like events
Laser generated events (USA)
UV flasher (Japan)

## Slide 17: Meteors and Strange quark matter
Meteors: Seconds, Solar system speed
Strange Quark matter (very dense): longer, constant signal, interstellar origin and speed
Light curve
40ms frames
Abruzzo, 26/6/2019
Meteor studies in the framework of the JEM-EUSO program. PLANETARY AND SPACE SCIENCE, 143(SI):245{255, SEP 1 2017.
JEM-EUSO: Meteor and nuclearite observations. Experimental Astronomy, 40:253{279, November 2015.

## Slide 18
UV emissions from night-Earth
    6.5 km resolution, from 2.5mus and above +-51°
    - from different lighting conditions, moon phase, year
    - from different inclinations
Map of night time Earth in UV
first night UV Map of the Earth
Apollo 16
1050-1260 Å and 1200-1550 Å.
Simulated wiew of Sicily with Mini-EUSO
Picture of the Earth from Apollo 16 mission Far Ultraviolet Camera/Spectrograph (UVC)
SES-14 GOLD instrument. It was taken at approximately 6 a.m
Emissions from 160 km

## Slide 19: 245 km * orbit path Oversampling down to 2.5km Possibility of inclining the detector in a second phase of observations Also use non-nadir window
Mapping night sky in UV

## Slide 20
Mini-EUSO & Debris
Norad data of known debris in f.o.v of minieuso (a few – termination line between dark and light)
Look for unknown debris (includes meteors for this purpose)
Laser shooting from ground (US) in f.o.b. of ISS

## Slide 21: Mini-EUSO elements
Secondary cameras onboard the Mini-EUSO experiment: Control software and calibration. Advances in Space Research, 64(5):1188{1198, Sep 2019.
Mini-EUSO: A high resolution detector for the study of terrestrial and cosmic UV emission from the International Space Station. Advances in Space Research, 62(10):2954{2965, Nov 2018.

## Slide 22
Optics:
Fresnel lens

## Slide 23: Mini-EUSO sensors
UV main camera
48*48 pixels
40 deg 243km 5km/pix
2.5mus and above
RGB camera
1280*960 pixels
33.2*24.8 degrees
231*174 km 180 m/pixel
1s
NIR camera
(BW with phosphor coating)
1280*960 pixels
33.2*24.8 degrees
231*174 km 180 m/pixel
4s
East-West Italy
Rome

## Slide 24
Ancillary detectors
UV sensors
Hamamatsu S1226-5BQ log 190-1000nm
ML8511 linear 280-400 nm
Silicon Photomultipliers
C13365 single pixel (used in Day/night assessment)
C14047-3050EA08 8*8 pixel Imaging system
(used in imaging of the Earth, in focal plane, 5km pixel)
Read by Mux
Light photodiodes
All temp compensated

## Slide 25: Mini-EUSO Operations
START
Connect 27V power supply
Connect grounding cable
Insert empty USB stick
Turn on switch
STOP
Turn off switch
Remove and store USB stick
Periodically copy selected files on station computer for later downlink
POWER ON LEDs
27 V POWER Supply
Ground stud
Switch
Storage USB Main
Storage USB Spare
Mini-EUSO control panel
Additional ops include latch/unlatch of instrument
In case of Sunday science, possibility to analyze data

## Slide 26: Integration of focal surface, LNF 2019

## Slide 27: Integration of focal surface, LNF 2019
SiPM UV UV
SiPM Array
Main Focal Surface

## Slide 28: Integration of focal surface, LNF 2019
SiPM UV UV
SiPM Array
Main Focal Surface

## Slide 29: Integration of focal surface, LNF 2019
UV CAMERA
VISIBLE CAMERA
NIR CAMERA

## Slide 30: FM closed and integrated, May 2019

## Slide 31: Mini-EUSO integrated with adapter flange
NADIR

## Slide 32: Acceptance tests in Baikonur and integration with Soyuz MS-14

## Slide 33: Roll-out of Soyuz MS-14, 19/8/2019

## Slide 34: Roll-out of Soyuz MS-14, 19/8/2019

## Slide 35: 22/8/2019 Launch, Site 31, Baikonur Cosmodrome

## Slide 36: First docking, 24/8/2019 unsuccessful

## Slide 37: Relocation of MS-13 from Zvezda to Poisk

## Slide 38: Second docking, 27/8/2019 successful

## Slide 39: LANFOS (Large Area Non-destructive Food Sampler) 食品の非破壊放射能検査を可能とする 低コスト検出器の開発 Development of a low cost radiation detector for non-destructive assessment of food contamination
JST, Japan Science and Technology funding
2012-2014
Minamisoma, Fukushima Region 2014-11-01

## Slide 40: Signal from Plastic and CsI

## Slide 41: Lanfos-H prototype, under test and calibration in RIKEN RNC RI hot-lab
Stainless steel container
Plastic cylinder
Scintillating Fibres

## Slide 42: Response of CsI + SiPm
Calibrated 137 Cs
Fukushima soil
137 Cs + 134 Cs

## Slide 43: 試作機の写真
Notes: Picture of Detector

## Slide 44: Next Steps
Turn on of Mini-EUSO
Fluche - Fluorescence and Cherenkov light detection with SiPM for space applications
Test of SiPms (Hamamatsu, FBK) on SPB2 (TBC)
Mini-EUSO-2 (SiPM, outside the ISS)