The NA62 RICH detector

A. Cassese1,2

1Department of Physics, University of Florence, Florence, Italy

2Sez. Di Firenze, INFN, Florence, Italy

The NA62 experiment is designed to measure the very rare kaon dacay K+→π+νν at the CERN SPS with a 10% accuracy. The Standard Model prediction for the branching ratio is (8.5±0.7)10-11. One of the challenging aspect of the experiment is the suppression of the K+→μ+νμ background at the 10-12 level. To satisfy this requirement a Ring Imaging Cherenkov Detector (RICH), able to separate π± from μ± in the momentum range between 15 and 35 GeV/c, with a μ rejection factor better than 510-3, is needed. The RICH must also have a time resolution of about 100 ps to disentangle accidental time associations of beam particles with pions. The RICH will have a very long focal lenght (17 m) and will be filled with Ne gas at atmospheric pressure. Two test beams were held at CERN in 2007 [1] and 2009 [2] with a RICH prototype. The results of the two test beams will be presented: the μ misidentification probability is found to be about 0.7% and the time resolution better than 100 ps in the whole momentum range.

References:

[1] G. Anzivino, etc., “Construction and test of a RICH prototype for the NA62 experiment”, Nuclear. Instrum. Meth. A, 593, 314-318, 2008.

[2] B. Angelucci, etc., “Pion-Muon separation with a RICH prototype for the NA62 experiment”, Nuclear. Instrum. Meth. A, 621, 205, 2010.