## Slide 1: Payloads at cryogenic temperature for 3rd generation g.w. detectors
Issues and Open Problems
Paola Puppo – INFN Roma

## Slide 2: The test mass Last Stage suspension
The role of the Last Stage Suspension is to compensate the residual seismic noise and to steer the optical components maintaining the relative position of the interferometer mirrors.
Components:
Marionette reaction Mass (MRM): Marionette actuation; it provides mechanical and thermal isolation from the Superattenuator;
Marionette: Angular control with actuators (coil-magnets, electrostatic) on the MRM;
Reaction Mass (RM): Mirror steering with (coil-magnets, electrostatic) actuators on the RM; Mirror protection;
Mirror: monolithic suspension.

## Slide 3
Conceptual scheme
Q from laser beam
Q from refrigerator
Mirror Reaction Mass:
Thermal Shield
Marionetta Reaction Mass:
Thermal Shield
High Efficiency Soft Thermal Links
(e.g. pure Al, copper)
Vacuum Chamber and Cryostat Thermal Shields
Silicon Monolithic Suspension
Different stage temperatures at the
steady state.

## Slide 4
Materials:
    UHV compatible;
    Amagnetic;
    No electrostatic charges;
    Internal Frequencies above the antenna bandwidth;
    Low frequencies of the system controllable;
Design Issues:
  Big Masses:
    reduces the recoils (control and suspension thermal noise)
    increases the violin modes frequencies
  Wires Length Increment:
    reduces the pendulum frequencies (suspension thermal noise)
  Wires Diameter Increment:
      cooling time reduction
Requirements

## Slide 5
Materials:
    High thermal conductivities  reduction of cooling time
    Low mechanical and optical losses  high perfomances coatings
    Low thermal expansions  negligible thermal lensing effects; reduction of position offsets
    Soft heat links  reduction of cooling noise transmission.
A promising material both as mirror substrate and wire is silicon having
    high thermal conductivity
    very low thermal expansion (zero below 17K)
Requirements for cryogenic temperatures

## Slide 6: Design of the cooling system
3
Tanks to R. Passaquieti
Cryo-Compatible Superattenuator
design
The upper part
(~15 m)
is at room temperature
and
insulated to the lower part by thermal screen

## Slide 7
Thermal Links I
A corona of thin beams (hardening problems with thermal cycles )
Long Braids (higher stiffness)

## Slide 8
Pure Materials as aluminum and copper
          RRR = rroom temperature / ro where ro resid. resist. at T~0 K
Thermal Links III

## Slide 9
Solution for the stationary state
(low stiffness and reliability when thermally cycled)
Use of a high purity material
k~2000 W/m/K in the range 1-10 K
Thermal link length 20 m
Thermal difference at the link ends ~ 1K
LF Int. ~200 mW ~8 wires r~1 mm
Thermal Links IV

## Slide 10
Cryogenic Payload Prototype:
    Silicon mirror suspended by using two Be-Cu wires loops (1.25mmX2.5mm section);
    Marionette with copper clamps,connected to the cooler by copper heat links, suspended with a titanium alloy cable;
    Reaction mass of the mirror and marionette position monitored with fiber bundle sensors to measure the system modes (suspended with copper wires);
    Reaction mass of the marionette holding the Virgo-like electromagnetic actuators (macor support, copper wire kapton insulated);
    MRM suspended with three titanium wires;
Experimental data
“A cryogenic payload for the 3rd generation of gravitational wave interferometers”, F. Basti, F. Frasconi, E. Majorana, L.Naticchioni, M. Perciballi, P. Puppo, P. Rapagnan, F. Ricci (accepted on Astroparticle Physics)”

## Slide 11: Payload Cooling
During the cooling several times the PT cryo-coolers were stoppes, because of failure in the water refrigeration system of the compressors.
Helium gas filling
Helium gas pumped out
The final mirror temperature results to be 30 K while the cold head is at 15 K.

## Slide 12
Thermal inputs Estimations
Mirror: 1.9 mW (CoBe3 wires)
Recoil Mass: 1 mW (Steel c70 wires)
Marionette: 6 mW (Ti6Al4 wires)
Most of the thermal power (>10W) is lost in the cooling process of the whole cryostat;
Thermal Gradient along the vacuum tank;
Improvement of the thermal overall insulation is needed;
26/05/11
30 K
27 K
23 K
29.5 K
PT cold head 15 K
Experimental vacuum chamber 30 K

## Slide 13: Transfer Functions
Longitudinal
Torsions
Pitch
very low influence of the thermal links on the dynamic of the mechanical system.

## Slide 14
Mechanical modes identification:
agreement with the simulation without links
very low influence of the thermal links on the dynamic of the mechanical system.

## Slide 15: Thermal drift: coils Joule effect
Significant thermal drift of the whole apparatus at low temperature has been induced (we measured ∼ 3·10-2 K/s on the silicon plate) during TF measurements (mainly for pitch )

## Slide 16
Very low influence of the thermal links on the dynamic of the mechanical system.
Development of the displacement monitoring at low temperature (LVDT, Fiber Bundles)
Need of a new actuator: coils made of Nb-Ti wires with an inner core made of copper. The inner core will insure an efficient use of the actuators at room temperature, while below the critical temperature of 10 K the superconducting Nb-Ti alloy will cancel the Joule effect.
Use Epoglass material for marionetta arms (reliability at low temperature).
What we learnt

## Slide 17
Coil-magnet actuation noise
Barkausen noise measurements
on a SmCo magnet at 4 K
P. Falferi Class. Quant. Grav. in press (2011)

## Slide 18: Parameters of a Payload for ET: (from small to big masses)
Cryo Prototype
 | Mirror | RM | Mario | MRM
Mass (kg) | 22 | 31 | 114 | 132
Wire L (m) | 0.6 | 0.6 | 0.45 | 0.46
Wire F(mm) | 2 | 0.6 | 3 | 4
Wire Mat | Co-Be2 | Steel C70 | Ti6Al4V | Ti6Al4V
Ixx (kg m2) | 0.19 | 0.77 | 0.77 | 6.7
Iyy (kg m2) | 0.19 | 0.74 | 1.7 | 11.4
Izz (kg m2) | 1.34 | 1.37 | 1.7 | 8.3
Cryo Payload
Last SA Filter | Mirror | RM | Mario | MRM
500 | 211 | 211 | 422 | 422
2 | 2 | 2 | 2 | 1
5 | 2 | 3 | 3 | 4
Ti6Al4V | Si | Si | Ti6Al4V | Ti6Al4V
65 | 8.38 | 13.7 | 21 | 19
45 | 8.38 | 13.7 | 35 | 30
65 | 5.2 | 15 | 21 | 22

## Slide 19: Monolithic suspensions: present technology 20-40 kg masses suspended with SiO2 wires
Virgo+ NI test mass
Silicate bonding
Ears and anchors attached with
silicate bonding
Fused silica wires produced with
laser machine

## Slide 20: Silicon sample prepared by micropulling
R&D is required:
Fiber payload
~ 200 cm long
Silicon fiber : the thermal conductivity

## Slide 21: Transfer function studies
Marzia Colombini with Octopus (P. Ruggi)
Marionette
MRM
RM&Mirror
Marionette
MRM
RM&Mirror
Series
Parallel
Series
Parallel
Comparison with the present payloads, in
which the position of the suspension points
are optimized to reduce the coupling between
the d.o.f.

## Slide 22: ET Payload
Suspension thermal noise for ET
Payload
Marionette: (Ti6Al4V wire)
d = 3 mm, M1: 422 kg, L=2 m T=5 K
Mirror (silicon wire)
dimensions: diam 45cm, thickness 57cm
d = 3 mm (pure Si cristal), M2: 211 kg, L=2 m T=10 K (only 18kW in cavity, 600 mm isotopically enriched Si)
Recoil Mass (silicon wire)
d = 3 mm, M3: 211 kg L=2 m T=10 K
Marionette
MRM
SA filter
The effect of the MRM on the thermal
noise is negligible.

## Slide 23: Conclusions
Informations gained from the study on the prototype:
    Different steady state temperatures
    Mechanical model useful for predictions (effect of the thermal links negligible)
    Transfer function prediction useful for checking the controllability
    Thermal noise model of the three last elements, the MRM act as mechanical isolation
    Use superconductive actuators
Open Problems:
    Silicon monolithic suspensions: silicate bondings, fiber production
    Improvement on the cooling time of payload