## Slide 1
The Naples' testbed for the SuperB computing model: first tests
G. Russo, D. Del Prete, S. Pardi

## Slide 2: The rationale
Following the Ferrara and Frascati meeting, we decided to setup a testbed for SuperB applications
The testbed is based on 12 servers (8 core, 32 GB, 8 disks), connected with a 2x10 GbE
A further server (48 core) under order
The tests will be based on:
  RoCE, MPI, data access, dataset distribution, monitoring tools

## Slide 3
The configuration of each node
10 Gbps
10 Gbps
1 Gbps
1 Gbps
2x CPU 2,13GHz 4Core, 4,80GT/s + 4,80GT/s QPI
8x 4GB Dual Rank 1066MHz
8x HDD 500GB 7200rpm SATA Hot-Plug 3,5”
UTP
Twinax
. . . 8x one node (12 nodes in this test)
96 core (8x 12), 384 GB Ram (32x 12), 48 TB HD (4x 12)

## Slide 4
The configuration of the shared storage
48 core (12x cpu), 64 GB Ram (16x cpu), 18 TB HD
Storage Server for the redundant and shared data

## Slide 5
Twinax 10Gbps connection
Gigabit Ethernet connection
Optical fiber Lan2
10Gbps
Optical fiber Lan1
10Gbps
4x Twinax 10Gbps connection
Server 48 Core
64 GB di RAM
Storage 18 TB
Rack n

## Slide 6
WN1/DataNode
10 GB Switch
WN2/DataNode
Shared/Redundant data Server
WN1/DataNode
10 GB Switch
WN2/DataNode
Shared/Redundant data Server
WN12/DataNode
WN12/DataNode
Rack 1
Rack n
2x 10 GB
4x 10 GB
4x 10 GB
2x 10 GB
Computing Model
6
4x CPU 12 Core
8x 8GB di RAM
Storage 6x 3TB
2x CPU 2,13GHz 4Core
8x 4GB
8x HDD 500GB

## Slide 7
Network Optimization Parameters:
MTU 9000
# TCP buffer sizes
net.ipv4.tcp_rmem = 131072 1048576 2097152
net.ipv4.tcp_wmem = 131072 1048576 2097152
net.ipv4.tcp_mem = 131072 1048576 2097152
net.core.rmem_default = 1048576
net.core.wmem_default = 1048576
net.core.rmem_max = 2097152
net.core.wmem_max = 2097152
# SACK and timestamps - turn off
net.ipv4.tcp_dsack = 0
net.ipv4.tcp_sack = 0
net.ipv4.tcp_timestamps = 0
# Network backlog
net.core.netdev_max_backlog = 10000
Basic: perfomance tests
Test Latency : 0.025 ms
Test Iperf : 5.6 Gbits/s
Computing Model

## Slide 8
DOUBLE FILE SYSTEM CONFIGURATION
CURRENT SETUP:
OS SL 5.5 with gLite 3.2 Middleare. The Nodes are ready to be include in the Atlas TIER2 and available for SuperB FastSim Program (to do in the next weeks)
IMPLEMENTATION OF THE HADOOP DISTRIBUTED FILE SYSTEM ON 8 NODE
IMPLEMENTATION OF GLUSTERFS DISTRIBUTED FILE SYSTEM ON 9 NODE
8

## Slide 9
HDSF-HADOOP IMPLEMENTATION
HDSF Name Node
WN1/DataNode
WN2/DataNode
WN../DataNode
WN8/DataNode
10 GIGABIT SW
HDFS FILE SYSTEM
1 NAME NODE
8 WORKER NODE / DATANODES that share
the local disk
All the DataNode mount
HDSF Posix Inferface through
Fuse module
9

## Slide 10
GLUSTER IMPLEMENTATION
WN1/DataNode
WN2/DataNode
WN../DataNode
WN9/DataNode
10 GIGABIT SW
GLUSTER
NO NAME NODE
9 WORKER NODE / DATANODES that share
the local disk
All the DataNode are client and server.
The Gluster FS is configured with replica 3
GLUSTERFS IS A FILE CLUSTER FILE SYSTEM THAT WORK WITHOUT DATA-NODES. IT CAN WORK IN 3 DIFFERENT CONFIGURATION: DISTRIBUTED, STRIPED AND REPLICA. IT USES THE POSIX EXENSION TO GUARANTEE THE CONSISTENCY OF FS.
10

## Slide 11: First Benchmark
Perfomance test executed through a SuperB Analysis job provided by Alejandro Perez.
It executes a real analysis test on a set of simulated root files previously replicated in the gluster-fs volume.
The following tests show the bandwidth occupation during a set of different job execution setup

## Slide 12: Network Occupation in a Single Node
Single Job max rate 59MB/s

## Slide 13: Network Occupation in a Single Node
2 Jobs max rate 113MB/s - 1 Gigabit nick cart is still enough but the CPU power is used at 25% - can code parallelization enhance this ratio?
113MB/s

## Slide 14: Network Occupation in a Single Node
8 Jobs (max box size) max rate 333MB/s
100% CPU Used but Network is at 30% more CPU can support from more 10Gbit/s Nic Cards
333MB/s

## Slide 15: Network Occupation over the box core size
16 Job on a 8 CPU Node
Whithout multi threading
24 Job on a 8 CPU Node
Without multi threading
Max Rate 422 MB/s
Need to extimate the
GLUSTERFS Overhead
326MB/s
422MB/s

## Slide 16: Network Occupation 8 job in each node
In this test we sent 8 analysis jobs for each 8 core server
We Compute an Aggregate
Network occupation of 10 Gbit/s In the Cluster

## Slide 17: Analysis
The Network Trend during data analysis Jobs show that:
We have a set of SuperB Analysis that use 20-50MB/s
To support future multicore architecture (24/48) we must move to a 10-20Gbit/s Network (nics now offer two ports); cost of switch is dominant (if using more than 24 ports)
We have some option in the open source File System that can support 400MB/s (GLUSTER File System, Hadoop)
A correct configuration and tuning of 10Gbit/s Nic cards is needed
17

## Slide 18: CONCLUSION
Preliminary tests on a full 10Gbit/s Farm show that the possibility to have data and computing in the same node is strictly correlate with the available network (for a 48Core two or four 10 Gbit/s nick card will be needed).
Interesting issue:
Comparison between different cluster file-system are interesting in terms of overhead, reliability and network usage and services offered.
Comparison with different setup or number of replica with the same FS.
Can Code Parallelization between core improve the ratio CPU used by Job vs Network requirement for data access?
18