## Slide 1
Analog Front End
For outer Layers of SVT (L.4 & L.5)
Team: Luca Bombelli Post Doc.
Bayan Nasri Ph.D. Student
Paolo Trigilio Master student
Carlo Fiorini Professor

## Slide 2: Table of Contents
ENC estimation of input MOSFET
“Ideal” Shapers noise performances
Proposed architecture of Front End circuit
Charge Pre-Amplifier performances
Shapers implementations
Conclusion and future activities

## Slide 3: ENC estimation of input MOSFET
Considered parameters: Detector parameters:
  1 MIP ≈ 27500 electrons
  Dynamic range ≈ ±15 MIP
  Noise = 1000 electrons
Detector
(Cd, Rs)
Charge preamplifier
(ideal)
Shaping amplifier
(CR-(RC)2 ideal)
(NMOS, PMOS)
Layer | Rs (W) | Cd (pF)
4 | 234 | 52.6
5 | 300 | 67.5

## Slide 4: Optimization of input MOSFET
ENC estimation for different sizes of input MOSFET
Example: Layer 5, NMOS, Ibias=500µA, TP=1µs

## Slide 5: Optimization of input MOSFET current
ENC estimation for different Ibias
Layer 5
TP=1µs
NMOS W=9mm, L=250nm
PMOS W=7mm, L=150mm
ENC estimation for different Ibias
Layer 4
TP=0.5µs
NMOS W=9mm, L=250nm
PMOS W=7mm, L=150mm

## Slide 6: Shaper study
Types of the shaper:
  Real-pole shaper
  Complex-pole shaper
Compared with the same
detection efficiency
(constant Tw)
  Peaking time of the Real shaper
  Peaking time of the Complex shaper
Order of the Shaper | RU-2 | RU-3 | RU-4 | RU-5 | RU-6 | RU-7 | RU-8 | RU-9
Peaking time(µs) | 1 | 1.47 | 1.92 | 2.26 | 2.57 | 2.83 | 3.11 | 3.32
Order of the Shaper | CU-2 | CU-3 | CU-4 | CU-5 | CU-6 | CU-7 | CU-9
Peaking time(µs) | 1 | 1.65 | 2.15 | 2.54 | 2.87 | 3.15 | 3.62
2° order
5° order

## Slide 7: Noise performance of the considered Shapers
  Increasing the order after 5 is not useful.
  The performance of both types are quite similar with a small advantage for the complex-pole shaper
Layer 5
NMOS: W=9mm L=250nm

## Slide 8: Readout architecture
  First pole of the shaper implemented in the preamplifier
  Advantages:
    Simple architecture (area, power)
    High sensitivity (1/Cf) in the charge preamplifier (no pile-up at the PRE output)
    Leakage current of detector intrinsically discharged
    Drawback:
    Noise of the Rf
  Complex or real poles

## Slide 9: Charge Pre-Amplifier
Types of the preamplifier:
  NMOS was selected as input FET
  Two charge Pre-amplifier were designed and compared
    3-stages amplifiers
    Folded-cascode architecture
  The results show better performance of 3-stage amplifier
Specification | 3-stage CPA | Folded-cascode CPA
DC gain (dB) | 82.8 | 71
BW (MHz) | 6.95 | 17.5
PM (Deg) | 117 | 103
Rise time (ns) | 28.7 | 17.56
Slew rate (V/µs) | 4.45 | 7.96
Dynamic range (MIP) | 57 | 47
Output voltage peak from DC level (mV) @ 15MIP | 290 | 261

## Slide 10: Charge Pre-Amplifier Dynamic Range
Cadence simulation of the preamplifier
Output of Charge Pre-amplifier in different MIPs
Linearity error of the charge Pre amplifier at the output of the shaper
+15 MIPs
-15 MIPs

## Slide 11: Preliminary shaper architecture : CR – RC2
  Very simple implementation of the real-poles
  Tentative shaper already designed.

## Slide 12: Preliminary implementation of the complex-pole shaper
  Implementation of 2 complex-pole with Sallen-key architecture.
  Possibility to design a fully differential architecture (currently under evaluation).

## Slide 13: Output preamp L5, 15 MIPs

## Slide 14: Power dissipation
Design targets:
1,2 mW/channel
All Triple-well nMOSFET, low-Vt pMOSFET
Keep constant power request Vs. Input signal
PSRR: Shaper Ok, differential amplifier
Preamplifier Sensibility to GND
Input Fet | Charge Pre-amplifier | Shaper | Rest of the circuit
500µA | 140µA | 83µA | NA
Current consumption
Used power: 0.87 mW

## Slide 15: Noise evaluation of the circuit
Charge Pre-Amplifier with real-pole shaper
 | Peak. time | Strip Rs | Input FET | Charge Pre-amplifier | Rf | Other shaper stages | Total
Layer5 | 1us | 445 | 416 | 181 | 594 | 285 | 915
Layer 4 | 500ns | 471 | 434 | 207 | 611 | 302 | 957
ENC of the different stages. (All values in electrons rms)

## Slide 16: Analog FE efficiency simulation
CR – RC2 shaping
Efficiency based on BG hit energy distribution
Data from: M. Manghisoni, L. Ratti, C. Stella.
Layer | CD (pF) | Selected Tp (ns) | Hit rate/stripe (KHz) | Efficiency
4 | 52.6 | 500 | 17.5 | 0.993
5 | 67.5 | 1000 | 11.3 | 0.990

## Slide 17: Conclusion and future activities
Refine preamplifier design and define ultimate performances
Choose shaper filter (type, order, differential structure?)
Design final shaper (also including an inversion stage)
Design the remaning blocks (BLR, trim. DACs, ToT, ....)