## Slide 1: DC trigger test
Present layout
Trigger electronics
Experience with cosmic
Experience at test beam

## Slide 2: DC SuperB present-1 design
 | SL1 | SL2 | SL3 | SL4 | SL5 | SL6 | SL7 | SL8 | SL9 | SL10 | TOT
Planes | 8 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 
Type | A | U | V | U | V | U | V | U | V | A | 
#wires | 172*4 204*4 1504 | 118*4 472 | 134*4 536 | 150*4 600 | 166*4 664 | 182*4 728 | 198*4 792 | 214*4 856 | 230*4 920 | 246*4 984 | 8056
#TSF 48 opt | 32 | 10 | 12 | 13 | 14 | 16 | 17 | 18 | 20 | 21 | 173
#NBCD 48 opt | 2 | 1 | 1 | 1 | 1 | 1 | 1/2 | 1/2 | 1/2 | 1/2 | 15
#TSF 64 opt | 24 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 132
#NDCB 64 opt | 1/2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 10/11
Number of wire could increase due to internal radius uncertainties.
The 48 vs 64 depends on the form factor of the FE board used at the moment a conservative
assumption has been made (i.e. 6U VME form factor)

## Slide 3: BaBar Strategy (1)

## Slide 4: BaBar Strategy (2)
Serialization occurs here
all DC hits on optical links
with this strategy 64 links.

## Slide 5: DC SuperB present design
Super B detector
8056 wires
from DC
FE crate SL1
FE crate SL2
FE crate SL3
FE crate SL4
FE crate SL5
FE crate SL6
FE crate SL7
FE crate SL8
FE crate SL9
FE crate SL10
1504 wires from DC
472 wires from DC
536 wires from DC
600 wires from DC
664 wires from DC
728 wires from DC
792 wires from DC
856 wires from DC
920 wires from DC
984 wires from DC
246 wires on SL10 is not what we would like to match the EMC sector in F. 240 would
be better because in this case we would have 40 cells a perfect match with 9 degree EMC
sector.

## Slide 6: DC SuperB present design
FE crate Super layer 10
CPU
DC FRONT END
Discriminator
DC FRONT END
Discriminator
DC FRONT END
Discriminator
• • •
ethernet
link
• • • • •
64 channels
64 channels
64 channels
copper/optical link
copper/optical link
copper/optical link
Test Discriminator needed @tbeam
Input signals
from DC front end
discriminated signals
In SuperB the discriminator board becomes a mez card and can be upgraded in order to compute TSFs and deliver them through a copper or optical link if there are radiation problems. Otherwise the «standard» solution would be welcome.

## Slide 7: RF emulator needed @tbeam
We have also built a ring oscillator to emulate RF when a machine trigger occurs.
And a transition board to feed Virtex6 demo board with LVDS signals.

## Slide 8: Some comments
In our case we had the signal from BTF. This signal intrisically jiitters by 10 ns. The reason being that the BTF cathode emits 350 micro bunch with a 28 ps time distance.
A single electron can belong to any of this micro-bunch.
The RF from BTF starts the ring-oscillator which mimicks the RF.

## Slide 9: Trigger setup
Clocked discriminator
discriminator
ring oscillator

## Slide 10: TSF (Track Segment Finder)
P
P
P
P
4 pattern for a fixed pivot tube. The other 4 pattern can be found via a parity transformation.
So in this example there are 8 patterns per pivot tube and 4 pivot tubes. In total 32 combinations. 5 bits are enough to code the info. 14.8 MHz sampling means 74 Mbit/s link.

## Slide 11: The prototype
It consists of 8 layers.
So it was natural from the trigger point of view to split it in two equivalent SLs.
Only track candidate with all hits are here considered.
At the moment we are investigating the problem delivering hits to an HPTDC

## Slide 12: What we got on cosmic
In our case 20 address per
single multilayer

## Slide 13: cosmics

## Slide 14: #Tracks vs sampling frequency data
Sampling frequency (MHz)
Number of tracks
addr1%addr2

## Slide 15: Number of fired lookup tables (on cosmic)

## Slide 16: Time correlation among hits cosmic
Correlation in time
the three hits with lowest time

## Slide 17: Number of fired lookup tables (on data)

## Slide 18: Time correlation among hits
Correlation in time
the three hits with lowest time

## Slide 19: Resolution studies on cosmic
only 2 lookup tables fired
RMS=17 counts i.e. 27 ns
more than 1 lookup tables fired
RMS=15.15 counts i.e. 24 ns
The algorithm is rather simple we assert the trigger on the basis of the first hit coincidence we
have

## Slide 20: Resolution studies on beam
only 2 lookup tables fired
RMS=18.8 counts i.e. 30 ns
more than 1 lookup tables fired
RMS=13.17 counts i.e. 21 ns