## Slide 1: Shortest Possible Beams from Conventional Accelerators
Generation of sub-fs electron beams
Klaus Floettmann
LAOLA Collaboration, Deutsches Elektronen-Synchrotron DESY

## Slide 2: well…
as short as an electron!
Generation of very low charge, very high quality, very short bunches
~ 5 MeV
80 fC (5 ·105 electrons)
transverse emittance < 50 nm
bunch length <10fs
for time resolved electron diffraction experiments
and
as probe for external injection experiments

## Slide 3: REGAE: The Relativistic Electron Gun for Atomic Exploration
Build in collaboration with University Hamburg and Max Planck Society

## Slide 4: REGAE: The Relativistic Electron Gun for Atomic Exploration

## Slide 5: Time Resolved Electron Diffraction
static diffraction pattern of Gold sample

## Slide 6: Simulation Example: 80 fC, 5 MeV (opt. assump. for bunch shape and thermal emittance to explore the limits)
Transverse emittance vs. longitudinal position
Simulation parameters:
Q = 80 fC
σxcath = 7 μm
σtcath = 500 fs
perfect cylindrical bunch
Ekin = 0.1 eV

## Slide 7: Simulation Example: 80 fC, 5 MeV (opt. assump. for bunch shape and thermal emittance to explore the limits)
Transverse beam size vs. longitudinal position
Simulation parameters:
Q = 80 fC
σxcath = 7 μm
σtcath = 500 fs
perfect cylindrical bunch
Ekin = 0.1 eV

## Slide 8: Simulation Example: 80 fC, 5 MeV (opt. assump. for bunch shape and thermal emittance to explore the limits)
7 fs
Bunch length vs. longitudinal position
Simulation parameters:
Q = 80 fC
σxcath = 7 μm
σtcath = 500 fs
perfect cylindrical bunch
Ekin = 0.1 eV

## Slide 9: What limits the compression?
induced RF chirp
defocussing space charge field

## Slide 10: transverse space charge field (in the rest frame)
L
R
For R < L the transverse space charge field at a position r scales as:
the transverse field is divergent!
even a zero emittance beam cannot be focused to zero beam size

## Slide 11: transverse space charge field
Focus without space charge
z
Laminar focus with space charge
z
Laminar focus with cross over trajectories
z
High charge calculation
over focused particles

## Slide 12: Transverse focus for plasma experiment
Courtesy Max Hachmann
xrms = yrms = 2.8 µm
zrms = 5 µm

## Slide 13: Emittance growth due to strong transverse focus
Courtesy Max Hachmann

## Slide 14: longitudinal space charge field (in the rest frame)
L
R
For L < R the longitudinal space charge field at a position ζ scales as:
the longitudinal force saturates for pan-cake like bunches
no problem with mixing of laminar and cross-over trajectories !

## Slide 15: What limits the compression?
induced RF chirp
defocussing space charge field
longitudinal Emittance
  space charge
  RF curvature
  non-linear bunch compression

## Slide 16: Long. emittance: Influence of the long. distribution
longitudinal phase space at the focus
uniform distribution
RF curvature & non linear compression
space charge
start a distribution with linear longitudinal field

## Slide 17: Long. emittance: Influence of the long. distribution
influence of the longitudinal distribution on the rms bunch length is negligible, but …

## Slide 18: Long. emittance: Influence of the long. distribution
uniform ellipsoid
parabola
start a parabolic beam and correct the curvature by a 3rd harmonic cavity

## Slide 19: Correction of the curvature with a 3rd harmonic cavity
longitudinal phase space at the focus
parabolic distribution plus 3rd harmonic cavity
rms bunch length in the focus:
0.6 µm = 2 fs

## Slide 20: Correction of the curvature with a 3rd harmonic cavity

## Slide 21: Correction of the curvature with a 3rd harmonic cavity
3rd harm. cavity
long. focus
trans. focus

## Slide 22: Correction of the curvature with a 3rd harmonic cavity

## Slide 23: Non-linear bunch compression
The longitudinal shift of two particles in a drift is given by:
with

## Slide 24
… with the correction cavity in place the compression is again emittance dominated. We can try to compress further by reducing the emittance and/or increasing the RF chirp …

## Slide 25: Generation of incoherent energy spread at the cathode
emission time
energy
head
tail
r = 0
r > 0

## Slide 26: Generation of incoherent energy spread at the cathode: uniform distribution
longitudinal position
energy

## Slide 27: Generation of incoherent energy spread at the cathode: parabolic distribution
longitudinal position
energy

## Slide 28: Generation of incoherent energy spread at the cathode: ellipsoidal distribution
longitudinal position
energy

## Slide 29: Dependence on initial bunch parameters

## Slide 30: Dependence on initial bunch parameters
parabola
uniform
ellipsoid

## Slide 31: minimal bunch length as function of emission time
700 as

## Slide 32: Longitudinal phase space for 2.0 ps emission time

## Slide 33: Conclusion
generation of very low emittance, sub fs bunches seems possible even at low energies
similar bunch length with higher charges and slightly higher emittance reached at higher beam energy: Talk by Alberto Bacci, Monday WG1.
still more work: parameter (energy) dependence of compensation, ellipsoidal bunch?, include wake fields, electron - electron scattering…