## Slide 1
An Overview of The Novel Accelerator Research Activities in Asia
Chuanxiang Tang (唐传祥）*
*Tang.xuh@tsinghua.edu.cn
Department of Engineering Physics, Tsinghua University, Beijing 100084, China
First European Advanced Accelerator Concepts Workshop (EAAC2013), June 2~7, 2013, La Biodola, Isola d’Elba, Italy

## Slide 2: Outline
1. Introduction
2. High Gradient Accelerating Structures
3. Laser Wakefield Accelerators
4. ICS g/x-ray Sources
5. Summary

## Slide 3
Past
A model of the first cyclotron of Livinston and Lawrence, which can accelerate protons to 80keV
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 4
Now
LHC-a 27km proton synchrotron at CERN, 2x7TeV
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 5
Future?
The Universe in a Nutshell, by Stephen William Hawking, Bantam, 2001
Without further novel technology, we will eventually need an accelerator as large as Hawking expected.
Sun
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 6
Because of the synchrotron radiation, the next high energy electron accelerator may be a linear accelerator, may be ILC or CLIC, or Both
High gradient is essential for LC, no matter how to get it…

## Slide 7
Develop Very High Gradient Accelerating Structures
From L-band and S-band, to C-band and X-band: achieve higher gradient
  Higher Frequency
  New Structure
  New Material
  New Manufacture Procedure
  New Understanding of Breakdown
Wakefield Accelerator
  Beam Driven Plasma Wakefield Accelerator
  Beam Driven Dielectric Wall Accelertor
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 8
Combine Laser Technology with Accelerators
Acceleration-Laser Plasma Wakefield Accelerator,…
Beam Diagnostics-Laser Wire, …
Electron or Ion Source: Photocathode Gun, Laser Plasma Ion Source,…
Light Source-Inverse Compton/Thomson Scattering X-ray Source, Seeded Free Electron Laser,…
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 9
A brief Overview of The Novel Accelerator Research Activities in Asia
High Gradient Accelerating Structures
Laser Plasma Wakefield Accelerators
Inverse Compton g-ray/Thomson Scattering X-ray Sources
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 10
The High Gradient Researches in Asia
X-band (11.424GHz) Structures development at KEK
Choked Mode Accelerating Structures
C-band (5.712GHz) at Spring-8
X-band (12GHz) at THU
Others :
SINAP-C Band Traveling Wave Disc Structures
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 11: High gradient in linear colliders
GHz MV/m GeV
SLAC 3 17 50
ATF 3 30 1
VLEPP 14 100 1000
GLC 11 50 1000
CLIC30 30 150 3000
ILC 1 31.5 500
CLIC12 12 100 3000
80’ Started serious R&D for LC
90’s proof in high gradient and mass production
00’s transition from warm to cold but keep warm alive
10’s reinforcing high gradient + wake field
T. Higo, Invited Talk at Symposium on High Gradient Accelerating Structures, THU, Beijing, May 19th 2013

## Slide 12
X-Band Accelerating Structure Development at KEK
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 13
A
B
Control
RF source for A
Shield A
Shield B
Nextef for high gradient R&D

## Slide 14: High-gradient test at Nextef
Basic studies at shield-B
TD24R05 #2
TD24_Disk_#4
High power components test
KT1 to shield-B
TD24R05 #4?
TD24R05(KEK)?
Replace klystron
T18_Disk_#2
TD18_Quad_#5
TD18_Disk_#2
Narrow waveguide test
KT1
Nextef
KX03 (60cm HDDS)
T24_Disk_#3
4 7 10 1 4 7 10 1 4 7 10 1 4 7 10 1 4 7 10 1 4 7 10 1
2008 2009 2010 2011 2012 2013
Shield-B
CLIC prototype tests
GLC
1
2
3
4
5
1.5

## Slide 15: CERN/SLAC/KEK test flow (as usual)
Design for CLIC (CERN)
Fabrication of parts (KEK)
Bonding (SLAC)
CP (SLAC)
VAC bake (SLAC)
High power test (NLCTA-SLAC)
High power test (Nextef-KEK)
Notes: プロトタイプの試験サイクル
ここでも 日米を基礎におく SLAC・KEK キープレーヤー

## Slide 16: Fabrication and test of LC prototype structures T18 TD18T24TD24TD24R05TD24R05
T18_Disk_#2
TD18_Disk_#2
T24_Disk_#3
TD24_Disk_#4
d
d
2009
2010
2011-2012
2011
TD24R05_#2
TD24R05_#4
d
Under vacuum balking at SLAC to be tested at KEK in April
2012
2013

## Slide 17
T. Shintake, EPAC1996, C-BAND CHOKE MODE ACCELERATOR STRUCTURE FOR THE LINEAR COLLIDER
C-band Choke Mode Accelerating Structure for LC
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 18
Spectra of seeded (red lines) and unseeded (blue lines) conditions given by experiment (a) and simulation (b)
http://xfel.riken.jp/eng/index.html,
http://www.s.u-tokyo.ac.jp/en/press/2011/01.html, May 31, 2013
T. Inagaki, et al, MOPB005, Proceedings of LINAC2012, Tel-Aviv, Israel
128 C-band Choke Mode Accelerating Structures of 5.7GHz Was Used at SACLA XFEL
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 19: New Choke Mode X-band Structure Designing for CLIC (CDS-C) by THU/CERN
Features include “two-section”, “impedance matching”, “detuning”
1.6mm
1.2mm
2.0mm
Hao Zha, et al, PRST ACCELERATORS AND BEAMS 15, 122003 (2012)

## Slide 20: Damping Result of The CDS-C Compared with WDS
 | W⊥ (s=0.15m) V/m/mm/pC
WDS | 5
CDS-A | ~30
CDS-C | 4~5
Freq(GHz) | Q | (R/Q)⊥
15.7 | 5.4 | 80.3
18.6 | 6.9 | 63.2
23.7 | 3.8 | 14.8
28.4 | 12.4 | 10.9
38.2 | 11.6 | 9.9
s | CDS | WDS
Fc | 1 | 1
Frms | 4 | 5
Fworst | 25 | 20

## Slide 21: Bunch Excitation to Measure the Damping
AWA at ANL
Structure can be moved, driven by step motor
  Offset to excite dipole modes
(No following bunch at the moment)
Under construction

## Slide 22: Experiment Layout
Time domain signal with fast scope (0~36GHz)
With -30dB attenuation signal strengh ~1V/nC/mm.

## Slide 23: Everything is ready, except…
3cells with SiC
3cells without SiC
RF probe installed

## Slide 24: Status of C-band at SINAP
Prototype accelerating structure is high tested.
The new structure is designed and fabricated.
Pulse compressor is designed and partially tested.
The first high power test box is ready, and second one is planed.
WenCheng FAN, CLIC Workshop 2013

## Slide 26
Simulations and Theoritial
Preparing Laser for LPWA
Experiments
JAEA:4TW,40fs
OSAKA U.:
Gekko PW
Hamatsu 4TW, 150fs
GIST:100TW, 75fs
KERI:20TW, 37fs
RRCAT:9TW, 45fs
NCU: 100TW,30FS
IoP: 100TW
THU:20TW,30fs
SIOFM: 300TW,30fs
CAEP:>100TW
CIAE
Dates from published papers after 2009
Laser Plasma Wakefield Accelerator Research Activities in Asia

## Slide 27
PKU: 200TW
SJTU: 200TW
THU/IHEP/CIAE/BNU
FDU
HZU
LZU
USTC
NUDT
More Universities and Institutes are involved in the LPWA .
SJTU and PKU have ordered their 200TW laser systems for LWFA studies.
Simulations and Theoritial
Preparing Laser for LPWA
With Experiment Systems
NCTU

## Slide 28
Electron Beam Quality Improvement Experiments

## Slide 29
ne=1.00 X1019 cm-3
Driver
a0=1.2
Injecting
a1=0.2
Energy: 134MeV
E Spread: 3.5%
Charge: 8.7pC
Divergence: 4mrad
Electron Optical Injection Experiments at JAEA
H. Kotaki, et al, PRL 103, 194803 (2009)
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 30
ne=3.95 X1019 cm-3
Driver
a0=0.6
Injecting
a1=0.1
Countercrossing: 135°
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 31
Electron beam profile according to laser’s polarization
Electron beam direction
Manipulation of laser accelerated electron beams at JAEA
H Kotaki, et al, Plasma Phys. Control. Fusion 53 (2011) 014009
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 32
100TW laser at GIST
Electron beams pointing instability from LWFA and Influence to energy measurement
H. J. Cha, et al, RSI 83, 063301 (2012)
Nasr A.M. Hafz et al,NIM A 637(2011)
N.Hafz, et al, AAC 14TH Workshop, 2010
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 33
LWFA with external magnetic field and laser prepulses
Tomonao Hosokai, et al, APPLIED PHYSICS LETTERS 96, 121501 2010
Magnetic field: 1T; Prepulse: ps~ns
Main Laser: 7TW
Electron energy :100 MeV, charge: 20 pC, emittance: 0.02 p.mm.mrad
Osaka U.
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 34
stable and low-divergence electron beam with Argon
M. Mori, et al, PRST - ACCELERATORS AND BEAMS 12, 082801 (2009)
4TW Laser
Argon
Helium
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 35
LWFA experiments in at RRCAT (India)
Sanyasi Rao Bobbili et al , New Journal of Physics 12 (2010) 045011
Bobbili Sanyasi Rao, et al, PoP 18, 093104 (2011)
Laser: 9~10TW, 45fs, 790~800nm
Helium Gas jet: 1-5x1019/cm3
Raja Ramanna Centre for Advanced Technology
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 36
Enhancement of injection and acceleration of electrons in a laser wakefield accelerator by using an argon-doped hydrogen gas jet and optically preformed plasma waveguide
Ho et al, Phys. Plasmas 18, 063102 (2011)
 | 800nm | 800nm | 900nm
Pulse Energy | 3.3J | 450mJ | 200mJ
Duration | 33fs | 27fs | 32fs
Power | 100TW | 16.7TW | 6TW
NCU, at Taiwan

## Slide 37
Experimental and Simulation with XL-II OF IoP
Plasma density and Laser pulse evolution
Beam quality:
23 MeV/~7%/4 pC/2 mrad
Normalized Emittance:
IHEP & IOP
Courtesy of J. Gao

## Slide 38
GeV Electron Beam

## Slide 39
Cascaded LWFA Experiment at SIOFM
J. S. Liu, et al, PRL107, 035001 (2011)
Shanghai Institute of Optics and Fine Mechanics
50TW laser
a 0.8-GeV quasi-monoenergetic electron beam
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 40
Numerical study of 1.1 GeV electron acceleration over a-few-millimeter-long plasma with a tapered density
M. S. Hur and H. Suk, PHYSICS OF PLASMAS 18, 033102 2011
GIST

## Slide 41
New Ideas of LPWA Studies

## Slide 42
Dense atto-second electron sheet generation from LWFA with a up-ramp plasma density
SJTU
Z.M. Sheng, et al, PRL110, 135002 (2013)
t-=71TL
t-=83TL
up-ramp plasma density profile followed by a plateau;
a fairly large laser focus diameter;
different from the bubble (complete blowout) regime
ultrathin (atto-second duration), high charge ( ~nC)
10 Hz, Ti: Sapphire laser
@ LLP, SJTU
800 nm, 200 TW, 25 fs
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 43
High Brightness Electron Beams via Ionization Injection by Transverse Colliding Lasers in a Beam-Driven PWA
Tsinghua U.
Pre-ionized Plasma +He gas
x emittance | y emittance | z emittance
8.5 nm·rad | 6.0 nm·rad | 0.06 keV·ps
Energy | Slice energy spread | Correlated energy spread
5.3 MeV | ~12 keV | 0.2 MeV
Charge | Peak current | Brightness
4.6 pC | 0.44 kA | 1.7×1019A∙rad-2 ∙m-2
W. Lu, et al, accepted by PRL;
TUPEA022, IPAC2013

## Slide 44
Snapshots Plasma Wakefield Using Ultrashort Electron Probe
Tsinghua U.
Electron density map of injection simulation
Density variation of the probe on the screen
total injected charge (red filled circle) using the recovered electric field and the externally injected charge (blue filled square) we set in the simulation
Electric field
W. Lu, et al, TUPEA027, IPAC2013
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 45
Proton or Ion Acceleration

## Slide 46
XQ Yan, et al, PRL 100, 135003 (2008)
Conditions of the PSA:
Phase Stability Acceleration (PSA)
PKU
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 47
“a quasiequilibrium for the electrons is established by the light pressure and the space charge electrostatic field at the interacting front of the laser pulse. The ions within the skin depth of the laser pulse are synchronously accelerated and bunched by the electrostatic field, and thereby a high-intensity monoenergetic proton beam can be generated.”
XQ Yan, et al, PRL 100, 135003 (2008)
PSA (II)
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 48
XQ Yan, et al, PRL 103, 135001 (2009)
GeV, Nanocoulomb, Collimated Proton Beam by PSA
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 49
Huang et al. Phys. Plasmas 19, 093109 (2012)
Ultra-relativistic ion acceleration in the laser-plasma interactions
CIAE
An analytical relativistic model is proposed to describe the relativistic ion acceleration in the interaction of ultra-intense laser pulses with thin-foil plasmas. It is found that there is a critical value of the ion momentum to make sure that the ions are trapped by the light sail and accelerated in the
radiation pressure acceleration (RPA) region.

## Slide 50: LAser proton accelerator (LAPA) at PKU

## Slide 51
Radiotherapy using a laser proton accelerator
M. Murakami, Y, Hishikawa, et al.
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 52
ICS Sources Based on LPWA
ICS X-ray
P Catravas, E Esarey and W P Leemans, Meas. Sci. Technol. Vol.12 P1828, 2001
LAL, LBNL,RAL Nature, Sept. 2004

## Slide 53
LWFA for ICS X-ray Sources of Hamamatsu
Yoshitaka Mori, et al, Applied Physics Express 5 (2012) 056401
A Ti:sapphire laser (pulse energy: 500 mJ; pulse width: 150 fs)
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 54
N. Hafz, et al, IEEE Trans. On PLASMA SCIENCE, VOL. 31, NO. 6( 2003)
N. Hafz, et al, AAC 11TH Workshop, 2004
J. Kim, et al, Journal of the Korean Physical Society, Vol. 51, No. 1,2007
Experiment at KERI
TS of LWFA Exp. Proposla
Experiment at GIST
Notes: 从加速器发展的历史，引出加速器的类型及其分类；从加速器的服务对象，给出加速器在各个领域的最新进展；
结论：加速器与激光技术的结合（激光加速、汤姆逊散射、自由电子激光、同步辐射的超快）；更高的加速梯度、更小型化的加速器

## Slide 55
SHI
ICS g/x-ray Sources in Asia*
Tokyo U
KERI
JAEA
KEK
Osaka U,
HAMAMATSU
Nagoya U.
AIST
Tsinghua U.
SINAP
Waseda U.
*Not all of the ICS Sources in Asia, only some of those with papers published these years.

## Slide 56
The ICS g/x-ray Sources Experiments in ASIA Recent Years
 | Inst. | Acc. type | E-beam | Laser | X-ray | Appl.& Others
1 | SHI (JPN) | S-band, SW | 38MeV, 0,8nC, 3ps, 30um (rms), 3p.mm.mrad | 200mJ, 50fs(FWHM), 800nm | 165deg.:33.7keV, 2x106 ph/p,3ps, 6%fluct., 10Hz. 90deg: 17.1, 5x105, 150fs, 11%, 10 | Imaging
2 | JAEA (JPN) | Microtron | 150MeV, 60pC/pulse, 35(H)/8 (V) p.mm.mrad, 10ps (rms), 10Hz, 97umx72um, spatial jitter 12um, 32um | Nd:YAG 840mJ, 23ns, 1064nm, 10Hz, 27umx22um | ~400keV, 45±20ph/pulse, 10ps. | Imaging
1. Fumio Sakai, et al, International Journal of Modern Physics B, Vol.21, No 3&4(2007)
2. K. Kawase, et al, REVIEW OF SCIENTIFIC INSTRUMENTS 79, 053302 2008

## Slide 57
 | Inst. | Acc. type | E-beam | Laser | X-ray | Appl.& Others
3 | KEK –STF QETP(JPN) | L-band, SRF | 23MeV, 0.9nC/bunch, 15ps, 150/train, 85/95um (rms),spacing 2.8ns | 4mirrors OC: 0.3mJ, 7ps(FWHM), 1064nm, 89/85um, Finesse 335 | 8~9keV, 5460ph./train, 8.2x106 ph/s,8% bandwidth(FWHM) | Biology Material Imaging
4 | KEK-LUCX (JPN) | S-band, TW | 43MeV, 0.5nC/bunch, 100/train | 2-mirror OC, 110 uJ/pulse | 104ph./train | Upgrading
3. J Urakawa, IX International Symposium on Radiation from Relativistic Electrons in
Periodic Structures (2012); K. Sakaue,et al, WEPWA017, IPAC2013.
4. Masafumi Fukuda , et al, NIM A637(2011) S67-71
5 | SINAP(China) | S-band, ther. gun | 108.1MeV, 2.5ns | 10MW, 35ns, 1064nm | 102~103 ph./s, ~30keV | Upgrading
6 | THU-TTX(China) | S-band, TW | 46.7MeV, 0.2nC/bunch,10Hz | 300mJ/pulse, 800nm, | 106ph./pulse, 51.7keV, | Imaging, detector colli.
6. C. Tang, et al, NIM A608, (2009) 70-74; Y. Du, et al, RSI, 84, 053301 (2013)
5. Courtesy of W. Xu (2012); and Proc. of SPIE Vol. 7385 73852D-3(2010)

## Slide 58
Tsinghua Thomson scattering X-ray source (TTX)
Electron beam |  | Laser beam | 
Energy | 45MeV | Wavelength | 800nm
Bunch length | 1~4ps | Pulse duration | ~30fs
Charge | ~0.7nC | Pulse energy | ~500mJ
Beam size | 30(H)x25(V)um | Beam size | ~30um
Parameters of Scattering X-ray | 
Photon energy | 24(90deg)~48(180deg)kev
Pulse duration | 0.16(90deg)~3(180deg)ps
Number photons | 8.4X106(90deg)~5.5X107(180deg)

## Slide 59
Electron Linac

## Slide 60
Laser System
800nm, ~20TW, ~30fs
266nm, 1mJ, 30fs~10ps
RF Gun
TS IP

## Slide 61
Thomson Scattering Interaction Point
Laser compressor
Delay stage
Interaction chamber
The laser is focused by a parabolic mirror with 4mm hole in center.
Ground glass screen for beam profile measurement
electron
laser
Dipole
Triplet

## Slide 62
Typical background and X-ray signal
Background x-ray from beam dump
Background x-ray from beam lost in the hole
The background from the beam is suppressed successfully.
Measured Electron and laser specifications
laser electron
Energy 800nm(1.55eV) 46.7MeV (spread 0.3%, rms)
Intensity 300mJ 0.2nC (~3mm.mrad)
Beam size ~100um (rms) ~35x40um^2(rms)
Pulse width ~70fs(FWHM) ~2.7ps
Expected (simulated)flux of X-rays: ~2.5X106;
Measured x-ray flux : ~1.0X106;
Thomson Scattering and Background X-ray Signals
Reasons:
misalignment in transverse and longitudinal?
A light at 2011

## Slide 63
X-ray signal according to the Laser power: Linearity is good between the laser power and the intensity of X-rays;
Measured X-ray pulse flux according to the laser power

## Slide 64
Instability (RMS) : 17%
Stability of the X-ray Pulses

## Slide 65
X-ray Profile measured by CsI screen and EMCCD
Simulation
Experiment

## Slide 66
X-ray pulse spectrum measurement
The scattered photon energy as a function of beam parameters for a head-on collision in Thomson scattering x-ray source can be written as
Scattering point
Silicon film
CsI screen
q

## Slide 67
X-ray pulse spectra

## Slide 68
X-ray pulse relative average energy according to the scattered x-ray photon direction

## Slide 69
X-ray imaging and other applications at TTX
X-ray detector calibration: time response, spectral response, polarization calibration (for astrophysics)
Mono-energy X-ray Imaging: small spot size; nm space resolution, PCI and other new imaging technologies.

## Slide 70
Next step of TTX-Improving the average brightness

## Slide 71
The mini electron storage ring
The electron storage ring is smaller, its physics more complicate, and more difficult to develop.
The circumstance of the mini-ring is 3.6m. Maybe it is too small…
Another 4.8m ring is under design.

## Slide 72
150cm
300cm
TTX-p : Setup Diagram – Dimensions & Distances
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
This drawing is not on scale
Coherent
Verdi-V6
Coherent
MIRA oscillator
λ/4
λ/2
Faraday
Isolator
EOM
FS
SLIT
PDH-PD
Coupling-PD
TL-SPD
PD
M1
M4
M2
M3
TRANSMISSION
CCD
A
B
1.1m
FSR=79.33MHz
47cm
?cm
20cm
55cm
f1=40cm
20cm
ρ=20cm
38cm
M6
18cm
7cm
？cm
f2=-?cm
f3=?cm
？cm
?cm
?cm
10cm
The optic cavity design

## Slide 73
HG x-band structures are producing and testing at KEK. Now THU is involved in the collaboration, and Choke mode structure is waiting for its first beam testing…
LWFA attracts lots of universities and institutes in Asia. Except for GeV beams, several experiments for improving the electron beam quality have been done. And big lasers have been bought specially for LWFA.
Several ICS x-ray sources have been developed, and used for different applications. Upgrading or new projects are putting forward.
There are lots of other Novel Accelerators Activities in Asia, which I am not mentioned here.
Summary

## Slide 74
Thanks for Your Attention！