## Slide 1
Laserwire: high resolution non-invasive beam profiling
for advanced accelerators
L. J. Nevay, S.T. Boogert, P. Karataev, K. Kruchinin,
JAI @ RHUL, Egham, UK
L. Corner, R. Walczak,
JAI @ Oxford University, UK
G. Blair,
STFC, UK
Aryshev, N. Terunuma, J. Urakawa,
KEK, Japan

## Slide 2
Linear colliders – ILC/CLIC
New colliders e-/e+ high precision machines.
Two main current designs - International Linear
Collider (ILC) and Compact Linear Collider (CLIC).
Extreme focusing/charge/luminosity requirements.
Making focussed beams of 1 – 5 nm.
Need high quality measurements of beam size,
emittance, position, charge, duration……….

## Slide 3
Laserwire beam size measurement
Focussed laser spot
translated across
electron beam
Compton scattered photons
detected downstream
after bending magnet
Measured scan is convolution of laser spot size and particle beam size
- small laser spot: good spatial quality, short l, excellent focusing optics.

## Slide 4
ATF2 major international collaboration – scaled test of ILC optics.
Aim – electron beam size < 40nm.
Major test of new diagnostics – high resolution (< 5nm) bpms, fast feedback etc.
Laserwire designed for highest resolution – measurement ~ 1mm.
Prototype installation – aim for turnkey operation.
ATF2 laserwire
Charge | 1 – 8 x 109 e
Energy | 1.28 GeV
Beam size (LWIP) | 100 x 1 mm
Bunch | 30 ps (3.12Hz, single bunch)
Laser (532nm, Nd:YAG) | 100 mJ, 77 ps

## Slide 5
IP
vacuum
chamber
electron beam
laser beam
actuator driven
mirrors
post IP diagnostics
Layout of ATF2 laserwire
Electron beam has large aspect ratio.
Difficult to accurately extract beam size – non
Gaussian convoluted scan.
Need to measure propagation properties of
laser and use these to fit H/V electron beam sizes.
Laser has poor spatial quality
and is astigmatic – hard to model.
Beam input to
final focus lens
2zR ~ 30 – 40 mm.

## Slide 6
ATF2 laserwire experiment
Entire vacuum chamber + focusing lens
moves vertically and horizontally to scan
laser focus over electron beam.
Detector
Laser beam transport
Laserwire IP

## Slide 7
Laserwire results
Rough vertical scan over electron beam:
find centre, optimise nonlinear scan
Initial alignment – temporal/spatial overlap of laser/electron beams:
10s ps, ~ 1mm.
Detailed scans over vertical/horizontal beam
Iteratively fit V/H size until converged.
Consistent measurement of vertical beam size = 1mm.
Analysis: L. Nevay

## Slide 8
Other experiment/measurements
Stanford Linear Collider – beam scanned across laser spot 350nm THG Nd:YLF, 1mJ, 10MW, prototype - Alley et. al., NIM A 379, 363 (1996).
KEK ATF2 damping ring – cw - cavity on moveable table scanned through beam
532nm, stored power 1 – 3W, e- s = 9.8 ± 1.5mm - Sakai et. al., PR STAB 5, 122801 (2002).
Oak Ridge SNS – H- ion laserwire, Nd:YAG, 1064nm, 30 Hz, 7ns
9 stations, 1 laser, beam sizes s ~ 2 – 3mm - Liu et. al., NIM A 612, 241 (2010).
PETRA – 2D scanning, 6 GeV e+, 130kHz, 40ps, Q switched 6ns Nd:YAG, 532nm, 20Hz, convoluted beam size s = 30mm (V) - Bosco et. al., NIM A 592, 162 (2008).
Measurements of source size for X-rays generated by scattering from laser plasma accelerated electrons – Chen et. al., PRL 110, 155003 (2013).

## Slide 9
Laser at the ATF not completely suitable for laser-wire.
Poor spatial quality – larger focus, worse resolution.
Temporal profile (77 ps) not ideally matched to electron bunch (30 ps).
Inefficient (flashlamp pumped), limited in repetition rate – no intratrain scanning.
Project in Oxford to develop
new fibre laser system for laserwire.
Fibres: efficient, waveguides, excellent spatial
mode quality, high repetition rate, diode pumped, no active cooling.
Standard SM fibre amplifiers – low energy.
Solution – very large mode area photonic crystal fibre – still single mode, energy 100uJs/pulse.
Laser improvements

## Slide 10
Aim – better laser source for laserwire, smaller laser spot, intratrain scanning.
Spec – 100mJ @ 6.49MHz ir, M2 <1.1, < 10ps, Dl < 1nm green.
Expt – amplify commercial fibre laser (Amplitude) in photonic crystal fibre, burst mode – pump first, then extract built up gain.
Results – pulses amplified from 1.4mJ to 268mJ in 70cm of PCF
M2x = 1.07 ± 0.02, M2y = 1.09 ± 0.02.
Lower energy pulse in green Dl = 0.5nm.
Lower energy pulse compressed to s < 1.5 ps.
Pulse trains inspired investigation of multiple pulse LWFA – see talks by Simon Hooker and Jens Limpert in WG1.
Beam at focus
Fibre laser results
Graphs: L. Nevay

## Slide 11
Summary
New diagnostics required for advanced accelerators.
Laserwire high resolution, high repetition rate non-invasive alternative
to screens, wires.
High resolution prototype installed at the ATF in Japan.
System successfully running and consistently measures 1mm beam size.
Non-ideal laser source – fibre laser development in Oxford.
Fibre laser performing to specification and suitable for intratrain scanning.