## Slide 1
Helical Accelerating Structure with Controllable Beam Emittance
S.V. Kuzikov1, A.A. Vikharev1, J.L. Hirshfield2,3
1Institute of Applied Physics RAS, Nizhny Novgorod, Russia
2Yale University, New Haven, CT, USA
3Omega-P, Inc., New Haven, CT, USA
Outline:
A problem of beam cooling in accelerators
Damping rings
Helical accelerating structure with asynchronous transverse fields (HSFC)
Calculation methods: perturbation theory and HFSS simulations
Parameter optimization in comparison with classical structure
Beam dynamics simulation by CST Microwave Studio
Conclusion

## Slide 2
0.3 ТeV ILC collider
Movement of particles in a focusing channel with dry friction
Transverse emittances:
Particles, moving in DC-magnet undulator,
produce synchrotron radiation which leads to cooling
According to Liouville’s theorem the phase volume can be reduced, if only there are friction forces in a system.
Wakefields cause growth of transverse emittances in accelerator behind damping rings.

## Slide 3
Low energy beams might be cooled in a damping ring:
Parameters:
W=5 GeV, I=400 mA, P=6700 m – total length of circumference, T=25 ms – transverse damping time.
ILC damping ring
In case of high energy particles the damping ring becomes too long.

## Slide 4
Such accelerating structure is impractical, because DC magnet system conflicts with feeding, focusing, and diagnostic systems. Inevitably large period does not allow to reach small emittance, because the smallest achievable emittance is proportional to squared wiggler period L.
The accelerator with alternating accelerating sections and wigglers reduces effective gradient.
- cooling rate in a periodic DC-magnet field.
H.H. Braun et al. Potential of Non-standard Emittance Damping Schemes for Linear Colliders, 2004.
, where W – particle energy.

## Slide 5: Helical Self Focusing and Cooling (HSFC) Accelerating Structure
Appealing features:
1. Non-synchronous transverse field components might provide: 1) emittance control (beam cooling due to synchrotron radiation of particles); 2) near axis beam focusing
2. A new structure has smooth shape of constant circular cross-section (no expansions or narrowings) and big aperture (no small irises)
3. A new technology of the mass production seems possible which allows avoiding junctions inside long accelerating section
E – accelerating field (synchronous with particles)
transverse field components
(far from Cherenkov synchronism)
Copper mandrel
HSFC = Accelerating structure + RF undulator + lens

## Slide 6
Dispersion curves: R=6.09 mm, P=8 mm, a=1.25 mm
Partial waves: 1) travelling TM01 mode + 2) near to cut off rotating TM11 mode
TM01: Ez0 at axis,
TM11: Ez=0 at axis, E  and H 0 at axis,
Normal waves
Partial waves
Slow normal wave 2 (vgrvph>0) consists of partial TM01 and TM11 waves.
The wave 2 is the operating wave (might be in synchronism, it has low group velocity).
Vphc
Vph0

## Slide 7
Electric field in HSFC accelerating structure. Calculation by HFSS.

## Slide 8
Complex amplitude of the electric field
Beam line

## Slide 9
Accelerating field component vs longitudinal coordinate for different phases (with step 5)
Accelerating component is uniform at beam line.

## Slide 10
Transverse electric field components at beam line vs length for different phases
Transverse components are also uniform and have much longer spatial period in comparison with period of the accelerating component.

## Slide 11
Phases of electric field components at beam line
Phase of accelerating component
Phases of transverse components
Accelerating E-field and transverse E-fields have opposite phase velocities!
Phase velocity of the accelerating component actually equals the light velocity.

## Slide 12
Transverse components of magnetic field at beam line
In HSFC structure both transverse electric and magnetic fields cause particle’s wiggling like in RF undulator.

## Slide 13
Phases of magnetic field components
Transverse magnetic fields together with transverse electric fields go toward electrons.

## Slide 14
Simulation of electric field evolution at beam line vs length (phase step is 20)
accelerating field
transverse fields

## Slide 15
Surface electric field
Surface magnetic field
Optimization requires maximum of accelerating field normalized on maximum of surface field:
Also maximum of shunt impedance is necessary:
Here holes and/or absorbers could be inserted to improve mode selection

## Slide 16
R=6.09 mm
a=1.25 mm
P=8 mm
hP=4.727
f=28.2 GHz
Q=10800
Eacc/Esurf=0.307
Rsh/L=18.9 MOhm/m
Results of HFSS optimization
Example:
f= 30 GHz structure, G=Eacc=100 MV/m, then B=0.75 T,
Beam energy W=25 GeV (=49000),
then necessary decay distance  2800 m.
Dispersion curve

## Slide 17
taper
Transverse particle momentums
Simulation of particle motion in 100 MV/m HSFC accelerating structure by CST Microwave Studio
Total length =10 periods
regular part
taper
TM01
Normal wave
taper
regular part

## Slide 18
Parameters of cooling in 100 MV/m HSFC structure

## Slide 19
In HSFC structure there is gradient of the asynchronous fields which leads to appearance of the ponderomotive (Miller’s) force:
Complex amplitude of electric field
at different cross-sections
The pondermotive force (due to longitudinal TM11 fields) in each cross-section is directed to the axis and provides beam focusing.
- frequency which electrons see.

## Slide 20
Bunch population during acceleration.
The blue color (at input) corresponds to low particle energy.
The red color (at output of structure) means the higher energy of the accelerated particles.
Simulation of ponderomotive force focusing in HSFC accelerating structure
by CST Microwave Studio
bunch
Parameters: initial energy 10 GeV, bunch length 1 ps, bunch diameter 3 mm, charge 100 nC, gradient 100 MV/m.

## Slide 21
Conclusion
TM01 – TM11 HSFC accelerating structure has non-synchronous electric and magnetic field components to be used in order to preserve low beam emittance and small energy spread.
Smooth beam focusing due to the pondermotive (Miller’s) force might also be used.
The structure allows high enough accelerating gradient normalized on maximum surface field (>0.3).
Shunt impedance is slightly less than in conventional accelerating structures. In order to increase shunt impedance, one might either to go to higher frequencies (Rsh/L~3/2) or to go to lower frequencies and to apply superconductivity .