## Slide 1: Advanced Positron Sources Alessandro Variola, LAL Orsay in2p3 - CNRS

## Slide 2: Outlook
Why positron sources are so important
Critical parameters
Classical sources. Schemes
Future colliders sources
Technology
What’s next?
Conclusions

## Slide 3: Why positron sources are so important for colliders?
Luminosity formula
Dependence: I ( N1, N2, f nb)
(sx, sy)
Both are mainly e+ source-dependent !!!! :
Positrons are anti-particles, need energy (at least 1 MeV) and conversion in a nuclear potential:
Production in a target, so the particle – matter interactions dominate……… They need a primary electron beam and in good approximation they have no memory (owing to the target).
1) Current => limited by the target characteristics (less dramatic for circular colliders)
2 ) Emittance => At the production 6D phase space is huge:
Longitudinal
Longitudinal
In bremsstrahlung sources the energy spectrum is wide, with a cut-off
Close to ~ electron beam energy. The captured positrons spectra are given
by the characteristics of the capture section. The flux captured depends on
the capture, the primary electron beam energy and density and....the emittance (not so much).
Transverse
The angular spread is given by the emission angle and the scattering that for the
Moliere theory is proportional to the √ of the target thickness and inversely
proportional to the momentum. So only the low density high
energy tail has a low production emittance (or very thin target)……the total distribution has a huge emittance > acceptance
Summarizing positron sources 6D emittance is defined by the capture system acceptance (very different from electron sources…!!) . Accepted flux is a function of target and primary beam characteristics

## Slide 4: What are the main constraints?
Conversion target technology. High Z allows high conversion efficiency. Thermal, mechanical and Bfield characteristics.
1) Melting point. AVERAGE EFFECT
Examples:
2) PEDD, Peak energy deposition. INSTANTANEOUS EFFECT
Thermo mechanical stress due to temperature gradient
Phonon velocity propagation
Experimental limits, SLAC (W 26Re) 6 X0, (~35J/g)
Moreover, electromagnetic shower => Hardness variation
Emitt => Capture constraints AMD (R.Helm 1960), QWT, lithium lenses
Acceptance is proportional to B0, Bs and the smallness parameter a (dB/dz)
Constraints: Pulsed Magnetic field B0 and power supply. Immersed target (rotation?),
Bs on the sections (L/S band dependent)
Summarizing : Captured flux is a function of the target constraints (multiple scattering, production..), the transverse and longitudinal production and capture
Tungsten | Carbon | Titanium | Renhium
3695 | 3800 | 1940 | 3460

## Slide 5: Classical sources, scheme
Electron primary
beam source
Electron primary
beam accelerator
Capture section
AMD/QWT
Lens
Converter
Target
e+-e- separator
e+
e-
DUMP
Injection Line
Post acceleration
Beam shaping
Damping ring
Can the DR be considered as a part of the positron source?
In my opinion it can. Its parameters result from the positron source and vice versa
e-
e+

## Slide 6: Classical sources, Capture
At the production the angular distribution is extremely large. A fast phase space rotation is necessary to transform the high divergence in big sizes/low divergence
AMD Adiabatic Matching Device. R = radius
High B Field on the target, then decreasing adiabatically
Radial acceptance r √ (Bsol/BQWT)…bigger than QWT
Angular acceptance q √(Bsol BQWT) r / P….smaller than QWT
QWT
Sharp B field decay
Radial acceptance r Bsol/BQWT
Angular Acceptance
Energy acceptance much better in AMD than in QWT, BUT asymptotic transport has
to be taken into account
Lithium lenses
Strong azimuthal B field
It works like a focusing lens
Angular acceptance A= r √K Sin (L √ K)
√ K = focusing strength
Focal = 5 r2 r / ( I L) with r = magnetic rigidity, I = current, L = lens length

## Slide 7: Classical sources / performances

## Slide 8: New colliders projects: challenges. The Current and the Polarization
Linear Colliders
ILC ~30 % polarization
At least 2 orders of
magnitude…!!!
Circular colliders =>
SuperKEKb, 1-4 nC / 2 bunches @50 Hz,En 3.5-4 GeV. Emittance 2100->10 mm
TLEP 2 1010 e+ sec. Top up injection
Polarized bremsstrahlung. JLAB CEBAF. PEPPo experiment as a demonstrator

## Slide 9: ‘New’ schemes
How can the constraints be reduced during the design phase?
PEDD and melting => Separate the gamma production and the pair production, reduction of the ionization losses : ILC => Undulator, CLIC=> Hybrid. Alternative Compton sources
Injection in damping rings. Stacking and consequently beam shaping
Polarized bremsstrahlung for low polarized intensity sources
Beam shaping before DR injection

## Slide 10
Sources

## Slide 11: Gamma separation: ILC Positron source schematic. Undulator Undulator and laser => Polarization
Balakin, Mikhailichenko

## Slide 12: Gamma separation: ILC Positron source schematic. Undulator
Photon collimator for pol. upgrade
Optical Matching Device for e+ capture enhancement
Main e- beam from electron main linac
Target for e+ production
Positron Target Area Pre-Accelerator (PTAPA ): L-band normal conducting RF accelerator to accelerate e+ beam up to ~125MeV
Positron Pre-Accelerator (PPA): Normal conducting L-band RF accelerator to accelerate e+ beam from 125MeV up to 400MeV
Positron Energy Booster (PBSTR): Cryo-modules to boost e+ energy from 400MeV up to 5GeV
g dump
e- dump
Damping ring
147 m helical undulator for photon production
g
Positron separation and capture section:
To separate e+ from e- and g
To clean up e+ which will not be accepted by damping
Positron Linac to damping Ring (PLTR): Energy compression and spin rotation
Main e- beam to IP
Used e+ production beam to dump

## Slide 13: E166 – results!!! Observation of Polarized Positrons from an Undulator-Based Source, G.Alexander et al. PRL 100, 210801 (2008)
46.6 GeV drive beam
10 Hz
109 e- pulse
Normalized emittance ~ 2 10-5 mm
Spot 35 mm
Undulator 0.9 m, aperture 0.9 mm

## Slide 14: Gamma separation CLIC Hybrid Source
1) Channeling

## Slide 15: CLIC Positron source
L.Rinolfi
Much more complex than the electron source !!!!!

## Slide 16: ILC-CLIC, Compton backscattering T. Omori et al., Nucl. Inst. Meth. A500 (2003) 232. => CO2 lasers S.Araki et al. arXiv:physics/0509016v2 [physics.acc-ph] 15 Sep 2005 => FP cavities I Pogorelski, V Yakimenko, PAC 2007 proceedings, Albuquerque I Chaikovska PhD Thesis
A laser can be seen, by the particle, as a ‘light’ undulator. The equation of motion is
the same as that of a helical undulator… so is the radiation field…linear and non linear
Pro : independent source (main beam few GeV), less thermal stress danger, easy in polarization handling
Main problem: for these applications the Compton cross section is extremely low….
Schemes :
CW => Compton Ring – ERL (FP cavities, high average power laser /stacking, multiple IPs)
Pulsed => Compton LINAC CO2 laser, regenerative, recirculator cavity – single shot
Alternative solutions for ILC and CLIC. A lot of R&D is needed….

## Slide 17
JLAB. Continuous Electron Beam Accelerator Facility
CW Electron beam in all Halls
Polarization: 85-90%
Max Energy: 11GeV(ABC) / 12GeV(D)
Max Current: 200 mA
3 existing end stations for nuclear physics experiments would benefit from a beam of polarized positrons:
  Parton Imaging
  Deeply Virtual Compton Scattering
  Two Photon Exchange
Other efforts may also benefit:
  Electron Ion Collider
  Materials Science Collaborations
So =>Polarized Bremsstrahlung & Pair Creation
Polarised bremsstrahlung. Polarization transfer in the high
energy tail. Good for capture but …low efficiency
E.G. Bessonov, A.A. Mikhailichenko, EPAC (1996)
A.P. Potylitsin, NIM A398 (1997) 395
J.Grames

## Slide 18
PEPPo Concept @ JLab
T1
T2
S1
S2
D
D
Pt
Pe-
Calorimeter
e+
e-
PEPPo
Longitudinal e- (Pe-) produce elliptical g whose circular (Pg) component is proportional to Pe-.
Pg transfers to e+ into longitudinal (Pe+) and transverse (Pt) polarization components. On the average Pt=0.
Ie = 1 µA
T1 = 1 mm

## Slide 19
Techniques

## Slide 20: Target technology, some examples
ILC: Rotating wheel
Daresbury prototype
I.R Baley et al. EPAC 08 Proceedings
Granular Target
small spheres of W, 2 mm diameter
P.Sievers, R.Chehab
Pendulum Target
R.Chehab, P.Sievers
ILC Grenada
Main problems to be solved (again R&D):
Vacuum transition
Rotation (oscillation) speed
Cooling integration
Eddy current (Rotating Wheel)….

## Slide 21: DR stacking and cooling
To increase the single bunch current it is possible to envisage a high frep production at low charge and stacking in the damping ring (or pre-damping ring)
K.Moenig
Simulation in the frame of the ILC-CLIC. For CLIC the pre damping ring is taken into account. For ILC different Compton sources are considered, Storage ring or ERL (Proceedings of PAC09, Vancouver, BC, Canada, F Zimmermann et al.)
Injection in Damping ring, ILC/CLIC – Superconductive DR. 95 % efficiency in simulations with a pre DR and a storage ring (see for example L.Rinolfi et al IPAC 11)

## Slide 22: Capture and shaping
Deceleration strategy. Reduce bunch lentgh -> at the end reduces En spread.
B. Aune and R. H. Miller, “New Method for positron production at SLAC”, LINAC1979, SLAC-PUB-2393.
High harmonics cavities
A.Variola et al. To be published
Studied for SuperB :
- Capture in L Band cavity in high order mode (or S band large iris)
Bunching effect increase with QWT and the reduction of En spread.
TM 020 preserves the transverse acceptance
-High order mode cavities can be used for linearization after L band Linac
T.Xenophonots stage report
F.Poirier

## Slide 23: Possible R&D…. A lot
Target and insertions (pendulum, granular, rotating wheel…)
AMD B Field. Peaked but also solenoid in RF sections!!!
RF Capture in AMD, bunching
Pulsed B Field, immersed target
Undulators
Warm and cold capture
Laser and optical cavities for CBS
Higher harmonic cavities for beam shaping
Lithium lenses / transitions windows and transverse electron flux
Etc….

## Slide 24
Future…dreams?

## Slide 25: Ultimate idea. Schwinger limit
Coherent pairs production in vacuum….laser = target. High h parameter (coherence) in QED regime (large G parameter, hw> mc2) for pairs production.
Primary gammas created in the laser field by CBS (SLAC E144 PRL 79,1626,1997)
Need of a high pulse peak power X FEL coupled with high energy e beam

## Slide 26: Positron sources and Plasma accelerators A point of view
At present the plasma channels acceptance does not allows for ‘colliders’ positrons beam.
Positrons can be created by plasma focusing (undulator K=173!!) gamma emission and conversion (principle of gamma separation..), E167 SLAC. Focusing field 90 T on 28.5 GeV beam. Gamma @ 50 MeV cut. Ti target 4 X0 2.5 106 – 107 positrons with 1-3 1017 cm-3 plasma (D.K Johnson et al PAC proceedings, 2005 Knoxville)
Simulations of e- driven capture and acceleration 1.75 GeV in 5 cm 1017 cm-3 plasma (with reasonable fluxes, 4 106 captured, 0.05% efficiency. SLAC Pub 13102 X Wang et al…).
Experiment made in positron wake, capture and plasma acceleration (less efficient than electron drive). 58 MeV/m in ~1.5 m lithium plasma (excimer laser excited). Efficiency ~5 %. (SLAC) (B.E.Blue et al–PRL 90-21, 30/05/03)
Theoretical considerations on high direct pairs production in a plasma by trident process. Ponderomotrice force -> h laser (>5). For lower intensity lasers ->plasma wakefield acceleration but with a threshold on beam energy (h=0 E>3mc2) (K.T.McDonald, Princeton U. October29, 1996, http:// puhep1. princeton.edu / ̃mcdonald/ accel/positron.pdf)
So at present no ‘total plasma collider’ configuration is a reality…. A lot of R&D is needed.
R&D => Maybe external injection from a classical positron source has to be evaluated.
If R&D on external injection has to be carried out the cost is too high!!! My (?) suggestion is to implement a positron accumulator as in a non neutral plasma physics experiment (Na radioactive sources): few meters and ‘moderate cost’. Applying the rotating wall technique the ‘at rest’ bunch sizes can be drastically reduced. After this, an extraction and small post acceleration system can deliver a positron bunch for the external injection.
Cons => frep ……few minutes

## Slide 27: Conclusions
Positron sources are a KEY element of past, present and future colliders.
The requirements for the future accelerators (especially for linear colliders) represent an incredible design and technological challenge. At present the constraints are imposed by the required current and the polarization.
Different ideas have been suggested and some of them have been successfully preliminary tested (undulator E166, Hybrid, Compton CO2, Mightylaser ).
The physics is amazing, the R&D needs are impressive but unfortunately little attention is devoted to this problem (difficult to find other applications). Only a prioritization policy on budget and manpower can improve the situation. 90 % is Technological R&D ($$).
Very appealing fundamental research can be associated (coherent pairs)
New acceleration techniques are far from an ‘all plasma collider’…Will it be possible in future…??? At present only an external injection can be envisaged -> my suggestion for R&D is to implement positrons accumulator line with rotating wall.

## Slide 28
Thanks for your attention
Thanks to all the colleagues for the slides (borrowed or stolen…)
Special Thanks to R.Chehab