## Slide 1: Primary Beam Lines for the Project at CERN
C.Bracco, F.M. Velotti, J. Bauche, A. Caldwell, B. Goddard, E. Gschwendtner, G. Le Godec, L.K. Jensen, M. Meddahi, P. Muggli, J.A. Osborne, A. Pardons, A. Petrenko

## Slide 2: Outlines
AWAKE p+ beam line
  Present CNGS layout
  Needed lattice modifications for AWAKE beam
  Optics
  Beam instrumentation
AWAKE e- beam
  Geometric layout and optics
  Preliminary results on space charge effects

## Slide 3: AWAKE in the CERN Accelerator Complex

## Slide 4: AWAKE in the CERN Accelerator Complex
AWAKE experiment will be installed @ the end of the CNGS beam line
CNGS

## Slide 5: Experimental Layout
Self-modulation instability (SMI)
p+ bunches produced by the CERN SPS enters the plasma cell  self-modulation instability (SMI)  microbunches spaced at the plasma wavelength (~ 1 mm) .
2 TW laser pulse, co-propagating and co-axial with the p+ beam  plasma ionisation + controlled SMI.
Witness bunch of 1.25·109 e- injected downstream of the SMI saturation  up to 40% e trapped and accelerated from 20 MeV up to 2.1 GeV over a 10 m plasma cell.

## Slide 6: End of CNGS Proton Beam Line
p+ Beam from SPS
Final focusing quadrupoles + trajectory correctors + Beam instrumentation
TARGET area

## Slide 7: End of CNGS Proton Beam Line
p+ Beam from SPS
Final focusing quadrupoles + trajectory correctors + Beam instrumentation
TARGET area
The end of the present CNGS line has to be modified to install the AWAKE plasma cell: new final focusing system + laser integration
Plasma cell
7.16 %

## Slide 8: Lattice Modifications
FODO
Final Focusing
Present Layout (end of the line)

## Slide 9: Lattice Modifications
FODO
Final Focusing
Present Layout (end of the line)
MBG dipoles:
Length [m] | 6.3
Aperture Width [mm] | 140
Aperture Height [mm] | 37
Max.Magnetic Field [T] | 1.91

## Slide 10: Lattice Modifications
FODO
Final Focusing
Present Layout (end of the line)
QTG quadrupoles:
Length [m] | 2.2
Aperture Width [mm] | 45
Aperture Height [mm] | 45
Max.Magnetic Field [T/m] | 34

## Slide 11: Lattice Modifications
FODO
Final Focusing
Present Layout (end of the line)
QTS quadrupoles:
Length [m] | 1.5
Aperture Width [mm] | 80
Aperture Height [mm] | 80
Max.Magnetic Field [T/m] | 24

## Slide 12: Lattice Modifications
FODO
Final Focusing
Present Layout (end of the line)
QTL quadrupoles:
Length [m] | 3.0
Aperture Width [mm] | 80
Aperture Height [mm] | 80
Max.Magnetic Field [T/m] | 24

## Slide 13: Lattice Modifications
2 quads (1 QTG + 1 QTS) are removed
FODO
Final Focusing
Present Layout (end of the line)
Future Layout
X
X
Plasma cell

## Slide 14: Lattice Modifications
2 quads (1 QTG + 1 QTS) are removed
7 left quads are displaced and reshuffled for the new final focusing
FODO
Final Focusing
Present Layout (end of the line)
Future Layout
Plasma cell

## Slide 15: Lattice Modifications
2 quads (1 QTG + 1 QTS) are removed
7 left quads are displaced and reshuffled for the new final focusing
1 MBG is displaced + 4 B190 are added to create the chicane for laser integration (1.9 m long, 1.6 T max. magnetic field)
FODO
Final Focusing
Present Layout (end of the line)
Future Layout
Plasma cell

## Slide 16: Chicane for Laser Integration
Present Beam
CNGS Tunnel wall
New Beam
4213
4214
4215
4216
4217
4218
-2980
-3000
-3020
-3040
-3060
-3080
-3100
y [m]
x [m]
Plasma cell
2 × B190
2 × B190
CNGS Tunnel wall
MAD-X conversion of CERN Coordinate System

## Slide 17: Chicane for Laser Integration
Present Beam
CNGS Tunnel wall
New Beam
4213
4214
4215
4216
4217
4218
-2980
-3000
-3020
-3040
-3060
-3080
-3100
y [m]
x [m]
Plasma cell
2 × B190
2 × B190
CNGS Tunnel wall
Laser
p+ beam
B190
1 mrad kick
B190
1 mrad kick
12 m
Offset between proton beam and laser axis = 24 mm
@ Mirror:
Beam size ~ 5 mm (6 sigma envelope + 3.5 mm mrad emittance + 1 mm orbit + 1 mm mechanical misalignment )
Laser spot size ~ 4.3 mm (1 sigma)
Mirror radius= 13.0mm (3 sigma, 0 angle, 9.2 mm for 45° angle)
Mirror thickness= 6 mm (4.2 mm for 45° angle)
Total needed offset ~ 18.4 mm
MAD-X conversion of CERN Coordinate System

## Slide 18: Final Focusing and Dispersion Matching
Plasma cell
bx =by = 4.9 m
Plasma cell
Dx= 0.029 m
Dy = 0.029 m
sx =sy = 224 mm
Experiment requirements:
round beam, beam size @ plasma cell entrance 1 s = 200 ± 20 mm  bx = by = 4.9 m & Dx = Dy = 0 (400 GeV, 3.5 mm mrad normalised emittance, Dp/p =1 ‰)
Achieved:

## Slide 19: Beam Instrumentation
Existing CNGS beam instrumentation + suitable modifications due to different intensity and bunch structure:
Beam Position Monitors (BPM):
  Exchange electronics
  Add two high precision BPM (50 mm) around the plasma cell to check the pointing precision (±100 mm and ±20 mrad, plasma and proton beam coaxial over the full length of the plasma cell)  interlock to stop extraction from the SPS if beyond tolerances
2 Optical Transition Radiation (OTR) screens around plasma cell for p+ beam setup (out when TW laser on!)
Cable lengths and signal filtering optimisation for Beam Current Transformers (BCT)
Present Beam Loss Monitors (BLMs) Ok.
 | # bunches | # p+ per bunch | Repetition Rate [s] | Energy [GeV]
CNGS | 2100 | 1.05 × 1010 | 6 | 400
AWAKE | 1 | 3.00 × 1011 | 30 | 400

## Slide 20: Electron Beam Line: Geometry
MAD-X conversion of CERN Coordinate System
e- beam
7.16 %
RF Gun
Plasma Cell
12.2 m long e- beam line from RF gun to plasma cell (tunnel for e-beam)
e- beam impinging perpendicularly w.r.t. plasma cell window
Line design based on Fermi@ELTTRA magnets

## Slide 21: Electron Beam Line: Geometry
MAD-X conversion of CERN Coordinate System
12.2 m long e- beam line from RF gun to plasma cell (tunnel for e-beam)
e- beam impinging perpendicularly w.r.t. plasma cell window
e- beam
7.16 %
V bends
H bends
Line design based on Fermi@ELTTRA magnets

## Slide 22: Electron Beam Line: Geometry
MAD-X conversion of CERN Coordinate System
12.2 m long e- beam line from RF gun to plasma cell (tunnel for e-beam)
e- beam impinging perpendicularly w.r.t. plasma cell window
e- beam
7.16 %
H bends
Line design based on Fermi@ELTTRA magnets

## Slide 23: Electrons Merging Point
Plasma cell
Diagnostics
Energy [MeV] | 10-20*
Bunch population | 1.25 × 109
Normalised emittance [mm mrad] | 0.5**
Bunch length [ps] | 0.3 – 10***
* Studies shown in the following refer to 16 MeV
** Emittance blowup in plasma 2 mm mrad @ merging point
*** Bunch compression option to be studied
Ideally possible to move merging point (2-5 m) and angle (5-20 mrad)  movable dipoles ?
30 cm max. aperture !!
~13 G m (1 m long dipoles, for 20 mrad)
To be studied!

## Slide 24: Electron Beam Optics
Experiment requirements:
Round beam, Beam size 1 s < 250 mm,
Dp/p < 1%
Achieved @ merging point*:
sx = 126 mm sy = 126 mm
(0.5 mm mrad norm. emittance)
sx = 251 mm sy = 253 mm
(2 mm mrad norm. emittance)
V bends
H bends
Quads
* 5 m from plasma cell entrance, no merging dipole (several optics to be studied)
Plasma cell

## Slide 25: Space Charge Studies: Assumptions
Tracking simulations:
  Code: PTC-ORBIT
  Initial distribution:
    Transverse plane: Gaussian (1 s cut) x-x’, y-y’
    Longitudinal plane: uniform in Df and Gaussian in Dp/p
  200 000 Macroparticles
Assumed RF frequency wRF = 3 GHz:
  10 ps ~ Df = 188.5 mrad
  0.3 ps ~ Df = 5.7 mrad
  Filled bucket area Df×Dp/p = constant
  (Dp/p = 1% @ 0.3 ps)
Df = 2p for full bucket  Dt ~ 1 ns
f
p
Dp
Df

## Slide 26: Space Charge Effects
10 ps, 0.3‰ Dp/p
0.3 ps, 1% Dp/p
Beam distribution @ merging point (5 m from beginning of plasma cell)
Preliminary results

## Slide 27: Space Charge Effects
10 ps, 0.3‰ Dp/p
0.3 ps, 1% Dp/p
Beam distribution @ merging point (5 m from beginning of plasma cell)
Preliminary results
Is this physical?

## Slide 28: Space Charge Effects
10 ps, 0.3‰ Dp/p
0.3 ps, 1% Dp/p
Beam distribution @ merging point (5 m from beginning of plasma cell)
Preliminary results
Is this physical?
Expected emittance growth when increasing e- beam intensity

## Slide 29: Conclusions
AWAKE p+ beam line:
  Experiment at the end of CNGS beam line
  Minor modifications of existing lattice to fit plasma cell and fulfill geometric and optics requirements
  Existing magnet hardware and beam instrumentation can be used (suitable changes due to different intensity and bunch structure)
AWAKE e- beam line
  Geometric layout defined
  Optics requirements fulfilled (matching for different optics needed)
  New hardware needed + dedicated studies for magnets around plasma cell (feasible changing merging point and angle? precision?)
  Very preliminary studies for space charge effects  need experts input for next steps:
    Other codes for benchmarking (TRACE-3D?)
    Bunch compression....

## Slide 30: THANK YOU FOR YOUR ATTENTION

## Slide 31: FFT Method for SC Calculations in Orbit