## Slide 2: LHC Machine Upgrade
Gianluigi Arduini – CERN - BE/ABP
on behalf of the HL-LHC Team
Acknowledgements: M. Benedikt, O. Brüning, S. Fartoukh, M. Giovannozzi, M. Lamont, E. Métral, T. Pieloni, S. Redaelli, L. Rossi, G. Rumolo, D. Schulte, R. Steerenberg, A. Valishev, J. Wenninger, F. Zimmermann

## Slide 3: Contents
The LHC: the challenges
The next 10 years
HL-LHC: why and how?
Beyond the Upgrade: FCC-hh
Disclaimer: I will focus on the LHC/FCC although a lot of work is on-going/will be needed for the Injectors both for HL-LHC and the future Colliders

## Slide 4: Contents
The LHC: the challenges
The next 10 years
HL-LHC: why and how?
Beyond the Upgrade: FCC-hh

## Slide 5: LHC layout
Total length: ~26.7 km
  8 arcs (aka sectors): ~2.8 km each
  8 long straight sections: ~700 m each
2-in-1 magnet design with separate vacuum chambers
  p-p, ion/ion, or p/ion collisions
  beams cross in 4 points
RF

## Slide 6: Interaction regions geometry
In the IRs, the beams are first combined into a single common vacuum chamber and then re-separated in the horizontal plane,
The beams move from inner to outer bore (or vice-versa),
The triplet quadrupoles are used to focus the beam at the IP.
194 mm
~ 260 m
Common vacuum chamber
D2
D1
D1
D2
Triplet
Triplet
D1,D2 :
separation/recombination dipoles
Machine geometry in H plane
IP
beam1
beam1
beam2
beam2
~ 40 m

## Slide 7: Separation and crossing
Because of the tight bunch spacing and to prevent undesired parasitic collisions in the common vacuum chamber:
  Parallel separation in one plane, collapsed to bring the beams in collision
  Crossing angle in the other plane
~ 8 mm
Not to scale !
q
4 mm (450 GeV)
1.3 mm (4 TeV)

## Slide 8: The quest for Luminosity
To maximize L:
  Many bunches (k)  tight bunch spacing
  Many protons per bunch (Nb)
  Small emittance e*
  Small b*
  Maximize the parameter F (<1) depending on the crossing angle
High beam “brightness” Nb/e*
(particles per phase space volume)
Injector chain performance !
Preservation in the LHC !!
LHC Optics/Configuration
(Round beams)

## Slide 9: What limits b*?
The triplet quadrupoles in the high luminosity IRs define the machine aperture limit for squeezed beams, b* is constrained by:
  the beam envelope
  the crossing angle
John Jowett
btriplet ~ 4 km
b* = 60 cm

## Slide 10: Crossing angle
e = 2.5 mm
q = 145 mrad
b* = 0.6 m  F = 0.81
Needed to minimize beam-beam effects
Drawbacks:
  luminosity geometric reduction factor due to bunch length ss and crossing angle becomes significant for low b*
  Reduction of the aperture
2q

## Slide 11: Wake fields and Impedances
Intense bunches generate electromagnetic fields when passing inside a structure (in particular Carbon collimators – opening of ~1 mm!!!)
→ results in an EM force, called wake field in time domain coupling with the beam
Avoid the abrupt transition for the beam fields at the location of the beam passage (taper)
Reduce the resistivity of the material
Abrupt transition
With taper
B. Salvant

## Slide 12: Wake fields and instabilities
Wake fields can couple the head and tail of a bunch or consecutive bunches leading to instabilities
s
v
~36 cm
~15 m
~1.6×1011 p

## Slide 13: Beam-beam effects
Strong non linear fields when counter-rotating beams share vacuum chamber.
 spread in betatronic frequencies  risk of overlapping resonances driven by magnetic errors
Head-on
Long-range
S. Fartoukh
T. Pieloni
Minimize magnetic errors  Paid off for the LHC
Devise correction schemes and sorting  Paid off for the LHC
Initially expected to have limit at DQBB ~ 0.003/IP

## Slide 14: Electron cloud effects
Possible consequences:
  instabilities, emittance growth, desorption, vacuum degradation, background
  excessive energy deposition in the cold sectors
Electron bombardment of a surface has been proven to reduce secondary electron yield (SEY) of a material as a function of the delivered electron dose. This technique, known as scrubbing, provides a mean to suppress electron cloud build-up.
Secondary emission yield [SEY]
SEY>SEYth  avalanche effect (multipacting)
SEYth depends on bunch spacing and population
G. Iadarola, G. Rumolo

## Slide 15: Pile-up density
25 reconstructed vertices – in a luminous region of 4.3 cm r.m.s. length
Peaks of >40 events per bunch crossing observed with luminosities in the range of 7x1033 cm-2s-1
That is why we are here…
Pile-up proportional to luminosity per bunch  more bunches (i.e. 25 ns) is better
Z mm

## Slide 16: Summary: 2010 to 2012
Parameter | 2010 | 2011 | 2012 | Nominal
Energy [TeV] | 3.5 | 3.5 | 4.0 | 7.0
Nb [1011 p/bunch] | 1.2 | 1.45 | 1.6 | 1.15
k (no. bunches) | 368 | 1380 | 1380 | 2808
Bunch spacing [ns] | 150 | 75 / 50 | 50 | 25
Stored energy [MJ] | 25 | 112 | 140 | 362
e* [mm] | 2.4 | 2.4 | 2.5 | 3.75
b* [m] | 3.5 | 1.5  1 | 0.6 | 0.55
Crossing angle [mrad] | 200 | 240 | 290 | 285
L [1034 cm-2s-1] | 0.02 | 0.35 | 0.76 | 1.0
Beam-beam parameter/IP (DQbb) | -0.0054 | -0.0065 | -0.0069 | -0.0033
Average Pile-up @ beg. of fill | 8 | 17 | 38 | 26

## Slide 17: Contents
The LHC: the challenges
The next 10 years
HL-LHC: why and how?
Beyond the Upgrade: FCC-hh

## Slide 18: Best performance for Run II/III (b*=40 cm)
Limited by:
  Inner triplet heat load due to collisions debris (1.7 x 1034 cm-2 s-1 ± 20% )
  Pile-up (here assumed to be 45 events/crossing)
  Will need levelling
 | Nbcoll [1011] | e*coll [mm] | # Coll. pairs IP1,5 | B-B Sep [s] | Full Xing angle [mrad] | Lpeak [1034 cm-2s-1] | Max. Avg. Peak-pile-up density/Pile-up [ev./mm]/[ev./xing]
BCMS | 1.24 | 1.65 | 2592 | 12 | 295 | 2.1 | 0.46/45
Standard | 1.24 | 2.0 | 2736 | 12 | 320 | 1.8 | 0.46/45
 | Llev [1034 cm-2s-1] | Lev. time [h] | Opt. Fill length [h]
BCMS | 1.5 | 2.9 | 8
Standard | 1.6 | 1.7 | 8.1
Expect to produce ~45-55 fb-1/year

## Slide 19: Best performance for Run II/III (b*=40 cm)
Variation of the b* during the fill (b* levelling) is the most likely technique to be applied for luminosity levelling

## Slide 20: LHC Schedule beyond LS1
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
LHC schedule approved by CERN management and LHC experiments spokespersons and technical coordinators (December 2013)
Beam commissioning
Technical stop
Shutdown
Physics
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
(Extended) Year End Technical Stop: (E)YETS
EYETS
YETS
YETS
YETS
YETS
YETS
300 fb-1
3’000 fb-1
30 fb-1

## Slide 21: Contents
The LHC: the challenges
The next 10 years
HL-LHC: why and how?
Beyond the Upgrade: FCC-hh

## Slide 22: Why an LHC Upgrade?
What to do to make this jump ?
M. Lamont

## Slide 23: Radiation damage to triplet
F. Cerutti, N. Mokhov, L. Esposito,…
Q2
27 MGy
MCBX3 20 MGy
Cold bore insulation
≈ 35 MGy

## Slide 24: Technical bottlenecks: Cryogenics
IT
IT
IT
IT
IT
IT
IT
IT
RF
RF
Cryo power limitation in Pt 4, interdependency of different systems with different cool-down time, reduced flexibility and no/little redundancy

## Slide 25: LHC Upgrade
Motivations:
  Target (very ambitious) of the upgrade: 200 – 300 fb-1/y (×10 today)
  Radiation damage limit of IR quadrupoles (~400 fb-1)
  Improve availability of the systems
2010-2012 experience:
  Head-on beam-beam limit higher than initially expected
  Single bunch with > 3x1011 ppb with 2.5 mm emittance accelerated in the SPS
  Low b* optics successfully tested during Machine Studies
Pile-up/pile-up density HL-LHC beam physics constraint  25 ns operation:
  Electron cloud
  Total current: collimation efficiency, upper limits from: dump, vacuum, machine protection, RP, …

## Slide 26: LHC and Injector Upgrade: when?
During Run II and Run III we will be limited by heat load in the triplet (luminosity debris) and pile-up at the experiments
Every 3 of 4 year a long shutdown period is planned for upgrade activities
LS2: 18 months
Connection of LINAC4
LHC Injectors Upgrade
ALICE, LHCb Upgrade
~5 months
Longer end-of-year stop (CMS)
LS3: 30 months
High Luminosity LHC
Machine and Experiments
Run III: 14 TeV c.m. with levelled luminosity of <1.7x1034 cm-2 s-1
Run II: 13 or 14 TeV c.m. with levelled luminosity of <1.7x1034 cm-2 s-1

## Slide 27: Ingredients for the Upgrade
…of course it requires larger aperture triplets
IR4
IR5
IR6
ATS=Achromatic Telescopic Squeeze - S. Fartoukh
b* [m]

## Slide 28: Ingredients for the Upgrade
L [1034 cm-2s-1]
t [h]
Virtual peak luminosity (F=1)
leveling at
5x1034cm-2s-1
teff=15 h, Tta=5 h
leveling at
2.5x1034cm-2s-1
teff=30 h, Tta=5 h
F. Zimmermann

## Slide 29: Ingredients for the Upgrade
Operation at pile-up/pile-up density limit:
  choose parameters that allow higher than design pile-up
    Low b*, Low Emittance, High Bunch population
    Crab Cavities as tool to maximize overlap among colliding bunches (i.e. virtual luminosity) and minimize pile-up density
  levelling mechanisms for controlling performance during run
    dynamic b* squeeze
    Long-range and beam-beam wire compensators to reduce crossing angle

## Slide 30: HL-LHC Performance Estimates
Parameter | Nominal | 25ns – HL-LHC
Bunch population Nb [1011] | 1.15 | 2.2
Number of bunches | 2808 | 2748
Beam current [A] | 0.58 | 1.12
Crossing angle [mrad] | 300 | 590
Beam separation [s] | 9.9 | 12.5
b* [m] | 0.55 | 0.15
Normalized emittance en [mm] | 3.75 | 2.5
eL [eVs] | 2.51 | 2.51
Relative energy spread [10-4] | 1.20 | 1.20
r.m.s. bunch length [m] | 0.075 | 0.075
Virtual Luminosity (w/o CC) [1034 cm-2s-1] | 1.2 (1.2) | 21.3 (7.2)
Max. Luminosity [1034 cm-2s-1] | 1 | 5.1
Levelled Pile-up/Pile-up density [evt. / evt./mm] | 26/0.2 | 140/1.25
DQbb ~ -0.01
Aim for ~250 fb-1/y
Notes: 50ns beam option provides HL-LHC performance levels at ultimate total beam currents; only the ‘large beta*’ option reaches beam-beam limit; IBS growth rates are a concern!; low beta option has 50% higher performance potential

## Slide 31: Pile-up density control
[mm-1]
z [m]
Baseline: CC in X-plane “only”
Crab-kissing:
CC also in ||-plane
... Work on-going together with the experiments
(S. Fartoukh, A. Valishev, A. Ball, B. Di Girolamo, et al.)
S. Fartoukh

## Slide 32: Hardware for the Upgrade
Main modifications:
  New high field/larger aperture interaction region magnets
  Cryo-collimators and high field 11 T dipoles in dispersion suppressors
  Crab Cavities to take advantage of the small b*
  New collimators (lower impedance)
  Additional cryo plants (P1, P4, P5)
  SC links to allow power converters to be moved to surface

## Slide 33: Triplet Area ATLAS/CMS
LHC point 5
Bore aperture : 70  150 mm.
Gain 3-4 in beam area (b* = 15 cm).
LHC
HL-LHC
IP

## Slide 34: Shielding against Radiation Damage
Tungsten shielding on the beam screen 16 mm in Q1 and 6 mm elsewhere
More than 600 W in the cold masses as well as in the beam screen (i.e. 1.2-1.3 kW in total)!!  Cryogenics
Expect same integrated radiation dose in HL-LHC after 3000 fb-1 as in LHC after 300 fb-1!!
F. Cerutti, L. Esposito

## Slide 35: High field dipoles / Cryo collimators
The goal is to develop a 10 m long 11.2 T Nb3Sn dipole to replace a standard LHC dipole and provide space for collimators downstream of the straight sections.
FNAL prototype MBHSP02
reached 11 T in May 2013
NbTi 8.3 T
Nb3Sn 11 T
Collimator
15 m
Same deflection !

## Slide 36: Magnet technology challenges
LHC dipoles feature 8.3 T in 56 mm (designed for 9.3 peak field)
LHC IT Quads features 205 T/m in 70 mm with 8 T peak field
HL-LHC:
  11 T dipole (designed for 12.3 T peak field, 60 mm)
  New IT Quads features 140 T/m in 150 mm > 12 T operational field, designed for 13.5 T).

## Slide 37: Radiation to Electronics (R2E)
R2E consolidation during LS1 not sufficient for the HL-LHC era (~2 fb-1/ day)  1 dump/day due to SEU
PC far from tunnel  SC links (HTS)
QPS systems out of the tunnel
M. Brügger
A. Ballarino

## Slide 38: Crab cavities: from drawings to reality…
LARP-BNL
LARP-ODU-JLAB
UniLancaster-CI-CERN

## Slide 39: Low impedence collimators
New material: MoGr
S. Redaelli, A. Bertarelli

## Slide 40: Electron cloud
Strategy for the arcs (to be validated in 2015):
  enhance electron cloud at 450 GeV to remove e-cloud in the dipoles “completely” with dedicated scrubbing
  Use of “doublet beam” to enhance scrubbing
  Need to leave with e-cloud in the quadrupoles (sufficient cryo-margin for that)
Strategy for the Insertion regions:
  Coat the beam screen of all new elements (triplets in particular) with materials with low SEY (amorphous Carbon) and install clearing electrodes

## Slide 41: Electron cloud
Back-up scenario:
  Detrimental e-cloud effects can be mitigated by using specially conceived filling patterns: bunch trains with long enough gaps interspersed
  Reduction of the number of bunches and of colliding pairs by 25%  corresponding reduction in luminosity
H. Damerau

## Slide 42: Contents
The LHC: the challenges
The next 10 years
HL-LHC: why and how?
Beyond the Upgrade: FCC-hh

## Slide 43: FCC Study Scope
CDR and cost review for the next European Strategy Update in 2018:
  pp-collider (FCC-hh): defining infrastructure requirements
    ~16 T  100 TeV pp in 100 km
    ~20 T  100 TeV pp in 80 km
  e+e- collider (FCC-ee) as potential intermediate step
  p-e collider (FCC-he) option
80-100 km infrastructure in Geneva area

## Slide 44: Main FCC-hh parameters
Two main experiments sharing the beam-beam tuneshift
  Two reserve experimental areas not contributing to tuneshift
Currently assume 25ns as baseline
 | LHC (Design) | HL-LHC | FCC-hh
Main parameters and geometrical aspects |  |  | 
C.o.M. Energy [TeV] | 14 |  | 100
Circumference C [km] | 26.7 |  | 100 (83)
Dipole field [T] | 8.33 |  | 16 (20)
Straight sections | 8 |  | 12
Number of IPs | 2 HL + 2 LL |  | 2 HL + 2 LL
Injection energy [TeV] | 0.45 |  | 3.3
Physics performance and beam parameters |  |  | 
Peak luminosity [1034 cm-2s-1] | 1.0 | 5.0 (lev.) | 5.0
Pile-up (25 ns/5 ns) [evts./crossing] | 27 | 140 (lev.) | 171/34

## Slide 45: FCC-hh beam parameters
 | LHC (Design) | HL-LHC | FCC-hh (100/83)
Beam parameters |  |  | 
Number of bunches k (25 ns/5 ns) | 2808 | 2748 | 10600 (8900) / 53000 (44500)
Nb [1011] | 1.15 | 2.2 | 1.0/0.2
e* (25 ns/5ns) [mm] | 3.75 | 2.5 | 2.2/0.44
Maximum total b-b tune shift DQbb/IP | -0.003 | -0.01 | -0.005
Beam current [A] | 0.584 | 1.12 | 0.5
RMS bunch length [cm] | 7.55 |  | 8 (7.55)
b* [m] | 0.55 | 0.15 | 1.1
RMS IP spot size (25 ns/5ns) [mm] | 16.7 | 7.1 (min) | 6.8/3
Full crossing angle [mrad] | 285 | 590 | 74/ n/a
Rather conservative parameters as compared to HL-LHC

## Slide 46: FCC-hh: Other parameters
 | LHC (Design) | HL-LHC | FCC-hh (100/83)
Stored Energy/beam [GJ] | 0.36 | 0.68 | 8.4
Arc SR heat load [W/m/aperture] | 0.17 | 0.33 | 28.4 (44.3)
Energy loss per turn [MeV] | 0.0067 |  | 4.6 (5.86)
Critical photon energy [keV] | 0.044 |  | 4.3 (5.5)
Total synchr. Power [MW] | 0.0072 | 0.0146 | 4.8 (5.8)
Long. emittance damping time [h] | 12.9 |  | 0.54 (0.32)
Hor. emittance damping time [h] | 25.8 |  | 1.08 (0.64)
Dipole coil aperture [mm] | 56 |  | 40
Huge beam (and magnetic) stored energy!!!!
Synchrotron radiation!!!
Half – way between a hadron and lepton machine

## Slide 47: FCC-hh Challenges: Magnets
FCC-hh baseline 16T Nb3Sn technology for 100 TeV in 100 km
  Develop Nb3Sn-based 16 T dipole technology
    with sufficient aperture (~40 mm) and
    accelerator features (field quality, protectability, cycled operation)  Nb3Sn magnets in the LHC (HL-LHC 11 T dipoles)
    In parallel conductor developments
  Possible goal:
    16T short dipole models by 2018 (America, Asia, Europe)
  In parallel HTS development targeting 20 T:
    HTS insert, generating O(5 T) additional field
    in large aperture O(100 mm, 15 T)
  Possible goal:
    demonstrate HTS/LTS 20 T technology in two steps
    a field record attempt to break the 20 T barrier (no aperture), and
    a 5 T insert, with sufficient aperture (40 mm) and accel. features

## Slide 48: FCC-hh Challenges
Energy in beam & magnets  dump, collimation, quench protection
  Stored beam energy > 20 x LHC
  Beam losses, radiation effects  collimation, shielding
High synchrotron radiation load on beam pipe
  Up to 26 W/m/aperture in arcs, total of ~5 MW for FCC-hh
  Heat extraction: photon stop, beam screen design, cryo load,
Synchrotron radiation damping
  controlled blow up, luminosity levelling, etc…
Impedances, instabilities, feedbacks
  Beam-beam, e-cloud, resistive wall, feedback systems design
Optics and beam dynamics
  IR design, dynamic aperture studies, SC magnet field quality

## Slide 49: Concluding remarks
The progress in the performance of the LHC has been so far breath-taking
  Some of the (beam dynamics) challenges that had to be faced have been outlined
  With run II we will explore high energies and operation with 25 ns (all but trivial). Aim for 300 fb-1 by the end of Run III
Luminosity performance and choices for the upgrade are now constrained by the acceptable detector pile-up/pile-up density
  To reach 3000 fb-1 by ~2035 we are pushing even further the above challenges…
  Several Technologies/Techniques are being developed to provide margin for the achievement of these challenging parameters
We start to look at the future beyond HL-LHC (it is time to do it to be ready…)

## Slide 51
Very First Ion Considerations
 | Unit | LHC Design | FCC-hh | FCC-hh
Operation mode | - | Pb-Pb | Pb-Pb | p-Pb
Number of bunches |  | 592 | 432 | 432
Part. P. bunch | [108] | 0.7 | 1.4 | 115(1.4)/1.4
β-function at the IP | [m] | 0.5 | 1.1 | 1.1
RMS beam size at IP | [] | 15.9 | 8.8 | 8.8
Initial luminosity | [1027cm-2s-1] | 1 | 3.2 | 267(3.2)
Peak luminosity | [1027cm-2s-1] | 1 | 12.7 | 5477(3356)
Integr. lumi. per fill | [mb-1] | <15 | 83 | 30240
Total cross-section | [b] | 515 | 597 | 2
Initial luminosity lifetime | [h] | <5.6 | 3.7 | 3.2 (10.6)
Much more work to be done: Improved injectors, integration into interaction region, …

## Slide 52: Cures for electron cloud effects
At the time of the construction of the LHC:
  NEG coating  would require activation to >200 oC  impractical
  Conditioning by beam-induced electron bombardment (“scrubbing”) leading to a progressive reduction of the SEY as a function of the accumulated electron dose  tested in the laboratory (on Cu surfaces) and in the SPS (Stainless Steel vacuum chambers)  Chosen strategy for the LHC operation with bunch trains – but it takes time!! (in particular for 25 ns operation)
More recently a-C coating has been successfully tested in the SPS showing SEY as low as 1.1  possible implementation for HL-LHC (interaction regions)

## Slide 53: Issues: electron cloud
2012 Experience:
  Scrubbing lowers SEY below SEYth (~1.45) at injection in the dipoles
  Not in quadrupoles (due to a significantly lower SEYth ~1.2)
  Despite 2-beam-50 ns operation in triplet for ~ 2 years, e-cloud still present in triplets, due to the presence of the two counter-rotating beams
Significant increase of heat load (~ factor 4) in the arcs during ramp:
  From e-cloud in the dipoles due to reduction of beam size/bunch length at the beginning of the ramp (SEYth decreasing to <1.4).
  No change in quadrupoles, always above threshold

## Slide 54: Issues: “Unidentified Falling Objects” (UFO)
Very fast and localized beam losses observed as soon as the LHC intensity was increased.
Traced back to dust particles falling into the beam – ‘UFO’.
If the losses are too high, the beams are dumped to avoid a magnet quench.
  ~20 beams dumped / year due to UFOs.
100µm
10µm
In one accelerator component UFOs were traced to Aluminum oxide particles.

## Slide 55: Issues: UFOs
Extrapolation to 7 TeV: ~100 beam dumps from UFOs
UFO rate depends on bunch spacing, stronger with 25 ns.
  fast conditioning observed over a few fills in 2012
  We have to expect serious deconditioning after LS1.
Quench tests: quench limits likely too pessimistic (x 2) at 4 TeV for UFO timescales.
T. Bär

## Slide 56: Beam-Beam long range compensator (BBC)
Initial proposal in 2001 (J.-P. Koutchouk)
Proof-of-principle requires BBLR prototype into machine well before HL-LHC
Operation close to MP envelope:
  Need to embed wire in collimator jaw type structure
Wire parameters:
  Solid wire radius of ~1mm → 1kW power dissipation
  sub-σ level of hor./ver. position control
R. Steinhagen

## Slide 57: Beam-Beam Long Range Compensator (BBC)
Can re-use nearly 100% of existing TCTP design (with BPMs).
Remaining challenge: finding space for the wire current feed-through amongst the cooling circuits and BPM button feedthroughs.
Aiming for installation during 2015-16 Technical Stop
S. Redaelli
Notes: Timescale: installation of infrastructure and installation after LS1 (Stefano?)
Technical stop 2015-16