## Slide 1
Vertexing & Tracking Detectors
Local mechanical supports
and cooling systems
IFD 2014
INFN Workshop on Future Detectors for HL-LHC
Simone Coelli
I.N.F.N. - SEZIONE DI MILANO

## Slide 2
SUMMARY:
STAVE DESIGN
EVAPORATIVE PROCESS
DETECTORS COOLING PLANT
CERN TRACKERS UPGRADE OVERVIEW (FROM THE POINT OF VIEW OF THE COOLED SUPPORTS)
R&D WORK IN PROGRESS

## Slide 3
TRACKERS LOCAL SUPPORTS: THE CHALLENGE
USUAL STAVE REQUIREMENTS:
TAKE IN PLACE WITH PRECISION THE TRACKER SENSORS
THERMAL MANAGEMENT: EXTRACT THE DISSIPATED POWER (>1 W/cm2)
SUB-ZERO WORKING TEMPERATURES (WHEN IN HARD RAD. ENVIRONMENT)
HOMOGENEOUS AND CONSTANT OPERATING TEMPERATURES
ROBUST SYSTEM - AFFORDABLE - MAINTENANCE FREE
LOW MATERIAL BUGET - GOOD X0 – MINIMUM MASS SYSTEM
STRUCTURAL STIFFNESS - NO VIBRATIONS
LOW DEFORMATION – LOW C.T.E. MATERIALS – LOW MISMATCH (AMB. TO -40 °C)
ELECTRIC AND FLUID CONNECTIVITY
CORROSION COMPATIBILITY (COOLANT)
PERFECT INTEGRATION SCHEME – ONE-STAVE-REMOVAL WHEN POSSIBLE

## Slide 4
«SUPPORT + COOLING SYSTEM» INTEGRATION
CFRP CARBON FIBERS ULTRA-LIGHT SUPPORT STRUCTURES (HIGH RIGIDITY AND STRENGHT, LOW DENSITY, VERY LONG RAD. LENGTH, LOW %X0)
CARBON FOAM MATERIALS (HIGH THERMAL CONDUCTIVITY, LOW DENSITY)
EVAPORATIVE COOLING
SMALL PIPES (F1-2 mm), EMBEDDED IN THE SUPPORT
IMPROVED GLUE THERMAL CONDUCTIVITY (ADDITIVES EPOXY + BN, THIN LAYERS 50 µm)
FLEX-BUS INTEGRATED IN THE STAVE
SOME EXPERIMENT ALREADY EXPLOITING MICRO-CHANNELING:
  SILICON MICRO-CHANNEL
  CARBON MICRO-CANNELS
12.8 mm
700 µm
TECHNOLOGICAL OPTIONS MOSTLY PURSUED

## Slide 5: TYPICAL STAVE‏ SECTION
REQUIREMENT WITH HIGHLY IRRADIATED SENSORS
TO AVOID THERMAL RUNAWAY
=> OPERATIVE TEMP.ERATURE < - 5 °C
  MANAGE THE THERMAL LOADS
  EXPLOITING THE BEST MATERIALS THERMAL CONDUCTION
  THERMAL CONVECTION TOWARDS THE FLUID
  PHASE CHANGE WHEN USING THE EVAPORATING COOLANT
THERMAL FLOW
STAVE DESIGN GOAL
THERMAL GRADIENTS

## Slide 6
FLUOROCARBONS
C2F6
C3F8
C4F10
C6F14 => USED IN SINGLE PHASE FLOWS ONLY (NEED TO BE UNDER VACUUM FOR TEMPERATURES LOWER THAN 56 °C)
PURE OR BLENDED TO OBTAIN SPECS.
CARBON DIOXIDE CO2 => HIGH LATENTHEAT, LOW PRESSURE DROP, more environmentally friendly and less expensive
CHARACTERISTICS OF THE EVAPORATIVE PROCESS
NEAR ISO-THERMAL => SMALL DT ALONG THE STAVE (LOW TEMP.GRADIENTS)
EFFICIENT: high heat transfer coefficient (W/m2K)
ALLOWS SMALL TUBES: low material; easy bending; low forces due to CTE mismatch
COOLANT => BOILING AT – 20 °C / - 40 °C inside the channel
DETECTOR COOLING FLUIDS
(RAD HARD, DIELECTRIC)
MOST LIKELY CANDIDATES FOR LOW-TEMPERATURE OPERATION

## Slide 7
THERMODYNAMICS OF THE EVAPORATIVE PROCESS
LATENT HEAT OF VAPORIZATION FOR CO2
IN THE RANGE OF INTEREST
DELTA H liq.=> vap. = 280 kJ/kg
  => 10 TO 20 bar COOLING FLUID
  OPER. PRESSURE
  COOLING FLUID OPER. TEMP.
  - 20 / - 30 °C
THE PURE CO2 SATURATION CURVE CORRELATES TEMPERATURE AND PRESSURE INSIDE THE EVAPORATION CHANNEL

## Slide 8
CERN EXPERIMENTS COOLING PLANT
2 PACL = 2-Phase Accumulator Controlled Loop
Used at CERN for:
LHCb Velo
Atlas Pixel IBL
CMS Pixel upgrade
LHCb UT upgrade
LHCb Velo microchannel upgrade
NEW INTEGRATED SYSTEM
patented: CERN & NIKHEF
CERN EXPERIMENT DETECTOR COOLING CIRCUIT SKETCH
TRACI UNITS
USES ONLY PASSIVE SYSTEMS IN THEUNACESSIBLE AREA

## Slide 9
DETECTOR COOLING PLANT
THE DETECTOR IS A PRESSURE SYSTEM
CO2 DESIGN PRESSURE ~ 100 bar (Safety Factor above the Critical Point pressure)
Pipe material baseline: Stainless Steel or Titanium ~ 0.1 mm wall thickness
NOTES:
OPERATIVE CONDITION LESS DEMANDING THAN TRANSIENTS => DESIGN
THERMO-HYDRAULIC INSTABILITIES
THE PROCESS IS DRIVEN BY MANIFOLDING AND CONNECTION DESIGN
PRESSURE DROP AT THE INLET OF THE BOILING CHANNELS ALWAYS BENEFICIAL FOR STABILITY => CAPILLARY PIPES / FLOW RESTRICTIONS IN SILICON MICROCHANNELS
TYPICAL DESIGN SPECIFICATION FOR A PIPE JOINT

## Slide 10
EXPERIMENT TRACKER | ACTUAL 2009-2012 | long shutdown 2013/2014 | Shutdown 2017/2018 | long shutdown 2017/2018 => PHASE-II
ATLAS | PIXEL Evaporative fluorocarbon system | + IBL PIXEL CO2 1.5 kW < BEAMPIPE DIAM |  | NEW TRACKER ALL SILICON CO2 > 200 kW
CMS | PIXEL Mono-phase fluorocarbon system |  | + PIXEL REPLACEMENT CO2 15 kW < BEAMPIPE DIAM | NEW TRACKER ALL SILICON CO2
LHCb | VELO FIRST 2PACL AT CERN CO2 1.5 KW GOOD EXPERIENCE! |  | VELO FIRST SILICON MICRO-CHANNEL CO2 4 KW UT TRIGGER (STRIPS) CO2 4 KW | 
ALICE | ULTRALIGHT SUPPORTS |  |  | => VERY ULTRALIGHT ENHANCED COOLING < BEAMPIPE DIAM
NA-62 GTK | SILICON | MICRO-CHANNEL | CO2 | 
UPGRADE OF THE CERN TRACKERS: TIMESCALE OVERVIEW

## Slide 11
in some cases:
PHASE-I UPGRADES
=> produce detectors that can operate successfully throughout PHASE-II
in other cases:
PHASE-I UPGRADES
provide an infrastructure that can facilitate the additional modifications necessary for PHASE-II
R&D for PHASE-II
=> builds on the design of the PHASE-I UPGRADES
demands of PHASE-II
=> may require the COMPLETE REPLACEMENT of some detectors
R&D for PHASE-II and PHASE-I UPGRADES
take place over the same 5 year period 2011-2016
=> .. competion for human and financial resources ..
COMMON CONSIDERATIONS

## Slide 12
I-beam concept prototype
layout of I-beams for two inner pixel layers
I-BEAM SOLUTION
baseline for the innermost two layers
different module sizes in the two layers
not need an external support structure
bare stave contribution to the material budget is only 0.43 % X0 per layer (normal)
inherent stiffness
end-supported
allows fast replacement
can be mounted as “clam shells” for extraction without breaking the LHC vacuum.
ATLAS
PIXEL
System
OVERVIEW OF THE TRACKER UPGRADES: SOME CLUES FROM THE LOCAL SUPPORT AND COOLING POINT OF VIEW
with CO2 cooling

## Slide 13
ATLAS PIXEL system
Prototype of an alpine stave
new design NO BARREL & DIS
=> USE OF STAVES WITH SENSORS FACING THE I.P.
with CO2 cooling
ALPINE ALTERNATIVE SOLUTION

## Slide 14
ATLAS STRIP system
with CO2 cooling
carbon fibre facings
core honeycomb/carbon foam
embedded cooling pipe(s)
TYPICAL DISK PETAL
TYPICAL BARREL STAVE
Extensive use of Sandwich technology

## Slide 15
ITK
coolant temperature of - 35 °C
ESTIMATED POWER TO BE EXTRACTED
180 kW nominal
240 kW with safety-factors
large development needed
scale up an IBL-like design to about 20 Kw
and then install 10 or so identical copies
back-up option of using fluorocarbon cooling
will require a mixture of C2F6 / C3F8
to achieve the required temperatures
COOLING SYSTEM FOR ATLAS PHASE-II

## Slide 16
CMS Upgrade
With CO2 cooling
15 kW
will replace the current single phase C6F14
A fullscale system has been built in the CERN CryoLab

## Slide 17
CMS Pixel System Upgrade
Edge Cooling Concept:
carbon fiber skins
carbon-carbon ring
cooling tube captured inside
Prototype of the mechanical structure for the innermost layer
mechanical stability of the ladder
is given by the cooling tubes
Solid TPG*(0.68 mm thick)
encapsulated with carbon-fiber facings (0.06 mm thick)
TPG =thermo-pyrolitic graphite
Thermal conductivity
Can reach 1500/1500/20 W/mK

## Slide 18
ALICE Upgrade
NEW ITS DETECTOR:
MATERIAL BUDGET => VERY STRINGENT REQUIREMENTS => ULTRALIGHT
THE DETECTOR WILL BE OPERATED AROUND ROOM TEMPERATURE (+ 30 °C)
COOLING SYSTEM 15 KW
water flow leakless (below atmospheric pressure)
for the Inner Layers alternative coolants sconsidered C4F10
Microchannel cooling systems
array fabricated either in:
polyimide substrate
silicon substrate

## Slide 19
ALICE Upgrade
minimization of the material budget
Silicon microchannel cooling

## Slide 20
LHCb Upgrade
  VELO UPGRADE
  => SILICON MICRO-CHANNEL
  UT UPGRADE
  DESIGN OPTIONS UNDER STUDY
with CO2 cooling
with CO2 cooling
SNAKE PIPE DESIGN
MORE THERMALLY EFFICIENT
STRAIGHT PIPES DESIGN
NEEDING DOUBLE PIPE AND TPG INSERTS
BENDED PIPE, PARALLEL CHANNELS
=> FLOW DISTRIBUTION ISSUES
TRACI COOLING SYSTEM TEST PLANNED
FOR THE NEW VELO AND UT DETECTORS
4000 W @ – 30 °C EACH
PLANNED DEVELOPMENT AND ONSTRUCTION
OF A COMMON PLANT

## Slide 21
  DESIGN:
  FINITE ELEMENT ANALYSIS
  THERMAL AND THERMO-MECHANICAL SIMULATIONS
  NEED CHARACTERIZATION TO HAVE REALISTIC MATERIAL PROPERTIES IN THE MODELS
  EXPERIENCE IN MESHING TECHNIQUES FOR VERY MULTY-THIN LAYERED OBJECTS (GLUE LAYERS)
  ANISOTROPIC MATERIALS, LAYERED CFRP MATERIALS
  THERMOHYDRAULIC CALCULATION
  FOR THE COOLING CIRCUIT
  CoBRA (CO2 BRANCH CALCULATOR)
  SPECIAL ATTENTION TO INSTABILITIES
  IN 2-PHASE EVAPORATING SYSTEMS
REQUIRED KNOW-HOW AND INNOVATIVE MATERIALS

## Slide 22
REQUIRED KNOW-HOW AND INNOVATIVE MATERIALS
  PROTOTYPE & DETECTOR REALIZATION:
  CO2 PIPING MATERIALS (MDP = 100 bar)
  TITANIUM: low CTE, high rad length, high strenght / pipe acquisition not easy
  STAINLESS STEEL
  ALUMINUM: used in the actual detector, not considered for upgrades
  CARBON BASED MATERIALS
  CFRP
  CARBON FOAMS
  GLUING IMPROVEMENTS
  TECHNOLOGY TO OBTAIN CALIBRATED GLUE LAYERS
  SUFFICIENT FOR STRUCTURAL AND THERMAL CONTACT
  NOT MORE THAN REQUIRED (MINIMIZING MATERIALS)

## Slide 23
Cooling
characterizing heat transfer in small channel through laboratory measurements
deriving guidelines for detector cooling optimization
developing numerical models that correctly describe the flows and heat transfers
design and engineering of the system
analysis of system aspects such as manifolding
novel challenges due to the much larger scale of the system
R&D steps

## Slide 24
R&D IN PROGRESS
Development of a portable CO2 laboratory cooling unit called Traci
  TRACI=Transportable Refrigeration Apparatus for Co2 Investigation.
Development in AIDA framework together with interested partners
  Nikhef & CERN lead development
  Co-funding from clients
  Collaboration with Sheffield, Oxford, Liverpool and Milano
AIDA funds => TRACI SYSTEM
FIRST UNIT will be identified as “the” final AIDA deliverable for WP 9.3.
AIDA-2
WILL CONTINUE THE COOLING ACTIVITIES IN PROGRESS..

## Slide 25
R&D
  FULL SILICON STAVE
  SILICON PACKAGE INCLUDING:
  ELECTRONICS
  STRUCTURAL SUPPORT / SELF SUPPORTING SYSTEM
  COOLING CHANNELS
  VELO LHCb
  ALICE ITS
  NA62 GTK
  … ATLAS & CMS FOR PHASE-II
  CARBON MICRO CHANNEL COOLING
  => See details in the 2 last slides
  from Filippo Bosi (INFN PISA)
  ADDITIVE TECHNOLOGY
  PEEK PIPE INTO CFRP
SILICON MICROCHANNEL PROTOTYPE
SupeB SVT LAYER-0 PROTOTYPE

## Slide 26
  VERY GOOD RAD LENGTH
  ALMOST ZERO CTE
  PRESSURE SYSTEM WITH MDP 100 BAR
  THICKNESS OF MATERIAL
  LOW TRANSVERSAL THERMAL CONDUCTIVITY => NEED R&D TO IMPROVE
  DEDICATED CONNECTIONS DEVELOPED
USING A CARBON-FIBER COOLING PIPE
COMPLIANT FOR FOR A CO2 PRESSURE SYSTEM
considered as an option for ATLAS IBL
.. and HL-LHC upgrade structures?
R&D
The Homogeneous Stave
ALL CARBON STAVE

Braids
Wrapping
several pipes have been produced that meet the specs and, at the moment, two are the validated techniques
full homogeneous stave
Institutes and collaborators (2008)
IVW : Institut für Verbundwerkstoffe GmbH Kaiserslautern
IFB :Institut für Flugzeugbau Universitat Stuttgart
Wuppertal University
INFN Milano
CPPM Marseille
LAPP Annecy
BERCELLA Carbon Fiber (Parma IT)

## Slide 27
R&D
JOINING TECHNIQUES
Orbital welding
Not for small 1.5 mm pipe
Swaging
Brazing work fine on a lot of material (Stainless steel, Ceramics, Titanium …)
compatible with modules on local supports during operation
permit mixture of materials
helpful for electrical breaks for example
IBL Brazing activity

## Slide 28
COLLABORATION WITH INDUSTRIES
Peculiarity of the present systems:
“Small”detector => Small quantity of material required
Not very attractive business for industry
always needed:
custom design and prototype qualification
custom production of detector components
=> expensive (small scale) material acquisition and external works
DESIDERABLE COLLABORATION INSIDE INFN
TO JOIN EFFORTS IN COMMON R&D
SOFTWARE SIMULATION CODES:
ALREADY DONE (NATIONAL CONTRACT) FOR:
CAD SYSTEMS
FEM ANSYS
ESACOMP
NOW NEED CoBRA code (CO2 BRANCH CALCULATOR)
PROTOTYPE TESTING R&D RESULTS & INDICATIONS
SHARING OF TECHNOLOGIES DEVELOPMENT AND LABORATORY INFRASTRUCTURES
COLLABORATION BETWEEN INSTITUTES

## Slide 29
Thank you
for your attention
BACK-UP
SLIDES

## Slide 30: Le linee R&D proposte per il Tracker: Micro Channel Cooling
I rivelatori a pixel per Fase-2 necessitano di un raffreddamento efficace:
  potenza dissipata dall’elettronica di front end con elevata densità di interconnessione (>1 W/cm2);
  danneggiamento da radiazione che implica condizioni di lavoro dei sensori a bassa temperatura ( -20° C);
  Localizzazione in rivelatori vicini al punto di interazione :
    Material budget minimizzato
    Distribuzione uniforme della potenza di raffreddamento con ponti termici tali da garantire temperatura costante del sensore;
    Sistema robusto e “maintenance-free” (zona sperimentale inaccessibile)
Micro-channel Cooling + CO2 a transizione di fase: soluzione promettente per il tracciatore di Fase-2.
  Metodo ed apparato sperimentale già parzialmente sviluppati a Pisa (per scambio termico monofase liquido con punto di lavoro a 30° e 2W/cm2 di dissipazione) per avere un cooling efficiente e con bassa quantità di materiale in zona attiva .
12.8 mm
700 µm
Micro tubi Compositi
- Carbon Fiber Reinforced Plastic
Eventuale sviluppo con FBK di micro-canali in Silicio
Tecnologia DRIE (Deep Reactive Ion Etching) , le stesse usate per i pixel 3D
Silicon oxide sealing
500/300 µm
150 µm
700 mm
700 mm
Carbon Fiber Pultrusion
Peek pipe
Dh=300 mm
CMS PIXEL TRACKER FASE 2: proposal R&D presentata alla CSN1 febbraio 2014
Silicon buried channels for pixel detector cooling : M.Boscardin et al., Nucl.Instrum.Meth. A718 (2013) 297-298
COURTESY OF FILIPPO BOSI (INFN PISA)

## Slide 31: Programma di lavoro Micro Channel Cooling
  Progettazione e produzione di sistema a CO2 evaporativo per la verifica della fattibilita’ di cooling a microchannel su supporti a microtubi costruiti in CFRP.
    Soluzione conservativa per questo R&D
    Focalizzazione a design specifici per un rivelatore plausibile per il vertex detector di CMS
  Ottimizzazione/minimizzazione delle dimensioni dei micro-tubi a partire da valori sperimentati: sezione < 700 x 700 μm2 e diametro idraulico < 300 μm.
  Riduzione del material budget: < 0.15% X0 - ottimizzazione in funzione della temperatura di lavoro.
12.8 mm
700 µm
Support Cross Section
Radiation lenght 0.15%X0
  Progettazione e produzione di un layout sperimentale per prototipi di supporto con lunghezza dei canali ottimizzata per un rivelatore di vertice (30-60 cm) con connessioni idrauliche idonee (alto DP e miniaturizzazione)
Light prototype support using micro-channel technology as high efficiency system for silicon pixel detector cooling : Nucl.Instrum.Meth. A650 (2011) 213-217
COURTESY OF FILIPPO BOSI (INFN PISA)

## Slide 32
Outlook
The upgrade of the Tracker for the high-luminosity operation of the LHC is a formidable challenge. A substantial amount of R&D is already ongoing, and all major aspects are receiving attention. Some of the developments, in particular those addressing the most advanced technologies, may soon be confronted with the lack of financial resources. Together with the R&D on the components, design, modelling and simulation studies (for tracking and trigger) are the key for an optimal choice of detector concept. The progress in the next two years will be crucial for the project, as it will lead to the choice of the detector concept to be designed and built.