## Slide 1
status of FCC-hh/FCC-ee machine studies
M. Benedikt, D. Schulte, F. Zimmermann
gratefully acknowledging input from FCC global design study team
Pisa, 3 February 2015

## Slide 2
(2) The location, depth, rotation and slope can be changed for a particular tunnel shape and circumference
(3) As the tunnel is moved around, the alignment profile shows a basic projection of the geology intersected along the circumference of the tunnel
(4) Information about the shafts is also given including their depth, the geology intersected by each shaft and the total shaft depth for a tunnel alignment
(1) All tunnel shapes and sizes that have been studied are stored in TOT
Tunnel Optimisation Tool (TOT)
J. Osborne

## Slide 3: input into the tool : some critical areas
Rhone leaving the Geneva Basin
Depth under lake Geneva
(in molasse or moraines)
Avoid Vuache faulting
J. Osborne

## Slide 4
geological tunnel optimization tool,
example: site study 93 km
PRELIMINARY
J. Osborne & C. Cook
Preliminary conclusions:
93 km fits geological situation really well, better than a smaller ring size.
100 km tunnel seems also well compatible with geological considerations.
The LHC could be used as an injector

## Slide 5: Lake Crossing: Tunnelling Considerations
Open Shield
Slurry TBM
Immersed Tube Tunnel
Superficial sediments
Moraine
Molasse
John Osborne (CERN-GS)

## Slide 6: Tunnel Optimization Tool (TOT) in the news
Arup News
Original news story on our website is here:
http://www.arup.com/News/2014_09_September/09_Sept_Arup_Arup_develops_BIM_tool_for_future_particle_accelerator)
NCE (Online and Print)
http://www.nce.co.uk/news/geotechnical/arup-to-develop-bim-for-cern-particle-accelerator/8669570.article
Construction Manager
http://www.construction-manager.co.uk/news/particle-physicists-and-engineers-build-bim-model-/
The Construction Index
http://www.theconstructionindex.co.uk/news/view/arup-develops-bim-tool-for-next-gen-cern-accelerator
Tunnels and Tunnelling:
http://www.tunnelsonline.info/news/arup-appointed-for-collider-tunnel-design-studies-4380226
BIM Crunch
http://www.bimcrunch.com/index.php/component/k2/item/1231-arup-developing-bim-tool-for-concept-design-of-future-particle-accelerator
WN.com
http://article.wn.com/view/2014/09/09/Arup_develops_BIM_tool_for_future_particle_accelerator_at_CE/
Construction Shows
http://www.constructionshows.com/new-building-information-tool-developed-arup-cutting-edge-project/1512656
Global Construction Review
http://www.globalconreview.com/news/arup-chosen-engineer-europes-100km-particle-accele/
In addition to these it will also be featured in:
UK Government’s BIM Task Force Newsletter (to be published)
The Structural Engineer Magazine (flagship publication for The Institution of Structural Engineers)
NON-CONSTRUCTION INDUSTRY PRESS
The Huffington Post
http://www.huffingtonpost.co.uk/2014/09/22/cern-particle-accelerator_n_5860116.html?utm_hp_ref=uk&ir=UK
Gizmodo UK
http://www.gizmodo.co.uk/2014/09/what-it-takes-to-build-the-largest-particle-collider-ever-made/
Interest from ILC Japan for a similar tool
Tool Application will be presented at IPAC15
J. Osborne

## Slide 7
Preliminary layout FCC-hh

## Slide 8: collimation optics
scaling from LHC: same half gaps & same phase advances
M. Fiascaris
S. Redaelli

## Slide 9
INJ + RF
EXP + RF
EXP + RF
EXP + RF
COLL + EXTR + RF
COLL + EXTR + RF
EXP + RF
INJ + RF
RF?
RF?
RF?
RF?
Preliminary layout FCC-ee

## Slide 10
Cms energy |  |  | 
Luminosity |  |  | 
parameter | LHC | HL-LHC | FCC-hh
c.m. energy [TeV] | 14 |  | 100
dipole magnet field [T] | 8.33 |  | 16 (20)
circumference [km] | 26.7 |  | 100 (83)
luminosity [1034 cm-2s-1] | 1 | 5 | 5 [→20?]
bunch spacing [ns] | 25 |  | 25 {5}
events / bunch crossing | 27 | 135 | 170 {34}
bunch population [1011] | 1.15 | 2.2 | 1 {0.2}
norm. transverse emitt. [mm] | 3.75 | 2.5 | 2.2 {0.44}
IP beta-function [m] | 0.55 | 0.15 | 1.1
IP beam size [mm] | 16.7 | 7.1 | 6.8 {3}
synchrotron rad. [W/m/aperture] | 0.17 | 0.33 | 28 (44)
critical energy [keV] | 0.044 |  | 4.3 (5.5)
total syn.rad. power [MW] | 0.0072 | 0.0146 | 4.8 (5.8)
longitudinal damping time [h] | 12.9 |  | 0.54 (0.32)
FCC-hh baseline parameters defined in EDMS No. 1342402, FCC-ACC-SPC-0001

## Slide 11: shielding of final triplet
50 MGy
at
3000/fb
l*=36 m
M.I. Besana and F. Cerutti

## Slide 12: b* reach
R. Martin
l*=36 m

## Slide 13
High synchrotron
radiation load (SR) of protons @ 50 TeV:
~30 W/m/beam (@16 T)
5 MW total in arcs
(LHC <0.2 W/m)
Beam screen to capture SR and “protect” cold mass
Power mostly cooled at beam screen temperature;
Only minor part going to magnets at 2 – 4 K
→ Optimisation of temperature, space, vacuum, impedance, e-cloud, etc.
FCC-hh synchrotron radiation

## Slide 14: advanced beam screen
Configuration:
A combined BS, made up of a LHC-like BS with a continuous slot and an “external” SR power absorber is proposed here.
43
18
15
Slotted BS solution
asymmetric
LHC-like BS solution
18
18
Continuous slot
V-shaped SR abs.
R. Kersevan

## Slide 15: photon tracks with slot & V
SR Ray-Tracing (Synrad+):
The high-energy small vertical angle opening of the primary SR fan passes almost unscathed inside of the 2x 1.57 mm-high continuous slot
All SR-induced gas load may interact with the beam
Only a fraction of the SR-induced gas load may interact with the beam
R. Kersevan

## Slide 16
P. Lebrun, L. Tavian
contributions: beam screen (BS) & cold bore (BS heat radiation)
At 1.9 K cm optimum BS temperature range: 50-100 K;
But impedance increases with temperature  instabilities
40-60 K favoured by vacuum & impedance considerations
 100 MW refrigerator power on cryo plant
FCC-hh: cryo power for SR heat
Contributions to cryo load:
beam screen (BS) &
cold bore (BS heat radiation)

## Slide 17
FCC-hh general considerations (assuming operation over 25 years)
  Initial luminosity should be equal to final HL LHC luminosity
     5x1034 cm-2s-1 with ~125 days effective operation / year
  Integrated luminosity (10 years, 125 days eff. operation/y) should be ~ equal to LHC total luminosity  O(3000 fb-1).
  FCC total luminosity should be one order higher than LHC total  O(30,000 fb-1)
FCC-hh luminosity goals & phases
Present parameter sets for the two operation phases:
  phase 1 (baseline):
    5x1034 cm-2s-1 (peak), average 250 fb-1/year (stops incl.)
     2500 fb-1 within total of 10 years (~HL LHC total luminosity)
  phase 2 (ultimate):
    2.5x1035 cm-2s-1 (peak), average 1000 fb-1/year (stops incl.)
       15,000 fb-1 within 15 years (~6x HL-LHC total luminosity).
  yielding total luminosity ~17,500 fb-1 over 25 years of operation

## Slide 18
luminosity evolution over 24 h
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h
  for both phases:
  beam current 0.5 A unchanged!
  total synchrotron radiation power ~5 MW.
→
radiation damping: t~1 h

## Slide 19
integrated luminosity / day
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h

## Slide 20
M. Mangano

## Slide 21
M. Mangano

## Slide 22
parameter | LEP2 | FCC-ee |  |  |  |  | CepC
 |  | Z | Z (c.w.) | W | H | t | H
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175 | 120
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100 | 54
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6 | 16.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98 | 50
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4 | 3.7
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2 | 6.8
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2 | 20
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0 | 0.8
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1 | 1.2
s*y [nm] | 3500 | 250 | 32 | 130 | 44 | 45 | 160
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16 | 2.3
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49 | 2.7
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73 | 0.61
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7 | 1.8
tbeam [min] | 300 | 287 | 39 | 72 | 30 | 23 | 40
the large number of bunches at Z, W & H requires 2 rings
short lifetimes due to high luminosity → continuous injection (top-up)
FCC-ee baseline parameters defined in EDMS No. 1346081, FCC-ACC-SPC-0003 (Rev. 2.0)

## Slide 23
parameter | LEP2 | FCC-ee |  |  |  | 
 |  | Z | Z (c.w.) | W | H | t
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175
beam-beam par. xy/IP | 0.06 | 0.03 | 0.175 | 0.06 | 0.093 | 0.092
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1
s*y [nm] | 3500 | 250 | 32 | 84 | 44 | 45
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7
tbeam [min] | 434 | 298 | 39 | 73 | 29 | 21

## Slide 24: FCC-ee alternative scheme
Z
W
H
crab waist & improved parameters
baseline
A. Bogomyagkov, E. Levichev, D. Shatilov

## Slide 25
Beam-Beam Optimization (120 GeV, y*= 1 mm)
 | Crab Waist |  Head-on  | Crossing (11 mrad)
RF voltage [GV] | 2.3 | 5.5 | 5.5
RF frequency [MHz] | 400 | 800 | 800
Tunes x /y /s | 0.54 / 0.57 / 0.009 | 0.54 / 0.61 / 0.0255 | 0.52 / 0.57 / 0.0255
Bunch length [mm] | 2.76 / 6.77 | 0.98 / 1.47 | 0.98 / 1.62
Bunch population | 3.5  1011 | 5  1010 | 6  1010
Footprint size x /y | 0.019 / 0.126 | 0.087 / 0.128 | 0.063 / 0.104
Lifetime bb+bs [min] | 17 | 120 | 200
Luminosity [cm-2s-1] | 9.8  1034 | 7.2  1034 | 5.8  1034
Luminosity (y = 2 mm) | 8.3  1034 | 6.8  1034 | 5.0  1034
Density contour plots |  |  | 
D. Shatilov

## Slide 26
Beam-Beam Optimization (175 GeV, y*= 2 mm)
 | Crab Waist |  Head-on  | Crossing (11 mrad)
RF voltage [GV] | 9.5 | 11 | 11
RF frequency [MHz] | 400 | 400 | 400
Tunes x /y /s | 0.54 / 0.57 / 0.0132 | 0.54 / 0.61 / 0.0172 | 0.52 / 0.57 / 0.0172
Bunch length [mm] | 2.75 / 3.74 | 2.11 / 2.56 | 2.11 / 2.68
Bunch population | 2.0  1011 | 1.1  1011 | 1.2  1011
Footprint size x /y | 0.023 / 0.079 | 0.071 / 0.137 | 0.047 / 0.106
Lifetime bs [min] | 18 | 35 | 25
Luminosity [cm-2s-1] | 1.15  1034 | 1.3  1034 | 1.2  1034
Luminosity (y = 1 mm) | 1.25  1034 | 1.3  1034 (800 MHz) | 1.25  1034 (800 MHz)
Density contour plots |  |  | 
If additional y growth due to coupling and dynamical x is accounted, crab waist could become the best.
D. Shatilov

## Slide 27: FCC-ee crab-waist IR
A. Bogomyagkov

## Slide 28: IR synchrotron radiation
further optimization required in the context of MDI (SR background→ weaker bends?)
M. Boscolo
H. Burkhardt
Photon energy ~350 keV very similar to LEP2 where this was acceptable with IRs designed for low synrad & ~100 collimators and local masks,

## Slide 29: Closed ring for FCC-ee optics
chromatic optics
functions over ¼ ring
energy acceptance ±2%
(lifetime OK even at 350 GeV)
A. Bogomyagkov

## Slide 30: IR with solenoids & crossing angle
V. Telnov,
A. Bogomyagkov
further optimization underway
vertical emittance growth
between 1% and 100%

## Slide 31: RF cavities
U. Wienands

## Slide 32
FCC-ee RF staging
U. Wienands
1 MW klystron driving 8 cavity-modules up to 12 MV (400 MHz), 1 cavity module consists of 2 two-cell cavities

## Slide 33
U. Wienands
FCC-ee staging

## Slide 34: energy sawtooth
U. Wienands

## Slide 35
how much luminosity is needed?
FCC-ee crab waist w 4 IPs
FCC-ee baseline w 2 IPs
ILC upgrades
CepC w 2 IPs
ILC baseline
Z W H ttbar
100 ab-1/yr
10 ab-1/yr
1 ab-1/yr
100 fb-1/yr
10 fb-1/yr
L [1034 cm-2s-1]
ECM [GeV]

## Slide 36: a few conclusions
work on both colliders is progressing well, in international collaboration
closed optics solutions are available now
tunnel optimization tool – first in the world !?
compatible ring layouts for hh and ee
first thoughts on vacuum, cryogenics & SRF
possibility of using LHC as hadron injector
performance potential better than baseline
  hh: phase-2 (smaller b*, larger DQ)
  ee: crab-waist option & optimization
much more work to be done …