## Slide 1: Fast Timing for High-Rate Environments with Micromegas
E. Delagnes, G. Fanourakis, E. Ferrer Ribas, I. Giomataris, C. Godinot, D. González Díaz, U. Joshi, Changguo Lu, M. Kebbiri, K.T. McDonald, H. Muller, E. Olivieri, T. Papaevangelou, A. Peyaud, F. Resnati, L. Ropelewsky, R. Veenhof, S. White

## Slide 2: Micromegas time scales
The electron multiplication takes place in high E field (> 20 kV/cm)
between the anode (strips, pads) and the mesh in one stage
small amplification gap (50-150 μm)
fast signals (~ 1 ns)
short recovery time (~50 ns)
high rate capabilities (> MHz/cm2)
high gain (up to 105 or more)
A GARFIELD simulation of a Micromegas avalanche (Lanzhou university)
micromesh signal
strip 1
strip 2
strip 3
Time response is limited from the continuous ionization on the drift gap

## Slide 3: Localizing the e- creation point
Limit the direct gas ionization
use a radiator / photocathode electron emitter:
Cherenkov light produced by charged particles crossing a MgF2 crystal
Photoelectrons extracted from a photocathode (CsI)
  Simultaneous & well localized ionization of the gas (time jitter for the Cherenkov light ~10 ps)
  Well defined, small drift gap with strong electric field (~10kV/cm), or no drift
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
preamplification
Charged particle
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
Charged particle
Reflective mode
Semitransparent mode
~80 photons/cm
~80 photons/cm

## Slide 4: Limiting the e- diffusion in the gap
Longitudinal time jitter as function of the drift field for several Ne mixtures. (R. Veenhof)
Small drift gap + strong electric field
  Limited diffusion
Simulations:
Few hundred μm drift field can provide time jitter per electron ~ 100 ps (Ed ~ 5kV/cm)
Several gas mixtures possible
Good performance for high amplification fields (>50 kV/cm)
 preamplification improves time resolution!
5%
10%
15%
20%

## Slide 5: RD51 common fund project
Title of project: Fast Timing for High-Rate Environments: A Micromegas Solution
Contact persons: Sebastian White (co-PI), Princeton/CERN Sebastian.White@cern.ch
Ioannis Giomataris (co-PI), Saclay ioa@hep.saclay.cea.fr
RD51 Institutes:
1. IRFU-Saclay, contact person Ioannis Giomataris ioa@hep.saclay.cea.fr
E. Delagnes, T. Papaevangelou, M. Kebbiri, E. Ferrer Ribas, A. Peyaud, C. Godinot
2. NCSR Demokritos, contact person George Fanourakis gfan@inp.demokritos.gr
3. CERN, contact person, Leszek Ropelewsky Leszek.Ropelewski@cern.ch E. Olivieri, H. Muller, F. Resnati
+ RD51&Uludag University, Rob Veenhof veenhof@mail.cern.ch
4. Universidad de Zaragoza, Diego González Díaz* diegogon@unizar.es
Ext. Collaborator:
Princeton University, contact person K.T. McDonald, kirkmcd@princeton.edu
Sebastian White, Changguo Lu
Awarded 3/2015
* Present Institute: Uludag/CERN

## Slide 6: The RD51 project
R&D on charged particle timing towards ~10 ps
   high rates / high radiation environment (HL-LHC)
Project goal: demonstrate this level of performance based on a Micromegas photomultiplier with Cerenkov-radiator front window
  Single electron time jitter ~100 ps
  produce sufficient photoelectrons to reach timing response ~ 10 ps.
Build a Micromegas prototype equipped with crystal / photocathode
Demonstrate the ~100 ps time jitter for single e- using high precision UV laser
  Semitransparent / Reflection mode
  Gas optimization
Measure time resolution @ MIP beam

## Slide 7: UV photon detection
Reflective photocathode:
Photosensitive material is deposited on the top surface of the micromesh.
Photoelectrons extracted by photons will follow the field lines to the amplification region
  The photocathode does not see the avalanche  no ion feedback effect  higher gain in single stage (~ 105)
  Better aging properties
  High electron extraction & collection efficiency
  Reflection on the crystal ?
  e- path variation
  Limitation to Microbulk / opaque meshes
Semi-transparent photocathode:
Photosensitive material is deposited on an aluminized MgF2 window (drift electrode)
  Extra preamplification stage  better long-term stability, higher total gain
  Various MM technologies & gas mixtures possible
  Lower photon extraction efficiency
  Photocathode resistance to sparks (?)
  Ion backflow  aging (?)
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
photon
electron
insulator
anode
micromesh
photocathode
avalanche
crystal
preamplification

## Slide 8: Design of the prototype
First tests with UV lamp / laser  quartz windows
Microbulk Micromegas ø 1cm
Possibility to deposit CsI on the mesh surface
Capacity ~ 35 pF
Bulk Micromegas ø 1cm
Capacity ~ 5 pF
Amplification gap 64 / 128 / 192 μm
Ensure homogeneous small drift gap & photocathode polarization
Photocathode: 10 nm Al
Stainless steel chamber compatible with sealed mode operation
Very thin detector active part (<5 mm)

## Slide 9: Detector prototype

## Slide 10: Tests with deuterium flash lamp
Estimated ~20 photoelectrons per pulse by comparing with the amplitude of the signal from a candle
24 hour run in sealed mode. Lamp not very stable

## Slide 11: Measuring single p.e.
IRAMIS facility @ CEA Saclay (thanks to Thomas Gustavsson! )
UV laser with σt ~ 100 fs
λ = 275-285 nm after doubling
intensity ~ 3 mJoule / pulse
Repetition 80 MHz (!!) - limitations on gain
  Reduced to 8 kHz on the second day
Light attenuators (fine micro-meshes 10-20% transparent)
Trigger from fast PD
Cividec 2 GHz, 40 db preamplifier (thanks to Erich )

## Slide 12: Measurements @ IRAMIS laser

## Slide 13: Data acquisition
Registration of Micromegas & photodiode waveforms with 2GHz oscilloscope @ 10 GS/s
Offline analysis
thanks to Xavier & w. R. Zuyeuski
for osciloscope & LabView software

## Slide 14: Response to single p.e.
Microbulk
Bulk 128
Signal modeling by
D. Gonzalez Diaz & F. Resnati
Strong attenuation, so that events with no pulse appear
UV light from continuous source (candle)

## Slide 15: Signal Modeling (D. Gonzalez Diaz, F. Resnati, R. Veenhof)

## Slide 16: Signal Modeling (D. Gonzalez Diaz, F. Resnati, R. Veenhof)

## Slide 17: Signal Modeling (D. Gonzalez Diaz, F. Resnati, R. Veenhof)

## Slide 18: Calculation of σT (~1 p.e.)
σΤ Micromegas
σΤ PD
Tmm – TPD [σT corr]
Edrift = 10 kV/cm2
Soft smoothing + CF
Calculate attenuation from <ampl>
Calculate <Np.e.> from zeros.
28.9% zeros  <Np.e.> = 1.26

## Slide 19: Calculation of σT (~50 p.e.)
σΤ Micromegas
σΤ PD
Tmm – TPD [σT corr]
Edrift = 10 kV/cm2
<Np.e.> = 51.4

## Slide 20: Constant Fraction analysis
Calibrated attenuators
Maximum attenuation  29% zeros  <N> ~1.26 p.e.
Results given for the mean photoelectron number – impossible to discriminate 1e/2e events
Resolution scaling with 1/sqrt(N) law
Gas used: Ne (90%) + C2H6 (10%)
  Not optimal!
Very promising result:
  ~180 ps for 1.26 p.e.

## Slide 21: Wavelet treatment (by Sebastian White)
CERN Detector Seminar 25/09/2015

## Slide 22: Wavelet treatment (by Sebastian White)

## Slide 23: Wavelet treatment (by Sebastian White)

## Slide 24: Comparison with the simulation
Improvement compared to the physical jitter due to the preamplification
Excellent agreement between data & simulation

## Slide 25: Optimum gas mixtures for timing
Look for the minimum time spread (‘fastest mixture’) at any given gain
now
By Rob Veenhof & Diego Gonzales
Notes:
Working fields in the MM for pure quenchers need to be about x2 higher. May limit the gain in case of defects.
Drift fields for pure quenchers need to be about x3 higher.
Dissociative attachment for CO2 and freons expected to be compensated by gain. Needs to be verified.
Selection of non flammable gas!
( eαG)

## Slide 26: Next steps – detector improvement
Detector studies
  Existing chamber
    Bulk technology for semi-transparent mode
    Microbulk for reflective mode
    Thin-mesh bulk Improve electron transparency / minimize path variations. First fabrication tests OK
  Laboratory tests (picosecond laser @ IRAMIS)
    Gas optimization (He mixtures, quenchers…)
    Reflective mode
    Continue single photo-electron performance studies
    Drift gaps
    Effect of the pillars
  Build a second setup @ CERN
  Particle beam tests
  Design of a pixelated prototype (~5×5 cm2).
    Scalable to ~1 m2
Simulations / Calculations
  Performance
  Detector design
  Gas selection / optimization
  Photocathode / crystal selection

## Slide 27: Next steps (photocathode, aging, robustness)
Radiator / photocathode
  Crystal selection / photon yield
  Photocathode (CsI fabrication, handling, storage, protection…)
  Aging tests
    Deterioration with time
    Particle flux => high rate tests @ IRAMIS
  Robustness
  Total reflection problem @ reflective mode ? Coating,...
Secondary Emitter (Collaboration with CEA/DRT)
  Replace the crystal + photocathode with secondary electron emitter
    Robustness / spark reduction
    Free choice of substrate material
  Investigate materials with high secondary electron yield. (Doped-) diamond deposition, DLC, graphene…
    Conductive
    Robust
  Multi layer detector
  Diamond / graphene layer for photocathode protection ?
Improvement with
reflective mode

## Slide 28: Next steps (Electronics)
Electronics
  SAMPIC (D. Breton / LAL)
  Radiation hard amplifiers  Mitch Newcomer / PENN
  Onboard electronics ?
  Improve signal transfer lines, bandwidth
  Fast charge preamplifier? (integration ~ps ?)

## Slide 29: Conclusions - outlook
A Micromegas photodetector has been constructed in order to study the potential for ~10 picosecond timing for charged particles
First tests with a laser are positive.
180 ps time resolution for <N>=1.26 p.e. has been measured with a standard bulk Micromegas in semi-transparent & sealed mode + preamplification
  Big margin for improvement
    Gas optimization
    Thin mesh
  Reflective mode to be studied.
  Alternative design with secondary emitter
R&D will continue. More resources (hopefully!)
Involvement of more groups / labs
  Involvement of the Saclay SPP group
Request for ANR funding
Encouraging results + growing interest!

## Slide 30: Thank you!

## Slide 31: Bulk technology
pillar
pad
Well established technique (lamination)
Woven Inox mesh 30 µm
vacrel 128 µm
Readout pads
Readout plane + mesh all in one
  Bulking: Process to encapsulate the mesh on a PCB (mesh = stretched wires)
  The pillars are attached to a woven mesh and to the readout plane (PCB)
  Typical mesh thickness 30 μm, gap 128 μm
  Uniformity, robustness, low cost, no supporting frame,
  Easy fabrication
  Large area detectors
  Mass production!
  Ideal gap for Ne/He - based mixtures
  One main disadvantage: Woven mesh  Not possible to deposit the photosensitive material

## Slide 32: Microbulk technology
Microbulk Micromegas
  The pillars are constructed by chemical processing of a kapton foil, on which the mesh and to the readout plane are attached. Mesh is a mask for the pillars!
  Typical mesh thickness 5 μm, gap 50/25 μm
  All advantages of a bulk Micromegas & enhanced performance
  In addition:
  Direct deposition of photosensitive material
  Big optical opacity (>90%)
    Big electron collection efficiency (>95%)
  Less outgassing
  But:
  Higher capacity
  Fabrication process of 2D readouts complicated
  Mesh can not be replaced if damaged
  Maximum gap 50 μm (present technology) is not optimum for Ne/He-based gas mixtures  maximum gain?
Readout plane + mesh all in one
Micromesh
5µm copper
Kapton 50 µm
Readout pads
Lower capacitance
Under development