## Slide 1
Study of Negative-Ion TPC using μ-PIC
for Directional Dark Matter search
Kentaro, Miuch (Kobe Univ.)
DANIEL, Snowden-ifft (Occidental College)
JEAN-LUC, Gauvreau (Occidental College)
+NEWAGE Group
Tomonori Ikeda (Kobe Univ.)
DM Experiments with MPGD
NEWAGE
Motivation
Measurement
Summary
Notes: Good morning.
I’m Tomonori Ikeda , a graduate student at Kobe University.
The theme is study of Negative-Ion TPC using μPIC for directional dark matter search.

## Slide 2
1. DM experiment with MPGD
Notes: First , I talk about Dark matter experiment with MPGD.

## Slide 3
Directional Dark Matter Search with MPGD
WIMP
nucleus
WIMP
Cygnus
γ
Recoil angle distribution gives strong evidence.
By MPGD
PLB578 (2004) 241–246
Reconstruct 3D track of nuclear recoil using MPGD
Dark matter is coming to the earth from Cygnus
60°
232km/s
Earth
Dec. 4th
Jun. 2nd
Sun
Image of elastic scattering
DM
Notes: I explain the method of Dark matter research by using MPGD.
This figure shows our galaxy. Galaxy has dark matter.
We are in solar system, move towards Cygnus.
So relativity dark matter is coming to the earth from Cygnus.
りらてぃゔり
Right figure shows WIMP-nucleus scattering .
Nucleus is recoild by WIMP.
We get this nuclear track with MPGDs and calcurate recoil angle gamma.
The distribution of gamma is expected to show an asymmetry.
There are many forward scatterings .
This signature should be strong evidence of dark mattter (ovsevation).

## Slide 4
25cm
30cm
1m
DM-TPC
・CCD(256um pitch)
・2D track
・Head/tail recognition
・Underground
DM experiments using Gas Detector
DRIFT
・MWPC(2mm pitch)
・First started gas detector
・Underground
・Low background
・Large size(~1m3)
MIMAC
・MicroMegas(~424um pitch)
・Underground
・10×10×25 cm3
NEWAGE
・μ-PIC(400um pitch)
・3D track
・Direction-sensitive limit
・Underground
Notes: Here I show you DM experiments using gas detector in the world.
DRIFT team use MWPC with negative ion.
DRIFT group has a low background , and large size detector in underground.
DM-TPC uses CCD camera and succeed in head/tail recognition.
MIMAC and NEWAGE use MPGDs,
For MIMAC, Micromegas which pich is almost 400 um, is used .
The Detector volume is 10 times 10 times 25 cubic centimeter.
NEWAGE use u-PIC.
Electrodes’s pich is 400 um.
We have the best direction-sensitive limit.
ずをさしながら言います。
DRIFT->DM=Tpc-> MIMAC->NEWAGE

## Slide 5
2. NEWAGE
Notes: I explan NEWAGE experiment in detail.

## Slide 6
NEWAGE0.3b’ Detector @Kamioka mine
GEM：Preamplifier (Gas gain ~10)
LCP 100μm
Detection volume
  30×30×41 cm3
Gas
  CF4(76 torr)
μ-PIC: Anode pitch 400 μm
Gasgain ~103
hole diameter : 70 μm
pitch : 140 μm
μ-PIC
30cm
30cm
31cm
41cm
GEM
Drift Cage
Good for spin dependent DM search
Notes: NEWAGE detector is at Kamioka mine in Japan.
This is the whole detector system.
Left module is electronics, and this is gsa circulation system.
This vessel is uTPC.
The length of Drift cage is fourty one centimeter.
GEM is thirty one times thirty one square centimeter.
And uPIC is 30 times thirty square centimeter.
So the Detecton volume is 30 times 30 times 41 cubic centimeter.
We use CF4 gas, because Fluorine has a large csoss section of Spin Dependent interaction.

## Slide 7
Latest Result
Conditions RUN14
period：2013/7/20~8/11, 10/19~11/12
live time ：31.6 days
fiducial volume：28×24×41 cm3
CF4 gas(76Torr)
mass：10.36 g
exposure：0.327 kg・days
Skymap in galactic coordinate
the best direction-sensitive limit (K.Nakamura et.al, PTEP(2015)043F01s)
Black point is nuclear recoil event
Gradation color: detector eficiency
Notes: Now I show you the latest result of NEWAGE。
This is obtained skymap of carbon and flourine recoils in galactic coordinate. CF
Horizontal axis is galactic longitude, and vertical axis is galactic latitude.
Black dots is observed recoil events and gradation color is detection efficiency.
And they are consistent.
We made a cosine distribution and obtained direction-sensitive limit.
In this figure, horizontal axis is mass of DM, and vertical axis is cross section.
This work is red limit curve.
NEWAGE has the best direction-sensitive limit.
the green line are non-directional dark matter search .
they have limits better than directional experiment.
So we need to reduce background event, in order to reach there limits

## Slide 8
3. Motivation
Notes: I would like to talk about why we want to use negative ion gas.

## Slide 9
C
Background
Main background event in μTPC
  ⑦ in the high energy region
  C in the low energy region
α-rays (U/Th-chain) from the glass cloth in PI 100μm of μ-PIC is dominant
NEWAGE0.3b’
The Z fiducialization is, if possible , very important.
Z
We already could XY fiducialize
Notes: This figure is a cross section view of NEWAGE0.3b’ detector
The green label is u-PIC and GEM, Drift plane.
Black arrows show background candidates.
We have already understood the main background source.
Main backgrounds are α-rays from radioactive contamination in u-PIC.
Shown by number 7 arrow, and C arrow, both come from u-PIC.
If we could fiducialize in the Z-direction, we can improve our sensitivity.
So Z fiducialization , if possible , is very important.

## Slide 10
Self Triggering TPC
e-
Electric field
Trigger timing
Z
μ-PIC & GEM
: absolute Z
: relative Z
Absolute Z-position cannot be known in self-trigger.
e-
Nuclear track
Notes: Here I explain the reason why we can’t detect absolute Z-position.
The problem is we don’t know time zero in self trigger.
In this figure, ionized electrons drift to u-PIC and GEM.
Time zero is here.
But our trigger timing is this point when electrons arrive at u-PIC.
So we can only get relative Z, red line , we can’t know absolute Z, the blue one.

## Slide 11
30 Torr CS2
10 Torr CF4
1 Torr O2
CS2-
minority peak
tb
ta
The first measurement of absolute Z-position in a self-triggering TPC
Using negative ion gas CS2 with a few percent O2
MWPC
Z
ta
tb
CS2-
minority charges
Z-fiducialization used by DRIFT
[Physics of the Dark Universe 9-10(2015)1-7]
Notes: Recently DRIFT group succeeded in the measurement of absolute Z-position.
They use CS2 gas mixed with a few percent O2.
CS2 catch ionized electrons and drift as negative ion CS2-.
With an existence of O2, another types of negative ion called minority charges are generated.
They are drifted at different speed and create peaks in arrival time called minority peaks.
Right panel is a typical wave form.
The last pulse is made by CS2-, and earlier pulses are made by minority charges.
Using this equation, we can calculate absolute Z-position.
Utilizing

## Slide 12
Negative Ion Gas
SF6
Negative Ion Gas Candidates
Non-toxic, Non-volatile, Nonflammable
Electron Affinity 1.1eV
Insulating gas
High electric field is necessary
Recently demonstrate with THGEM
Requirement of gas gain
,using amplifier[1V/pC], then the amplitude of minority peak will be 15mV at Nuclear recoil (50keV)
CF4(electron drift(normal) gas)
Being used for NEWAGE
Typical drift velocity : ~cm/μs
Operation Gas gain 3000 (76Torr)
Amplifer gain 160mV/pC(ASDchip)
Typical drift velocity: 10-2cm/μs
We can use slow shaping time amplifier(good S/N).
[N.Phan talk at CYGNUS2015 , June 2015]
Toxic, Volatile, inflammable
Electron Affinity 0.89eV
Used with MWPC
Requirement of gas gain
Doesn’t have Flourine
CS2
We need to add CF4.
76Torr
P
~480・
using amplifier(1V/pC)
76Torr
P
~980・
Notes: Now I discuss the candidate of negative ion gas.
Typical negative ion gas for TPC is CS2.
CS2 gas is hard to handle because of three properties.
It is toxic, volatile and inflammable.
The requirement of gas gain is only 480, because drift velocity of negative ion is very slow.
The order is 10 to the minus two cm/us.
we can use slow shaping time amplifier.
It is good S/N, and good gain.
For DM experiment, A disadvantage of CS2 gas is it doesn’t have flurine.
So we need to add CF4.
As another candidate of negative ion gas, recently SF6 gas is demonstrated for THGEM.
It is non-toxic non-volatile and nonflammable.
It is easily to handle
The advantage is SF6 gas has flourine.
So we doesn’t need adding another gas.
But it is used as insulating gas , its electron affinity is very large , so it is expected to difficult to achieve sufficient gas gain.
If we can use, very happy.

## Slide 13
4. Measurement
Notes: We tested uPIC+GEM system with CS2 gas and SF6 gas.

## Slide 14
Anode readout
Cathode readout
Drift mesh
GEM
μ-PIC 10×10 cm2
Drift mesh(SUS)
GEM (10×10cm) LCP 100um
μ-PIC (10×10cm)
10mm
3mm
readout
Amplifier
1.1V/pC or 160mV/pC
NEWAGE0.1c detector
Notes: For test of negative ion gas, we construct detector,
uPIC has a detection area of 10 times 10 square cm.
GEM is made of LCP , width is 100um, and set 3mm above uPIC.
Drift mesh is set 10mm above GEM

## Slide 15
4.1 CS2
Notes: Next, for CS2 gas measurement.

## Slide 16
Test CS2 with u-PIC+GEM @Occidental collage
Gain Curve
CS2 76Torr and 38Torr give more than 1000 total gain!
for 76Torr
for 38 Torr
Notes: At Occidental collage, a test with CS2 gas was performed.
This figure is gain curve.
Xaxis is anode voltage of upic.
The blue point is CF4 gas ,76Torr,
CS2 gas 76Torr is green point. Total gas gain is higher than CF4 .
Total gas gain achieved requirement of gas gain, so we expecte to detect nuclear recoil events at lower energy.
Red point is Cs2 gas 38torr,.
For CS2 38torr,, total gas gain also achieved requirement.
this is good trend.
Because in lower pressure , nuclear track will be longer ,so we can expect angular resolution become better.

## Slide 17
Gain Curve
ΔGEM Dependence
μ-PIC+GEM system with CS2 worked very well.
Adding O2 gas , we will be able to observe minority peak.
for 76Torr
for 38 Torr
Notes:   We measured delta gem dependence..
  X-axis is delta GEM voltage.
  at uPIC anode=550V, CF4 76Torr and CS2 76 Torr showed almost same trend.
  As a result, uPIC+GEM system with CS2 worked very well.
  Adding O2 gas , we will be able to observe minority peak.

## Slide 18
4.2 SF6
Notes: I talk about SF6 gas measurement.

## Slide 19
SF6 waveform
test SF6 with uPIC+GEM @ Kobe Univ.
252Cf Nuclear Recoil
waveform
CF4 152Torr
SF6 152Torr
E = 674 V/cm
Anode = 539V
ΔGEM = 363V
Amp:τ=1μs
E = 1100 V/cm
Anode =630V
ΔGEM = 650V
Amp:τ=1μs
Notes: Here I show you typicall waveform.
We use Californium two handred fifty five as source.
Top panel is waveform of SF6 .
The pressure is one handred fifty two Torr.
And we use amplifier which shaping time is 1 microsec.
So pulse width is very long about 10 micosec..
The feature is rise time is slow, because of drift velocity of negtive ion SF6 minus.
Compared to CF4 gas shown by bottom panel, it is clear.
It is no problem for low rate experiment.

## Slide 20
仮
E = 1047 V/cm
SF6 152torr
Anode = 670V
ΔGEM = 728V
Gain ~300
SF6 Gas Gain
Total gas gain is about 300.
When we improve the amplifier , this gas gain is sufficient.
Then minority peak will be appeared.
55Fe
Notes: Finally we measured gas gain by using iron fifty five.
Gas pressure is 152Torr.
Total gas gain is about 300.
Thank for strong electric field of MPGD, Gas gain could achieve several handred .
When we improve amplifier,
the gas gain is sufficient for Nuclear recoil (100keV), then minority peak will be appeared.
We are planig to test with long drift system, and try to observe minority peaks.
requirement
Ampのimprovemnet

## Slide 21
At 76Torr, Photon feedback was observed between u-PIC and GEM.
Drift velocity
~10-2 cm/μs
Drift Velocity of SF6-
SF6 76Torr
photon
photon
SF6 76Torr
μ-PIC
GEM
wave form
Notes: Photon feedback was observed between u-PIC and GEM ,
Using this effect, we measure Drift velocity of SF6-.
This figure shows dependence of electric field over pressure.
Drift velocity is proportional to electric field, and we obtained about 10 to the three minus cm/us.
It is consistent with measurement of Drift group.

## Slide 22
MPGDs with negative ion gas will create more opportunities for low background experiment.
A first test of μ-PIC+GEM with negative ion gas was performed.
For CS2, the total gas gain is higher than 10000.
In the future, with both of them, minority peaks will be observed.
SF6 gas needs optimization , going to study
For SF6, the total gas gain is about 300.
5. Summary
Notes: A first test of u-PIC + GEM with negativeion gas was performed.
For CS2, the total gas gain is higher than 10000.
For SF6, the total gas gain is about 300.
SF6 gas need to optimize , going to study.
In the future, with both of them, minority peaks will be to observed with uPIC+GEM system.
we are planning to use SF6 gas because of safety aspect.
And we can remove background event, will achieve smaller scattering coss-section.
At the end, MPGDs with negativ ion gas will create more opportunities for low background experiment.

## Slide 23
Thank you for your attention!

## Slide 24
4. Back-up

## Slide 25
Electronics for CS2
We used CREMAT’s CR-111 charge sensitive preamplifier.
CS2 76Torr
55Fe
CH2 (anode 13cstrips sum)
20mV/div
CH4 (cathode 13cstrips sum)
20mV/div
100us/div
VDRIFT=-1.5kV
GEM=-800V/-460V
uIPC anode=550V

## Slide 26
Electronics
CLEAR-PULSE
CS515-1 1V/pC
IN
OUT
1nF
100pF
100pF
100
100
10K
10K
100
100
50
50
1K
Highpass τ=1μs
1st Lowpass Filter
2nd Lowpass Filter
Shaping amplifier for SF6
Amplifier 1.1 V/pC
120 nC/pC
Electronics for SF6
Notes: Drift velocity of negative ion is slower than electrons, typically ten to the negative second cm par micro sec.
So rise time is very long, shaping time is needed micro sec order.
We made slow time constant and high gain amplifier.

## Slide 27
Spin dependent(SD) cross section
The SD cross section is written using σSD as

## Slide 28
From N. Phan, Cygnus 2015
THGEM( 4mm)
Minority Peak of SF6

## Slide 29
Amplifier for liquid Argon TPC
Development of LTARS ASIC
  pre-amp. & shapers in a chip
  high density (32ch I n a chip)
  power supply voltage ±0.9V
  ENC ~2000@300pF
  conv.gain ~9V/pC

## Slide 30
Detection efficiency in detector coordinate