## Slide 1: Status of COMPASS RICH-1 upgrade with MPGD-based Photon Detectors
The COMPASS RICH-1 PD upgrade
The structure of the hybrid detector
The THGEM raw material selection
Production of THGEMs and Micromegas
Detector assembly, test and installation
Conclusions
Fulvio Tessarotto ( I.N.F.N. – Trieste )
on behalf of the COMPASS THGEM group:
Alessandria, Aveiro, Calcutta, Freiburg, Liberec, Prague, Torino, Trieste

## Slide 2
COMPASS II Collaboration
Experiments with muon beam:
  Spin structure, Gluon polarization
  Flavor decomposition
  Transversity
  Transverse Momentum-dependent PDF
  DVCS and HEMP
  Unpolarized SIDIS and TMDs
COMPASS - I (2002 – 2011)
COMPASS - II (2012 – 2017) …
Experiments with hadron beams:
  Pion polarizability
  Diffractive and Central production
  Light meson spectroscopy
  Baryon spectroscopy
  Pion and Kaon polarizabilities
  Drell-Yan studies
Bochum,
Bonn (ISKP
& PI),Erlangen,Freiburg,
Mainz,München TU
USA (UIUC)
Saclay
Tel Aviv
Calcutta (Matriviani)
Torino (University,INFN),
Trieste (University,INFN)
Warsawa (NCBJ),
Warsawa (TU)
Warsawa (U)
CERN
Yamagata
Praha (CU/CTU)
Liberec (TU)
Brno (ISI-ASCR)
Дубна (LPP and LNP), Москва (INR, LPI, State University),Протвино
Lisboa/Aveiro
Taipei (AS)
~ 250 physicists
from 24 Institutions
of 13 Countries

## Slide 3
IN THE COMPASS SPECTROMETER
Muon-filter2,MW2
Veto
SM1 dipole
SM2 dipole
Polarised Target
HCAL1
Muon-filter1,MW1
Micromegas,DC,SciFi
Gems,SciFi,DCs,straws
MWPC Gems Scifi
trigger-hodoscopes
Silicon
RICH_1
BMS
Gem_11
ECAL2,HCAL2
straws,MWPC,Gems,SciFi
straws
DW45
SciFi
Beam:
160 GeV µ+
2 . 108 µ/spill
(4.8 s/16.8s)
Pm ~ 80%
P. Abbon et al., NIM A 577 (2007) 455
P. Abbon et al., NIM A 779 (2015) 69

## Slide 4
hadron PID from 3 to 60 GeV/c
acceptance: H: 500 mrad V: 400 mrad
trigger rates: up to ~100 KHz
beam rates up to ~108 Hz
material in the beam region: 2.4% Xo
material in the acceptance: 22% Xo
detector designed in 1996
in operation since 2002
first PD upgrade in 2006
( total investment: ~ 4 M € )
radiator:
C4F10
5 m
6 m
3 m
MWPC’s + CsI
UV mirror
wall
Al vessel
radiator gas: C4F10
HADRON PID IS PROVIDED BY RICH-1
COMPASS RICH-1: a large gaseous RICH
with two kind of photon detectors
providing:
PMT’s
beam pipe
PD’s: ~6 m2

## Slide 5: Gas radiator, mirrors, PD’s

## Slide 6
COMPASS RICH-1 MWPC’s with CsI

## Slide 7
The CsI photocathodes

## Slide 8: COMPASS RICH-1 PD upgrade
radiator:
C4F10
5 m
6 m
3 m
MWPC’s
UV mirror
wall
Al vessel
radiator gas: C4F10
PMTs
beam pipe
MPGD-based PDs
for COMPASS run 2016
MWPC’s
MPGD-based PDs
1.4 m2
4 new detectors of 600 mm x 600 mm

## Slide 9
The new photon detectors
Staggered THGEMs
each detectors consists of two modules having 600 x 300 mm2
hybrid: 2 THGEMs + 1 Bulk Micromegas
Multi-Pad Anode 8mm X 8mm pads
at positive HV
Signal read out via capacitive coupling pad readout and APV25 F/E boards

## Slide 10
Result of 7 years of dedicated R&D
Effective gain = 0.91 · 106
Ar/CH4: 50/50
PARAMETERS:
Diam. = 0.4 mm
Pitch = 0.8 mm
Thickn. = 0.4 mm
Rim = 10 μm
a. u.
Photon yield & Charged Particles vs Drift Field
see the poster by Shuddha Dasgupta

## Slide 11: The design of the COMPASS THGEM
12 sectors on both top and bottom, 0.7 mm separation
24 fixation points to guarantee THGEMs flatness
Thickness: 0.4 mm, hole diameter: 0.4 mm, pitch: 0.8 mm
border holes diam.: 0.5 mm
pillars in PEEK

## Slide 12: THGEM raw material selection
Our thickness uniformity requirements are stricter than those offered by producers  material selection
50 foils of 1245 mm x 1092 mm  cut out borders  800 mm x 800 mm  thickness measurement
Mitutoyo EURO CA776
coordinate measuring machine with ruby touch probe,
hosted in a thermalized room
for each foil 36 x 36 points in square pattern are measured
2 measurements (direct and reversed) to allow consistency checks.
  underpressure induced flatness

## Slide 13: THGEM raw material selection
  typical result for a good piece.
THGEM 313
THGEM 413
49 p.cs
2%<δ<3%
  from each foil twoTHGEMS can be produced:
  50 foils  100 raw THGEM pcb
  THGEM pcb size = 620 mm x 320 mm,
  active area = 581 mm x 287 mm
  δ for the 100 raw THGEM pcb (%)
  about half of the foils sent to ELTOS for THGEM production
  serial production ongoing
  all foils have been labelled and measured  database of local thickness of all THGEMS

## Slide 14
Production of the THGEMs at ELTOS
  stripping dry-film
  development
  etching
  image transfer
  multi-spindle drilling
  mounting
In Trieste a specific cleaning procedure is applied : polish with fine grain pumice powder, pressure water cleaning, ultrasonic Bath with Sonica PCB solution (PH11), distilled water rinsing and oven @ 160 ºC

## Slide 15
THGEM quality assessment
rejected piece
current monitor recording,
discharge counting
rejected
accepted
first 4 pieces: 1 rejected. Possibly recovered by repeating the cleaning treatment
ΔV(V)
Gain uniformity measurement
AMPTEK Mini-X Au used at 15 kV, 200µA + Cu foil provides 8 keV X-rays uniform illumination at a rate > 5 kHz cm-2 (for 1 cm Ar/CO2 70/30)

## Slide 16: Storage, transport, Au and CsI coating
  THGEM ready for coating
  CsI coating plant
  handling frame
  Storage box with N2 flow
  individual label is visible on the top face of each THGEM
  New glove box

## Slide 17: Final size Micromegas prototypes
s/<G> = 5% for each of the two Micromegas

## Slide 18
Serial production of final MM
anodic pad pcbs produced by TVR
Final Micromegas by CERN
Next steps: gluing Micromegas on support frames and testing them
With their APV25 electronic F/E board
anodic pad: + HV via large R
70 µm fiberglass
readout pad: at ground via F/E, embedded inside anodic pcb
Tests on 2500 pads:
electrical continuity
and capacity meas.
 38-42 pF/pad
signals
R (HV)
R (HV)
48 pads

## Slide 19
one of the 2 pads at standard voltage :
no trips observed
only effect: 2V drop  ~4% drop in gain
discharge cross-talk via pads
Two adjacent pads kept at anomalous high voltage (720 V) to enhance trip frequency (~ 0.2 Hz)

## Slide 20
Time variations of the hybrid detector gain
GAIN MEASUREMENTS
ALTERNATING
W, W/O CORRECTION
applying voltage compensation: gain evolution ~ 40%  ~ 10 %
Correction of Voltage LabVIEW based system fully automated + logging
p, T sensor at gas input and output

## Slide 21: The need of field shaping electrodes
THGEM border study
large field values at the chamber edges and on the guard wires
Field shaping electrodes in the isolating material protections of the chamber frames
isolating material (Tufnol 6F/45) protection

## Slide 22
The mechanical frames and the wires
drift and field wires: Cu-Be, Au coated
4 mm pitch, 100 µm diam.
manual soldering
tension meter

## Slide 23: The final mechanical structure is complex

## Slide 24: non trivial integration with other RICH PDs

## Slide 25: CONCLUSIONS & OUTLOOK
final parameters for MPGD-based PD’s after 7 years of R&D
Hybrid: 2 THGEMs + Micromegas; detector with 2 modules 600x300
COMPASS THGEM production well advanced, MM production started
Systematic quality control procedure defined
Final detector assembly, test and installation are challenging
RICH-1 will be upgraded with MPGD-based PD’s for 2016 run