## Slide 1: New substrate, high spatial resolution and big-area THGEMs: development and applications
State Key Laboratory of Particle Detection and Electronics
Institute of High Energy Physics, CAS
and University of Science and Technology of China
Yuguang Xie
ygxie@ihep.ac.cn
Oct. 14 2015
MPGD2015, Trieste, Italy

## Slide 2: Outline
New substrate THGEMs
High spatial resolution THGEM
Big-area THGEM
Applications
Summary

## Slide 3
New substrate THGEMs
Motivation
low neutron absorption and scattering, for neutron(thermal) detection
low natural radioactivity, for low background experiments
Substrate | S-Area/m^2 | HD/mm | Pitch/mm | TH/mm | Delivery/day
FR-4 | <=0.5*1.0 | 0.15~0.3(0.2) | >=0.4 (0.6) | 0.1~0.3(0.2) | 20
PTFE (Teflon) | <=0.5*1.0 | 0.15~0.3(0.2) | >=0.4 (0.6) | 0.1~0.3(0.2) | 30
Kapton | <=0.5*1.0 | 0.15~0.3(0.2) | >=0.4 (0.6) | 0.05~0.3(0.2) | 30
Ceramic | <=0.5*0.5 | 0.15~0.3(0.2) | >=0.4 (0.6) | 0.1~0.3(0.2) | 30
Development and production
Mechanical drilling, PCB-type substrates
In some cases, FR-4 is not the best choice.
Y. Xie et al. / NIM A 729 (2013) 809–815

## Slide 4
Ceramic
Kapton
Performance
FR-4
PTFE

## Slide 5
Longterm gain
Energy resolution
Less erating time &HV connection error
T & P not controlled

## Slide 6
Scattering and absorption on thermal neutron
Simulation done in G4, thermal neutron(0.0254eV), full components for substrates(0.2mm)
Separate effects: adsorption and elastic scattering
Separate cases: bare, bare+25um Cu and bare+25um Cu + 5 um Au laminates.
Cu results in loss by both absorption and scattering;
Au results in loss by absorption mainly.
total neutron absorption and scattering ratio: Kapton(high) > FR-4 > Ceramic > PTFE (low)
Gamma-induced electron background: Ceramic > PTFE > FR-4 > Kapton

## Slide 7
Low radioactivity
Samples
The HPGe detector( 0.01cps, 0.6cpm, crystal φ60mm )
The PCB-type substrates are not as “pure” as original materials
The natural radioactivity is 3-4 order higher than pure materials applied to low background experiments.
The PCB-type materials are good for THGEM making and can reach good performance.
THGEMs based on the pure materials are worthy of development

## Slide 8
Therefore, it’s not easy to find an all-purpose THGEM substrate . Substrates should be chosen according to applications!
Summary of new substrate THGEMs
Substrate | FR-4 | Ceramic | PTFE (Teflon) | Kapton (PI)
Material comparison |  |  |  | 
Thickness/mm | 0.1-3.2 | 0.06-1 | 0.2-3 | 0.01-0.5
Electrical characteristics | general | HF transmission | Corrosion&T resistance | high insulation
Mechanical properties | rigid & tough | fragible | tough, flexible | toughn, flexible
Cost | Cheap | High | High | High
Regular performance：Ar+IsoB：97-3，120h test |  |  |  | 
Withstand voltage (in air) /V | 1400 | 1200 | 1600 | 1800
Gain of single layer | 8.0*10^3 | 5.0*10^3 | 1.0*10^4 | 1.0*10^4
Stability | Good | weak | Good | Good
Special performance ( 4(high) > 3 > 2 > 1(low)) |  |  |  | 
Neutron absorp and elastic | 3 | 2 | 1 | 4
Gamma-induced e BG | 2 | 4 | 3 | 1
Natural radioactivity | 4 | 1 | 2 | 3
Total score | 9 | 7 | 6 | 8
Applications |  |  |  | 
Neutron detection | v_v | ^_^ | v_v | v_v
Low BG experiment | v_v | ^_^ | ^_^ | -_-
Big-area detector/m^2 | ^_^ | v_v | ^_^ | ^_^

## Slide 9
动 机
THGEM(Thick GEM), 2004 by A. Breskin
GEM | Items | THGEM
50 | T/um | >=200
70 | D/um | >=200
140 | P/um | >=500
10 | Rim/u | >=20
~10^3 | GainS | >=10^4
~10^4 | GainD | >=10^5
<20% | σE(FWHM)S | ~20%
~25% | σE(FWHM)D | ~30%
<100u | σx | <500u
High | Tech | Normal
High | Cost | Low
Fragile | Durability | Robust
Good | Stability | +++
Kapton Ceramic? | Substrates | FR-4, PTFE, Ceramic , Kapton
50um Kapton
3um Cu
9
GEM(Gas Electron Multiplier), 1997 by F. Sauli）
High spacial resolution THGEM
Motivation

## Slide 10
GEM
THGEM
Intrinsic spacial resolution
The spacial resoluton is determined by both readout method (strip or pad) and THGEM foil, here we focus on THGEM itself.
The only way is to reduce the pitch of holes!

## Slide 11
Mechanical drilling
Laser bombardment
HD:100um
Pitch:300um
TH:100um
Rim :20um
Intrinsic σx:87um
150um - HD
400um - Pitch
100um - TH
70um - Rim
116um - Intrinsic σx
Regular：HD: 200um, Pitch: 500um
Limit： HD: 150um, Pitch: 350um
Regular：HD: 100um, Pitch: 300um
Limit： HD: 50um, Pitch: 150um

## Slide 12
Energy resolution
24%@gain=4×10^3
THGEM by laser ( 60*60mm^2), double layer
Gain
>1×10^4@ArCO2=80:20
>5×10^4@ArISOB=97:3
The THGEM by laser can be used to achieve high spacial resolution
close to that of standard GEM

## Slide 13
Big-area THGEM
Motivation
Big-area THGEMs are the necessary requirement for many real applications:
Digital hadron calorimeter(DHCAL), Muon detector, etc. Big area means > 0.5*0.5m^2 here.
Difficulty and technologies
Difficulty：It is time-consuming to produce big-area THGEMs by mechanical drilling.
Typical hole density: 3.2holes/mm^2 (pitch:0.6mm), drilling speed: 350hole/min
Area >0.2*0.2m^2, hole number>128000/piece , time >6h!;
Area >0.5*0.5m^2, hole number>800000, time>38h!!!。
 | 2013( from Rui’s talk) | Goal
GEM： | 1.2m*0.5m | 2.0m*0.5m
Resistive Micromegas | 2m^2 | 3.4m*2.2m
THGEM | 0.6m*0.6m | 1.0m*0.5m（this work）
Technologies：
1. Laser bombardment
High producing efficiency, high precision, very small hole pitch(<200um)
2. Chemical etching
A possible way, but it is not reported to produce THGEM yet.

## Slide 14
Samples by mechanical drilling
So far, it is still the only reliable way to produce big area THGEM by mechanical driling, even though it is time-consuming. Another limitation is the width of PCB production line and the dimension of the numerical control drilling machine. So max size is 1.2*0.5m^2。
500×500, HD:0.3, Pitch: 1.0mm, 6.25h!
1000×500, HD:0.3, Pitch: 1.5mm, 9.62h！
1000×500

## Slide 15
It is also used to produce standard GEM foil, such as in Japan. This technology can break the bottleneck of mechanical drilling. The max size can be produce: 1.2×0.5m^2 (this work)
Laser bombardment
Double-side laser bombardment
Both FR-4 and Kapton is OK. Six main steps.
The key step is double-side bombardment
Laser：HD 0.10mm, 300h/s, 18000h/min
Foil: HD 0.10mm, Pitch 0.3mm
Mechanical：0.15mm, 200h/min; 0.2mm, 350h/min; 0.25mm, 500h/min;
Foil: HD 0.2mm, Pitch 0.6mm;
Speed comparison

## Slide 16
60×60, 100×100, 200×200, and 500×500mm^2
<= 100×100: tested and have good performance, but yield rate need to be improved;
> 200×200: samples made, to be tested, still under development
500×500mm^2
200×200mm^2
Samples by laser bombardment
60×60mm^2
100×100mm^2
Pitch <=300um
Intrinsic σx <=86um

## Slide 17: Applications
1.B-coated neutron detector( CSNS, Jianrong Zhou et.al, poster for details)
Ceramic THGEM，low neutron scattering and adsorption, 200×200mm^2 THGEMs
Good performances .
n, 2D
Test 1 @ CIAE: Reflect spectrummeter：
Monochromator： Graphite
Neutron wavelength：4.75 /2.4 Å
FLux：~5×103 n/cm2·s
Beam size：~20mm×40mm
TOF result
2.4 Å 4.7 Å
Focus measurement

## Slide 18
Test 2 @ CMRR: Powder diffraction spectrometer
  Neutron wavelength：1.59 Å (0.0324eV)
  Flux：～3*104 n/cm2.s
  Beam size：～25mm×30mm
Beam pipe
Monochromator
Sample Env
Detector
FWHM:
2.87±0.01 3.00±0.01 2.75±0.01
TOF
Aging test
WL@TOF

## Slide 19
2. Tracking and imaging for electron
Tracking：THGEM-TPC, σx-100um,
0.1~50MeV electron, works in vacuum tank.
Gain: single: 5*10^3
double 2*10^4
TPC THGEMs, homemade, as default
high precision, pitch0.3mm,
Standard GEMs, as reference
CERN( Rui et.al ), test is ongoing.
TPC fieldcage length 120mm
Minor strip structure
80mm
45
Induced readout board
Pad size: 0.46*0.46mm, Gap:0.1mm
72*7 PADs + 7 strips= 511 chs
FEE: CASAGEM ASIC, Q&T/ch
Track sampling 3-D

## Slide 20
Imaging：particle distribution detector (PDD) σx-100um,
0.1~50MeV electron, works in vacuum tank.
Beam test, 142PC+572
Pi(MIP) 400~700MeV
60mm
Strip: 0.46mm, Gap:0.1mm
X 100 + Y 100 = 200 chs
FEE: CASAGEM ASIC, Q/ch
Detector + ASIC FEE +
ADC + DAQ commissioning

## Slide 21
Structure：preAmp + 5 trends shaping
Gain：2mV/fC, 4mV/fC, 20mV/fC, 40mV/fC
Shaping time：20ns、40ns、60ns、80ns
Channel：16+1(1 trigger)
Output： Single-ended parallel output
Front-end electronics, CASAGEM ASIC chips
designed by Tsinghua University, 16ch/chip
Ortec:142PC+572
CASAGEM

## Slide 22
5、Mu detector (for CEPC)
THGEM as an option
Big-area production
2-D readout/layer
The upgrade of CMS & ATLAS u detectors will adopt MPGD。
4、Digital hadron calorimiter
(for Circular E-P Collider, CEPC )
3、GPM(LAr/LXe experiments )
Low BG, high gain THGEM

## Slide 23: Summary
New substrate THGEMs had been made and tested, good performance was achieved, including: FR-4、Ceramic、PTFE and Kapton PCT-type substrates.
The ceramic and PTFE substrates have lower natural radioactivity and neutron adsorption and scattering.
THGEM can reach <=86um intrinsic spacial resolution by laser technology, HD<=100um, Pitch<=300um.
4. THGEM of 1.0×0.5m^2 has been made by mechanical drilling, but huge time-consuming. THGEM of 0.5×0.5m^2 has been made by laser bombardment with very high production efficiency. Laser bombardment is a promising method for big-area THGEM production.
5. New types and big-area THGEMs are applying to experiments.
Thank you for attention!