## Slide 1
Accelerator Laboratory:
RF ACCELERATING STRUCTURES

## Slide 2
RF Crew
RF Accelerating Structures
Summary
Introduction
Standing Wave Structures (Resonant cavities)
Travelling Wave Structures (Iris loaded waveguides)
Lab Experimental activity
Characterization of an Aluminum model of the S-band RF GUN for the ELI-NP project
Characterization of an Aluminum model of the S-band RF deflector for the CTF3 project
The LNF RF Team:
D. Alesini, M. Bellaveglia, F. Cardelli, A. Gallo, A.Mostacci, L. Piersanti

## Slide 3
RF Crew
RF Accelerating Structures
Fundamental relations of the relativistic dynamics

## Slide 4
RF Crew
RF Accelerating Structures
Velocity variations are negligible at energies well above the particle rest energy!
β= v/c
Energy-velocity plot
Leptons (light particles) are pratically fully relativistic in any existing dedicated accelerators (Wk>>W0, with the exception of the very first acceleration stage) while protons and ions are typically weakly relativistic (Wk<W0 – but not always, see high energy hadron colliders such as the LHC).
For leptons the accelerating process occurs at constant particle velocity (v ≈ c), while protons and ions velocity may change a lot during acceleration. This implies major important differences in the technical characteristics of the dedicated accelerating structures.
e- relativistic ( ) at W>1MeV (W0=511keV)
p relativistic at W>1000 MeV (W0=938MeV)
Particle energies are typically expressed in electron-volt [eV], equal to the energy gained by 1 electron accelerated through an electrostatic potential of 1 volt:
1 eV=1.6x10-19 J
Wk[MeV]

## Slide 5
RF Crew
RF Accelerating Structures
Fundamental equation of the particle motion
ACCELERATION
BENDING AND FOCUSSING
Beam
Electric field
Transverse Dynamics
Longitudinal Dynamics
Deflection
(magnetic field)

## Slide 6
RF Crew
RF Accelerating Structures
PRINCIPLE:
The DC voltage of a generator is used to accelerate particles
cathode
The first historical particle accelerator was built by the Nobel prize Wilhelm Conrad Röntgen. It consisted in a vacuum tube containing a cathode connected to the negative pole of a DC voltage generator. Electrons emitted by the heated cathode were accelerated while flowing to another electrode connected to the positive generator pole (anode). Collisions between energetic electrons and anode produced X-rays.
anode
-
+
e-
X
The energy gained by the electrons travelling from cathode to anode is equal to their charge multiplied the electrostatic potential difference between the two electrodes.
From Electrostatic to RF acceleration
Basic limitation: the energy gain ∆W=q∆V is proportional to the DC voltage ∆V which is limited by unavoidable breakdown phenomena!

## Slide 7
RF Crew
RF Accelerating Structures
DC voltage as large as 15 MV can be obtained (E ~ 15MeV)
To increase the achievable maximum energy Van de Graaff invented an electrostatic generator based on a dielectric belt transporting positive charges to an isolated electrode hosting an ion source. The positive ions generated in a large positive potential were accelerated toward ground by the static electric field.
APPLICATIONS
Still ~ 350 Van De Graaff are in operation worldwide, typically at V<25MV, I<100mA. They are used for:
Material analysis:
such as Semiconductors structure analysis,
X-ray production, …;
Material modification:
ion implantation for semiconductors

## Slide 8
RF Crew
RF Accelerating Structures
The original idea of Ising (1924) was implemented by Wideroe (1927) who applied a sine-wave voltage to a sequence of drift tubes. The particles do not experience any force while travelling inside the tubes (equipotential regions) and are accelerated across the gaps. This kind of structure is called Drift Tube LINAC (DTL).
If the length of the tubes increases with the particle velocity during the acceleration such that the time of flight is kept constant and equal to half of the RF period , the particles are subject to a synchronous accelerating voltage and experience an energy gain of ∆W=q∆V at each gap crossing.
In principle a single AC voltage can be used to indefinitely accelerate a beam, avoiding the breakdown limitation affecting the electrostatic accelerators.
Please notice that this technique requires bunched beams, i.e. in order to be synchronous with the external AC field, particles have to be gathered in non-uniform temporal structures
RF Acceleration : the Wideröe “Drift Tube LINAC” (DTL)
In 1928 Wideröe by means of 3 tubes (2 gaps) accelerated Na e K ions at 50 keV with an RF of 25 kV and 1 MHz.
In 1931 Sloan e Lawrence used 30 tubes to accelerate Hg ions to the energy of 1.25 MeV with an RF of 42 kV e 10 MHz; in 1934, by using 36 tubes and a higher RF voltage, they got to 2.8 MeV.
gap
Basic idea:
The particles produced by a filament are accelerated by the electric field in the gap between electrodes connected alternatively to the poles of an AC generator.

## Slide 9
RF Crew
RF Accelerating Structures
Beam -to-accelerating field synchronization
The Wideröe DTL provides synchronization between a charge particle in motion and an accelerating E-field.
The condition Ln<<RF (necessary to model the tube as an equipotential region) requires <<1. The Wideröe technique can not be applied to relativistic particles
The length of the n-th drift tube has to be
:
If particles enter the LINAC with an energy Win, while travelling inside the n-th drift tube they will show energy Wn and velocity vn given by:

## Slide 10
RF Crew
RF Accelerating Structures
Standing Wave (SW) Accelerating Structures: Resonant Cavities
beam
Electric field

## Slide 11
RF Crew
RF Accelerating Structures
Resonant Cavity Shapes
Reentrant or nose-cone cavities
Disk-loaded or coaxial cavities
/2
/4
Pill-box or cylindrical cavities

## Slide 12
RF Crew
RF Accelerating Structures
Pill-box like (or bell-shape)
Resonant Cavity Examples

## Slide 13
RF Crew
RF Accelerating Structures
Acceleration with SW cavities

## Slide 14
RF Crew
RF Accelerating Structures
Cavity dissipation – Q factor
skin depth
conductivity

## Slide 15
Mode field
configuration
Frequency and
material conductivity
RF Crew
RF Accelerating Structures
Shunt impedance

## Slide 16
RF Crew
RF Accelerating Structures
The resonant cavity modes are solutions of the homogeneous Maxwell equations inside closed volumes surrounded by perfectly conducting walls. The mathematical problem has the following formal expression:
Modes of a Resonant Cavity: General Problem
Homogeneous Maxwell Equations
(wave equation)
+
perfect metallic boundaries

## Slide 17
RF Crew
RF Accelerating Structures
Analytical field solutions: the Pill-box cavity
TM01
TM02
TM11
TE11
TE01
Wave Type
Circular waveguide modes

## Slide 18
RF Crew
RF Accelerating Structures
Numerical Solutions
In the majority of cases analytical field solutions are not available and numerical methods are applied.
There are various codes dedicated to the solution of the Maxwell equations in closed and/or open volumes starting from a discretized model of the structure under study. Codes can be classified in various ways:
2D (2-dimensionals) and 3D (3-dimensionals) codes;
Finite differences and finite elements codes;
Time-domain and frequency domain codes.

## Slide 19
RF Crew
RF Accelerating Structures
Figure of merit of a SW cavity

## Slide 20
RF Crew
RF Accelerating Structures
Input-Output coupling
Magnetic (loop)
input coupler
Waveguide (slot)
input coupler

## Slide 21
RF Crew
RF Accelerating Structures
Coupling and loading parameters of a cavity
It can be easily demonstrated that, provided that all the monitor ports are weakly coupled (βn<<1), the input coupling of a cavity is related to the input reflection coefficient ρ by:

## Slide 22
RF Crew
RF Accelerating Structures
Tuning

## Slide 23
RF Crew
RF Accelerating Structures
Perturbations
It turns out that if the perturbing object is a perfectly conducting sphere the values of the form factors are:
If a sphere of radius a is moved along the beam axis of a cavity, the E field profile and the R/Q of a resonant accelerating mode can be estimated according to:
sign of the E-field profile

## Slide 24
RF Crew
RF Accelerating Structures
Multi-cell Cavities

## Slide 25
RF Crew
RF Accelerating Structures
RF Superconductivity
Surface resistance
RBCS vs. f
(Log-Log)
RBCS vs. T
(Log scale)
1.3 GHz, 2-cell cavity for Cornell ERL injector.
John Bardeen, Leon Neil Cooper and John Robert Schrieffer (BCS) , 1957.

## Slide 26
RF Crew
RF Accelerating Structures
Examples of multi-cell cavity: the TESLA / ILC cavity

## Slide 27
RF Crew
RF Accelerating Structures
Particle beams can be accelerated not only by standing waves but also by traveling waves.
In this case it is necessary to let an e.m. wave with non-zero longitudinal electric field travel together with the beam in a special guide in which the wave phase velocity matches the particle velocity. If this is the case the beam absorbs energy from the wave and it is continuously accelerated.
By solving the wave (Helmholtz) equation it turns out that an e.m. wave propagating in a constant cross section guide will never be synchronous with a particle beam since the propagation speed (i.e. the wave phase velocity) is always larger than the speed of light c.
Let’s consider for instance the first mode (TM01) with a non zero longitudinal electric field of a circular waveguide . The accelerating field at a given frequency  has the following expression:
Traveling Wave (TW) Accelerating Structures
Constant cross-section waveguides
propagation constant
phase velocity

## Slide 28
RF Crew
RF Accelerating Structures
The wave phase velocity and the propagation constant  are simply related by:
while, solving the wave equation, the propagation constant and the phase velocity result to be functions of the frequency according to:
As already mentioned the wave phase velocity is always larger than c, so that the accelerating field and the particles in the beam can never be synchronous.
Please notice that the phase velocity is not the energy propagation velocity of the structure. In fact the energy propagates with the group velocity given by:
specific of the guide geometry and of the selected mode

## Slide 29
RF Crew
RF Accelerating Structures
Dispersion plot
Constant cross section
waveguides:
w*
b*
The  vs.  plot is called dispersion curve of the waveguide.
Noticeable aspects are:
a) the tangent of the ph angle is the wave phase velocity at the operating frequency  ;
b) the propagation constant  is real (propagating mode ) only if  > c (c = cut-off frequency of the selected mode);
c) if  < c the mode does not propagate in the structure;
d) the tangent of the g is the wave group velocity in the structure. In constant cross section waveguide, phase and group velocities have the same sign (forward waves), but this is not true in general since in some peculiar guides (like periodical iris loaded structures) they may have opposite signs (backward waves);
e) The plot for negative  corresponds to waves propagating in opposite direction (towards negative z).

## Slide 30
RF Crew
RF Accelerating Structures
Periodic structures
A typical dispersion curve of an iris loaded structure has the following characteristics:
the plot is periodic respect to the variable , and the period is 2/D;
each period is the dispersion curve of a different spatial harmonic;
the geometry of the guide can be designed such that the fundamental spatial harmonic E0 is synchronous with the beam (i.e. phase velocity = beam particle velocity) for a selected operating frequency *;
the high-order harmonics (n=1,2,3,...) are asynchronous respect to the beam, so they do not contribute to the acceleration;
periodic structures can only operate in limited frequency bands (stopbands associated with periodicity, as in other physics process ...)
In order to slow-down the wave phase velocity, iris- loaded periodic structure are used.
According to the Floquet theorem, the field in this kind of structures is that of a special wave travelling within a spatial periodic profile, with the same spatial period D of the structure. The periodic field profile can be Fourier expanded in a series of traveling waves (spatial harmonics) with different phase velocity according to:
z

## Slide 31
RF Crew
RF Accelerating Structures
Merit Figures of a periodic structure
Traveling wave (TW) accelerating structures are typically qualified by the following merit figures :
a) Shunt impedance per unit length Z: It is defined as the ratio between the squared amplitude of the fundamental harmonic accelerating field (E0) and the power dissipated per unit length in the structure (dP/dz):
The higher the Z value, the higher the available accelerating field for a given RF power dissipation per unit length;
b) Q factor per unit length: It is defined as the ratio between the stored energy per unit length (w) the power dissipated per unit length (dP/dz), times the operating frequency *:

## Slide 32
RF Crew
RF Accelerating Structures
c) Z/Q ratio: From previous definitions it turns out:
Similarly to the SW structures, this parameter only depends on the structure design, which means that it is independent on the conductivity of the structure inner surface. Since for a given E0 value the stored energy per unit length w is inversely proportional to w2 (for homotetic scaling of the dimensions):
and since the operating frequency * is inversely proportional to the dimension scaling factor, the Z/Q factor, differently from the SW case, results to grow linearly with frequency.
d) Group velocity vg: The group velocity is defined as:
and it represents the velocity of the energy flow in the structure. It may be demonstrated that the group velocity approximately scales with a and b dimensions according to:

## Slide 33
RF Crew
RF Accelerating Structures
High group velocities allow reducing the duration of the RF pulse feeding the structure. However, the RF power P flowing through the structure (P = flux of the Poynting vector) and the stored energy per unit length w are related by:
and since E0 is proportional to the square root of w, clearly a low group velocity is preferable to increase the effective accelerating field for a given power flowing in the structure.
e) Frequency *. Since:
To increase Z the operating design frequency must be the highest possible. However, the power available from ordinary RF power sources at high frequencies decreases rapidly with frequency. Also RF power density on the structure surface increases and the irises diameter decrease linearly with frequency, so problems related with heating increase and beam stay clear reduction at high frequencies have to be taken into account.
The group velocity vg is a very important qualifying parameter of a TW structure. The filling time tf, i.e. the time necessary to propagate an RF wavefront from the input to the end of a TW accelerating section of length L is given by:

## Slide 34
RF Crew
RF Accelerating Structures
In a purely periodic guide, made by a sequence of identical cells (also called “constant impedance structure”),  does not depend on z and both the RF power flux and the intensity of the accelerating field decay exponentially along the structure :
It is possible to design structures with nearly constant accelerating field along z . The diameter of the cell irises has to be gradually reduced, reducing the group velocity along the structure in order to keep nearly constant the energy stored per unit length w and power dissipated per unit length dP/dz . These are called “constant gradient structures”, and are not exactly periodic.
g) Working mode: It is defined as the phase advance of the
fundamental harmonic over a period D:
For practical reasons related to the experimental measurement of the dispersion curve of actual devices, the working modes are typically designed to be:
f) attenuation:. Because of the wall dissipation, the RF power flux decreases along the structure according to the following equation:
where  is the structure attenuation coefficient. It may be shown that:

## Slide 35
RF Crew
RF Accelerating Structures
Examples of TW structure: the Stanford LINAC (SLAC)
L ≈ 3 m

## Slide 36
RF Crew
RF Accelerating Structures
EDIT 2015 – Accelerator Lab
RF Measurements
Instrumentation Description
Experience #1: characterization of a SW cavity (S-band RF Gun)
Experience #2: characterization of a TW structure (S-band RF deflector)

## Slide 37
RF Crew
RF Accelerating Structures
VNA conceptual scheme: the 4 blocks
Source
Z0 LOAD
Signal
Separation
Detector and
Receiver
Process and
Display
Incident
Reflected
Transmitted
DUT
1
2
3
4
A Vector Network Analyzer measures the scattering matrix elements sij – i.e. Input/output matching and forward/backward transfer function – of a Device Under Test.
An internal sine-wave sorce is made sweeping a given frequancy span and reflected and transmitted signas are measuerd and normalized to the source. The direction of the excitation can be inverted.

## Slide 38
RF Crew
RF Accelerating Structures
Network Analyzer Block Diagram
RECEIVER / DETECTOR
PROCESSOR / DISPLAY
REFLECTED
(A)
TRANSMITTED
(B)
INCIDENT (R)
SIGNAL
SEPARATION
SOURCE
Incident
Reflected
Transmitted
DUT

## Slide 39
RF Crew
RF Accelerating Structures
Spectrum Analyzer Block Diagram
A Spectrum Analyzer characterizes signals in frequency domain. An internal source sweeps a selected frequency range to downconvert and filter the input signal. The IF filter output power reveals the spectral content of the signal at the instantaneous frequency scanned by the instrument.

## Slide 40
RF Crew
RF Accelerating Structures
Digital Oscilloscopes
A Digital Oscilloscope characterizes signals in time domain. The input signal is buffered by a front-end amplifier and then A-to-D converted. Instrument BW and resolution depend essentially by the characteristics of the front-end ADC . Digital data stream is stored, processed and displayed according to experimental needs. Special algorithms working on the acquired samples allow smart triggering of the instrument.

## Slide 41
RF Crew
RF Accelerating Structures
Experience #1: ELI-NP S-band RF-Gun
½ cell
cell
beam pipe
cathode
bead
Parameter | Design value (Cu) | Meas. value (Al)
Working frequency | 2.856 (GHz) | ?
Working mode | π | ?
Unloaded Q | 14500 | ?
Input coupling coeff. (ß) | 3 | ?
Input external Q | 4800 | ?
Filling time | 420 ns | ?
Shunt impedance (R) | 1.7 MΩ | ?
R/Q factor | 117 Ω | ?
Repetition rate | 100 Hz | X
Max RF input power | 16 MW | X
Peak field at cathode | 120 MV/m | X

## Slide 42
RF Crew
RF Accelerating Structures
Experience #1: RF characterization of an Aluminum model of the ELI-NP S-band RF-Gun
f0, fπ, ∆f, QL, Q0, ß measurement with Network Analizer
Longitudinal electric field profile measurement with “bead-drop” technique (mode π):
  Ticks drawn on the fishing line are equally spaced every 5 mm
  Fill an excel spreadsheet with 2 columns: bead position (z) and fres
  Calculate and plot ∆f/f vs z;
Longitudinal electric field profile measurement with “bead-drop” technique (mode 0):
  Same as mode π… but centered at f0
Shunt impedance (or R/Q) calculation:
  From the same spreadsheet, calculate Vacc and then use the formula for R (or R/Q);
Filling time measurement (time domain with realistic RF pulse)

## Slide 43
RF Crew
RF Accelerating Structures
Travelling Wave structure
Dispersion curve
RF power
couplers
accelerating cell
beam pipe
The Aluminum model of the CTF3 combiner ring RF deflector

## Slide 44
RF Crew
RF Accelerating Structures
Experience #2: RF Travelling Wave structure
Example of a disassembled C-band TW structure;
BW measurement at fRF=3 GHz with Network Analizer;
Filling time measurement #1:
  Using a realistic pulse from RF signal generator (fRF=3 GHz, tpulse =1 µs, rep.rate=10-100 Hz) fed to the structure;
Filling time measurement #2:
  Using a CW RF reference with amplitude modulation, according to the scheme of slide 3 (fmod=5 MHz, Ampl=1 Vpp, offset=2.5 V);
  With spectrum analizer monitor the frequency content of the feeding signal;
  Measure with the oscilloscope the time needed to traverse the structure from the distance of the 2 maxima.

## Slide 45
RF Crew
RF Accelerating Structures
TW structure filling time measurement setup
fRF
CPL
TW structure
Oscilloscope
ATT 10 dB
Funct. generator
LO
IF
RF
CPL
TRG
TTL

## Slide 46
RF Crew
RF Accelerating Structures
N.A. settings and measurement results
Parameter | Mode π | Mode 0
Working frequency | 2.85564 (GHz) | 2.81422 (GHz)
S11 @ fres | -10.8 dB (lin = 0.289) | -23.2 dB (lin = 0.07)
Q0 | 8990 | 10100
QL | 3200 | 4700
Coupling coefficient (ß) | 1.81 | 1.15
General measurement
settings:
IF BW 40 kHz
# points 1601
fcenter = 2.83 GHz
fspan = 100 MHz
Single mode measurement
settings:
IF BW 40 kHz
# points 1601
fcenter = fres
fspan = 10 MHz