## Slide 1: Accelerator R&D Program at Integrable Optics Test Accelerator
Alexander Valishev
Fermilab
16 April 2015

## Slide 2: Outline
Motivation, strategy and goals
Scope, physics of the main accelerator R&D experiments
Existing infrastructure
Status, plans, and outlook
Collaboration and training

## Slide 3: Fermilab after the Tevatron
Fermilab operates the largest HEP accelerator complex in the U.S., 2nd largest in the world (even after termination of the Tevatron)
Also part of operations:
  Proton Improvement Plan (PIP)
  Muon Campus projects
  Test facilities (magnets, SRF cavities)
Projects: Muon g-2, Mu2e, LBNF, MicroBooNE, LCLS-II (at SLAC), PIP-II
Programs: MAP, LARP, ILC
Research and Development
Commercialization of our accelerator technologies.

## Slide 4: Accelerators
Fermilab operates a total of 16 km of accelerators and beamlines
A 400-MeV proton linear accelerator (0.15 km)
An 8-GeV Booster synchrotron (0.5 km)
An 8-GeV accumulator ring (3.3 km)
A 120-GeV synchrotron (3.3 km)
A Muon Campus Delivery ring (0.5 km)
Soon: Muon g-2 ring
Transfer lines and fixed target beam lines (8 km)
Two high power target stations, several low-power targets
People: 660 (AD, APC, TD) – ops, projects, programs, R&D, program support, WFO

## Slide 5: Strategic Plan for U.S. Particle Physics
May 2014 report of the Particle Physics Project Prioritization Panel (P5)
Short-term
  Proton Improvement Plan II (PIP-II)
  High-Luminosity Large Hadron Collider (HL-LHC)
  International Linear Collider (ILC)
Medium-term (Next Step)
  Multi-MW proton accelerator for research at the Intensity Frontier, including neutrino physics
  Very high-energy proton-proton collider
  TeV-scale ILC upgrade
Long-term (Further Future)
  Multi-TeV e+e- collider
  Neutrino factory

## Slide 6: Strategic Plan for Accelerator R&D in the U.S.
April 2015 report of the High Energy Physics Advisory Panel (HEPAP) subpanel on Accelerator R&D
Short-term
  Covered under respective projects
Emphasys on Medium-term (Next Step) R&D
  Multi-MW proton accelerator
    High-power component R&D (targets for Multi-MW)
    Experimental studies of high-current dynamics in rings (strong space-charge)
    Superconducting RF
  Very high-energy proton-proton collider
    Superconducting magnet development
  TeV-scale ILC upgrade
    SRF technology at lower cost

## Slide 7: Strategic Plan for Accelerator R&D in the U.S.
April 2015 report of the High Energy Physics Advisory Panel (HEPAP) subpanel on Accelerator R&D
Long-term (Further Future)
  Multi-TeV e+e- collider
    Pursue particle-driven plasma wakefield acceleration of positrons at FACET in the time remaining for the operation of the facility. FACET-II construction is not affordable in Scenario A.
    Continue to support laser-driven plasma wakefield acceleration experiments on BELLA.
    Reduce funding for direct laser acceleration research activities.
    Develop R&D roadmaps with a series of milestones and common down-selection criteria towards the goal of constructing a multi-TeV e+e- collider.
    Continue research on normal conducting RF.

## Slide 8: R&D Towards Multi-MW Beams at Fermilab
Innovative design approaches will allow multi-MW beam power at lower cost
Either overcome fundamental beam physics phenomena in circular proton machines to increase current by factor 3-4. Main limitations come from:
  space-charge effects
  beam halo formation and related particle losses
  transverse and longitudinal instabilities
Or reduce cost of the SRF / GeV by a factor of 3-4 – not part of this talk

## Slide 9: Strategy
There is a lack of dedicated ring-based accelerator test facilities in the US for high intensity research
  This hampers the training of next generation of accelerator scientists for HEP
  At present, the only machine to study SC effects is UMER at University of Maryland with very low (10keV) electrons
We are creating a transformational Accelerator R&D program centered at Fermilab’s IOTA – Integrable Optics Test Accelerator
IOTA will become a unique machine for revolutionary proof-of-principle R&D towards future high intensity machines
  push performance limits of rings by 3-4 times to enable multi-MW beam power – DQSC>1, lower losses, stable beams
  become the focal point for collaboration and training

## Slide 10: IOTA Roadmap
Construct and commission the Integrable Optics Test Accelerator (IOTA) storage ring and its proton and electron injectors, and establish reliable and time-effective operation of the facility for accelerator research program.
Carry out transformative beam dynamics experiments
  Integrable optics with non-linear magnets and with electron lenses.
  Space charge compensation with electron lenses and electron columns.
  Optical stochastic cooling demonstration
Open new opportunities for training young researchers
All in collaboration with national and international partners on corresponding modeling, design, and analysis efforts

## Slide 11: Existing Infrastructure
IOTA/ASTA capitalizes on the investments made by OHEP for highly successful ILC/SRF R&D Program.
Construction of ASTA (formerly NML) began in 2006 as part of the ILC/SRF R&D Program and later American Recovery and Reinvestment Act (ARRA). The facility was motivated by the goal of building, testing and operating a complete ILC RF unit.
Multi-million (>$90M) investment resulted in the successful commissioning of 1.3 GHz SRF cryomodule (CM2).
  Beam through low-energy photo injector
  Facility nears completion
The addition of IOTA expands scope to host high-intensity accelerator research.

## Slide 12: ASTA Facility

## Slide 13: ASTA Schematic

## Slide 14: First Electrons Through Photoinjector!
Sign-offs Wednesday, 25 March
Electrons beyond the gun - Wednesday, 25 March
Beam after CC2, towards end of line – Thursday, 26 March
Electrons seen at low energy beam absorber ( ~20 MeV) – Friday morning, 27 March
OTR Screen after 22.5° bend
Initial CC2 Phase Scan

## Slide 15: Integrable Optics Test Accelerator
Unique features:
  Can operate with either electrons or protons (up to 150 MeV/c momentum)
  Large aperture
  Significant flexibility of the lattice
  Precise control of the optics quality and stability
  Set up for very high intensity operation (with protons)
Based on conventional technology (magnets, RF)
Cost-effective solution
  Balance between low energy (low cost) and discovery potential

## Slide 16: IOTA Ring
e- beam line
2.5 MeV RFQ
p beam line

## Slide 17: IOTA Layout
NL1
NL2
EL
OSC

## Slide 18: IOTA Parameters
Nominal kinetic energy | e-: 150 MeV, p+: 2.5 MeV
Nominal intensity | e-: 1×109, p+: 1×1011
Circumference | 40 m
Bending dipole field | 0.7 T
Beam pipe aperture | 50 mm dia.
Maximum b-function (x,y) | 12, 5 m
Momentum compaction | 0.02 ÷ 0.1
Betatron tune (integer) | 3 ÷ 5
Natural chromaticity | -5 ÷ -10
Transverse emittance r.m.s. | e-: 0.1 mm, p+: 2mm
SR damping time | 0.6s (5×106 turns)
RF V,f,q | e-: 1 kV, 30 MHz, 4
Synchrotron tune | e-: 0.002 ÷ 0.005
Bunch length, momentum spread | e-: 12 cm, 1.4×10-4

## Slide 19: Ring Elements in Hand
Dipole magnets (ordered)
Vacuum chambers
for dipoles (received)
32 quads from JINR (Dubna) received
Magnet support stands
from MIT (received)
Also:
BPM bodies and electronics
Vacuum system
Dipole power supply
Corrector power supplies
Notes: Dubna quadrupoles – in-kind

## Slide 20: IOTA Physics Drivers
Experimental demonstration of Nonlinear Integrable Optics lattice
Space Charge Compensation in high intensity circular accelerators

## Slide 21: IOTA Physics Drivers
Integrable Optics

## Slide 22: Space Charge in Linear Optics
System: linear FOFO 100 A linear KV w/mismatch
Result: quickly drives test-particles into the halo
Tech-X, RadiaSoft simulation
DQsc ~ –0.7

## Slide 23: Halo Formation from Beam Mismatch
LEDA and UMER (NA PAC 13, H.D. Zhang et al.) have confirmed the theoretical basis for halo formation in space-charge dominated beams
Linear optics + breathing mode – parametric resonance is the “engine” driving particles into halo
image courtesy
UMD

## Slide 24: Introducing Landau Damping
CBX layout (1962)
1965 Priceton-Stanford CBX: First mention of an 8-pole magnet
  Observed vertical resistive wall instability
  With octupoles, increased beam current from ~5 to 500 mA
CERN PS: In 1959 had 10 octupoles; not used until 1968
  At 1012 protons/pulse observed (1st time) head-tail instability. Octupoles helped.
  Once understood, chromaticity jump at transition was developed using sextupoles.
  More instabilities were discovered; helped by octupoles, fb

## Slide 25: Stability of Linear Lattices
The main feature of all present accelerators – linear focusing lattice: particles have nearly identical betatron frequencies (tunes) by design. Such machines are built using dipoles and quadrupoles.
  All nonlinearities (both magnet imperfections and specially introduced) are perturbations and make single particle motion unstable due to resonant conditions

## Slide 26: Focusing: Linear vs. Nonlinear
Accelerators are linear systems by design (frequency is independent of amplitude).
In accelerators, nonlinearities are unavoidable (space charge, beam-beam) and some are useful (Landau damping).
All nonlinearities (in present rings) lead to resonances and dynamic aperture limits.
Are there “magic” nonlinearities with zero resonance strength?
The answer is – yes (we call them “integrable”)

## Slide 27: Do Accelerators Need to be Linear?
Search for solutions that are strongly nonlinear yet stable
Orlov (1963)
McMillan (1967) – 1D solution
Perevedentsev, Danilov (1990) – generalization of McMillan case to 2D, round colliding beams. Require non-Laplacian potentials to realize
  Round colliding beams possess 1 invariant – VEPP-2000 at BINP (Novosibirsk, Russia) commissioned in 2006. Record-high beam-beam tune shift ~0.25 attained in 2013
Chow, Cary (1994)
Nonlinear Integrable Optics: Danilov and Nagaitsev solution for nonlinear lattice with 2 invariants of motion that can be implemented with Laplacian potential, i.e. with special magnets – Phys. Rev. ST Accel. Beams 13, 084002 (2010)

## Slide 28: 2D Generalization of McMillan Mapping
1D – thin lens kick
2D – a thin lens solution can be carried over to 2D case in axially symmetric system
1. The ring with transfer matrix
2. Axially-symmetric thin kick
can be created with electron lens

## Slide 29: 2D Generalization of McMillan Mapping
The system is integrable. Two integrals of motion (transverse):
  Angular momentum:
  McMillan-type integral, quadratic in momentum
For large amplitudes, the fractional tune is 0.25
For small amplitude, the electron (defocusing) lens can give a tune shift of ~ –0.3 per cell !
Potentially, can cross an integer resonance

## Slide 30: IOTA Electron Lens
Capitalize on the Tevatron experience and recent LARP work
Re-use Tevatron EL components
G.Stancari

## Slide 31: Nonlinear Integrable Optics with Laplacian Potential
Start with a round axially-symmetric linear lattice (FOFO) with the element of periodicity consisting of
  Drift L
  Axially-symmetric
  focusing block “T-insert”
  with phase advance n×p
Add special nonlinear potential V(x,y,s) in the drift such that
can be also

## Slide 32: Time-Independent Hamiltonian
Start with a Hamiltonian
Choose s-dependence of the nonlinear potential such that H is time-independent in normalized variables
This results in H being the integral of motion
Note there was no requirement on V – can be made with any conventional magnets, i.e. octupoles

## Slide 33: Special Potential – Second Integral of Motion
Find potentials that result in the Hamiltonian having a second integral of motion quadratic in momentum
  All such potentials are separable in some variables (cartesian, polar, elliptic, parabolic)
  First comprehensive study by Gaston Darboux (1901)
Darboux equation
  General solution in elliptic variables x, h , with f and g arbitrary
  Solution that satisfies the Laplace equation

## Slide 34: Maximum Tune Shift
Multipole expansion of U:
For small-amplitude motion to be
stable*, t<0.5
Theoretical maximum nonlinear tune shift per cell is
  0.5 for mode 1, or 50% per cell
  0.25 for mode 2, or 25% per cell
x
c
-c

## Slide 35: Nonlinear Magnet
Joint effort with RadiaBeam Technologies (Phase I and II SBIR)
FNAL Concept: 2-m long
nonlinear magnet
RadiaBeam short prototype. The full 2-m magnet will be designed, fabricated and delivered to IOTA in Phase II

## Slide 36: What is Unique About These Solutions?
One can add the special potential (Laplacian or E-Lens) to a drift of a conventional accelerator (albeit specially designed and carefully controlled) and make the lattice integrable.
  Does not require new technology for the significant portion of accelerator circumference – same cost!

## Slide 37: Stability of Nonlinear Lattices
Nonlinear systems can be more stable!
1D systems: non-linear (unharmonic) oscillations can remain stable under the influence of periodic external force perturbation. Example:
2D: The resonant conditions
are valid only for certain amplitudes.
Nekhoroshev’s condition guaranties detuning from resonance and, thus, stability.
  An Exponential Estimate of the Time of Stability of Nearly-Integrable Hamiltonian Systems. Russian Math. Surveys 32:6 (1977) from Uspekhi Mat. Nauk 32:6 (1977)
Notes: change ref.

## Slide 38: Space Charge in NL Integrable Optics
Tech-X, RadiaSoft simulation
System: linear FOFO 100 A linear KV w/mismatch
Result: nonlinear decoherence suppresses halo
DQsc ~ –0.7

## Slide 39: IOTA Goals for Integrable Optics
The IOTA experiment has the goal to demonstrate the possibility to implement nonlinear integrable optics with a large betatron frequency spread DQ>1 and stable particle motion in a realistic accelerator design
Benefits of nonlinear integrable optics include
Increased Landau damping
Improved stability to perturbations
Resonance detuning

## Slide 40: IOTA Staging – Phase I
Phase I will concentrate on the academic aspect of single-particle motion stability using e- beams
  Achieve large nonlinear tune shift/spread without degradation of dynamic aperture by “painting” the accelerator aperture with a “pencil” beam
  Suppress strong lattice resonances = cross the integer resonance by part of the beam without intensity loss
  Investigate stability of nonlinear systems to perturbations, develop practical designs of nonlinear magnets
  The measure of success will be the achievement of high nonlinear tune shift = 0.25
Notes: color pencil beam

## Slide 41: IOTA Staging – Phase I
The magnet quality, optics stability, instrumentation system and optics measurement techniques must be of highest standards in order to meet the requirements for integrable optics
  1% or better measurement and control of b-function, and 0.001 or better control of betatron phase
This is why Phase I needs pencil e- beams as such optics parameters are not immediately reachable in a small ring operating with protons

## Slide 42: IOTA Staging – Phase II
After the IOTA commissioning, we will move the existing 2.5 MeV proton/H- RFQ into the ASTA hall to inject protons into the IOTA ring.
Allows tests of Integrable Optics with protons and realistic space charge beam dynamics studies
Allows space charge compensation experiments
Unique capability
2.5 MeV RFQ
DQSC =0.6 for one-turn injection
*multi-turn injection possible
Notes: multi-tun injection possible

## Slide 43: IOTA Physics Drivers
Space Charge Compensation

## Slide 44: Space Charge Compensation
B=E
r, across the beam

## Slide 45: Possible Implementations
1. The impact of electrons is equal to the total impact of space-charge over the ring
2. The transverse profile of the electron is made the same as that of the proton beam
 use of solenoid
3. The system of magnetized electrons and protons is now dynamically stable
E-lens concept
E-column concept

## Slide 46: Roadmap to High-Intensity Rings
Theory and modeling to develop basis for high intensity circular machines
Proof-of-principle experiments at IOTA
Ultimately, develop a recipe for a new generation rapid cycling synchrotron for super-high beam intensity (× 3-5 present)
  Self-consistent or compensated space-charge
  Strong non-linearity (for Landau damping) to suppress instabilities
  Stable particle motion at large amplitudes
  This strategic initiative received support through LDRD

## Slide 47: Plan of Activities
Phase 1: FY15-17
Construction of main elements of the ASTA/IOTA facility: a) IOTA ring; b) electron injector based on existing ASTA electron linac; c) proton injector based on existing HINS proton source; d) special equipment for AARD experiments.
Commissioning of the IOTA ring with electron beam.
Study of single-particle dynamics in integrable optics with electron beams.

## Slide 48: Plan of Activities
Phase 2: FY18-20
Commission IOTA operation with proton beams.
Carry out space-charge compensation experiments with nonlinear optics and electron lenses.
Phase 3: FY21 and beyond
Study the application of space-charge compensation techiques to next generation high intensity machines.
Expand the program beyond these high priority goals to allow Fermilab scientists and a broader accelerator HEP community to utilize unique proton and electron beam capabilities of the ASTA/IOTA facility

## Slide 49: Collaboration
participants of the 2nd ASTA Collaboration Meeting, June 2014

## Slide 50: Collaboration
A lot of interest to participate in IOTA from the accelerator community
  2 annual Collaboration Meetings, ~60 participants
Significant intellectual and in-kind contributions, expressions of interest
  NIU, UMD, RadiaSoft, CERN, ORNL, BINP, Colorado State, Univ. Mexico – integrable optics, space charge effects, phase space manipulation
  LBNL, ANL – optical stochastic cooling demonstration
  UMD – multi-pickup beam profile monitor for IOTA
  JINR – integrable optics and space charge, contributed quadrupole magnets for IOTA
  Univ. Frankfurt – electron lens

## Slide 51: International Space Charge Collaboration at IOTA
Collaborating institutions (at present): Fermilab, ORNL, CERN, RadiaSoft, UMD
Work on the scientific case, hardware development, simulations, planning and execution of space charge compensation experiments with protons in IOTA
Major topics
  Operation of IOTA with protons, injection, and space charge measurements
  Space charge compensation in nonlinear integrable lattice
  Special magnets
  Electron lens
  Space charge compensation with electron columns
  Space charge suppression with circular modes

## Slide 52: IOTA Optical Stochastic Cooling Demonstration
Example of
Broad research potential of the facility
Collaboration-driven research (with LBNL and ANL)
Goal – Experimental demonstration of the optical stochastic cooling technique
Why IOTA
  Low energy (~100 MeV – minimal synchrotron radiation damping) is ideal for demonstration purposes
  Flexible lattice e- storage ring
Motivation – Beam cooling for future high energy accelerators/colliders

## Slide 53: Principles of OSC
V. Lebedev
Mikhailichenko, Zolotorev, PRL 71, 4146 (1993)
Zolotorev, Zholents, PRE 50, 4, 3087 (1994)

## Slide 54: Training and University Collaboration
Excellent connection to the university community through the Joint Fermilab/University PhD program
  Already 9 graduate students doing thesis research at ASTA/IOTA
    7 NIU, 1 U.Chicago, 1 IIT, 2 more to join soon
Partnership with university groups
  NIU – DOE GARD grant on OSC
  Univ. of Maryland – NSF grant for IOTA-related work
  Univ. Frankfurt – IOTA electron lens
  Univ. Mexico – ASTA linac commissioning
  Colorado State – ASTA gun stability
  Interest from: UC Berkeley, MIT, Oxford

## Slide 55: Summary
Experimental accelerator R&D at IOTA is one of the cornerstones of the proposed national R&D thrust “Multi-MW Beams and Targets”, and is well aligned with P5 priorities
IOTA offers a unique scientific program aiming at breakthrough research to allow for x3-5 increase of beam intensity in future proton rings
  IOTA augments the US program lacking ring facilities for accelerator research and training
IOTA experiments are a great opportunity to explore something truly novel with circular accelerators
IOTA will be a strong driver of national and international collaboration and training

## Slide 56: Acknowledgments
A.Burov, K.Carlson, A.Didenko, N.Eddy, V.Kashikhin, V.Lebedev, J.Leibfritz, M.McGee, S.Nagaitsev, L.Nobrega, A.Romanov, G.Romanov, A.Valishev, S.Wesseln, D.Wolff (FNAL)
D.Shatilov (BINP)
G. Kafka (IIT)
S. Danilov (ORNL),
S. Antipov (U of Chicago)
J. Cary (Tech-X)
D. Bruhwiler, S. Webb (RadiaSoft)
F.O’Shea, A.Murokh (RadiaBeam)
R.Kishek, K.Ruisard (UMD)
JINR, Dubna