## Slide 1: GBT and lpGBT Overview
Paulo Moreira 2018/06/18
Additional information can be found in:
GBT: https://espace.cern.ch/GBT-Project/GBTX/Manuals/Forms/AllItems.aspx
lpGBT: https://espace.cern.ch/GBT-Project/LpGBT/Specifications/LpGbtxSpecifications.pdf

## Slide 2: HEP Optical Link Architecture
On-Detector
Radiation Hard Electronics
Off-Detector
Commercial Off-The-Shelf (COTS)
SerDes
TIA
LD
PD
LD
Custom ASICs
Timing & Trigger
DAQ
Slow Control
Timing & Trigger
DAQ
Slow Control
FPGA
No or small radiation doses
High radiation doses
LHC: up to 100 Mrad (1014 1MeV n/cm2) HL – LHC: up to 1 Grad (1016 1MeV n/cm2)
Short distance optical links: 50 to 300 m
Electrical links to the frontend modules. Lengths: cm to few m
Custom optocomponents

## Slide 3
GBTX

## Slide 4: The GBT System
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
Clock[7:0]
CLK Manager
CLK Reference/xPLL
External clock reference
control
data
One 80 Mb/s port
I2C
Port
I2C (light)
JTAG
JTAG
Port
80, 160 and 320 Mb/s ports
GBTIA
GBLD
GBTX
e-Link
clock
data-up
data-down
ePLLTx
ePLLRx
clocks

## Slide 5: GBTX Data Bandwidth
The GBTX supports three frame types:
  “GBT” Frame
  “Wide Bus” Frame
  “8B/10B” Frame
“GBT” Mode
  User bandwidth: 3.28 Gb/s
    Up/down-links
“Wide Bus” and “8B/10B”frames are only supported for the uplink
  The downlink always uses the “GBT” frame.
“8B/10B” Mode
  Downlink data 8B/10B encoded
  No FEC
  User bandwidth: 3.52 Gb/s
“Wide Bus” Mode:
  Uplink data scrambled
  No FEC
  User bandwidth: 4.48 Gb/s
GBT Frame:
Frame Synchronization:
  DC balanced and “redundant” header
Forward Error Correction:
  Interleaved Reed-Solomon double error correction
  4-bit symbols (RS(15,11))
  Interleaving: 2
  Error correction capability:
    2 Interleaving × 2 RS = 4 symbols = 16-bits
  Code efficiency: 88/120 = 73%

## Slide 6: GBTX Functionality (1/4)
e-Links
40 bi-directional e-Links
  Up to 40 @ 80 Mb/s
  Up to 20 @ 160 Mb/s
  Up to 10 @ 320 Mb/s
e-Port data rate can be set independently for:
  each group
  Input / output ports
1 bi-directional e-Link:
  80 Mb/s
40 e-Link clocks (fixed phase) programable in frequency:
  40/80/160/320 MHz (per group)
  (independently of the bit rate)
Automatic, semi-automatic or user controlled phase alignment of the incoming serial data embedded in the e-Ports
  Automatic alignment
    Tracks temperature and voltage variations
    Transparent to the user
    Works on any type of data:
      DC balanced / un-balanced
      A few “occasional” transition enough to ensure correct operation
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 7: GBTX Functionality (2/4)
e-Links Special cases
8B/10B mode:
  44 input (max @ 80 Mb/s)
  36 output (max @ 80 Mb/s)
    (Four outputs reused as inputs)
Wide-Bus mode:
  56 input (max @ 80 Mb/s)
  24 output (max @ 80 Mb/s)
    (16 “outputs” reused as inputs)
e-Links electrical characteristics
Drivers:
  SLVS signaling
Receivers:
  SLVS/LVDS signaling
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 8: GBTX Functionality (3/4)
Phase-Shifter
8 independent clocks
Programable in frequency:
  40 / 80 / 160 / 320 MHz
Programable in phase:
  0 to 360◦
  Phase resolution: 50 ps
    (for all frequencies)
Clock driver electrical levels:
  SLVS
Reference clock:
On package crystal
Built-in crystal oscillator
Built-in VCXO based PLL (xPLL)
External reference can used as well
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 9: GBTX Functionality (4/4)
Chip Control
e-Fuse register bank for burn in configuration
  Standalone operation
  Ready at power up
Dynamic configuration and control
  I2C Slave interface
  IC control channel trough the optical link
Watchdog circuit for chip operation supervision.
GBLD Control
GBLD dedicated I2C master interface
  Copies configuration burned in the GBTX into the GBLD
  Allows to program the GBLD either through the IC channel or through the I2C slave port
Phase – Aligners + Ser/Des for E – Ports
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
CLK Manager
CLK Reference/xPLL
JTAG
GBTX
ePLLTx
ePLLRx

## Slide 10: GBTX In Numbers
½ million gates
Approximately:
  300 8-bit programable registers (all TMR)
  300 8-bit e-Fuse memory
Clock tree (chip wide):
  9 clock trees (all TMR)
  Frequencies: 40/80/160/320 MHz
7 PLLs:
  RX: CDR PLL + Reference PLL (2.4 GHz)
  Serializer PLL (4.8 GHz)
  Phase-Shifter PLL (1.28 GHz)
  xPLL (VCXO based PLL, 80 MHz)
  (2x) ePLL (320 MHz)
17 master DLLs:
  9 for phase alignment of the e-links
  8 for clock de-skewing
56 replica delay lines:
  For phase alignment of the e-links
7 power domains:
  Serializer (1.5V)
  DESerializer (1.5V)
  Clock Manager (1.5V)
  Phase shifter (1.5V)
  Core digital (1.5V)
  I/O (1.5V)
  Fuses (3.3V)
17 mm
17 mm
Total height including solder balls: ~3 mm
4.3 mm
4.3 mm

## Slide 11: GBTX – Floor Plan and Modelling
10 “Macro-cells”:
Serializer:
  Full custom
  “Analogue-Verilog" modelling
Clock Manager:
  Standard cells
  Verilog modelling
DESerializer
  Full custom
  + “custom” digital
  + standard cells
  “Analogue-Verilog" + Verilog modelling
XPLL
  Full custom
  “Analogue-Verilog" modelling
EPLL (x2)
  Full custom
  “Analogue-Verilog" modelling
Phase-Shifter
  Full custom
Phase Aligners (x8)
  Full custom
  “Analogue-Verilog" modelling
Prompt (x3)
  Full custom
  Verilog modelling
Power on reset
  Full custom
  Verilog modelling
e-Fuses (x300)
  Foundry IP
  Verilog modelling
SER
ePLL
Phase-Aligners
Phase-Aligners
Phase-Aligners
I/O Cells
Phase-Shifter
E-Fuses
PROMPT
xPLL
PON-RST
CLK-MAN
DES
Standard Cells: “everywhere”

## Slide 12
lpGBT

## Slide 13: Outline
LpGBTX Block Diagram
Main Features:
  Optical Link
  E-Links
  Slow Control
  Clock Distribution
  Power Dissipation
  Radiation Hardness
  Package
LpGBT frame and eLinks bandwidth use:
  Down-Link
  Up-Link:
    FEC5
    FEC12
eLink – Transmitter / Receiver
High Speed Line Driver

## Slide 14: LpGBTX Block Diagram
5.12 / 10.24 Gb/s
2.56 Gb/s
refClk40MHz
cdrOut [63:0]
serIn [255:0]
DEC
&
DSCR
rxData[31:0]
SCR
&
ENC
rxEc[1:0]
ePortTx
eLinkOut[15:0]
ecOut
ePortRx
eLinkIn[27:0]
ecIn
40/…/1280 MHz
40 MHz
SCA
(Reduced set)
txData[159:0]
txEc[3:0]
Phase Shifter
eClock[27:0]
LpGBTX
Control
SerDes
40 MHz
40 MHz
40 / 80 / 160 / 320 / 640 /1280 MHz
rxIc[1:0]
txIc[1:0]
40/…/1280 MHz
40 MHz
40/…/320 MHz
cnt[x:0]
psClk[3:0]
I2C (x3)
adcIn[7:0]
pio[15:0]
analog
data
control
clock
ePortClk
40/…/1280 MHz
ecClock

## Slide 15: Main Features (1/…)
“Optical” link:
Down-link:
  2.56 Gb/s (64 – bit frame)
  Encoding: FEC12
  Bandwidth:
    IC (Internal Control (ASIC control)): 80 Mb/s
    EC (External Control (SCA e-Link)): 80 Mb/s
    D (Data): 1.28 Gb/s
  Eye Scan
  BER Monitoring based on the FEC activity

## Slide 16: Main Features (2/…)
Up-link:
  Bandwidth @ 5.12 Gb/s (128 – bit frame):
    IC: 80 Mb/s
    EC: 80 Mb/s
    D:
      FEC12: 3.84 Gb/s
      FEC5: 4.48 Gb/s
  10.24 Gb/s (256 – bit frame)
    IC: 80 Mb/s
    EC: 80 Mb/s
    D:
      FEC12: 7.68 Gb/s
      FEC5: 8.96 Gb/s
  Programable pre-emphasis

## Slide 17: Main Features (3/…)
E-Links:
Down-link:
  Bandwidths: 80/160/320 Mb/s
  Number of links*: 16/8/4
    “Mirror” function:
      80 Mb/s: no;
      160 Mb/s: each channel is available on 2 outputs;
      320 Mb/s: each channel is available on 4 outputs.
  One EC channel @ 80 Mbit/s
Up-Link:
  FEC5 @ 5.12 Gb/s:
    Data rate: 160 / 320 / 640 Mb/s
    # eLinks*: 28 / 14 / 7
  FEC5 @ 10.24 Gb/s:
    Bandwidth: 320 / 640 / 1280 Mb/s
    # eLinks*: 28 / 14 / 7
  FEC12 @ 5.12 Gb/s:
    Bandwidth: 160 / 320 / 640 Mb/s
    # eLinks*: 24 / 12 / 6
  FEC12 @ 10.24 Gb/s:
    Bandwidth: 320 / 640 / 1280 Mb/s
    # eLinks*: 24 / 12 / 6
  One EC channel @ 80 Mbit/s
  Phase alignment on a per channel basis:
    User programable phase
    Automatic phase tracking
* Excluding the EC channel

## Slide 18: Main Features (4/…)
Latency
Both the RX and TX will have fixed and “deterministic” latency
eLink Line Drivers
Programable:
  Driving current: 1, 2 and 4 mA
  Common mode voltage: 600 mV
  Receiving end termination 100 W
  Pre-emphasis
eLink Line Receivers
Programable:
  100 W differential terminations (on/off)
  Auto bias for AC coupling (on/off)
  Line equalization

## Slide 19: Main Features (5/…)
ASIC control:
IC channel: 80 Mb/s
I2C interface
EC channel with double role:
  When the LpGBT works as a Transceiver:
    The EC channel is used to convey (control) data to and from the GBT – SCA, an ASIC or a frontend module
  When the LpGBT works as a Simplex Receiver or Transmitter:
    The EC channel is used as an ASIC control channel (having a similar role and functionality as the IC channel).

## Slide 20: Main Features (6/…)
Slow Control:
LpGLD control:
  I2C master
Experiment control:
  Two I2C masters
  Programmable parallel port:
    16 x DIO
Environmental monitoring:
  10-bit ADC:
    8 inputs
  Temperature:
    On chip: yes
    Programable current source to drive an external temperature sensor
Environmental stimulus:
  8 – bit DAC:
    Single output
    Range: 0 to 800 mV
    Noise: < 1 mV
    DNL: < 1 LSB
    INL:
      Full range: < 3 LSB
      Range 200 to 800 mV: < 1 LSB

## Slide 21: Main Features (7/…)
Clock distribution:
Phase/Frequency – 4 programmable clocks
  4 independent
  Phase resolution: 50 ps
  Frequencies: 40 / 80 / 160 / 320 / 640 / 1280 MHz
eLink Clocks:
  28 independent
  Fixed phase
  Frequency programable
  Frequencies: 40 / 80 / 160 / 320 / 640 / 1280 MHz
Clock jitter:
  < 5 ps rms
Power dissipation:
500 mW @ 5.12 Gb/s
750 mW @ 10.24 Gb/s
Radiation hardness:
Total dose:
  200 Mrad
SEU robust

## Slide 22: Main Features (8/.)
Package:
BGA
Fine Pitch:
  0.5 mm
Pin count:
  289 (17 x 17)
Size:
  9 mm x 9 mm x 1.8 mm

## Slide 23: LpGBT Frame and eLinks Bandwidth Use

## Slide 24: Downlink
Single data rate:
  2.56 Gb/s
Frame:
  IC field:
    2 – bit
    80 Mb/s
  EC field:
    2 – bit
    80 Mb/s
  Data field:
    32 – bit
    1.28 Gb/s
  FEC field:
    24 – bit
Error correction:
  FEC:
    Interleaving: 4
    Symbol width: 3 – bit
    Number of wrong symbols: 1 ( × 4)
  Up to 12 consecutive bits
  Efficiency: 56%
eLinks:
  Data
    16 eLinks @ 80 Mb/s
    8 eLinks @ 160 Mb/s
    4 eLinks @ 320 Mb/s
  EC
    1 eLink @ 80 Mb/s
Option |  | 37
Frame (bits) |  | 64
Header (bits) |  | 4
Coded header |  | Yes
User field (bits) |  | 36
Code (bits) |  | 24
8-bit multiplicity |  | 4.5
User Bandwidth (GHz) |  | 1.44
# eLinks groups (8 bit) |  | 4
eLinks bandwidth (MHz) |  | 80/160/320
#eLinks |  | 16/8/4
EC bandwidth (MHz) |  | 80
IC bandwidth (MHz) |  | 80
Corrected (bits) |  | 12
Efficiency |  | 56%

## Slide 25: Uplink – FEC 5
Dual data rate:
  5.12 Gb/s
  10.24 Gb/s
Frame:
  Header:
    2 / 4 – bits
    2’b10 (high) & 2’b01 (low)
  IC field:
    2 – bit
    80 Mb/s
  EC field:
    2 – bit
    80 Mb/s
  Data field:
    112 / 224 – bit
    4.48 / 8.96 Gb/s
  FEC field:
    10 / 20 – bit
Error correction:
  FEC:
    Interleaving: 1 / 2
    Symbol width: 5 – bit
    Number of wrong symbols: 1 ( × 1 / × 2)
  Up to 5 / 10 consecutive bits
  Efficiency: 91%
eLinks:
  Data
    28 eLinks @ 160 / 320 Mb/s
    14 eLinks @ 320 / 640 Mb/s
    7 eLinks @ 640 / 1280 Mb/s
  EC
    1 eLink @ 80 Mb/s
FEC5 |  |  |  |  | 
 |  | 5.12 Gb/s |  | 10.24 Gb/s | 
Option |  | 7 |  | 7 | 
Frame (bits) |  | 128 |  | 2 x 128 | 
Header (bits) |  | 2 |  | 2+2 | 
Coded header |  | no |  | no | 
User field (bits) |  | 116 |  | 232 | 
Code (bits) |  | 10 |  | 20 | 
16-bit multiplicity |  | 7.250 |  | 14.5 | 
Remainder bits |  | 4 |  | 8 | 
User Bandwidth (GHz) |  | 4.64 |  | 9.28 | 
# eLinks groups (16 bit) |  | 7 |  | 7 | 
eLinks bandwidth (MHz) |  | 160/320/640 |  | 320/640/1280 | 
#eLinks |  | 28/14/7 |  | 28/14/7 | 
EC bandwidth (MHz) |  | 80 |  | 80/160 | 
IC bandwidth (MHz) |  | 80 |  | 80/160 | 
Unassigned bits |  | 0 |  | 4 | 
Corrected (bits) |  | 5 |  | 2 x 5 | 
Efficiency |  | 91% |  | 91% | 

## Slide 26: Uplink – FEC 12
Dual data rate:
  5.12 Gb/s
  10.24 Gb/s
Frame:
  Header:
    2 / 4 – bits
    10 (high) & 01 (low)
  IC field:
    2 – bit
    80 Mb/s
  EC field:
    2 – bit
    80 Mb/s
  Data field:
    96 / 192 – bit
    3.84 / 7.68 Gb/s
  FEC field:
    24 / 48 – bit
Error correction:
  FEC:
    Interleaving: 3 / 6
    Symbol width: 4 – bit
    Number of wrong symbols: 1 ( × 3 / × 6)
  Up to 12 / 24 consecutive bits
  Efficiency: 78% (if accounting for the unassigned bits)
eLinks:
  Data
    24 eLinks @ 160 / 320 Mb/s
    12 eLinks @ 320 / 640 Mb/s
    6 eLinks @ 640 / 1280 Mb/s
  EC
    1 eLink @ 80 Mb/s
FEC12 |  |  |  |  | 
 |  | 5.12 Gb/s |  | 10.24 Gb/s | 
Option |  | 28 |  | 28 | 
Frame (bits) |  | 128 |  | 2 x 128 | 
Header (bits) |  | 2 |  | 2+2 | 
Coded header |  | no |  | no | 
User field (bits) |  | 102 |  | 204 | 
Code (bits) |  | 24 |  | 48 | 
16-bit multiplicity |  | 6.375 |  | 12.75 | 
Remainder bits |  | 6 |  | 12 | 
User Bandwidth (GHz) |  | 4.08 |  | 8.16 | 
# eLinks groups (16 bit) |  | 6 |  | 6 | 
eLinks bandwidth (MHz) |  | 160/320/640 |  | 320/640/1280 | 
#eLinks |  | 24/12/6 |  | 24/12/6 | 
EC bandwidth (MHz) |  | 80 |  | 80/160 | 
IC bandwidth (MHz) |  | 80 |  | 80/160 | 
Unassigned bits |  | 2 |  | 8 | 
Corrected (bits) |  | 12 |  | 2 x 12 | 
Efficiency |  | 80% |  | 80% | 

## Slide 27: eLink – Transmitter / Receiver Overview
Signaling: “CERN Low Power Signaling” (CLPS)
Down-link Transmitter (eTx):
  Bandwidths:
    Data: up to 320 Mb/s
      To be used as a macro cell the eTx will be designed to support 1.28 Gb/s data transmission
    Clock: up to 1.28 GHz
  Programable:
    Driving current: 1 to 4 mA in 0.5 mA steps
    Receiving end termination 100 W
    Voltage amplitude in 100 W:
      100 mV to 400 mV (single-ended PP amplitude)
      200 mV to 800 mV (differential PP amplitude)
      Common mode voltage: 600 mV
    Pre-emphasis:
      Driving current: 1 to 4 mA in 0.5 mA steps
      Pulse width: T bit / 2
Up-Link Receiver (eRx):
  Bandwidth:
    Data: up to 1.28 Gb/s
  Programable:
    100 W differential terminations (on/off)
    Auto bias for AC coupling (on/off)
    Line equalization
      Under specification
Vout+
Vout-
Single-ended PP amplitude:
  max(Vout+) – min(Vout+)
Differential PP amplitude:
  max(Vout+ - Vout-) – min(Vout+ - Vout-)
Vcm:

## Slide 28: eRx Specification
Parameter | Description | Min | Nom | Max | Units
VDD | Supply voltage range | 1.08 | 1.2 | 1.32 | V
IDD | Average current consumption |  | 850 |  | μA
VCMRX | Common-mode voltage rangeA | 70 | 600 | 1200 | mV
VCM | Common-mode set voltageB |  | VDD/2 |  | 
¦VID¦ | Differential voltageC | 140 | 200 | 450E | mV
VIDTH | Differential inputC high threshold |  |  | 70 | mV
VIDTL | Differential inputC low threshold | -70 |  |  | mV
VIH | Single-ended input high voltage |  | 700 | VDD+200 | mV
VIL | Single-ended input low voltage | -40 | 500 |  | mV
ZID | Differential input impedance | 80 | 100 | 125 | Ω
JR | Random noise jitter |  |  | 10F | ps rms
JPW | Pattern or pulse width dependent jitterD |  |  | 10F | ps
TR/F | Output rise/fall time |  | 30 |  | ps
PSR | Power supply rejection |  |  | 10F | ps/100mV
CMR | Common mode rejection |  |  | 10F | ps/100mV
CCM | Common mode termination capacitance |  | tbd. |  | pF
LO | Output load |  | 100 |  | fF
A Common mode: (VDP + VDN) / 2 B For AC coupled signals C Differential voltage: VDP - VDN D Change of delay through the receiver with PRBS 212-1 @ 1.28Gbit/s or varying pulse width TPW > 1ns E For LVDS: 400mV F If <=1ps possible (even with reduced input range), receiver could be used as hit receiver

## Slide 29: eTx Specification
Parameter | Description | Min | Nom | Max | Units
VDD | Supply voltage range | 1.08 | 1.2 | 1.32 | V
VCMTX | Common-mode voltageA,B | 430 | 600 | 770 | mV
¦ΔVCMTX(1,0)¦ | VCMTX mismatch when output is Differential-1 or Differential-0 |  |  | 5 | mV
¦VOD¦ | Differential voltageB,C | 140 | 200 | 270 | mV
¦ΔVOD¦ | VOD mismatch when output is Differential-1 or Differential-0 |  |  | 10 | mV
VOH | Single-ended output high voltageB |  | 700 | 900 | mV
VOL | Single-ended output low voltageB | 300 | 500 |  | mV
IMOD | Modulation output current D | 0.7 | 1 to 4 | 5.4 | mA
IPRE | Pre-emphasis output current D | 0.7 | 1 to 4 | 5.4 | mA
ZL | Load impedance |  | 100 |  | Ω
A Common mode: (VDP + VDN) / 2. B Value when driving into differential load impedance 100 Ω. Termination load is external. C Differential voltage: VDP - VDN ,values for 2mA setting, scales accordingly for other currents.
D Modulation and pre-emphasis currents are programable in 0.5 mA steps from 1 mA to 4 mA. Default setting for the LpGBT is 2mA.

## Slide 30: 5 - 10 Gb/s Line Driver Specifications
# | Specification | Min | Typ | Max | Unit | Notes
1.1 | Supply Voltage |  | 1.2 |  | V | 
1.2 | Supply Current |  | 40 |  | mA | 
1.3 | Input Swing | 0.2 |  | 0.8 | V | Differential
1.4 | Output Swing | 0.2 |  | 0.6 | V | Differential, programmable
1.5 | Emphasis Magnitude | 0 |  | 10 | dB | Programmable
1.6 | Rise/Fall Time |  |  | 40 | ps | 
1.7 | Random Jitter |  |  | 1.2 | ps | 
1.8 | Deterministic Jitter |  |  | 20 | ps | 
1.9 | Input Common Voltage |  | 0.75 |  | V | 
1.10 | Input Capacitance |  | 300 |  | fF |