## Slide 1: Inside the LpGBT
Paulo Moreira CERN
Geneva – Switzerland
Optoelectronics conversion in data transmission from detectors
18 – 20 June 2018, Torino – Italy
&
Ecole IN2P3 de Microélectronique
15 – 19 May 2017, Bénodet – France

## Slide 2: Introduction
Subject:
  Data transmission systems in the context of HEP.
What is the problem:
  Transmission of Physics data from the frontend systems on the detectors to the DAQ systems in the counting room.
  Transmission of control information from the counting room to the detector systems
Communication systems [almost] universally process and transmit data in digital form:
  Thus, [bidirectional] digital transmission between the frontend and the DAQ systems will be considered.
Practical examples of circuits and systems will be drawn from the GBT and LpGBT projects!

## Slide 3: Typical Data Link in HEP – On Detector
Frontend
Modules
& ASICS
Data Aggregation
Control
Serialization
CDR
Timing
Trigger
Control
Broadcast
Electrical links [to the frontend electronics]
Data rate: 80 Mb/s to 1.28 Gb/s (ATLAS pixel is considering 5 Gb/s)
Length: few cm to 1 or 2 meters
LD
RX
Electrical links [to the optoelectronics]
Data rate: 2.56 to 10.24 Gb/s
Length: few cms
To the counting room
From the counting room
Optical links
Data rate: 2.56 to 10.24 Gb/s
Length: 50 to 200 m
Uplink bandwidth larger than the down link
Radiation Hardness
Required

## Slide 4: Typical Data Link in HEP – In the Counting Room
LD
RX
From the detector
To the detector
LD
RX
Large Scale FPGA
Communications Management
Signal Processing
And
TTC
Custom communication systems developed for the detectors must be compatible with FPGAs
No Radiation Hardness
Required

## Slide 5: HEP Communications Idiosyncrasies
Typically simpler that long haul communications systems:
  Localized and short distance systems (< 200 m)
  Bandwidth is not at a premium!
However the radiation environment in which they are installed raises several challenges:
  Total Ionizing Dose (TID) will degrade the performance of the systems to the point that they will eventually fail!
    ASICs and Optoelectronics must be designed and qualified to guaranty “survival” during the lifetime of the detector!
  Single Event Upsets (SEU) will disturb momentarily the operation of the systems/circuits!
    They must be built to mitigate the effects of SEUs and avoid altogether system interrupts
Besides these two “peculiarities”, HEP systems are based on the same principles as the telecommunication systems:
  And thus should be compatible with them as much as possible.
  More specifically, with FPGAs which are the ubiquitous building blocks of HEP DAQ systems!

## Slide 6: Outline
Basic concepts in data transmission systems
  Building blocks
  Impairments
  Optical vs Electrical
Radiation in electronics and optoelectronics devices
  Impact of radiation robustness on circuit performance
The LpGBT – Materializing the concepts
Connecting the ASICs to the world

## Slide 7
Data Transmission Systems
Basic Concepts

## Slide 8: Why Digital Communications?
Digital communication systems are widely used for data acquisition, trigger and control links in HEP:
  A few exceptions: e.g. the CMS tracker data links
Advantages:
  Digital communications can be done virtually error free
    When appropriate codes are used, transmission errors can be:
      Detected
      Corrected
  They are “natural” for digital systems
  Easy handling of multiple data sources and destinations
  Easy re-routing between multiple sources and destination

## Slide 9: Optical Link Architecture
DATA
SER
DAV
Digital System
(data source)
LD
DATA
DES
DAV
Digital System
(data sink)
RX
H: 1001000
i: 1101001
g: 1100111
g: 1100111
s: 1110011
Idle
Idle
STOP
Start
T
Bit-Rate = 1/T
Frame, 37 bits:
35 data bits
2 control bits
“Code efficiency” : 35/37 = 94%

## Slide 10: BW – Limited Channel (1/2)
Transmitter
Channel (cable/fibre)
Equalizer
Threshold
Detector
Retiming
Circuit
Clock
Recovery
V(data)
V(channel)
V(equalizer)
V(detector)
V(rxclock)
V(retimed)

## Slide 11: BW – Limited Channel (2/2)
Due to the limited channel bandwidth the transmitted pulses are broadened in time.
If the broadening is significant, the signal corresponding to one symbol (bit) will overlap in time the signal of the next symbol!
  This is called Intersymbol Interference (ISI)
ISI is seen in an eye-diagram as:
  Vertical eye-closure:
    Reduction of the vertical eye-opening
  Horizontal eye-closure:
    Random positions of the threshold level crossings (Jitter or Phase Noise)
Equalization (high-pass filtering in this case) can be used to “restore” the signal high frequency content:
  Reduces ISI
  Improves Jitter
  Can never fully compensate the channel
Two additional steps are needed to restore the signal to their “original” shape:
  Threshold detection, restores the symbol levels by comparing a signal with a “pre-defined” level
  The signal is retimed using the recovered clock, restoring the signal levels with minimum jitter
Two additional phenomena impair error free data transmission:
  Attenuation
  Noise
Vertical eye-closure
Jitter Horizontal eye-closure
After Equalization
Before Equalization

## Slide 12: Noise - Amplitude
The average bit error probability:
It is a strong function of the signal to noise ratio:
In the limit the measured Bit Error Rate BER is equal to Pe
  SNR = 8.64 (18.7 dB)  BER = 10-9
    Testing time to “count” 100 errors: 20 s @ 5 Gb/s
  SNR = 10.84 (20.7 dB)  BER = 10-15
    Testing time to “count” 100 errors: 231 days @ 5 Gb/s
V1
V0
assuming

## Slide 13: Noise - Jitter
Jitter is phase-noise:
  Random position of the bit crossings.
[As seen] Bandwidth limitations cause intersymbol interference that besides reducing the eye-opening also generates jitter
Amplitude noise will also convert into jitter due to the finite rise and fall times of the signal!
In summary: bandwidth limitations contribute to eye-closure due to ISI and conversion of amplitude noise into jitter.
sv
st
Slope =
Example:
5 Gb/s PIN – Receiver
Vdd = 1.2 V
Sensitivity limit (10-9): SNR = 8.64
sV = Vdd/SNR = 139 mV
BW = 0.7*5 Gb/s = 3.5 GHz
∆𝑉/∆𝑡 = 2p x BW x Vdd = 26 mV/ps
st = 5.3 ps
Popt = -12 dBm
Popt = -6 dBm
GBTIA 5 Gb/s)

## Slide 14: Jitter
Deviations from the optimum sampling instant drastically increase the BER because the SNR decreases due to:
  Signal jitter
  Signal finite rise and fall times
    The signal magnitude |V –D| decreases because of the finite raising/fall times of the signal
Two main causes for non-optimum sampling:
  Retiming clock static phase error
    E.g. due to an unbalance in the CDR PLL charge-pump
  Retiming clock jitter
    E.g. due to the CDR tracking behaviour or VCO noise
BER
Optimum sampling time
Non-0ptimum sampling time

## Slide 15: Error Control Coding
Due to Noise or ISI the received message might differ from the transmitted
  Some of the transmitted bits will be wrongly detected
Error control coding introduces extra bits in the transmitted message:
These allow to:
  Detect the presence of errors
  Correct detected errors
Error control is done at the expense of bandwidth
 | [6] | [5] | [4] | [3] | [2] | [1] | [0] | R.P.
H | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
i | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
g | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
g | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
s | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
C.P. | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
 | [6] | [5] | [4] | [3] | [2] | [1] | [0] | R.P.
H | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
i | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0
g | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1
f | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1
s | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
C.P. | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
Row parity
Column parity
Matrix parity
Transmitted message
Received message
Even parity: Parity bits are computed such that the number of “1s” in each row and column is even
Discrepancy between the received row/column parities and the parities computed by the receiver!

## Slide 16: Line Coding
Apart from detecting and correcting errors, coding is also applied to condition the signal to the transmission medium and/or the transmitter/receiver architecture. This is called line coding.
Most common addressed problems are:
  DC wander caused by AC coupling (“high-pass” type response):
    DC blocking between circuits
    Laser-driver mean power control
    Offset cancelation circuits in pin-receivers
  Lack of signal transitions to keep the RX clock locked on the data
Line codes typically have the following properties:
  limit the low frequency content in the signal spectrum
  Guarantee a high density of symbol transitions
Some popular examples:
  8B/10B
  Scrambling
Decision threshold
AC coupled signal
Input | Output |  | 
Disparity | + | 0 | -
000 | 1101 |  | 0010
001 |  | 1001 | 
010 |  | 1010 | 
011 |  | 0011 | 
100 |  | 1100 | 
101 |  | 0101 | 
110 |  | 0110 | 
111 | 1011 |  | 0100
3B/4B

## Slide 17: Why Optical Links in HEP?
Transmission distance?
  Telecom: up to transcontinental distances! (long – haul)
  HEP: at most a few hundreds of meters (short – haul)
Bandwidth?
  Telecom: the larger the better!
  HEP:
    The larger the better?
    Does using THz bandwidths per fibre makes sense?
      Needs data aggregation systems inside the detectors!
      “Third generation” systems are complex, power hungry [and costly]
    5 to 10 Gb/s systems are being engineered for Phase II upgrades
Especially important for HEP:
  Small optical fibre cross section (material budget)
  Immunity to interferences
  Non EMI generator
  No contribution to ground loops

## Slide 18: Optical vs Electrical
Optical fibers allow bandwidths and transmission distances that are orders of magnitude that of electrical cables.
Most systems installed in HEP are “1st Generation” systems, that is they use 850 nm lasers and multimode, graded index, fibers.
Warning: for such systems the “dispersion limit” limits the transmission distance to less than 200 m at 10 Gb/s
  Probably [LHC] installed fibers need to be replaced to support 10 Gb/s transmission
Multimode
Ecole IN2P3 d’electronique numerique
Aussois, France
23-27 November 1998

## Slide 19
Radiation Effects

## Slide 20: Radiation (TID) In CMOS Circuits (65 nm)
TID Induced “Ion” Degradation
PMOS are more sensitive to TID than NMOS:
  Minimum size NMOS: -20% @ 200 Mrad
  Minimum size PMOS: -60% @ 200 Mrad
TID induced DIon degradation is a function of the channel length L!
  The longer, the smaller the degradation, but
  High speed circuits need minimum L transistors!
DIon degradation is also a function of the channel width W:
  The wider, the smaller the degradation
Enclosed Layout Transistors (ELT) are the least sensitive!
Depending on the circuit function, the use of large W might introduce a power penalty!
  Particularly important for digital circuits where the gate count is high!
NMOS DIon [%]
PMOS DIon [%]

## Slide 21: Standard Cell Libraries TID Sensitivity
Set of ring oscillators irradiated up to 700 Mrad (at room temperature):
  Annealing not shown in the graph
As expected, from the tests of individual devices, libraries made out of large devices are radiation harder than the smaller devices counter parts
  Large devices lead to large power dissipation and larger area circuits!
Chart: INVD1 ring oscillator frequency (normalized to the pre-rad value)
| 0 | 10.061739049999998 | 20.122313416666664 | 30.186856150000001 | 40.248885749999999 | 50.310336733333337 | 60.371961549999995 | 70.43348206666667 | 80.494739349999989 | 90.55578058333333 | 100.61677959999999 | 110.67796735 | 120.73954249999998 | 130.80074514999998 | 140.86546419999999 | 150.92685061666666 | 160.98970220000001 | 171.05119043333332 | 181.11304868333335 | 191.17341196666663 | 201.23399874999998 | 211.29581726666666 | 221.35757618333332 | 231.41861741666665 | 241.48090776666666 | 251.54187698333334 | 261.60712498333334 | 271.66851388333333 | 281.73000459999997 | 291.79073541666662 | 301.85166241666667 | 311.9127135833333 | 321.97485989999996 | 332.03553359999995 | 342.09760045000002 | 352.15819964999997 | 360 | 400 | 500 | 600 | 700 | 800 | 900
9T_NVT | 100.8013 | 100.284 | 98.8738 | 98.2238 | 97.4333 | 96.6297 | 95.5851 | 94.8833 | 94.091 | 93.4202 | 92.6324 | 91.8855 | 90.8159 | 90.0563 | 89.4335 | 88.4397 | 87.6473 | 86.7258 | 86.0662 | 85.17 | 84.0865 | 83.2189 | 82.2384 | 81.3898 | 80.4401 | 79.525 | 78.572 | 77.6252 | 76.6487 | 75.5954 | 74.6586 | 73.6791 | 72.5732 | 71.5314 | 70.5489 | 69.4876 | 68.6406 | 64.1505 | 53.3698 | 42.7561 | 32.4573 | 10.8029 | 8.4525
9T_HVT | 100.0861 | 99.9283 | 98.7488 | 97.7216 | 96.8137 | 95.8399 | 94.8922 | 93.9035 | 93.0709 | 92.1034 | 91.1429 | 90.1617 | 89.3596 | 88.3382 | 87.3598 | 86.3049 | 85.3857 | 84.2671 | 83.2392 | 82.2533 | 81.2651 | 80.1715 | 79.1569 | 78.0315 | 76.9444 | 75.889 | 74.705 | 73.6796 | 72.5477 | 71.449 | 70.3324 | 69.1953 | 68.0674 | 66.7822 | 65.6679 | 64.5665 | 63.539 | 58.7771 | 46.7863 | 35.5229 | 25.2983 | 0 | 0
7T_HVT | 100.3914 | 99.6062 | 97.6068 | 95.9797 | 94.2622 | 92.6412 | 91.0912 | 89.2819 | 87.691 | 86.156 | 84.3415 | 82.6482 | 81.05 | 79.1529 | 77.5278 | 75.9168 | 74.1436 | 72.4127 | 70.6906 | 69.0372 | 67.3296 | 65.4458 | 63.6787 | 61.7959 | 60.1208 | 58.3747 | 56.7249 | 55.0371 | 53.3699 | 51.6113 | 49.9332 | 48.3018 | 46.6575 | 44.9947 | 43.463 | 41.9746 | 40.7144 | 34.3745 | 21.8956 | 12.9688 | 7.1398 | 0 | 0
9T_NVTR | 100.2853 | 99.8957 | 98.869 | 98.3312 | 97.2924 | 96.593 | 95.9956 | 95.0354 | 94.1494 | 93.7776 | 92.6993 | 92.0257 | 91.1613 | 90.2854 | 89.5522 | 88.911 | 87.8365 | 87.0987 | 86.2522 | 85.3401 | 84.4692 | 83.642 | 82.8398 | 82.0163 | 81.1077 | 80.3157 | 79.3461 | 78.4286 | 77.4923 | 76.6004 | 75.6512 | 74.692 | 73.7332 | 72.7259 | 71.7969 | 70.9303 | 69.9805 | 65.9711 | 55.7826 | 45.6515 | 35.733 | 28.3501 | 0
12T_NVT | 100.4358 | 100.0081 | 99.0824 | 98.3035 | 97.6213 | 96.8529 | 96.1684 | 95.4549 | 94.8746 | 94.2734 | 93.4913 | 92.9053 | 92.2018 | 91.666 | 90.9065 | 90.2362 | 89.6511 | 89.0111 | 88.2607 | 87.6226 | 86.9011 | 86.2885 | 85.6281 | 84.8839 | 84.233 | 83.5598 | 82.7843 | 82.0703 | 81.3223 | 80.7249 | 79.8926 | 79.1924 | 78.4164 | 77.6693 | 76.9099 | 76.1765 | 75.3589 | 72.1099 | 64.1009 | 55.5087 | 46.6146 | 0 | 0
12T_LVT | 100.6315 | 100.7165 | 100.7827 | 99.6927 | 99.1064 | 99.2017 | 98.5936 | 97.8348 | 97.6523 | 97.1132 | 96.3719 | 96.0065 | 95.4539 | 95.128 | 94.1669 | 94.0917 | 93.3131 | 92.6977 | 92.2523 | 92.1269 | 91.1021 | 90.663 | 90.3232 | 89.5801 | 88.9634 | 88.4618 | 87.967 | 86.9879 | 86.3354 | 86.2175 | 85.5022 | 84.7516 | 84.33 | 83.5357 | 82.8189 | 82.2634 | 81.5672 | 78.8718 | 71.2621 | 63.526 | 54.8801 | 0 | 0
12T_HVT | 100.1997 | 100.4366 | 99.7337 | 99.1347 | 98.4609 | 97.6661 | 97.2044 | 96.5987 | 95.9345 | 95.2645 | 94.6256 | 93.9695 | 93.2442 | 92.7163 | 91.9019 | 91.2933 | 90.6645 | 89.7956 | 89.0213 | 88.3145 | 87.4905 | 86.7936 | 86.0489 | 85.2411 | 84.4406 | 83.6295 | 82.9504 | 82.0801 | 81.2903 | 80.4691 | 79.5307 | 78.6969 | 77.8861 | 76.9756 | 76.1227 | 75.187 | 74.3962 | 70.6545 | 60.9036 | 50.5953 | 40.2266 | 0 | 0
12T_NVT_R | 100.5281 | 100.9549 | 100.7147 | 100.3118 | 99.9341 | 99.6329 | 99.0574 | 98.8366 | 98.5864 | 98.1785 | 97.8108 | 97.3964 | 96.8308 | 96.5536 | 96.1605 | 95.8477 | 95.5212 | 95.0926 | 94.6203 | 94.2894 | 93.7876 | 93.2921 | 92.9106 | 92.4622 | 92.043 | 91.503 | 91.0596 | 90.5864 | 90.0511 | 89.5826 | 88.9869 | 88.5668 | 87.9313 | 87.4622 | 86.9174 | 86.4398 | 85.7939 | 83.4688 | 77.2124 | 70.2788 | 62.6276 | 0 | 0
18T_LVT | 100.6402 | 100.6335 | 100.3396 | 100.7544 | 100.5422 | 100.02 | 100.1098 | 100.0793 | 99.6818 | 99.9247 | 99.1478 | 98.9804 | 98.8281 | 98.7018 | 98.7035 | 98.7091 | 97.9993 | 97.8234 | 97.8829 | 97.9696 | 97.4618 | 97.1723 | 96.8947 | 96.7517 | 96.5689 | 96.296 | 96.0766 | 95.8673 | 95.4411 | 95.1302 | 95.2332 | 94.9066 | 94.3776 | 94.0041 | 93.8919 | 93.6305 | 93.2139 | 92.0045 | 88.3488 | 83.9096 | 78.8937 | 0 | 0
18T (ELT)
12T
9T
7T
7T
9T
12T
18T

## Slide 22: Single Event Upsets
GND
VDD
GND
VDD
Static RAM cell
1
1
0
0
1 0
Highly energetic particle

## Slide 23: TMR (full triplication)
Reg
logic
Reg
logic
Reg
logic
clkA
clkB
clkC
inA[K:0]
Voter
Voter
Voter
outA[N:0]
outB[N:0]
outC[N:0]
stateA[M:0]
stateB[M:0]
stateC[M:0]
inB[K:0]
inC[K:0]

## Slide 24: TID Robust Design: Impact on Performance (1/2)
Case study:
In the LpGBT, for frame alignment, a special frequency pre-scaler is needed:
  Normally divides by 2 but, upon request, executes a single divide by 3 cycle
  The pre-scaler waits for the request to be released before it is ready to accept the next one
  It works at the down-link clock frequency: 2.56 GHz
  The pre-scaler allows to shift the received down-link frame by 390 ps at a time
A logic synthesizer was used to synthesise the pre-scaler under two conditions:
  Relaxed target frequency: 100 MHz
  Target operation frequency: 2.56 GHz
  In both cases non-TMR and TMR logic was synthesised

## Slide 25: TID Robust Design: Impact on Performance (2/2)
Gate count:
  No TMR: 32 Gates
  TMR (full): 157 Gates [x4.9]
    Besides triplicating the logic, the registers, the clocks and adding voters, additional buffers are needed to account for the higher loading of the signals!
As a consequence:
  TMR can increase the power dissipation by 4.0 to 4.9 times!
  TMR reduces the operation frequency by a factor between 1.4 to 1.5
The large device libraries, 12TLVT and 18TLVT (ELT), are the only ones capable of achieving the target operation frequency for this particular circuit with a TMR implementation!
The 18TLVT library has an edge on radiation tolerance so it was selected for the high speed circuits of the LpGBT!
The smaller libraries, 7T and 9T have prohibitive degradation with radiation and can only be used in circuits for which the timing margin is very relaxed
  Notice that, using HVT libraries (or smaller size) does not always pays off in terms of dynamic power if high frequency operation is the target. Larger amounts of buffering and slower rise and fall times (“high short circuit current”) might degrade the power consumption figure.
Target: 100 MHz
Target: 2.56 GHz

## Slide 26: CML - TID
CML gates offer the best speed potential in “CMOS” circuits:
  Only NMOS transistors used;
  Loads are resistors:
    Very low parasitic capacitance, compared with Cdb of the PMOS transistors
  Speed to a large extent set by the RC time constant in the drain circuit:
    If IT (or DV) are stabilized the delay suffers little variation with the process parameters!
    Thus in principle robust against TID
Main disadvantages:
  Requires a bias circuit
  Relatively large power consumption!
    DC power consumption
  Relatively large area
out+
in+
RL
RL
out-
in-
t
IT

## Slide 27: CML – Buffer Simulations
Three process corners:
  SS, TT, FF (actives and passives)
  Bias current [almost] constant
  Voltage and Temperature kept constant to assess the effects of process only:
    This to “simulate” the effects TID < 200 Mrad in the NMOS (SS process)
out+
in+
RL
RL
out-
in-
t
IT
RL = 1.2 kW
IT = 500 mA
W/L = 2.4 mm / 60 nm
Dt
tr, tf
x2
FF
TT
SS
Power dissipation is high!
Delay variation very much dependent on the R variations
f = 5.12 GHz
Notice that the power dissipation of a single inverter/buffer is about ¼ of the full TMR 18TLVT pre-scaler circuit just presented!!!

## Slide 28: Radiation Damage in Optoelectronics
Damage mechanism dominated by Displacement Damage (DD) caused by Non-Ionizing Energy Loss (NIEL) from heavy particles (neutral/charged hadrons, energetic leptons).
PIN - Diodes:
  Increasing of the dark current by several orders of magnitude (from pA to mA)
  Reduction of the responsivity (R = Iph/Popt)
VCSELs:
  Increase in the threshold current and voltage
  Decrease of the laser slope-efficiency (S = Popt / Imod)
  VCSELs display higher radiation tolerance than EE diodes
“Radiation Tolerance Limit”
for VCSELs and PINs: ~1015 n/cm2

## Slide 30: LpGBT ASIC – High Speed SerDes
Data transceiver with fixed and “deterministic” latency both for up and down links.
  Clocks and Data
Down link:
  2.56 Gb/s
  FEC12
Up link:
  5.12 Gb/s or 10.24 Gb/s
  FEC5 or FEC12
E-Links:
  Data rates:
    160 /320 / 640 / 1280 Mb/s
  Count:
    FEC5
      Up to 28 @ 160 Mb/s
      Up to 7 @ 1.28 Gb/s
    FEC12
      Up to 24 @ 160 Mb/s
      Up to 6 @ 1.28 Gb/s
Power dissipation:
  Target: ≤ 500 mW @ 5.12 Gb/s
Small Footprint:
  Size: 9 mm x 9 mm
  Fine Pitch: 0.5 mm
  Pin count: 289 (17 x 17)
Radiation tolerance:
  200 Mrad
  SEU robust
ROC
ROC
ROC
LpGBT
Data rate: 160 Mb/s to 1.28 Gb/s
Length: cm to meters
Data rate: 5 - 10 Gb/s
Length: few cm
Data rate: Rx: 2.56 Gb/s Tx: 5.12 and 10.24 Gb/s Length: <200 m

## Slide 31: LpGBT Block Diagram (Simplified)
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBT
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 32: Connecting with the Front-end Modules (ASICs)
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 33: CLPS - eLinks
Signalling:
  CLPS “CERN Low Power Signalling”
    [This should] avoid any confusion with LVDS or SLVS
Main specifications:
  Link type:
    Point – to – point
    Multi – drop transmitter
  Max data rate:
    1.28 Gb/s (NRZ)
  Max clock frequency:
    1.28 GHz
  Programmable signalling level:
    100 mV to 400 mV (single-ended PP amplitude)
    200 mV to 800 mV (differential PP amplitude)
  Common mode voltage:
    600 mV (nominal)
  Load impedance:
    100 W
Vout+
Vout-
Single-ended PP amplitude:
  max(Vout+) – min(Vout+)
Differential PP amplitude:
  max(Vout+ - Vout-) – min(Vout+ - Vout-)
Vcm:
Termination load close to the last receiver in the transmission line
100 W transmission line, twisted pair, etc.
Common mode in the middle of the supply (Vdd/2) for best tolerance to ground fluctuations between modules;

## Slide 34: eLink Driver – eTx
Data rate:
  Up to 1.28 Gb/s
Clock frequency:
  Up to 1.28 GHz
Driving current:
  Programmable: 1 to 4 mA in 0.5 mA steps
Receiving end termination:
  100 W
Voltage amplitude in 100 W:
  100 mV to 400 mV (SE PP amplitude)
  200 mV to 800 mV (DIFF PP amplitude)
Common mode voltage:
  600 mV
Pre-emphasis:
  Driving current: 1 to 4 mA in 0.5 mA steps
  Pulse width:
    Externally timed
    Self timed: 120 ps to 960 ps in steps of 120 ps
    Clock timed: T bit / 2
Pre-emphasis logic

## Slide 35: eTx Design
eTx output stage circuit architecture was driven by radiation tolerance considerations:
  eTx interfaces with other ASICs so it is important that its performance degrades as little as possible with TID.
Poly resistors are insensitive to TID
The circuit relies on having the resistors setting the current and not the transistors
R
Unit cell curent: 0.5 mA (in 100 W)
R
DOWN
UP
OUT
All transistor sizes have to be chosen so that the resistors set the current values (and not the transistors).
Besides the normal P/N ratio, PMOS W
could be set 40% to 60% bigger than
needed to accommodate radiation
damage (NMOS 20% bigger)
R set the driver
and pre-emphasis currents,
respectively

## Slide 36: eTx Output Stage is Pseudo Differential
R
Unit cell curent: 0.5 mA (in 100 W)
R
OUT+
R
Unit cell curent: 0.5 mA (in 100 W)
R
OUT-
100 W
(External termination)
Enabling Logic
Enabling Logic
enableUnitCell
data
“1”
“0”
UP
DOWN
UP
DOWN
Unit cell can be disabled by keeping: UP = “1” and DOWN = “0”

## Slide 37: eTx Output Stage is Pseudo Differential
Unit Cell
Unit Cell
Unit Cell
Unit Cell
x1
x1
x2
x4
Unit Cell
Unit Cell
Unit Cell
Unit Cell
x1
x1
x2
x4
Unit Cell
Unit Cell
Unit Cell
Unit Cell
x1
x1
x2
x4
Unit Cell
Unit Cell
Unit Cell
Unit Cell
x1
x1
x2
x4
100 W
(External termination)
Summing nodes
Unit cells are grouped in a “binary” weighted form for current programmability: 1x, 1x, 2x and 4x
Driver cells
Pre-emphasis
Driver cells
enableDriver[0]
enableDriver[1]
enableDriver[2]
enableDriver[3]
enablePreDriver[0]
enablePreDriver[1]
enablePreDriver[2]
enablePreDriver[3]
enableDriver[0]
enableDriver[1]
enableDriver[2]
enableDriver[3]
enablePreDriver[0]
enablePreDriver[1]
enablePreDriver[2]
enablePreDriver[3]
data
preEmpPulse
data
preEmpPulse

## Slide 38: eTx – Amplitude control & Power Consumption
Differential output: 500 MHz Clock
Programmable amplitude
The power consumption depends on the programmed strength (load current) and on the operation frequency. That is also on the dynamic power dissipated in the CMOS circuits that control the output stage!

## Slide 39: What is Pre-Emphasis (1/4)
To transmit NRZ data with little ISI the transmission channel must have a bandwidth of at least (rule of thumb):
  BW = 0.7 × Bit Rate
For example, for transmission at 5 Gb/s the bandwidth required is:
  BW = 0.7 × 5 Gb/s = 3.5 GHz
For illustration purposes lets suppose that:
  The driver is modelled by an ideal current source
  And the circuit driven is modelled by a RC network with 3.5 GHz bandwidth:
    R = 50 W
    C = 0.91 pF
Simulated eye-diagram:
  There is very little ISI:
  The eye is well opened vertically and horizontally
  The jitter is very low
Data Source
out
  BW = 3.5 GHz

## Slide 40: What is Pre-Emphasis (2/4)
Lets suppose now that the bandwidth of the circuit being driven is four times lower:
  BW = 3.5 GHz / 4 = 795 MHz
  R = 50 W
  C = 3.64 pF
Simulated eye-diagram
  There are significant amounts of ISI:
  A “bit” extends for much longer than a bit period
  The eye-diagram is almost closed vertically and horizontally
  Jitter is high
The BER would be “prohibitive” for such a system!
Data Source
out
  BW = 0.8 GHz

## Slide 41: What is Pre-Emphasis (3/4)
The problem with the low bandwidth is that:
  For fast successions of “0s”and “1s” the signal has no time to reach the final value before a new “0” or a new “1” is transmitted.
In an RC type of circuit this can be “easily” overcome:
  At every “0”-to-“1” or “1”-to-“0” transition drive the circuit to a higher (or lower) voltage than the final one:
    In our case this is accomplished by using a larger current than the final one
  Once the voltage reaches the desired amplitude switch to the nominal current.
In practice, no level crossing detection is made:
  Immediately after a transition and for a “short” time a current pulse is added to the “nominal” modulation current
  The pre-emphasis pulse duration is adjusted to open the eye-diagram
Time [s]
Amplitude [V]
Exponential (RC) behaviour
Target
amplitude
t’r
tr
t’r < tr
Cut the pre-emphasis pulse here!

## Slide 42: What is Pre-Emphasis (4/4)
Data Source
out
Dt
  BW = 0.8 GHz
rise
fall
Imod
Irise
Ifall
Dt = 0.5 × T
Imod = “1”
Irise = 1.35 × Imod
Ifall = 1.35 × Imod
I = Imod + Irise + Ifall
I
Data Rate: 3.5 GHz
Remember the rule of thumb:
BW = 70% Bit Rate → 2.45 GHz
This network only has 32% of the required bandwidth!
Data
Time [s]
I
Time [s]

## Slide 43: In the Frequency Domain
BW 70% Bit Rate
BW
22% Bit Rate
70% Bit Rate

## Slide 44: eTx Pre-Emphasis Functions
Programmable delay line allows to generate pre-emphasis pulse widths between 120 and 960 ps
Pre-emphasis amplitude
programmable
Pre-emphasis mode selectable
Pre-emphasis self-timed pulse width selectable
Half bit period pre-emphasis pulse width
“User generated” pre-emphasis pulse width
Pre-emphasis pulse

## Slide 45: eTx – Pre-Emphasis
500 MHz Clock
Ipre = 0 mA
With Pre-Emphasis
CL = 1 pF
Driver Strength = 2 mA
Pre-Emphasis Strength = 1 mA
Pulse width = T/2
With Pre-Emphasis
CL = 10 pF
Driver Strength = 2 mA
Pre-Emphasis Strength = 0, 1, 1,5 and 2 mA
Pulse width = T/2
Ipre = 1 mA
Ipre = 1.5 mA
Ipre = 2 mA
Output with low capacitive loading
Output with high capacitive loading
Single ended
Differential

## Slide 46: eTx – Pre-Emphasis
No Pre-Emphasis
Driver Strength = 2 mA
Pre-Emphasis Strength = 0 mA
Pulse width = n.a.
With Pre-Emphasis
Driver Strength = 2 mA
Pre-Emphasis Strength = 2 mA
Pulse width = T/2
Data: PRBS 7
Data rate: 2.56 Gb/s
CL = 2 x 5 pF

## Slide 47
More on Practical [Annoying] Details of Designing for TID Tolerance!

## Slide 48: Some Practical Aspects of TID Robustness
ELT gates use non-minimal device sizes:
  NMOS: Wn = 1.42 um
  PMOS: Wp = 3.74 um
  Basically dictated by the geometry constraints and balancing between NMOS and PMOS current driving
These “large” devices will introduce noise in Vdd and Vss when switching:
  They drive relatively important loading capacitances (other ELT gates)
  During the gate signal transition time they represent a low impedance between the supply and ground
How much noise goes into the supply and ground?
Test case:
  Take the “most innocent gate” (minimum size ELT inverter – LVT)
  Load it with other gates (a reasonable number is 4)
  Drive it with a 1.28 GHz clock (that is the maximum specified frequency for the eTx)
  Measure Idd and Iss
(ELT = Enclosed Layout Transistor)

## Slide 49: Test Case Simulation
Simulation conditions:
  C0 (TT, Vdd = 1.2V, T = 27C)
  C4 (FF, Vdd = 1.08V, T = 100C)
  C16 (SS, Vdd = 1.08V, T = 100C)
Main observations:
  The inverter is [easily] 1.28 GHz capable [all corners]
  Large peak currents go into the VSS and VDD power rails!
    These current peaks can reach: 1.3 mA for the fastest PVT conditions!
  This is for a simple inverter!
    What are the consequences for a complex circuit or full scale ASIC?
1.28 mA
1.28 mA

## Slide 50: eTx Driver Supply Noise!
Current in the output stage is “constant” except when the output switches!
Output DC level: 3.2 mA
Output peak: 3.2 mA
Driver logic peak: 14.4 mA
The logic driving the output stage exhibits large current peaks!
  Up to 14.4 mA
In the LpGBT there might be:
  17 Data Drivers
  33 Clock Drivers
  All working synchronously
This could represent up to 720 mA of [noise] current being injected in the power supply and ground!
This noise has to be mitigated!

## Slide 51: eTx Driver Supply Noise!
Solution:
  Decrease the peak amplitude by spreading the current pulse in time;
How
  RC filter the IO supply and ground locally in the I/O cell
For this to be effective the I/O cell must be enclosed in a deep well:
  Otherwise the substrate resistance would “short-circuit” the ground filtering
Values adopted:
  R = 10 W, C = 10 pF
R = 0 W
R = 5 W
R = 10 W
R = 20 W
R = 0 W
R = 5 W
R = 10 W
R = 20 W
VDD IO
VSS IO

## Slide 52: Scheme Adopted for the I/O Power
I/O Cell
I/O
Circuit
i/o+
i/o-
ESD
ESD
Digital core power domain
I/0 power domain
VDD(Core)
VDD(IO)
10 pF
VSS(IO)
VSS(Core)
inputSignal(s)
outputSignal(s)
10 W
10 W
Rise and fall times of the signals in these nodes must be as short as possible to avoid added jitter due to
power supply [noisy] domain crossing!
Local buffers in the I/O Cell powered by the core power
Circuit design tip:
For systems trying to achieve pico second jitter it is clear that supply noise must be kept low and raise and fall times short! (Particularly important at the crossings between power domains)
Example: assume the relative noise between the core and IO supplies to be 100 mV. If jitter is to be kept below 1 ps then the signal slopes should be bigger than 100 mV/ 1 ps. For a 1.2 V supply:
tr = tf < 0.8*1.2 V / 100 mV/ps < 9.6 ps!

## Slide 53: Receiving data from the Front-end Modules (ASICs)
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 54: Optimum Sampling
CDR
Clock and Data Recovery
Optimum sampling point
(highest SNR)
Non-Optimum sampling point
Jitter or static phase offset (low SNR)
CDR circuit “extracts” the frequency
and phase of the incoming data.
The LpGBT is the clock source to the front-end modules;
All the clocks generated by the LpGBT are synchronous with the LHC machine clock;
Thus the LpGBT “knows” exactly the frequency of the incoming data!
A CDR circuit is thus not needed for each ePort.
However, the incoming phase of the data is not known!
A mechanism is thus needed to sample the incoming data at the optimum sampling point!

## Slide 55: Up eLink – Phase Alignment
The phase of the incoming data signals is “unknown” in relation to the internal sampling clock!
There are up to 28 eLink inputs (potentially) all with random phase offsets
The solution:
  “Measure” the phase offset of each eLink input
  Delay individually each incoming bit stream to phase align it with the internal sampling clock
eLink “i”
eLink “j”
Good sampling instants
LpGBT internal clock
Bad sampling instants
LpGBT
Clock (explicitly) provided to the front-end by an eLink clock.
Clock embedded in the data, CDR needed at the front-end
Phase relationship between the received data and the internal clock unknown!

## Slide 56: Phase aligner - Principle of operation
Delay Line (reference)
PD
CP
LPF
Delay Line (replica)
bitRateClock
MUX
Phase Selection Logic
trackMode [2:0]
phaseSelectChannel [3:0]
Q D
CK
(x4)
(x1)
dataRate[2:0]
enableChannel
trainChannel
resetChannel
dllConfig [3:0]
dllReset
Input Data (unknown phase)
Resampled Data
Reference DLL

## Slide 57: Phase - Selection
T/8
“Examine” all the phases
Detect where the data “edges” are in relation to the clock;
Choose the phase that has the edges better centered around the clock
Once aligned, the PA can track the data phase wanders that cover virtually a full clock cycle:
  To allow for this the delay line covers more than one bit period: 1.75 × Tbit
  And, during initialization only phases 4 to 11 are allowed
-3/8 T
+3/8 T

## Slide 58: Phase Generation – Principle
The scheme depends on “accurately” matching the “unit cell delay” with the bit period:
  Dt = Tbit/8
For that, the reference DLL contains 16 “unit cells” and it is calibrated to twice the bit period (fbit/2):
  Leading to Dt = Tbit/8
The exception is the 160 Mb/s case where the DLL is calibrated at the same frequency as the bit rate (160 MHz):
  Leading to Dt = Tbit/16
  Dt = Tbit/8 requires two unit cells
  To cover 1.75 × Tbit the length of the delay line is doubled!
PD
LF
1
2
3
16
1
2
3
14
15
16
17
28
Phase - Multiplexer
dataIn
delayedDataOut
Clock
For 320, 640
and 1280 Mb/s
Bit Rate | Clock
[Mb/s] | [MHz]
160 | 160
320 | 160
640 | 320
1280 | 640
For 160 Mb/s
The multiplexer selects only the even number cells as outputs!

## Slide 59: Unit Cell Delay
160 / 320 Mb/s: Dt = 390.6 ps (Tbit/8 )
640 Mb/s: Dt = 195.3 ps
1.28 Gb/s: Dt = 97.6 ps [“Just about” for all process corners]
Chart: “Unit cell” delay vs Control voltage
| 0.25 | 0.3 | 0.35 | 0.4 | 0.45 | 0.5 | 0.55000000000000004 | 0.6 | 0.65 | 0.7
C0_27C_1V2_tt | 0.99255 | 0.4716 | 0.2403 | 0.1367 | 0.08953 | 0.066585 | 0.05497 | 0.04916
 | 1.825 | 0.86215 | 0.41365 | 0.21175 | 0.1178 | 0.07449 | 0.0532 | 0.042165 | 0.036185 | 0.03295
C2_n20C_1V32_ff | 0.5448 | 0.31395 | 0.1896 | 0.1209 | 0.083835 | 0.06319 | 0.05141 | 0.04458 | 0.040585 | 0.038205
 | 1.087 | 0.48645 | 0.23115 | 0.1234 | 0.077835 | 0.057185 | 0.04745 | 0.04292 | 0.04063
 | 0.60695 | 0.3292 | 0.19065 | 0.1203 | 0.08485 | 0.06629 | 0.05646 | 0.05124 | 0.048265 | 0.046385
 | 1.746 | 0.75605 | 0.3471 | 0.17315 | 0.099245 | 0.0665 | 0.05069 | 0.04252 | 0.03827
 | 0.9029 | 0.4828 | 0.26895 | 0.16005 | 0.10475 | 0.075895 | 0.0602 | 0.051385 | 0.04637 | 0.043475
 | 0.84005 | 0.36055 | 0.17755 | 0.1045 | 0.073 | 0.0588 | 0.0526 | 0.049595
 | 0.97065 | 0.49015 | 0.263 | 0.1569 | 0.106 | 0.080505 | 0.06742 | 0.060725 | 0.05703 | 0.054745
 | 1.7195 | 0.74455 | 0.3476 | 0.1779 | 0.10395 | 0.070355 | 0.05383
 | 1.8195 | 0.9288 | 0.49145 | 0.27435 | 0.16445 | 0.10845 | 0.0791 | 0.063095 | 0.054165
 | 0.8841 | 0.3914 | 0.1935 | 0.11265 | 0.078165 | 0.06284
Probably the max data rate this method can be comfortably used in 65 nm CMOS!

## Slide 60: Phase Generation – Performance (640 Mb/s)
B = 640 Mb/s
T = 1540.8 ps
DT = 192.6 ps
Jmax = 35.7 ps
Jmax/T = 2%
Jmax/DT= 18%
Chart: Delay vs “Tap” selection
| tap1 | tap2 | tap3 | tap4 | tap5 | tap6 | tap7 | tap8 | tap9 | tap10 | tap11 | tap12 | tap13 | tap14
actual delays | 194.25 | 389.1 | 584.15 | 779.85 | 975.45 | 1171.45 | 1367.55 | 1563.45 | 1759.6 | 1955.7 | 2151.95 | 2348.75 | 2545.95 | 2743.5
ideal delays | 195.3 | 390.6 | 585.9 | 781.2 | 976.5 | 1171.8 | 1367.1 | 1562.4 | 1757.7 | 1953 | 2148.3 | 2343.6 | 2538.9 | 2734.2
Chart: Jitter vs “Tap” selection
| tap0 | tap1 | tap2 | tap3 | tap4 | tap5 | tap6 | tap7 | tap8 | tap9 | tap10 | tap11 | tap12 | tap13 | tap14
 | 4.456 | 8.306 | 8.387 | 11.9 | 10.39 | 14.33 | 13.27 | 16.84 | 20.29 | 22.75 | 30.57 | 25.85 | 34.55 | 26.95 | 35.86

## Slide 61: Edge Detection – Principle
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D
Q
D

Q
D
serDataIn
dataRate[1:0]
Data Rate Switch

e[13]

e[12]

e[11]

e[10]

e[9]

e[8]

e[7]

e[6]

e[5]

e[4]

e[3]

e[2]
e[1]
sampleSelect [2:0]
serDataOut
samplingClock
Idle: shiftClock = 1’b1
160 Mb/s, clock = 160MHz
320 Mb/s, lock = 320MHz
640 Mb/s, clock = 640MHz
1.28 Gb/s, clock = 1280MHz
Standard cells
Full custom

## Slide 62: Phase Alignment vs Power Dissipation (1.28 Gb/s)
Chart: Power dissipation vs “Tap” selection
| tap0 | tap1 | tap2 | tap3 | tap4 | tap5 | tap6 | tap7 | tap8 | tap9 | tap10 | tap11 | tap12 | tap13 | tap14 | auto
 | 2.186 | 2.205 | 2.228 | 2.251 | 2.275 | 2.297 | 2.321 | 2.331 | 2.366 | 2.387 | 2.413 | 2.432 | 2.465 | 2.478 | 2.502
 | 2.992
Three modes of operation:
  Automatic phase tracking
  Training with learned static phase
  Static phase selection
Automatic phase tracking requires the lock state machine to constantly monitor the edge transitions and update the phase selection when necessary
Static phase-selection requires the operator to select the proper phase (the selection is unlikely to change during a full run).
In this mode, it is possible to reduce the power consumption by:
  Disable the delay-line outputs, except the one required
  Prevent the signal from propagating further though the delay line.
Automatic phase tracking
Max is 82% of automatic phase tracking
Delay Line power dissipation [mW] |  |  | 
Mode | Static |  | Automatic
Corner | 1st Tap | Last Tap | 
C0 | 2.7 | 3.4 | 4.3
C2 | 6.7 | 7.9 | 9.2
C15 | 1.8 | 2.3 | 3.0

## Slide 63: Details That Count!
Unit cell
enable
enable
VDD
Dummy gate
In the “Training mode”, the circuit switches from “automatic” to “Static phase”, disabling the unused outputs and stopping the propagation of the signal further down the delay-line.
However, the absolute value of the “unit” cell delay is affected up to 8% even if careful buffering is added!
To avoid this, a dummy gate is added and enabled each time the output gate is disabled.
This allows to maintain the same loading conditions for all the cells and minimizes the delay mismatch!
  Less than 0.2% in C0
Enabled on the active cells for which the output is not used

## Slide 64: Phase – Aligner Layout
2 replica delay lines
DLL
2 replica delay lines
109.8um
624.6um
LPF Cap

## Slide 65: Connecting With the Counting Room
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 66: High – Speed Links
The LpGBT supports the following data rates:
  Down link: 2.56 Gb/s
  Up-link: 5.12 / 10.24 Gb/s
In all cases data is transmitted as a frame composed of:
  Header
  The data field
  A forward error correction field: FEC5 / FEC12
The data field is scrambled to allow for CDR at no [additional] bandwidth penalty
Efficiency = # data bits/# frame bits
 | Down-link | Up-Link |  |  | 
 | 2.56 Gb/s | 5.12 Gb/s |  | 10.24 Gb/s | 
 |  | FEC5 | FEC12 | FEC5 | FEC12
Frame [bits] | 64 | 128 |  | 256 | 
Header [bits] | 4 | 2 |  | 2 | 
Data [bits] | 36 | 116 | 102 | 232 | 204
FEC [bits] | 24 | 10 | 24 | 20 | 48
Correction [bits] | 12 | 5 | 12 | 10 | 24
Efficiency | 56% | 91% | 80% | 91% | 80%
H
Message
FEC
Forward Error Correction
(Allows to correct transmission errors)
Header
(Delimits the frame boundaries)
Data
(User data payload)

## Slide 67: The order of operations is important
Scrambler
FEC
Coding
Interleaving
Serializer
data[N:0]
header
serialData
Up-Link
DeScrambler
FEC
DeCoding
(error detection /correction)
DeInterleaving
CDR &
DeSerializer
data[N:0]
header
serialData
Down-Link

## Slide 68: Scrambling
Converts a bit stream into a “random” sequence of bits
Objective:
  Remove the “DC” contents of the data (so called DC balance)
Needed for:
  Transmission over an “AC” coupled channel
  Guaranty enough transitions so that the receiver can recover the clock from the data
Scrambler/DeScramblers types:
  Synchronous
  Self-synchronizing (used in the LpGBT)
Scrambler order
Serial scramblers require the shift registers to run at the bit rate!

## Slide 69: Parallel Implementation
 | Down-link | Up-Link |  |  | 
 | 2.56 Gb/s | 5.12 Gb/s |  | 10.24 Gb/s | 
 |  | FEC5 | FEC12 | FEC5 | FEC12
Data [bits] | 36 | 116 | 102 | 232 | 204
Scrambler width [bits] | 36 | 58 | 51 | 58 | 51
Scrambler order | 36 | 58 | 49 | 58 | 49
Number of scramblers | 1 | 2 |  | 4 | 
Recursive equation | eq 1 | eq 2 | eq 3 | eq 2 | eq 3
Q D
CK
Di+1[n:0]
Si+1[n:0]
Xi[k:1]
Clk
bypass
Si[n:0]
D Q
CK
DSi[n:0]
Si[n:0]
Xi[k:1]
Clk
bypass
D Q
CK
eq 1: Si = Di xnor Si-25 xnor Si-36
eq 2: Si = Di xnor Si-39 xnor Si-58
eq 3: Si = Di xnor Si-40 xnor Si-49
Scrambler
DeScrambler

## Slide 70: Error Correction Codes
Due to Noise, Intersymbol Interference or SEUs information might be corrupted as it passes through a channel
Forward Error Correction (FEC) gives the possibility of correcting errors without asking back the transmitted information
This is achieved by adding “parity” bits to the transmitted data
Bandwidth is tradeoff against transmission robustness
source
sink
encoding
decoding
channel
1101
1101XXX
m
c
r
d
k bits = 4
n bits = 7
1001XXX
1101

## Slide 71: Reed-Solomon Codes
Non-binary code:
  Based on symbols of length m-bits
k-symbols of message are encoded into a n-symbol code word:
The number of parity symbols is:
Allowing to correct up to
  t =
symbols
Example:
  RS(7,5)
    n = 7 (code word length)
    k = 5 (symbols to be coded)
  m = log2(7+1) = 3 bits
  Error correction capability:
    t = (7-5)/2 = 1 symbol
S0
S1
S2
S3
S4
S5
S6
n = 7
k = 5
7 – 5
m = 3 - bits

## Slide 72: LpGBT Down Link
Down-link FEC:
  4 codes interleaved
  RS(5,3), m = 3 bits
    This code is a “shortened” version of RS(7,5)
    Due to frame size restrictions only 5 out of the 7 symbols are transmitted!
      “Missing” symbols have to be used at coding time and assume received (known) by the decoder
This code can correct:
  Any random error in a frame of 36 bits (not considering parity bits)
  Any burst error of length 10 bits
  It can decode burst errors of length 12 bits if it is contained in the boundary of four symbols
…
S0
S0
S1
S1
S4
S0
S0
S1
S1
S4
Symbols of RS0
Symbols of RS1
Symbols of RS3
Symbols of RS4

## Slide 73: Experimental: LpGBT Down Link (LpGBT-FPGA)
System dominated by random noise
For the same optical power the BER can be dramatically improved
For a target BER, the margin on the optical power budget margin is increased.

## Slide 74: Experimental: GBTX Down - Link
Radiation levels at 20 cm radius from the beam:
  2 ×1015 neutrons/cm2
  1 × 1015 hadrons/cm2
  50 Mrad total dose
High rates of Single Event Upsets (SEU) are expected for SLHC links:
  Particle “detection” by Photodiodes used in optical receivers
  SEUs on Receivers,
  SEUs on Laser-drivers
  SEUs on SERDES circuits
Experimental results confirmed that:
  Error correction is mandatory to achieve error-rates ≤ 10-12
Upsets lasting for multiple bit periods will occur on PIN detectors!
Upset lasting for multiple frames can occur in commercial TIAs
No errors were observed in the FEC-coded data-stream in the SEU dominated region with beam on!
Test conditions:
70 MeV proton beam
Flux of 2 × 108 p/cm2/s
≈ 2 × the flux in the HL-LHC trackers
(J. Troska, et al., TWEPP 2011)
(beam on)
SEU dominated
NOISE dominated

## Slide 75: High-Speed Serializer
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 76: Serializer
The LpGBT transmitter works at two data rates:
  5.12 Gb/s and 10.24 Gb/s
This means that the Serializer has to convert the parallel data at 40 MHz into a serial bit stream:
  128 – bits @ 5.12 Gb/s
  256 – bits @ 10.24 Gb/s
So what is a Serializer?
  A “glorified” name for a shift register!
D Q
CK
0
1
D Q
CK
SR[N]
SR[N-1:0]
clock40MHz
load
clock10GHz
(x 256)
(x 256)

## Slide 77: Should a Serializer be Implemented as a Shift Register?
10 Gb/s, LpGBT case:
  256 registers running at 40 MHz
  256 registers running at 10 GHz
  256 Multiplexers
    MUX has to react to 100 ps pulse
    MUX is reducing the setup time for the shift register
  Timing between the “load” and the 10 GHz clock is critical!
FFs:
  Total of 512 need
  All the FFs in the shift register need to be 10 GHz capable [not the input register]
And how about power consumption?
  Power [in CMOS] consumption is proportional to frequency
D Q
CK
0
1
D Q
CK
SR[N]
{SR[N-1:0],0}
clock40MHz
load
clock10GHz
FF power in mW/GHz
40 MHz
(x 256)
(x 256)
(x 256)
P(LpGBT) = 257 x 260uW = 66.8 mW

## Slide 78: “Multi – Level Serializer”
Next level:
  Has half the number of FF
  Runs twice as fast
The power per Serialization level remains constant:
Ten levels are needed to go from 40 MHz to 10.24 GHz
The Serializer power is:
Although this architecture requires “twice” as much FFs (1023), it only requires 10/257 = 3.9% of the power consumption!!!
1
0
D Q
CK
40 MHz
(x 128)
D Q
CK
(x 128)
(x 128)
D[257, 255, …, 1]
D[256, 254, …, 0]
1
0
D Q
CK
(x 64)
D Q
CK
(x 64)
(x 64)
1
0
D Q
CK
(x 2)
D Q
CK
(x 2)
(x 2)
1
0
D Q
CK
(x 1)
D Q
CK
(x 1)
(x 1)
80 MHz
D Q
CK
10.24 GHz
5.12 GHz
2.56 GHz
Next Serializer level has half the number of FF and runs twice as fast!
10.24 Gb/s

## Slide 79: LpGBT Serializer
Since the clock frequency increases with the serialization level, it is possible to optimize the speed-power at each level:
  Not possible for the simple shift register
And a similar power saving goes in the clock tree!
Also only the last 2 / 3 stages are timing critical
The LpGBT does not use the last “resampling” stage at 10.24 GHz.
At the output of the last MUX the signal is already at 10.24 Gb/s
  Double data rate
Low jitter requires thus the last MUX to be fast and the 5.12 GHz clock to have “perfect” duty-cycle
1
0
D Q
CK
(x 2)
D Q
CK
(x 2)
(x 2)
1
0
D Q
CK
(x 1)
D Q
CK
(x 1)
(x 1)
5.12 GHz
2.56 GHz
10.24 Gb/s

## Slide 80: 5.12 and 10.24 Gb/s
D Q
D Q
L
D Q
P[2]
P[0]
P[3]/P[1]
P[1]/P[0]
S0
S0*
S1
serOut
clk5G12*
clk5G12
select10G24
I1
I0
I1
I0
I1
I0
“0”
S20
S31
clk2G56
Serializer 2-to-1:
2.56 Gb/s to 5.12 Gb/s
Serializer 4-to-1:
2.56 Gb/s to 10.24 Gb/s
I1
I0
rxLoopback
enLoopback
D Q
D Q
D Q
D Q
For 5.12 Gb/s this branch is off (clock off) and the multiplexer “static”
I1
I0
CMOS
CML
The (fast) MUX also converts from CMOS to CML
5.12 Gb/s

## Slide 81: Fast Multiplexer
Basically an AOI gate!
Advantages:
  Simplicity
  Speed potential of CML
Disadvantages:
  “Perfect” symmetry between select and ~select required for low duty-cycle distortion
I1
select
~select
I0
Y
Y = ~(I1 & select + I0 & ~select)

## Slide 82: Fast Multiplexer
Voltages in these
nodes depends on
the history of I1 and I0
C0 (TT, T = 27C, Vdd = 1.2V)
500 mV
Data dependent jitter
C16 (SS, T = 100C, Vdd = 1.08V)
320 mV
(64%)
Advantage:
  A “natural” building block for “double data rate”
Disadvantages:
  Data dependent jitter
  Amplitude “badly defined”
Amplitude depends
on the relative
“strength” of the
resistors and the transistors
I1
select
~select
I0
Y
1x
1x
1x
1x
1k W
tr = 40.2 ps
tf = 32.6 ps
“Typical corner”
“Worst corner”

## Slide 83: Signal Anatomy
~select
I1
select
I0
Y
1x
1x
1x
1x
1k W
n1
n0
For the short period that both “select” and “~select” transistors are weakly turned on, the resistor pulls node “Y” high!
The height depends on the states of “I0” or “I1” inputs.
Vth
select
~select
“select” and “~select” transistors weakly turned on during this phase
When “select” or “~select” transistors turn on, there is charge sharing between node “Y” and nodes “n0” or “n1”, pulling node “Y” down. The amount of charge shared depends on the history of nodes “n0” and “n1”.

## Slide 84: Improving Data Dependent Jitter
History in theses nodes is cleared while the branch is “inactive” reducing
the data dependent jitter
C0
C16
“No” data dependent jitter
485 mV
325 mV (67%)
I1
select
~select
I0
Y
1x
1x
1x
1x
1x
1x
1k W
tr = 46.0 ps
tf = 35.2 ps
Always the same amount of charge sharing!

## Slide 85: “Amplitude Stabilization”
C0
C16
485 mV
394 mV
(81%)
I1
select
~select
I0
Y
1x
2x
2x
2x
1x
2x
1k W
0.86k W
tr = 46.0 ps
tf = 27.3 ps
x2 -> small “Ron”
(basically) sets “Rpull down”

## Slide 86: 5.12 and 10.24 Gb/s
For 10.24 Gb/s operation “select” and “~select” alternately select the “I1” and “I0” inputs
For 5.12 Gb/s operation the “select” input is kept at “0” and the “~select” at “1”. The input “I0” passes thus inverted to the output.
The circuit is single ended! To interface with the CML logic, two circuits used as “pseudo differential” are needed!
I1
select
~select
I0
Y
5.12 Gb/s signal path
5.12 Gb/s operation
~I1
~I0
~Select
~Select
~serOut
~I1
~I0
~Select
~Select
~clk5G12*
clk5G12*
serOut
S0*
S1
“pseudo CML”

## Slide 87: High Speed Line – Driver
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 88: Line – Driver Topology
Accommodate the large capacitive load
RC delay to generate the pre-emphasis pulse
Pre-emphasis current driver
On-chip 100 Ω matching
Buffer Stage
Imax = 12 mA
Imax = 8 mA

## Slide 89: Bandwidth Broadening using Inductive Peaking (1/2)
Add an inductor in series with the load resistor
The bandwidth can be extended up to 1.85 times
For optimum group delay response the BW gain is 1.6 times
The circuit displays a second order transfer function
  The frequency response is characterized by the ratio “m”

## Slide 90: Bandwidth Broadening using Inductive Peaking (2/2)
Power optimization:
For a CML stage the bandwidth can be enhanced by increasing the tail current:
  By reducing RL at fixed DV
Or, for by using inductive peaking for a given current and RL
A specified bandwidth can thus be achieved with lower current if inductive peaking is used.
out+
in+
RL
RL
out-
in-
IT
out+
in+
RL
RL
out-
in-
IT
LP
LP

## Slide 91: 2nd Buffer Stage
190 µm
235 µm

## Slide 92: Modulation Stage
150 µm
200 µm

## Slide 93: Delay “Stage”
Parasitic capacitance from Emphasis Stage

## Slide 94: 10 Gb/s Post-layout Simulations

## Slide 95: 10 Gb/s Pre-Emphasis
Icc = 40 mA
Imod = 12 mA
Ipre = 8 mA
Cout = 500 fF
Process:
SS_100C_1.2V
Im
Ipre
Iout
= +
“long” delay
“short” delay
Advantage:
Pre-emphasis is made by subtracting the “bit stream” to itself after inversion and scaling!
No narrow pulses required (as needed for the eTx scheme)
Disadvantage:
The pre-emphasis is done by reducing the amplitude rather than peaking the signal during the pre-emphasis phase.
The driver consumes in permanence Im + Ipre.

## Slide 96: High-Speed Line Receiver
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 97: Equalization
100 cm Differential Strip Line in FR4
3.5 dB
7 GHz (10 Gb/s) → -27 dB !!!
(100 cm)

## Slide 98: High Pass – Filter Equalization
Driver
Transmission Line
Equalizer
RX
(100 cm)

## Slide 99: Equalization vs Pre-Emphasis
Both pre-emphasis and Equalization are attempts to restore the baseband signal spectrum
Pre-emphasis (done at the transmitter):
  Tries to generate a wave shape with an “exaggerated” spectral contents at the frequencies that are most attenuated by the channel [typically the high frequencies]
  No degradation of the SNR
Equalization (done at the receiver):
  Amplifies more the high frequency contents of the spectrum than the low frequency. It is an attempt to achieve a combined response of the channel and equalizer that will approach a channel that has no intersymbol interference
  Degradation of the SNR
Because of the SNR degradation resulting from equalization, the best approach is to combine pre-emphasis and equalization:
  Enhance the transmitted high frequency content rather than do all the high frequency peaking at the receiver side

## Slide 100: The Equalizer in the LpGBT
Passive attenuator: allows to handle signals as high as 1 V
Attenuation: 0, -3.5 and -9.5 dB
Restores the signal
to CML levels
Four equalizing stages allow
to flexibly control the shape of the transfer function.

## Slide 101: Equalizer Stage – RC Degenerated Differential Pair
RD
RD
Vout
Vin
CP
CP
RS
CS
f
fp1
fp2
fz
rSelect
cSelect
 | All Stages | Stage |  |  |  |  | 
Setting |  | 1st and 2nd |  | 3rd |  | 4rd | 
 | Cs [fF] | Rs [kW] | fz [MHz] | Rs [kW] | fz [MHz] | Rs [kW] | fz [MHz]
1 |  | 3.0 | 758 | 0.6 | 3789 | 0.4 | 5684
2 | 70 | 4.9 | 464 | 1.2 | 1895 | 1.0 | 2274
3 |  | 7.0 | 325 | 2.4 | 947 | 1.6 | 1421
4 |  | 3.0 | 379 | 0.6 | 1895 | 0.4 | 2842
5 | 140 | 4.9 | 232 | 1.2 | 947 | 1.0 | 1137
6 |  | 7.0 | 162 | 2.4 | 474 | 1.6 | 711
7 |  | 3.0 | 189 | 0.6 | 947 | 0.4 | 1421
8 | 280 | 4.9 | 116 | 1.2 | 474 | 1.0 | 568
9 |  | 7.0 | 81 | 2.4 | 237 | 1.6 | 355

## Slide 102: First Stage Gain
Degeneration resistance
  3 kΩ, 5 kΩ, 7 kΩ
Degeneration capacitance
  70 fF
Load cap
  Cp  10 fF
    Cds+ Next stage (Cgs + Miller)
Load resistance
  6 kOHm
Due to the limited GBW of the technology, peaking is achieved by attenuating the low frequency gain rather than busting the high frequency gain!

## Slide 103: 75 cm Coaxial Cable
Simulation conditions:
  Data rate:
    2.56 Gb/s
  Signal amplitude:
    100 mV
  Process:
    FF, VDD = 1.08 V, T = 100 °C
Results (worst case):
  Power dissipation:
    2.34 mW (max)
  PP jitter:
    70 ps (max)
  SNR:
    20 (26 dB) (min)
Worst case Eye diagram (SNR20)

## Slide 104: Eye Opening Monitor
Goal:
  Monitor the opening of the received data eye diagram and the equalizer’s performance
What is the problem:
  BER is limited by intersymbol interference (ISI), cross-talk with neighbour channels, reflections due to impedance mismatch
Solutions:
  Employ differential signalling, Pre-Emphasis at the transmitter, Continuous Time Linear Equalizer (CTLE) and Decision-Feedback Equalization (DFE) at the receiver
  The Eye-Opening Monitor (EOM) in the LpGBT will be used to monitor the performance of the down-link and to optimize the equalizer performance (CTLE).
CDR
Eye-O-Monitor
equalizer
param
data input
Recovered clock

## Slide 105: Eye Opening Monitor
Provides an “eye diagram picture” by using a “signal-scan” approach
The scan is performed across the time (x-axis) and across the amplitude (y-axis), yielding a “signal density” per point
  The input signal [data] is compared with a reference voltage “Vof”
  The comparator’s result is sampled by the rising edge of a clock synchronous to the incoming data
  The sampled result drives a ripple counter to accumulate statistics
  The counter is enabled for a well defined period.
Vof (y-axis)
Sampling Clock (x-axis)
Vof (y-axis)
VCM
VCM
data
Vof
toCounter
samplingClk
DFF
The counter is only incremented when Vof is between the data amplitude values

## Slide 106: Eye Opening Monitor
VCM
comp
data - vof
1
Vof
0
1
0
0/1
0
0/1
0
0
0
0
0
“toCounter” toggles when Vof is within the input signal amplitude’s maximum and minimum at the rising edge of the sampling clock!
samplingClock
Uncertainty zone due to noise and ISI
If Vof is within the data amplitude levels the comparator toggles
Signal amplitude  Vof Comparator toggles “statistically”
If Vof is outside the data amplitude levels the comparator never toggles
1
0/1
1
0/1
1
1
1
1

## Slide 107: EOM in the lpGBT
Y-axis:
  31 points, step = ~20 mV (covers from VDD/2 up to VDD)
X-axis:
  64 points, step = ~6.1 ps in typical
DFF
CML
CMOS
Phase
Interpolator
data+
DAC
data-
Vof+
Vof-
clk5G12
clk2G56pi
toCounter
comp
Vof+
Vof-
polarity
vSel[3:0]
compQ
selPhase[5:0]
Notes: The DAC is designed with a resistive network plus passgates

## Slide 108: EOM in the lpGBT (y-axis)
The comparator uses a differential difference amplifier
This eliminates the dependence on the common-mode of the input signals
data+
data-
Vof-
Vof+
Vdiff+
Vdiff-
Vout+
Vout-
Vdiff = Av[(data+ – Vof-) – (data- – Vof+)]
meaning
Vdiff = Av[(data+ – data-) – (Vof+ – Vof-)]
Gain stages
Differential difference stage
Notes: Comparator goes around ~1.5mA consumption

## Slide 109: EOM in the lpGBT (x-axis)
Phase interpolator (1/2)
  Receives the VCO clock (5.12 GHz)
  Generates in-phase “I” and quadrature “Q” signals
  Uses those for phase interpolation:
    Full phase rotation with  6.1 ps resolution (64 possible phases)
Phase
Interpolator
clk5G12
clk2G56pi
selPhase[5:0]
DFF
clk5G12
clk2G56I
DFF
clk2G56Q
phase interpolator core
Quadrature generation
selPhase[5:0]
clk2G56pi
φ
I
Q
clk5G12
clk2G56I
clk2G56Q

## Slide 110: EOM in the lpGBT (x-axis)
~Q
Q
~I
I
Phase interpolator (2/2)
Reference: A 40 Gb/s CDR with Adaptive Decision-Point Control Using Eye-Opening-Monitor Feedback, H. Noguchi et al, ISSCC. 2008
S0+
S1+
ckI+
ckI-
ckI+
cSelI+
cSelI-
ckQ+
ckQ-
ckQ+
cSelQ+
cSelQ+
S0-
S1-
S15-
S15+
x15
ckpi+
clkpi-
Current steering using DAC
Circuit tradeoff:
Low rise/fall times on ckI and ckQ will improve linearity, but will increase jitter
phase interpolator core
Notes: clkI – inphase 2.56 GHz
clkQ – inphase 2.56 GHz
cSelI, cSelQ – clock selection - mux to select between the 4 quadrants
S0 – S15, mux for the current steering interpolation

## Slide 111: Clock and Data Recovery
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
I2C Masters
ADC
Control Logic
Configuration
(e-Fuses + reg-Bank)
One 80 Mb/s port
I2C
Ports
aIn[7:0]
IO[15:0]
160 Mb/s to
1.28 Gb/s ports
LpGBTIA
LpGBLD
LpGBTX
e-Link
clock
data-up
data-down
control
data
clocks
LR
Ref CLK (optional)
LD
CLK Manager
CDR/PLL
DeSER
DEC
DSCR
ENC
SCR
SER
I2C Slave
I2C
Port
PIO
2.56 Gb/s
5.12 Gb/s or 10.24 Gb/s

## Slide 112: PLL/CDR
MUX
counter[3]
2.56Gbps
serial data
40 MHz
clock input
PD
VCO
5.12 GHz
fbDiv
clk2G56 ... clk40M
PFD
fbClkI_40M
fbClkI_2G56
fbClkQ_2G56
fbClkI_40M
fbClkI_2G56
FD
fbClkI_2G56
fbClkQ_2G56
enPFD
enPD
enFD
refClkSelect
MUX
selectPD_PFD
CP0
CP1
Icp0[x:0]
Icp1[x:0]
RC
LPF
Vref = VDD/2
res[x:0]
cap[x:0]
reset?
overrideVControl
capBank[x:0]
retimedData
refClk_PFD
pre scaler CML
skipCycle
clk5G12
Clock Race

## Slide 113: The LpGBT
For low jitter the PLL uses an LC oscillator (VCO)
Advantage:
  Low phase noise (jitter)
Disadvantage:
  Limited tuning range
Due to PVT it is unlikely the VCO center frequency will be 5.12 GHz (fLHC x 128)
A calibration of the VCO is required at beginning of operation!
The process is easy in the PLL mode since a reference clock (fLHC) is available:
  The VCO control voltage is fixed (VDD/4)
  The VCO clock frequency is compared with the reference.
  Switched capacitors are switched in or out.
  Based on the frequency measurement, the best capacitor setting is selected
But what if the ASIC is used as a receiver and no reference clock is available?
Target frequency 5.12 GHz
VCO control voltage fixed to 0.3V
Frequency that best approaches fLHC x 128
This curve will be selected for operation

## Slide 114: Reference-Less Locking
When working as a CDR, although a clock reference is not present, the serial data itself can be used to calibrate the VCO centre frequency!
2.56 Gbps
1 UI = 390.6 ps
Alternating
“1s” and “0s”
2 UI
4 UI on average
NRZ data
On average, the signal looks like a 2.56GHz/4 = 640 MHz clock!
Divide by 16
2.56Gbps
serial data
On average, due to NRZ data probability, the distance between two consecutive rising edges is 4 UI
Minimum distance between rising edges
If this signal drives a “divide by 16” counter, a 40 MHz clock reference is obtained!
This is a rather imprecise frequency but if further divided the accuracy increases
Vcnt
(forced)
fbDiv
1/2
VCO
5.12 GHz
VCO 1st?
1/210
1/210
40 MHz
VCO Fast
VCO Slow
enable count

## Slide 115: TID Radiation: Topology Matters (1/2)
Two PLLs working at 2.5 GHz
Same circuits except the VCO:
  LC VCO
  Ring oscillator VCO
Same power dissipation
Same loop dynamics

## Slide 116: TID Radiation: Topology Matters (2/2)
Pre/post-rad jitter (rms):
  LC: 0.3 / 1.0 ps
  RO: 5.6 / 22 ps
600 Mrad + Annealing:
  LC: Df < 5% (LC: Passives set the frequency)
  RO: Df < 40% (Ring: Actives set the frequency)
24 hours room Temp
4, 24 hours @ 100 C
24 hours room Temp
24 hours @ 100 C
NMOS: L = 100 nm ; W = 2 um; nf = 32 x 4
PMOS: L = 100 nm ; W = 3 um; nf = 32 x 4
PMOS: L = 60 nm ; W = 3um; nf = 12
NMOS:
L = 180 nm; W = 3um; nf = 8
L = 180 nm; W = 3um; nf = 15
(Free running oscillation)
(Free running oscillation)

## Slide 117: SEU Radiation: Topology Matters – Round 1
Heavy ion testing:
  LET: 3.2 to 69.2 MeV.cm2/mg
LC oscillator displays a significantly higher sensitivity than the ring oscillator!
  Contrary to expectations!
SEU Phase jumps:
  Type: phase unlock
  Ring oscillator: both polarities
  LC: Mainly positive
Two-Photon Absorption (TPA) laser tests point to the VARACTOR as the main culprit!
  Total cross section of the LC-oscillator is 4 10-5cm2 from which 70% is contributed by the varactor area!
Limit points
Ring oscillator
LC oscillator
GBTX cross section ~10-6 cm2!

## Slide 118: TID Radiation: Topology Matters – Round 2
A new design prototyped to test the hypothesis:
  Smaller varactor area
  Different frequency tuning topology:
    Grounded vs floating well!
1/600

## Slide 119: Clock Recovery
PLL
Q
D
t
Retimed data
NRZ data
d
NRZ Data
Edge detector
No spectral-line at
the bit rate frequency
Spectral-line at the bit
rate frequency present
d
A PLL can’t lock to NRZ data
But it can lock to such a signal
Problem:
Difficult to match the delay of the two paths so that the recovered clock samples the data at the middle of the data eye over all process, temperature
and supply variations.
Ideal sampling instant
Notes: Serial data transmission is most of the time done without simultaneous transmission of the bit rate clock. Moreover, the Non Return to Zero (NRZ) data spectrum contains no spectral-line at the bit rate frequency. Locking to such a signal is thus not possible with a standard PLL.
NRZ data can be processed in such a way that a spectral-line appears in the spectrum of the signal so obtained. One possibility is to generate narrow pulses at every transition of the NRZ data stream. This signal can now be fed to a PLL that will lock to it producing a clock at the bit rate frequency. This operation is called clock recovery. It is still necessary to guaranty that the recovered clock is used to sample the data at the middle of the bit period so that the bit error rate is minimized. This is difficult to guaranty over all process, temperature and supply voltage variations. Notice that absence of pulses will be interpreted by the PLL as a phase error, making the recovered clock phase wander more or less strongly depending on the density of the data transitions, giving origin to the so called data-dependent jitter. To minimize this problem data is very rarely transmitted either without a periodic frame pulse or a line code such as the 8B/10B code mentioned before. Note that not all phase detectors described so far are suitable clock recovery. In particular, the PFD can not be used since any missing pulse will be interpreted as a phase error driving the PLL away from the correct frequency.

## Slide 120: Alexander Phase Detector - Principle
It is a bang-bang detector:
  Only early/late information
To take the Early/Late decision:
  1st Look for transitions
  2nd Take an Early/Late decision at every transition
Three samples of the serial data are necessary to find the transition and resolve the phase relationship.
No data transition present:
  S1 = S2 = S3
  S1  S3 = 0 and S1  S2 = 0
  Charge-pump: Hold
Data transition + Early clock:
  Sample S1 ≠ S3 and S1 = S2
  S1  S3 = 1 and S1  S2 = 0
  Charge-pump: Down = (S1  S3) & ~(S1  S2)
Data transition + Late clock:
  Sample S1 ≠ S3 and S1 ≠ S2
  S1  S3 = 1 and S1  S2 = 1
  Charge-pump: Up= (S1  S3) & (S1  S2)
The falling edge of the clock aligns with the data transition instants:
  In lock, S1 or S3 are thus at the optimum sampling instants
S1
S2
S3
Clock is early
Clock is Late
S1
S2
S3
Notes: It is also possible use a bang-bang phase detector to lock on random data. However, the simple DFF phase detector wouldn’t work in this case. For that, a modified type of detector is required and the most commonly used is the Alexander phase detector.
J. D. Alexander, ‘Clock Recovery From Random Binary Data,’ Electronics Letters, vol. 11, October 1975, pp. 541 542
As we have seen before when locking to random data if data transitions are not present it is not possible to decide if the phase is early or late. Because of that, in the Alexander “Bang-Bang” detector, it is introduced a third state where no charge is added/removed to/from the loop-filter. The Alexander detector is thus not strictly a bang-bang phase detector since it has three states but it is in the sense that only early/late information is given about the phase and no linear measure of the phase error is provided.
Referring to the pictures above we can see that by taking three consecutive samples of the data using the rising and falling edges of the clock, it is possible to identify if a data transition is present (S1  S3 = 1 ) and in that case if the clock is early or late in relation to the data. The principle is quite simple:
If no data transitions are present them all the samples will have the same value. In this case a phase decision cannot be taken and the charge pump has to be maintained in the high impedance state to minimize the phase and frequency wander of the recovered clock.
If the clock is early in relation to the data, the sampled values S1 and S3 are going to be different and S1 and S2 identical. The “Down” signal can thus be written as: down = (S1  S3) & ~(S1  S2)
When the clock is late, Samples S1 and S3 are different and samples S1 and S2 are different. The “Up” signal is thus written as: up = (S1  S3) & (S1  S2)

## Slide 121: Alexander Phase Detector
Down = X & ~Y
Up = X & Y
Q
D
Retimed data
NRZ data
Q
D
VCO clock
Q
D
Q
D
S1
S2
S3
S4
Y
X
Sampling FFs
Delay FFs
FF1
FF2
FF3
FF4
×1 load
×3 load
×2 load
Notes: To make a practical implementation of an Alexander phase detector one must keep in mind that sample S1, S2 and S3 are taken in sequence and are thus not available simultaneously to calculate the “Up” and “Down” outputs. To solve this problem it is necessary to delay by one clock cycle the sample S1 and by half a clock cycle the sample S2. These are the roles of FF1 and FF2 in the schematic above. FF3 and FF4 are the sampling flip-flops.
With the arrangement shown above, FF3 samples the data at the raising edge of the clock generating S1 which will be then shifted to the output of FF1 a clock cycle later. At the same time that S1 is shifted to FF1, FF3 samples S3 (which is in fact also S1 for the next decision cycle). That is, both S1 and S3 are simultaneously available at the outputs of FF1 and FF3. Because FF4 is clocked by the inverted clock it samples S2 half a clock cycle after FF3 had sampled S1. Since FF2 is clocked with the non inverted clock, sample S2 is transferred to FF2 half a clock cycle later it had been sampled by FF4. We can now see that the three samples S1, S2 and S3 are simultaneously available at the output of flip-flops FF1 making the output of the XOR gate permanently valid.
One should note that using such a phase detector the loop tries to align the falling edge of the clock with the data transitions. Consequently, sample S1 (or S3) is the retimed data.

## Slide 122
Connectors, PCB & PACKAGE

## Slide 123: Reaching the ASIC
Silicon Die
BGA Package
Rx Termination
Rx Diff. T-Line
Tx Diff. T-Line
Optical TRX SFP
Probe Effect ?
Test board ?
Package ?
Chip Design ?
4.8 Gb/s Frame

## Slide 124: “Build” Models
Ansoft Designer
S Parameters
S Parameters
S Parameters
Equivalent circuit
Spice Netlist
HSpice Netlist
SIwave
SIwave
SIwave (2.5D)
HFSS (3D)

## Slide 125: Fully Model the Signal Path

## Slide 126: Unpopulated Board (no GBTX)
Measurement (yellow) and simulation (blue) with 100 ohms termination at the BGA pads

## Slide 127: Fully Populated Board
Probe is at the receiver termination , ≈ 3.5 mm from the input buffer.
Measurement (yellow) and Simulation (Brown).

## Slide 128: Checking the Models
Chart: 
SMA
MECT
CONNECTOR
Package and Die
Measurement
Simulation
Time [ps]

## Slide 129: Schrodinger In High Frequency Electronics!?
Can signals be observed without being disturbed?
Manufacturers provide equivalent electrical modes for their oscilloscope probes
Simulate to evaluate how much the system is being disturbed
In our case the loading effect of the probe was small!
No Probe (blue)
With Probe (gray)

## Slide 130: “Virtual Probe” - Simulation
1Gbps
3.2Gbps
4.8Gbps
At the Termination
At the Input buffer

## Slide 131: Improving the Package
Original design: Dark blue
131
Move the termination close to the input buffer
At the Termination
At the Input buffer

## Slide 132: Credits
This talk reflects the work of many people in the GBT and LpGBT projects and it wouldn’t have been possible without their contribution. So I do collectively thank them.
In particular some people have prepared specific simulations, drawings,… for this set of slides. I specially thank their help:
Bram Faes
Eduardo Mendes
Pedro Leitao
Quan Sun
Rui Francisco
Szymon Kulis