## Slide 1
GBTx ASIC
Davide Falchieri
INFN Bologna
Corso nazionale INFN "Optoelectronic conversion in the data transmission from detectors"

## Slide 2
Radiation-hard optical link
front-end electronics
optical link
off-detector electronics
down-link
up-link
Requirements on the optical link:
  radiation-hard
  high bandwidth
  able to self-recover errors
  able to transmit:
    clock + data + triggers + slow control
clock + data + triggers + SC
clock + data + triggers + SC

## Slide 3
Radiation-hard optical link
GBTx
GBTIA
GBLD
4.8 Gb/s Transimpedance Amplifier:
it amplifies the weak photo-current
detected by the PIN diode
4.8 Gb/s Laser Driver:
it modulates laser current to achieve
electro-optical conversion
GBT FPGA

## Slide 4
VTRx

## Slide 5
Radiation-hard optical link
GBTx
VTRx
optical fiber

## Slide 6
GBTx ASIC from CERN
FE Module
FE Module
Phase – Aligners + Ser/Des for E – Ports
FE Module
E – Port
E – Port
E – Port
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
Clock[7:0]
CLK Manager
CLK Reference/xPLL
External clock reference
control
data
One 80 Mb/s port
I2C
Port
I2C (light)
JTAG
JTAG
Port
80, 160 and 320 Mb/s ports
GBTIA
GBLD
GBTX
e-Link
clock
data-up
data-down
ePLLTx
ePLLRx
clocks

## Slide 7
20 x 20 matrix:
0.8 mm pitch, 0.5 mm ball diameter
GBTx package

## Slide 8
GBTx power supply
VDDTX
VDDRX
VDDIO
VDDCM
VDDPS
VDD CORE
phase shifter
clock manager
phase shifter
clock manager
6 1.5V power domains

## Slide 9
GBTx configuration

## Slide 10
GBTx configuration pins
GBTx
configSelect
efusePower
3.3V during fuse prog, 1.5V otherwise
efuseWritePulse
I2c address
4
mode
4
transceiver modes
refClkSelect
rxDataValid
rxLockMode
rxRdy
autoReset
stateOverride
disables automatic power-up FSM
txDataValid
txRdy
ldReset
ldScl
ldSda
selects I2C or IC
selects the reference clock
testClockOut
testOutput
2

## Slide 11
GBTx
GBTx configuration
GBT FPGA
configuration pins
E-Fuse bank
I2C
IC
The basic transceiver modes are selected via dedicated configuration pins that must be hardwired in the user application according to the use of the GBTx. Further default configuration of the GBTx is loaded from its internal E-Fuse bank at power-up into the register bank.
The selection of IC or I2C is made using the pin configSelect.
In all modes the GBTx needs a local clock reference (from the on-package quartz crystal XTAL or from an external reference) to correctly initialize itself and the optical link.
register bank

## Slide 12
GBTx register bank
366 R/W registers
70 R-only registers
categories:
clock manager
test outputs
Ios
EPLL-TX
EPLL-RX
XPLL
phase shifter
serializer
deserializer
TX logic
RX logic
TX control
RX control
power-up
GBLD access
EportRX
EportTX
Eport-EC
Efuses
+

## Slide 13
GBTx register bank
CLOCK
PHASE SHIFTER
E-port config
old Web site: https://gbtx-configuration.web.cern.ch
(no longer available)

## Slide 14
GBTx register bank
https://espace.cern.ch/GBT-Project/VLDB/Control/Forms/AllItems.aspx
new SW tool

## Slide 15
GBTx register access
IC
I2C
configSelect pin = 0
configSelect pin = 1
The two bits IC[1:0] of the SC field in the received GBT frame contain the configuration data. These are de-multiplexed to form 8-bit words which follow a frame-based protocol.
The I2C slave port allows to write and read the GBTx configuration registers. This can be used when the GBTx is operated in any mode. The GBTx is equipped with a standard I2C slave interface and is accessed by an I2C master, for example the GBT-SCA, transmitting data with the correct address.
Write to register operation

## Slide 16
GBLD register access through the GBTx
I2C master
7 registers in the GBTx are reserved for storing the values to write to the GBLD. These can be accessed by a normal write to the GBTx by the IC interface or by I2C. These values are then transmitted to the GBLD by accessing a reserved memory address within the GBTx, again either through I2C or the IC interface.

## Slide 17
GBTx transceiver modes

## Slide 18
GBTx transceiver modes
no clock coming from the off-detector electronics
the GBTX works as a simple link receiver, receiving data and the clock reference from the counting room through the optical fiber channel
System CLK

## Slide 19
GBTx transceiver modes
The GBTx delivers the global system clock reference, coming from the counting room, to all front-ends
System CLK

## Slide 20
Transceiver modes
GBT
GBT
GBT
GBT

## Slide 21
GBTx encoding / decoding
GBTx
GBT FPGA
data pattern in
data pattern out

## Slide 22
GBTx encoding / decoding
RS: Reed Solomon algorithm

## Slide 23
GBTx: scrambler
Aim of the scrambling:
  reduce the occurrence of long sequences of '0' (or '1') only;
  achieve a good DC-balance
Scrambler features:
  doesn't add any redundancy/overhead
  has a latency of 1 clock cycle
  generates a pseudo random signal

## Slide 24
GBTx: Reed Solomon encoder
Aim of the Reed Solomon encoding:
  protect the data against transmission errors
Reed Solomon encoder features:
  composed of 2 RS encoder (15,11), symbol = 4 bits
  only combinatorial logic
  allows to correct up to 2 symbols (8 consecutive bits for example)
FEC (Forward Error Correction) is built by interleaving two Reed-Solomon encoded words with 4-bit symbols, each capable of correcting a double symbol error. This means that a sequence of up to 16 consecutive corrupted bits can be corrected.

## Slide 25
GBTx: interleaver
Aim of the interleaving:
  improve the capacity of the code to correct long burst of errors
Interleaver characteristics:
  interleaving made at a symbol level (4 bits)
  only “routing”, no clock cycles
  increases the code correction capability from 2 to 4 consecutive symbols (16 consecutive bits) without increasing overhead

## Slide 26
GBTx encoding

## Slide 27
GBTx frame format
FEC
header
120 bit @ 40 MHz = 4.8 Gbps
Forward Error Correction
84 bit @ 40 MHz = 3.36 Gbps
total bandwidth
effective bandwidth
Data transmitted has fixed latency in both directions enabling its efficient use for trigger information and timing control
SC = IC +EC
Internal Control
External Slow Control (like SCA)

## Slide 28
GBTx wide bus frame format
The forward error correction functionality is traded off for bandwidth
only for the uplink direction
The additional 32 bits dIn[111:80] are made available on pins normally used as outputs in groups 3 and 4, implying that in this mode when operating the E-Links at 80 Mb/s fewer output data bits will be available on the downlink E-links

## Slide 29
Frame fields
A 4-bit header field is transmitted at the beginning of each frame. The header field is required to synchronize the data stream at the frame level:
    repeated recognition of a valid header indicates correct frame-locking.
    repeated non-valid header recognition indicates that frame synchronization has been lost and that a frame synchronization cycle has to be initiated.
DC-balanced codes
txDataValid = 1, rxDataValid = 1
txDataValid = 0, rxDataValid = 0

## Slide 30
Frame detection modes
frame lock acquisition
frame tracking
For each received frame the four bits in the header position are checked for header validity (both data and idle frame headers are considered valid). If NHF consecutive frames contain a valid header the frame is considered locked. Otherwise, the frame is shifted by one bit and the valid header checking procedure is repeated. After frame-lock is achieved, the receiver switches to the frame-tracking mode.
lock achieved
In this mode the receiver strives to maintain frame synchronization. It checks the validity of the headers and counts the number of invalid headers received in consecutive frames after the first invalid header has been detected. If the number of invalid headers received in consecutive frames is bigger than NMIH, then the receiver re-enters the frame-lock acquisition mode.
If, after detection of one or more invalid headers (that don’t exceed NMIH), a specified minimum number of consecutive valid headers (NMVH) are detected, then the count of invalid errors is reset to zero.

## Slide 31
E-links

## Slide 32
E-Links: duplex serial links
front
end
GBTx
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
Overall in the GBTx 240 pins are dedicated to E-Links.
40 bi-directional e-Links
  up to 40 @ 80 Mb/s
  up to 20 @ 160 Mb/s
  up to 10 @ 320 Mb/s
e-Port data rate can be set independently for:
  each group
1 bi-directional e-Link:
  80 Mb/s
Frontend
Module
Frontend
Module
Frontend
Module
Frontend
Module
GBT-SCA
IC Control
GBTX
eLinks: 80 /160 / 320 Mbps
Data and clock line (optional)
GBT-Frame
4.8 Gbps
optical-fibre link

## Slide 33
e-Port drivers and receivers
LVDS
SLVS
1.2V
+ 400 mV
- 400 mV
0.2V
+ 200 mV
- 200 mV
programmable output current
SLVS
0.2V
+ 200 mV
- 200 mV

## Slide 34
front
end
GBTx
40
40
clock @ 40 MHz
E-Link connections to the front-end
GBTx
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
…
x 40 front end chips
@ 80 Mb/s
x 5
x 5
x 5
@ 80 Mb/s
Each front-end contributes 2 bits per BC

## Slide 35
GBTx
front
end
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
…
x 20 front end chips
@ 160 Mb/s
GBTx
front
end
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
front
end
dClk+/dClk-
dOut+/dOut-
dIn+/dIn-
…
x 10 front end chips
@ 320 Mb/s
E-Link connections to the front-end
Each front-end contributes 4 bits per BC
Each front-end contributes 8 bits per BC

## Slide 36
E-Link connections to the front-end: parallel
front
end
GBTx
40 @ 80 Mb/s
clock @ 40 MHz
40 @ 80 Mb/s
E-links can be grouped together as lanes to obtain higher effective data bandwidth to/from a single front-end module. In this case a single dClk+/dClk- can be used for several dOut+/dOut- and/or dIn+/dIn- serial data signals.

## Slide 37
E-Link clocks
40 e-Link clocks programmable in frequency, but with fixed phase:
40/80/160/320 MHz (per group, independently of the bit rate)
the e-Link data and its associated clock basically run as a Double Date Rate (DDR) connection with the clock having rising and falling transitions occurring in the middle of the bit period

## Slide 38
E-Link clocks
40 e-Link clocks programmable in frequency, but with fixed phase:
40/80/160/320 MHz (per group, independently of the bit rate)
in the front-end module there will be a phase uncertainty with relation to the 25 ns basic clock/frame cycle. It is fully up to the user to resolve this at the system level (e.g. sending specific synchronization data at initialization).

## Slide 39
Phase alignment: downlink
clock and data are sent to the front-end:
trace lengths have to be equalized
(clock and data phases are OK on GBTx outputs)
only data are sent to the front-end:
a CDR circuit has to be present on the front-end

## Slide 40
Phase alignment: uplink
The phase aligner circuit ensures that the E-link data received by the GBTx is sampled by the GBTx internal clock in the middle of the eye-diagram.
phase aligner
Each replica delay-line can adjust the phase of the incoming data via the delay taps along the delay line.

## Slide 41
Phase alignment of the incoming serial data embedded in the e-ports can be:
  static phase selection
      values configured at system initialization
  initial training with learned static phase selection
      put the e-port in phase training mode, while FE sends DC-balanced data
      configure the registers accordingly
  automatic phase tracking
      data from FE are checked and after 64 correct transitions, the channel is declared locked
      tracks temperature and voltage variations
      transparent to the user
      works also on DC un-balanced data (with enough transitions)
Phase alignment: uplink
eLink “i”
eLink “j”
Good sampling instants
GBTX internal clock
Bad sampling instants

## Slide 42
E-port TX

## Slide 43
E-port RX

## Slide 44
Latency and phase stability
The GBTx guarantees constant latency over time and from one power-up/initialization to the next. Constant latency enables the GBTx to be used in clock synchronous trigger systems and for precise TTC distribution to the many front-end destinations.

## Slide 45
Latency and phase stability

## Slide 46
GBTx datapath
RX
TX
120
dOut
rxDataValid
120
dIn
txDataValid
txClock40
rxClock40

## Slide 47
TxData Select
txTestMode
2
header + IC + e-Port data
120
120
120
120
header + AAA_BBBB_AAAA_BBBB_AAAA_BBBB_AAAA_BB
header + counter[25:0] + counter[29:0] + counter[29:0] + counter[29:0]
header + 4’h0 + prbs[6:0] x 1
120
GBTx datapath: injecting data
normal data
fixed pattern
up counter
pseudo-random pattern

## Slide 48
RxData Select
rxTestMode
3
header + IC + e-Port data
120
120
120
GBTx datapath: receiving data
normal data
e-Port TX
fixed patterns depending on mode
000
111

## Slide 49
RX control
Clock and Data Recovery Circuit (CDR)
Frame Aligner (FA)
Frequency Locking (FL)
Phase Locking (PL)
A Half-Rate (HR) CDR architecture is used which results in a 180 degree phase ambiguity that is resolved with the help of the frame aligner circuit
the frequency of the CDR PLL is pulled close to 2.4 GHz
after completion of frequency calibration, the CDR loop is enabled and the CDR PLL locks to the frequency and phase of the incoming data stream

## Slide 50
In the automatic DAC frequency calibration mode, the LCSM (Lock Control State Machine) uses two 11-bit counters to compare the frequency of the CDR VCO (divided by 60) to the frequency of the reference clock. During a binary search cycle the two counters are simultaneously reset and then allowed to count up till one of them reaches the “end count”. One of the counters runs with the reference clock (40 MHz) and is called referenceFast and the other, vcoFast, runs with the RX clock rxClock40. Whichever counter reaches the end count first gives an indication to the state machine if the CDR VCO clock frequency is high or low in relation to the reference clock.
Frequency and phase locking
Frequency Locking (FL)
Phase Locking (PL)
rxSelectDataInPhase
The intrinsic 180 degree phase ambiguity of the recovered clock is resolved

## Slide 51
Frame aligner
4.8 Gb/s
CDR
dataPh0
dataPh180
clock2400MHz
frame aligner
120
GBT frame
Frame aligner tasks:
To convert the two half rate serial streams into two 60-bit words.
To produce the lower clock frequencies needed to run the GBTx receiver (rxClk160MHz, rxClk80MHz and rxClk40MHz).
To phase align the clock signal rxClk40MHz with the phase of the header of the incoming GBT frame

## Slide 52
Reference clock - XPLL

## Slide 53
xPLL
The xPLL is an on chip Phase-Locked Loop (PLL) based on a Voltage Controlled Quartz Crystal Oscillator (VCXO). The main function of the xPLL is to provide a reference clock to the GBTz receiver, transmitter, start-up and watchdog logic. This clock can be generated by the xPLL by setting the xPLL in the Quartz Crystal Oscillator (XOSC) or the PLL mode.
xPLL in PLL mode
ext 40.0789 MHz
low-jitter reference clock
xPLL in XOSC mode
reference clock signal
(not synchronous with the system clock)
xPLL bypassed
high quality ext 40.0789 MHz
low-jitter reference clock
no external reference clock required

## Slide 54
xPLL

## Slide 55
TX (SER) reference clock
RX (CDR) reference clock

## Slide 56
ePLL
The GBTx contains two 320 MHz Phase Lock Loops (ePLL) that are dedicated to generate the 160 and 320 MHz clock signals required by the ePorts when operating at data rates of 160 and 320 Mb/s, respectively. One ePLL is associated with the GBTx receiver, while the other one with the transmitter.
The reference clock of the ePLLs can be set to 40, 80 or 160 MHz or be disabled altogether (in case the 160 and 320 Mb/s data rates are not used). For normal operation the ePLLs use the 160 MHz clocks produced by the GBTX SER or CDR circuits for the transmitter and receiver ePLL, respectively.
The phases of the 160 and 320 MHz clocks can be phase shifted up to 360 degrees in steps of 195.31 ps.

## Slide 57
Phase shifter
The GBTx ASIC provides 8 SLVS clock outputs that can be used as local timing references for the front-end modules. These clocks are generated by the phase-shifter circuit and are fully synchronous with one of the GBTx 40 MHz clocks (depending on the transceiver mode), which in turn are synchronous with LHC bunch crossing reference and maintain with it a stable phase relationship.
The 8 reference clocks are programmable both in phase, 48.8 ps resolution and frequency 40, 80, 160 and 320 MHz.

## Slide 58
Phase shifter jitter

## Slide 59
Phase shifter reference clock

## Slide 60
GBTx startup: recommendations
If a fail-safe mechanism of providing a reset to the GBTx is available, this should be used by connecting it to the RESETb input.
If the GBTx is in XOSC mode, then the FSM will pass through a 300 us wait-state. In some cases, these 300 us will be sufficient for the power supply to stabilize before the fuse sampling starts.
In all scenarios, the user should implement a passive resistor-capacitor network connected to the RESETB input of the GBTx. The resistor should be connected between RESETB and VDDIO, and the capacitor between RESETB and GND. The values of R and C depend on the ramp-up time of the supply. As an example, for the FEAST-MP DC-DC convertor typically used to power the GBTX, values of R = 5 kΩ and C = 100nF are found to be ideal.
If the FEAST-MP DC-DC convertor is used, the ‘power-good’ output of this device can be used as a power-on-reset signal to the GBTx directly connected to its RESETB input. The ‘power-good’ output of the FEAST-MP is an open-drain configuration that requires a pull-up resistor to the output voltage of the convertor. The ‘power-good’ signal can be used together with a passive resistor-capacitor network.
If the GBTx is operated with an external clock (REFCLKSELECT=1), the user should enable this clock only after the power is switched on and has stabilized.
The timeOut function should be enabled.

## Slide 61
GBTx startup FSM
wait for 300 us
fuse sampling
pause for I2C access
wait for XPLL to lock
wait for deserializer to lock
wait for serializer to lock
wait for e-PLL RX to lock
wait for e-PLL TX to lock
wait for DLL in e-Port RX to lock
phase aligner reset
initialize scrambler
wait for DLL in phase shifter to lock
GBTx is operational !
txRdy and rxRdy are asserted

## Slide 62
GBTx watchdog + timeout
Watchdog
When enabled, this will monitor the state of each sub-block. If any sub-block stops operating correctly (for example a PLL loses lock), the watchdog will force the FSM to return to the reset state of that sub-block and the sequence will continue from that point until normal operating conditions are achieved.
For example, if the FSM is in the Idle state and the ePLL-TX loses lock, the FSM will jump back to the resetTXEPLL state and re-start the sequence from there.
The intended use of the watchdog is to allow the chip to automatically recover from a functional interruption (such as a fiber disconnect) without the need of power-cycling or resetting.
Timeout
The ‘wait-states’ have time-outs (set at 2 seconds). If this time is exceeded the FSM moves back to the reset state and re-starts the full start-up procedure. If a fiber is unplugged, the FSM will continue this time-out loop until the fiber is plugged back in and the deserializer can lock.

## Slide 63
Backup

## Slide 64
½ million gates
Approximately:
  300 8-bit programmable registers (all TMR)
  300 8-bit e-Fuse memory
Clock tree (chip wide):
  9 clock trees (all TMR)
  Frequencies: 40/80/160/320 MHz
7 PLLs:
  RX: CDR PLL + Reference PLL (2.4 GHz)
  TX: Serializer PLL (4.8 GHz)
  Phase-Shifter PLL (1.28 GHz)
  xPLL (VCXO based PLL, 80 MHz)
  (2x) ePLL (160-320 MHz)
17 master DLLs:
  9 for phase alignment of the e-links
  8 for clock de-skewing
17 mm
17 mm
Total height including solder balls: ~3 mm
4.3 mm
4.3 mm
GBTx in numbers
56 replica delay lines:
  for phase alignment of the e-links
7 power domains:
  Serializer (1.5V)
  DESerializer (1.5V)
  Clock Manager (1.5V)
  Phase shifter (1.5V)
  Core digital (1.5V)
  I/O (1.5V)
  Fuses (3.3V)