## Slide 1
GBTx use in ALICE TOF readout board
Casimiro Baldanza, Davide Falchieri
INFN Bologna
20 giugno 2018
Corso nazionale INFN "Optoelectronic conversion in the data transmission from detectors"

## Slide 2
Outline
Quick overview of ALICE TOF
  DRM1
  GBTx test board
  DRM2
How we use the GBTx in our readout board:
  power supply
  configuration signals
  E-fuse bank + registers configuration:
  JTAG port
  I2C port
  IC field
  e-Links
  clock manager (register 281)
  clock reference (XOSC vs xPLL)
  phase shifter

## Slide 3
area: 140 m2 (~152k readout pads 3.5 x 2.5 cm2)
resolution: ~80 ps
distance: 3.7 m from the beam pipe
ALICE TOF provides particle identification at intermediate momentum
ALICE TOF @ CERN

## Slide 4
MRPC has 10 gas gaps (two stacks of 5 gas gaps), each gap being 250 mm wide
MRPC strip
…
…
120 cm
7 cm
96 pick-up pads (channels) of 3.5 x 2.5 cm2
1
2
3
4
95
96
MRPC (Multi Resistive Plate Chamber)

## Slide 5
2 VME crates
2 VME crates
2 VME crates
2 VME crates
9.3 m
1 SuperModule = 91 MRPC strips = 8736 channels
TOF = 18 SuperModules = ~152k channels
TOF building blocks: SuperModule

## Slide 6
strip
fast amplifier + discriminator
TRM: TDC Readout Module
one TRM (30 HPTDCs, 25 ps LSB) reads 2.5 MRPC strips ( = 240 channels)
1.5-6m
Current TOF readout

## Slide 7
DRM1: Digital Readout Module 1
strip
LTM
CPDM
1.5-6m
fast amplifier + discriminator
DRM1
Current TOF readout

## Slide 8
DRM1
LTM
TRM
TRM
TRM
[…]
1
VME64x
40 MB/s
30
2
10
32
clock
CTTM
L0 input to CTP
DDL1
TTC
high quality (low jitter) LHC CLK
3
1
2
LDC
LTU/CTP
CPDM
30
30
DRM1
matching window: 600 ns
latency: ~ 8 ms
triggered readout
88 ms
matching window
L2
L1
L0
hits
HPTDC
HPTDC
HPTDC
32
32
TOF readout in RUN1-RUN2

## Slide 9
DRM2
LTM
TRM
TRM
TRM
[…]
1
VME64x 2eSST
160 MB/s
30
2
10
32 bit parallel bus
clock
CTTM
L0 input to CTP
high quality (low jitter) LHC CLK
3
1
2
CPDM
30
30
CRU
trigger & clock
data
HPTDC
HPTDC
HPTDC
Advantages of DRM2 over DRM1:
replaces both CPDM and DRM1
improved DAQ + trigger interfaces with GBTx
faster VME readout with VME64x 2eSST (160 MB/s)
modern FPGA (Igloo2) with SERDES
DRM1
DRM2
TOF upgrade: the DRM2 card

## Slide 10
DRM1 (2006)

## Slide 11
DRM2 (2017-2018)

## Slide 12
Devices disappearing from DRM1 to DRM2
Two FPGAs
DDL
TTCrq

## Slide 13
VTRx
+
GBTx
FPGA
Igloo2
Clock distribution mezzanine
DRM2

## Slide 14
GBTx
Igloo2
SSRAM
A1500
2eSST VME
P1
P2
VTRx
clock to TRMs
SFP CONET2
DAQ, trigger
data from TRMs via VME
DRM2 data flow

## Slide 15
SELI2C
slow control link
A1500
PXL_D
PXL_A
A3818
NI8451
GBTx I2C master
I2C
I2C
slave
GBTx control
I2C
decoder
control signals
I2C
Igloo2
GBTx interface
data / trigger
A1500
INTERFACE
CONET2
INTERFACE
local bus
GBTx
PCIe
USB
ETH
SSRAM
BRAM
FIFOs
FIFOs
FIFOs
VME
VME int
TRMs
DRM2 firmware blocks

## Slide 16
DRM2 now

## Slide 17
DRM2
DRM1
GBTx test board
DRM1 to DRM2 migration

## Slide 18
Before designing the DRM2 we developed a prototype device with limited features (no VME) which allowed us to extensively test GBTx and Igloo2 features
IGLOO2
GBTx
VTRx
SSRAM
A1500
(Linux ARM)
BER <= 10-14
(80m long optical fiber)
total jitter on the GBTx received clock is ~ 50 ps
First step towards DRM2: GBTx test board

## Slide 19
Main regulators,
switching
LDO
GBTX-VTRX
LDO
Hardware
3V3GBTX
3V3HW
1V2 FPGA
P2V5GE
P2V5FS
P1V2FS
P1V5FP
FPGA: 3V3 power supply
P1V2FD: FPGA CORE power supply, 1V2
P3V3HW: Other FPGA power supply
P2V5GE: ELINK blocks power supply
P2V5FS(C): PLL power supply
P1V2FS: SERDES core power supply
P1V5FP: FPGA bank 2, GBTX controls
SFP
CONET2
I2C
SCA
(piggyback)
GBTX
VTRX
GBTX VTRX power supply (5+1)
DIN
DOUT
Controls
A1500
GBTX
VTRX
4,5Gbps
optic
GBTx test board block diagram

## Slide 20
Documentazione

## Slide 21
GBTX in ALICE DRM2:
Ricetrasmettitore bidirezionale
Interfacciamento diretto FPGA-ePort.
Due uscite di clock usate.
Funzioni di monitoraggio e controllo attraverso EC/IC non utilizzate (per ora)e no GBT SCA. Controllo GBTX attraverso FPGA e I2C locale
Frame standard con correzione errori implementato nel GBTX
Alcune caratteristiche del GBTX:
Può essere configurato per essere:
  un ricetrasmettitore bidirezionale
  un trasmettitore unidirezionale
  un ricevitore unidirezionale.
Interfacciamento all’elettronica di front-end tramite 40 ePort
  3 linee differenziali per ePort: ingresso , uscita, clock
Ampie funzioni per il controllo del timing e dei clock. 8 uscite di clock
Funzioni di monitoraggio e controllo tramite sezione di slow control nel frame (EC/IC) e GBT-SCA. Il GBTX è in grado di funzionare stand alone.
Altissimo livello di correzione degli errori da SEU, 3 tipi di frame: standard, esteso, 8b/10b
GBTx on DRM2: choices

## Slide 22
Phase – Aligners + Ser/Des for E – Ports
GBT – SCA
E – Port
Phase - Shifter
E – Port
E – Port
E – Port
E – Port
CDR
DEC/DSCR
SER
SCR/ENC
I2C Master
I2C Slave
Control Logic
Configuration
(e-Fuses + reg-Bank)
Clock[7:0]
CLK Manager
CLK Reference/xPLL
External clock reference
control
data
One 80 Mb/s port
I2C (light)
JTAG
JTAG
Port
GBTIA
GBLD
GBTX
e-Link
clock
data-up
data-down
ePLLTx
ePLLRx
clocks
I2C GBTX
I2C AUX
SFP
CONET2
SERDES
transceiver mode
4 output clocks
I2C
no SCA
40 e-Links @80 Mb/s
GBTx on DRM2: choices

## Slide 23
Power supply

## Slide 24
VDDIO
2.5V VTRx
VDDCM+VDDPS
VDDTX
VDDRX
VDD CORE
Power supply (GBTx test board)
3,3V
Jumper
Alimentazioni separate su ogni ramo

## Slide 25
VDDIO
2.5V VTRx
VDDCM+VDDPS
VDDTX
VDDRX
VDD CORE
Power supply (GBTx test board)
3,3V
Jumper
VDDRX unita a VDDTX
VDDCORE unita a VDDIO
VDDCM/VDDPS da sola

## Slide 26
VDDIO
2.5V VTRx
VDDCM+VDDPS
VDDTX
VDDRX
VDD CORE
Power supply (GBTx test board)
3,3V
Jumper
VDDRX unita a VDDTX e VDDCM/VDDPS
VDDCORE unita a VDDIO

## Slide 27
VDDIO
2.5V VTRx
VDDCM+VDDPS
VDDTX
VDDRX
VDD CORE
Power supply (GBTx test board)
3,3V
Jumper
Tutti i rami di alimentazione collegati a un solo LDO

## Slide 28
Power supply (GBTx test board)
VDDIO
2.5V VTRx
VDDCM+VDDPS
VDDTX
VDDRX
VDD CORE
Heatsink
I2C voltage current sensor

## Slide 29
Power supply (GBTx test board)

## Slide 30
Power supply (DRM2)
VDDTX
VDDRX
VDDIO
VDDCM
VDDPS
VDD CORE
one 1.5V regulator
max ~800 mA
one 1.5V regulator
max ~700 mA
2.5V VTRx
current sensor

## Slide 31
GBTx configuration pins
GBTx
configSelect
efusePower
efuseWritePulse
I2c address
4
mode
4
refClkSelect
rxDataValid
rxLockMode
rxRdy
autoReset
stateOverride
txDataValid
txRdy
ldReset
ldScl
ldSda
testClockOut
testOutput

## Slide 32
GBTx configuration pins

## Slide 33
GBTx configuration pins
Set MODE[3:0] as desired (check GBTX manual; 8b/10b mode is implemented but not tested);
RXLOCKMODE[1:0] = 2’b01 (The Automatic DAC frequency calibration is highly recommended)
STATEOVERRIDE pull down to GND (debug pin)
CONFIGSELECT
  Tie to VDD if I2C
  Tie to GND if IC channel
REFCLKSELECT:
  Tie to GND in order to select the xPLL/xOSC clock (only for the internal state machines. The clock used by the high-speed SERDES is selected by the internal register 281, cmReferenceClockSelect[1:0]; check chapter CLOCK MANAGER in the GBTX manual)
  Tie to VDD in order to use externalClk (REFCLKPIN)
GBTX_TXDATAVALID: if high, the 4.8Gb/s header is DATAVALID (this only changes the header; user selectable)
SLVSTESTINJECT
  This pin is also called AutoReset; it is active high and will enable the auto reset, timeout feature; recommended to be HIGH
RESETB: several ways to perform the power-on reset (reset is active LOW)
  During debug stage add an on-site push button
  Use a RC network (connected to VDD) to provide a time delay – you can add extra footprints in the PCB for bigger caps, the values will depend on the risingslewrate of VDD
  Use a “POWER_GOOD” signal from a DC-DC that is powering the GBTX (e.g., can be FEAST DCDC ASIC is used)
SCCLK, SCIN and SCOUT used for SCA; tie SCIN if the SCA is not used
Disable JTAG and remove it from the daisy-chain. Set TRESETB to GND, tie all inputs
GBTX_TESTCLOCKOUT and GBTX_TESTOUTPUT can be helpful during debugging process; you can connect a testpoint to it (they are CMOS outputs)
GBTX_TESTCLOCKIN1, GBTX_TESTCLOCKIN2 are debug pins; tie either to VDD or GND
9.3.1.1 Lock mode selection
Important note: During production testing, it has been found that in some chips the reference PLL frequency calibration mode does not work (RXLOCKMODE[1:0]=2’b10). So for yield reasons, the users should not use this mode and must use the DAC frequency calibration (RXLOCKMODE[1:0]=2’b01).

## Slide 34
GBTx configuration pins

## Slide 35
GBTx configuration pins

## Slide 36
GBTx
Igloo2
all GBTx configuration signals are hardwired, except configselect and resetb
  GBTx I2C pins available also on a strip for debug
  GBTx JTAG port disabled
GBTx configuration pins

## Slide 37
GBTx configuration pins
GBTx
configSelect
efusePower
3.3V during fuse prog, 1.5V otherwise
efuseWritePulse
I2c address
4
mode
4
“0010” = FEC transceiver
refClkSelect
rxDataValid
rxLockMode
rxRdy
autoReset
stateOverride
‘0’ = PS FSM always on
txDataValid
txRdy
ldReset
ldScl
ldSda
Igloo2 selects I2C
‘0’ = XOSC
“01” = DAC frequency calibr
“1000”
‘1’ = avoid unpredicted state at startup
testClockOut
testOutput

## Slide 38
GBTx e-Fuse pins

## Slide 39
the strip connector J813 allows to program the GBTx e-fuses
We developed a custom dongle for programming the GBTx E-Fuses
NON implementato in GBTX test board
GBTx e-Fuse pins

## Slide 40
GBTX
I2C interface
EFUSE voltage enable
EFUSE program pulse
3.3V
1.5V
GBTX
I2C
EFUSEPROGRAMPULSE
EFUSEPOWER
FPGA
EFUSE
DONGLE
E-fuse burning sequence:
Connect the eFuse dongle. This small device is a safety pass through for the pulse signals and a switch for the 3.3V for the GBTx programming, without which it is not possible to burn the eFuses.
Start the programming in the Labview I2C GBTx software, via the I2C interface this program execute this sequence:
  Enable the 3.3V for programming
  Set the EFUSE address and data through the GBTX I2C
  Enable the programming pulse monostable
  Repeat the phase 2 and 3 for every register and for the updateEnable register #366 to enable the EFUSE reading during startup
GBTx e-Fuse (burning dongle)

## Slide 41
GBTx e-Fuse (VI I2C)

## Slide 42
GBTX E-links

## Slide 43
FPGA
GBTx
DI[39:0]_P
DI[39:0]_N
DO[39:0]_P
DO[39:0]_N
bank 5
bank 8
FPGA – GBTx connection consists of a single 40-bit large parallel lane.
The data connection is direct, without any external polarization resistors in both directions (tested already on the GBTx test board)
The choice of 40 E-links@80 Mbps comes from conservative reasons and we went directly for the “smoothest” solution
@80 Mb/s
LVDS
SLVS
SLVS
100-ohm input terminations enabled
GBTx E-Links
Igloo2
GBTx
40
40
clock @ 40 MHz
@ 80 Mb/s
100-ohm input terminations enabled

## Slide 44
GBTx E-Links: eportTX (dataOut)

## Slide 45
GBTx E-Links: eportRX (dataIn)

## Slide 46
GBTx E-Links: schematic
FPGA
FPGA
TIPO | PS | HoutV max | VOD min | VOCM max
LVDS | 2,5 | 1,600 | 0,250 | 1,375
B-LVDS | 2,5 | 1,600 | 0,065 | 1,500
M-LVDS | 2,5 | 1,600 | 0,300 | 2,100
Mini-LVDS | 2,5 | 1,6 | 0,300 | 1,600
RSDS | 2,5 | 1,6 | 0,600 | 1,500
GBTx RX | 1,5 | Max PS+0,3 (in) | < 0,050 (in) | Max PS+0,3 (in)
TIPO | PS | VID min | VICM min
LVDS | 2,5 | 0,100 | 0,050
B-LVDS | 2,5 | 0,100 | 0,050
M-LVDS | 2,5 | 0,050 | 0,300
Mini-LVDS | 2,5 | 0,100 | 0,300
RSDS | 2,5 | 0,100 | 0,300
GBTx TX | 1,5 | 0, 330 (out max) | 0,110 (out)
COMPARAZIONE I/Os IGLOO2, GBTX out to IGLOO2 input
COMPARAZIONE I/Os IGLOO2, IGLOO2 out to GBTX input
VOCM (Volt common mode in uscita)
HoutV (tensione in uscita livello alto)
VOD (Volt differenziali in uscita)
VID (Volt differenziali in ingresso)
VICM (Volt common mode in ingresso)
GBTx
GBTx
?
2,6mA@, 2mA@10 su 100Ω
Differential lines
GBTx  IGLOO2
GBTx E-Links

## Slide 47
Termination schemes on GBTx test board
GBTx E-Links

## Slide 48
GBTx E-Links

## Slide 49
GBTx
Igloo2
GBTx E-Links: layout
trace length equalization down to …
Recommendation:
do not use vias at all if possible

## Slide 50
Of all the 40 DCK coming from the E-Link clocks, just one (DCLK0) is connected to the FPGA. All the others are left unconnected.
GBTx e-Link clock
Igloo2
GBTx
40
40
clock @ 40 MHz
@ 80 Mb/s
@ 80 Mb/s
no need to use the internal phase aligner on the uplink

## Slide 51
Clock distribution

## Slide 52
Clock distribution
GBTx input clock
no input clock to the GBTx on the DRM2 board

## Slide 53
Clock distribution
GBTX test board

## Slide 54
Clock distribution
DRM2
local 40 MHz quartz
clocks from GBTx PS
MAX9310
(from DRM1)
Igloo2
Igloo2
to TRMs
from Igloo2

## Slide 55
IDEA: a logical block, on the Igloo2, synchronous with the internal oscillator checks the availability of the GBTx clock (by checking the value of a counter clocked on GBTx PS clock). When the GBTx PS clock is missing, the local 40 MHz quartz clock is chosen (not OK for physics)
Clock distribution
40 MHz quartz
clock from GBTx PS
clock to Igloo2 and TRMs
CLK_SEL (from Igloo2)
40.079 MHz
40.00 MHz

## Slide 56
VTRx

## Slide 57
VTRx
GBTx
GBTx
GBTX test board
DRM2 board
VTRx cage

## Slide 58
GBTx
VTRx
VTRx

## Slide 59
GBTx
VTRx
aluminum cage
VTRx cage

## Slide 60
VTRx
VI GBTX test board

## Slide 61
VTRx
VI EXT I2C DRM2

## Slide 64
*** RESET LUNGO per problemi allo startup
*** Problema WATCHDOG su registri
*** Startup state machine

## Slide 65
Others points
GBTx I/O IBIS models not available
Troubleshooting
Disable JTAG (set TRSETB = 0)
testClockOut and testOutput can be helpful for debugging process
https://espace.cern.ch/GBT-Project/VLDB/Working%20documents/
GBT_Support_Question_tree.pdf

## Slide 66
https://espace.cern.ch/GBT-Project/GBTX/Manuals/GBTX_Production_Package/maximumReflowCondition.pdf
Soldering profile