## Slide 1: High-speed FPGA-based Serial Links
Raffaele Giordano
Università degli Studi di Napoli “Federico II”, I-80126, Italy, and
INFN Sezione di Napoli, I-80126, Italy
Presenter email: rgiordano@na.infn.it

## Slide 2: About the Presenter
Since 2007 - Contributed to R&D of electronics for TDAQ in Nuclear and Subnuclear Physics experiments, including ATLAS, RD51, Belle2 and SuperB
Since 2016 - RTD-A at Department of Physics of the University of Naples «Federico II»
Since 2016 - Principal Investigator for the ROAL project (RecOnfigurable self-repairing and Adaptive high-speed Links) funded by the Italian Ministry of Education, University and Research in the framework of the 2014 Scientific Independence of young Researchers (SIR) program
Notes: 2010 – PhD in Fundamental and Applied Physics at University of Naples «Federico II»

## Slide 3: Overview
Introduction: why serial transmission?
  FPGAs and High-speed IOs
Anatomy of a FPGA-Embedded SERDES: The GTP Transceiver
Line Coding
Fixed Latency data transmission
Applications
  G-Link Emulation for the ATLAS Experiment
  (optional) A lightweight JESD204B core for remote applications

## Slide 4: why serial transmission?

## Slide 5: Why Serial Transmission ?
W.r.t. parallel transmission, serial transmission has
  Advantages
    Simplified PCB layout and routing: fewer signals, fewer layers needed, smaller PCB
    Fewer IO pins on components
    Embedded clock => no clock/data skew to be managed
    Higher data rates (several Gbps)
  Drawbacks
    Latency
    Complexity of the transmitter and receiver
Parallel
Serial

## Slide 6: SERializers-DESserializers
SERDES make is possible to
  Encode, serialize and trasmit data
  Recover a clock from the incoming data stream and use it to…
  …receive, deserialize, align and decode data
FIFOs included since transmission clock and recovered clock usually do not match system clock
Modern FPGAs support HSS IO via embedded SERDESes
REC
CLK
DATA
DATA
Basic Block Diagram of a SERDES

## Slide 7: Anatomy of a FPGA-EMBEDDED SERDES: The GTP Transceiver

## Slide 8: High-Speed FPGA-embedded SERDESes
Main Vendors: Xilinx, Altera, Microsemi, Lattice, we focus on Xilinx
Xilinx Virtex 5, Spartan 6 and Artix 7 Family include GTPs transceivers :
  High data-rate: Up to 3.125 Gb/s
  Low power: 100 mW @ 3 Gb/s
  Up to 24 in a single FPGA
  Many customizable features (e.g. word width : 8,10,16 and 20 bits)
  8b10b encoding native support
  They are available as a hard macro or “tile”
Notes: Picture of V5 FPGA with GTPs

## Slide 9: GTP Placement
GTP tiles are in 1 column on right of die
Each tile has 2 transceivers plus:
  Shared resources, including PLL
  1 set of bonded out reference clock pins
  1 set of dedicated power pins
  CRC-32 blocks for TX and RX
Virtex 5 50T floorplan
Generic IOs
Notes: GTP transceiver are ‘twins’

## Slide 10: GTP Architecture: “Dual” Tile
Two Tx/Rx pairs per tile
Shared components: PLL, clocking, reset, power, DRP
Dedicated clock routing and differential buffer
Several clocking schemes can be chosen, depending on input word width, data-rate, latency requirements etc.
FPGA
Fabric
FPGA
Pins

## Slide 11: The Shared PLL
The PLL generates a high speed clock for the serial section
  Between 1.0 GHz and 2.2 GHz
  Requires a low jitter reference clock
  Also requires a clean power supply
  Provides lock flag (PLLLKDET)
Notes: Main role of shared PLL: generate serial clock out of reference clock by multiplying it up
Advantage: only one PLL for two GTP transceiver (less power and area)
Disadvantage: two GTP transceiver transmit and receive data rates are [1, 2, 4] of each other (restriction)

## Slide 12: Internal datapath width
Tile datapaths can be 8 bits or 10 bits wide
  10 bit wide datapaths required for 8B/10B
  10 bit or 8 bit datapath can be used w/o encoding
  INTDATAWIDTH = 0 -> 8 bit internal datapath
  INTDATAWIDTH = 1 -> 10 bit internal datapath
Datapath width impacts all parallel blocks in tile
Shared PLL includes divider to account for internal datapath width
Notes: Main role of shared PLL: generate serial clock out of reference clock by multiplying it up
Advantage: only one PLL for two GTP transceiver (less power and area)
Disadvantage: two GTP transceiver transmit and receive data rates are [1, 2, 4] of each other (restriction)

## Slide 13: GTP Architecture: Transmitter
1 serial clock domain and 3 Parallel clock domain (colors mark clock domains)
2 clocks provided by the fabric (TXUSRCLK/2), 2 clocks from the PLL for internal operations(HSCLK and XLCK)
FIFO or phase align-circuitry to enter the internally generated clock-domain (XCLK)
TX
Driver
PISO
FIFO
8b
/
10b
FPGA
Interface
TXDATA
TXUSRCLK2
Parallel Clock
(XCLK)
Serial
Clock
Parallel Clock
(TXUSRCLK)
differential pair
Serial Section (PMA)
Parallel Section (PCS)
Bypass if
phase adjusted
Dedicated
differential
clock input
(REFCLKIN)
Dedicated
routing
FPGA fabric
0
0
0
1
1
1
0
0
00111000
TXUSRCLK
REFCLKOUT
Phase
Adjust
Package
Pins
TXOUTCLK
CLKIN
Shared
PLL

## Slide 14: FPGA TX Interface
Available data widths are 8,10,16, and 20 bits
  Available widths determined by internal data path width
Must provide two parallel clocks
  TXUSRCLK and TXUSRCLK2
  Edge aligned and TXUSRCLK2
    For double widths (16,20 bits) toggles at half the frequency (f/2) w.r.t. TXUSRCLK (f), for single width (8,10 bits) same frequency
TX Reset

## Slide 15: TX Data Width
INTDATAWIDTH controls width of internal datapath
  Can be 8 bits or 10 bits wide
  10 bits required for 8B/10B
TXDATAWIDTH port controls width of FPGA TX Interface
  If 8B/10B is turned on:
    TXDATAWIDTH = 0 : 8-bit FPGA TX interface
    TXDATAWIDTH = 1 : 16-bit FPGA TX interface
  Otherwise (no encoding):
    TXDATAWIDTH = 0: FPGA TX interface = internal datapath width
    TXDATAWIDTH = 1: FPGA TX interface = 2 x internal datapath width

## Slide 16: Clocking TX Data
TXUSRCLK/TXUSRCLK2 must come from refclk oscillator
  They may be divided, multiplied, or out of phase, but need to have a fixed phase relationship w.r.t. refclk
  If they come from another oscillator, the fabric TX clocks (TXUSRCLK/TXUSRCLK2) will not stay aligned to the internal TX clocks (XCLK, Serial TX Clock)
GTP has 2 options for sourcing TXUSRCLK/TXUSRCLK2
  TXOUTCLK
  REFCLKOUT

## Slide 17: Parallel Clock Sources
REFCLKOUT is a copy of CLKIN
  It is freerunning
    (doesn’t stop when the PLL stops)
  It may need to be divided or multiplied to get TXUSRCLK/TXUSRCLK2 rates
TXOUTCLK0/1 is a copy of XCLK
  It runs at the TXUSRCLK rate
    You may need to /2 to get TXUSRCLK2
  It is not freerunning
  It must not be used when the TX Phase Alignment circuit is in use (more on this later)
Notes: Explain here the different sections starting with the shared PLL and its main role.
Point out Reset Control and it’s sequencing features.

## Slide 18: 8B10B Byte Swap
TX Datapath includes a bypassable 8B10B encoder
  Bypass to reduce latency
8B/10B encodes 8 parallel bits into 10 serial bits
  The order of the serial bits is bit ‘a’ (leftmost) first
GTP sends rightmost bit first
  Encoder flips encoded output to send bit ‘a’ first
  When using 2-byte interface, bytes must also be flipped
    First byte for transmission must be on TXDATA[7:0]

## Slide 19: TX Buffer/Phase Alignment
Let us suppose that XCLK and TXUSRCLK are same frequency, but not guaranteed phase aligned
For data to pass from TXUSRCLK domain to XCLK domain
  Must use the TX Buffer (Phase Adjust FIFO) - or -
  Must force TXUSRCLK and XCLK to be in phase (phase alignment circuit)
TX
Driver
PISO
FIFO
8b
/
10b
FPGA
Interface
TXDATA
TXUSRCLK2
Parallel Clock
(XCLK)
Serial
Clock
Parallel Clock
(TXUSRCLK)
differential pair
Serial Section (PMA)
Parallel Section (PCS)
Bypass if
phase adjusted
Dedicated
differential
clock input
(REFCLKIN)
Dedicated
routing
FPGA fabric
Package
Pins
Shared
PLL
TXUSRCLK
REFCLKOUT
Phase
Adjust
TXOUTCLK
CLKIN

## Slide 20: Phase Alignment Circuit
Complications
  TX Phase alignment affects TX for both GTPs on tile
    TXUSRCLK and XCLK must be same on both GTPs
  TXOUTCLK phase driven by phase alignment
    TXOUTCLK cannot be used to drive TXUSRCLK
      Circuit will attempt to make phase of clock equal
      If TXOUTCLK is used, XCLK will always be chasing TXUSRCLK but will never catch up
Benefits
  Latency is lower when TX Buffer is bypassed
  Latency is also fixed (even after a power cycle)
  Can be used to channel-bind lanes

## Slide 21: Built in PRBS
PRBS = Pseudo Random Bit Sequence
  Appears random, so behaves like real data
  Deterministic, so you can check the results
  Has properties such as run length
    Can be used to prove out channel for specific protocols
PRBS Generator can be used to test channel
  Does PRBS-7, PRBS-23, and PRBS-31
  Takes over channel when turned on
Matching checker in RX side

## Slide 22: TX Pre-emphasis
Physical channels tend to act as low pass filters
  High frequencies get attenuated more than low frequencies
Pre-emphasis equalizes the signal through the channel by providing more power for the high frequency parts of the signal
In time, this looks like overshoots on the quickly changing parts of the signal

## Slide 23: TX Pre-emphasis (2)
no pre-emphasis or equalization
The signal here is the eye of a PRBS-31 pattern at the RX side of a 76 cm FR4 channel
with pre-emphasis and equalization

## Slide 24: TX Driver and OOB
Most PCBs are designed for 50 or 75 ohm traces
Matching the source impedance to the trace minimizes signal distortion due to reflection
Can be set individually for each transceiver at to 50 or 75
Impedance is calibrated by a high precision resistor
Xilinx HSSIOs use Current Mode Logic signaling
  Differential around a common mode voltage
  Non-differential signals are also possible (OOB signals)

## Slide 25: Questions?

## Slide 26: GTP Architecture: Receiver
RXRECCLK
Like for the Tx, 1 reference clock, 2 input clocks and same internal clocking architecture
Comma detector/aligner (optional)
FIFO or phase align-circuitry to enter the user-clock domain (RXUSRCLK)
CLKIN
Shared
PLL
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
RXDATA
RXUSRCLK
RXUSRCLK2
Serial
Clock
Parallel Clock
(XCLK)
Parallel Clock
(RXUSRCLK)
Clock Divider
Bypass if
phase adjusted
Serial
Section
Parallel Section
Phase Adjust
Differential
pair
REFCLKOUT
Dedicated
clock input
(REFCLK)
FPGA fabric
1010101010101010101101010100111000
0
0
0
1
1
1
0
0
10110101010101010101011010101
Package
Pins

## Slide 27: CML RX and Equalization
CML = Current Mode Logic receiver
  Differential current flow determines logic level
  Optional built in AC coupling
  Built in termination resistance: 50 or 75 ohms
  Termination reference can be controlled
    Allows ground reference for PCI Express
GTP has configurable linear RX Equalization
Notes: I think it would be good to show here the diagram out of the UG
Slides 30&31 content could be on notes handout

## Slide 28: RX Equalization
As discussed in TX, channels act as low pass filters
  RX Eq. boosts high frequency signals to compensate
GTP Equalization mixes regular input (wideband) with output of a high pass filter
  Result is an equalized signal
  Can control mix ratio and cutoff for high pass filter

## Slide 29: Electrical Idle detection
Electrical Idle (OOB signal) is transmitted by driving the differential serial lines to the same value
  Differential voltage drops to 0
  Detect by checking that differential voltage
    Must be within predefined distance from 0 differential volts

## Slide 30: Rx CDR
CDR = Clock/Data Recovery
  Takes the serial stream and recovers a clock
  Uses locally divided PLL Clock to get RX Line Rate
  The CDR locks using a phase rotator
    Rotates phase to match PLL Clock to incoming transitions
  Can tolerate +/- 350 ppm clock difference
  Tolerates spread spectrum clocking

## Slide 31: Interpolator based CDR
Local Oscillator (LO) generates the clock
Phase Detector (PD) recognizes if the sampling point is in the optimal position
The Interpolator controls the clock frequency
a Flip Flop resamples the signal
Interpolator
Clk+/-100ppm
LO
PD
FF
Recovered data
Incoming data
Recovered clock

## Slide 32: SIPO (Serial In Parallel Out)
Parallel width = internal datapath width
Crosses boundary between serial RX clock and XCLK

## Slide 33: PRBS Checker
Pairs with Tx PRBS
Checks incoming data for PRBS errors
  Supports PRBS-7, PRBS-23, and PRBS-31
  Self-synchronizes to selected pattern
  Counts deviations from the pattern
  Has programmable error thresholds
  Does not otherwise affect incoming data

## Slide 34: Comma Align/Detect
The block searches for commas in the incoming data
When it finds one, it shifts the mapping from in to out
Shifts comma to be aligned to closest valid boundary
  Closest = least shifting required
  Valid = depends on ALIGN_COMMA_WORD setting
Aligns incoming data to byte (or word) boundaries
Possible to join two 10-bit commas to form a 20-bit comma (aligns on word boundaries)

## Slide 35: Manual Alignment
RXSLIDE signal to manually adjust comma alignment
  Must be de-asserted for 2 cycles after each use

## Slide 36: 8B10B decoder
Decodes incoming 8B/10B data
  Reports errors when they occur
  Can be bypassed to reduce latency
Byte swap required for 2 byte interfaces due to serialization order (same as the TX)

## Slide 37: RX Elastic Buffer
Performs 3 important functions:
  Phase alignment
    Can be replaced by phase align circuit in some cases
  Clock Correction
  Channel Bonding

## Slide 38: Phase Alignment
RX clock domains similar to TX
  Fabric provides RXUSRCLK and RXUSRCLK2
  CDR provides RX Serial Clock and RX XCLK
CLKIN
Shared
PLL
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
RXDATA
Receiver Unit
RXUSRCLK
Serial
Clock
Parallel Clock
(XCLK or RXUSRCLK)
Parallel Clock
(RXUSRCLK)
Divider & Shifter
RXSLIDE
PMA
PCS
RXRECCLK
Seed
Clock
HSCLK
Package
Pins
Phase Adjust
XCLK
RXUSRCLK2
Notes: Point out that this is one GTP channel, IMHO correlated numbering is excellent

## Slide 39: Phase Alignment Circuit
Buffer bypass ok if no Clock Correction or Channel Bonding
  Requires use of phase align circuit, similar to TX
  Unlike TX, each RX has an individual phase align circuit
Bypass RX Buffer
  Advantage = reduced latency, more deterministic latency
  Disadvantage = must initialize phase align before use, more complex

## Slide 40: Phase Alignment Circuit (2)
Phase align circuit forces SIPO phase (XCLK) to match RXUSRCLK
Dedicated GTP input port (RXPMARESETPHASE)
Shared
PLL
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
RXDATA
Receiver Unit
RXUSRCLK
Serial
Clock
Parallel Clock
(RXUSRCLK)
Parallel Clock
(RXUSRCLK)
Divider & Shifter
RXSLIDE
PMA
PCS
RXRECCLK
Seed
Clock
HSCLK
Package
Pins
Phase Adjust
XCLK
FPGA fabric
RXUSRCLK2
Notes: Point out that this is one GTP channel, IMHO correlated numbering is excellent

## Slide 41: Clock Correction (1)
Data crosses phase boundary from XCLK to RXUSRCLK
May also have to cross a frequency boundary
  This can occur when separate oscillator generates the data
RXUSRCLK ≠ XCLK -> Clock Correction required

## Slide 42: Clock Correction (2)
Allows RX Buffer to be used to cross frequency boundary between XCLK and RXUSRCLK
CC circuit searches incoming data for a pre-defined sequence
  When sequence is found CC event can be triggered
  Trigger happens if buffer too full or too empty

## Slide 43: Clock Correction: Slow down
Write clock faster than read clock
Slowing the effective write rate to compensate the little difference between recovered and local oscillator frequency
Clock Correction Sequence
Alarm: FIFO almost full!
Remove CC symbol
Removing the Clock correction Sequence when the FIFO is almost full

## Slide 44: Clock Correction: Speed Up
Read clock faster than write clock
Speed up the write data rate to compensate the little difference between recovered and local oscillator frequency
Clock Correction Sequence
Alarm: FIFO almost empty!!
Add CC symbol
Adding the Clock Correction Sequence when the FIFO is almost empty

## Slide 45: Channel Bonding
Sometimes we need several serial lanes, and we need them stay synchronized
CB circuit searches incoming data for CB sequence
  One lane is master, remaining lanes are slaves
  Transmitter lanes all send CB sequence at same time
  When CB active, when master finds CB sequence, informs slaves
  Slaves attempt to find same sequence in their RX Buffer
  If sequence found, slaves adjust FIFO pointers to remove skew

## Slide 46: Channel Bonding
RX Buffer aligns CB sequences removes skew between lanes
Channel bonding
sequence
Moving reading pointer
position inside the FIFO
Aligned parallel data
With increased width
GTP1
GTP2
GTP3
FIFO
FIFO
FIFO

## Slide 47: FPGA RX Interface
Same data widths as TX
Clocking options similar to TX
  Drive RXUSERCLK and RXUSRCLK2 using TX clocks
  Drive RXUSRCLK using RXRECCLK
    RXUSRCLK2 can use RXRECCLK or RXRECCLK2, depending on RXDATAWIDTH setting
Deserialization order same as TX
RXRESET Resets the PCS

## Slide 48: FPGA RX Interface
RXRECCLK is the recovered clock from the CDR
  It runs at the RXUSRCLK rate
  Can be cleaned up before use using CMT PLL

## Slide 49: FPGA RX Interface

## Slide 50: Questions?

## Slide 51: Parallel to Serial 4:1 interface example
PLL
CLK
CLKx4
Divider by 4
Parallel data
d1
d2
d3
d4
d1
d2
d3
d4
Fabric
FPGA
Fabric
clock
Output Serial Data
FPGA

## Slide 52: It does not work
In commercial Tx HSSIO the clock is provided from the board, and not from the FPGA core
We can measure the clock coming from the core is jittered, while the clock coming from the board is much more clean
If we use the jittered clock to serialize data, many errors occur (higher Bit Error Ratio)
Notes: DIRECTIONAL INTERFACE : clock and data travel in parallel and in the same direction

## Slide 53: Jitter grows in the clock tree
The latency in the repeater is function of the power supply. If the power supply is noisy, the latency is modulated. Phase modulation is synonymous of jitter.
  Power supply noise: each buffer (repeater) adds some jitter to the clock
  As consequence a dedicated clock tree is always preferred respect to a common core clock tree
The strong relationship between jitter and latency
  The space between buffers depends from the number of loads allowed per each buffer. In the dedicated clock distribution the loads are few and few repeaters are needed
to GTP1
repeater
to GTP2
repeater
The clock coming from the board
The clock coming
from the board
to fabric FFs

## Slide 54: Core Noise
What is Core Noise ?
  Core noise is noise on the Core Voltage supply of the FPGA. This is VCCINT in the case of the Xilinx FPGAs
Topics related to causes of Core Noise
  Simultaneously Switching Flip-Flops and Instantaneous Current
  Simultaneous Switching and Core Noise Correlation
  Core Noise from Switching and Its Relationship to Jitter

## Slide 55
Core Noise and its Causes
Core noise is induced any time a signal switches
  Capacitance is being charged, requiring an instantaneous current
  Instantaneous current induces a voltage in the core supply due to change in current through the package inductance
Die
Package
Ground (Die)
Ground (Package)
VCCINT(Die)
ICCINT
ICCINT
VCCINT(Die)
VCCINT(Die)
VCCINT(Die)
VCCINT(Package)

## Slide 56: Questions?

## Slide 57: Why a Line Coding?
If there are enough transitions in the data then the clock can be recovered from the data using the CDR
Line coding makes it possible to provide enough transitions
Moreover it normally minimizes running disparity (# of transmitted 1’s – # of 0’s)
DC-Balance, needed for AC coupling
CDR
PLL
DATA
CLOCK
PLL
Data w/
embedded clock
Flip-
Flop

## Slide 58: 8b10b Coding
Widely adopted industrial standard
  E.g. Ethernet, PCI Express, JESD204B
Maximum run length (n. of identical symbols) = 5
Running Disparity +1/-1=> DC Balance
8 bits => 256 different values
10 bits => 1024 different values
8B10B code is built out of:
  (5 to 6 bit code) + (3 to 4 bit code)

## Slide 59: 8b10b Coding (2)
Not all 1024 values are valid according to 8b10b
– For example “0100000011” has run length 6
For most 8b symbols a positive or negative RD 10b symbol is chosen according the current running disparity
So about 512 useful values are selected from 1024…
  …and there are still a few codes left

## Slide 60: 8b10b: K Characters
How do we use the left codes?
12 “Special” K Characters, some of which can be used as commas
  A comma is one or two symbols specified to be the alignment sequence
  K28.1, K28.5, and K28.7, contain the a special bit sequence (1100000 or 0011111) which cannot be obtained by combining any other two code symbols
  Very useful for alignment

## Slide 61: Conditional Inversion Master Transition
Agilent G-Link chip-set adopts the CIMT protocol
CIMT stream : sequence of 20-bit words
4-bit C-Field plus 16-bit D-Field (payload)
C-Field Flags each word as Control, Data or Idle
Idle words used to synchronize link and keep it phase locked when no data is transmitted
Master Transition guaranteed in the middle of C-Field
DC balance assured through Conditional Inversion

## Slide 62: Scrambling
At Tx data is XOR’ed with PRBS from LFSR
At Rx, scrambled data sets a twin LFSR and data is restored
Provides pseudo-random data, improves DC-balance of serial stream
Requires additional mechanisms for byte boundary alignment (e.g. header)

## Slide 63: Questions?

## Slide 64: References
«Virtex-5 FPGA RocketIO GTP Transceiver», Xilinx Inc., San Jose, Calif. USA, UG196 (v2.1) December 3, 2009
A. Athavale and C. Christensen, “High-Speed Serial I/O Made Simple,” Edition 1.0, Xilinx
N. Holland, “Interfacing Between LVPECL, VML, CML, and LVDS Levels,” Application Report SLLA120 - December 2002, Texas Instruments

## Slide 65: FIXED LATENCY

## Slide 66: Latency of a Serial Link
Often in instrumentation for Physics we need a predictable data transfer time (e.g. in Trigger systems)
The latency of a serial link is the delay between data at the input of the link and at the output (from A to B)
The phase of the recovered clock is not the same as transmitter clock
Latency may change after a power up of the link

## Slide 67: Latency Variations in Serial Links
Recovered clock

## Slide 68: Latency Variations in Serial Links (2)
Some of the possible reasons :
  FIFOs not always filled in with the same number of words before start being read (leads to mTp variation)
  multiplication and subsequent division of a clock => phase information lost! (leads to nTs variation)
  On the receiver recovered clock at line rate is divided to obtain the recovered clock for the parallel domain
  On the transmitter the same may happen with the reference clock

## Slide 69: Clock-related Latency Variations
Multiplying and dividing a clock frequency may lead to different phases
In the GTP
  Serial part is Double Data Rate => HSCLK is divided by 5
  For each alignment: clock phase shift ([0..4]*THSCLK)
  Barrel shifter: two logical alignments possible with the same clock phase

## Slide 70: A Closer Look to Manual Alignment
On odd RXSLIDE assertions => data is logically shifted, the clock is not shifted
On even RXSLIDE assertions => data is not logically shifted, but the clock is shifted by 2Ts

## Slide 71: Aligning for Fixed-Latency
FSMs checks the number of slides needed to align
  If even, slides the byte boundary and the alignment is achieved
  If odd resets the receiver and waits for a new lock
Double average lock time w.r.t. to variable latency
FSMs checks if the alignment is already correct (no slides needed)
  If so, the alignment is achieved
  If not, resets the receiver and waits for a new lock
Higher average lock time, simpler logic
Warning: in both approaches reference clocks at transmitter and receiver must be independent!
Roulette approach: odd slide rejection
Roulette approach: any slide rejection

## Slide 72: An 8b10b Fixed-latency Link
On Tx, latency is fixed by the phase alignment circuit
On Rx, comma alignment and 8b10b decoding had to be reimplemented in the fabric
  RXRECCLK is recovered with a predictable phase

## Slide 73: Comma Detector and Aligner
Comma detector searches for 10-bit commas and determines number of bit slides needed to align
Aligner implements roulette approach and drives RXSLIDE signal

## Slide 74: Latency Measurements
Two ML505 boards (V5LX50T)
Separate reference clocks (Freq. diff. < 100 ppm )
To ensure fixed-latency across power-cycles, the link is reset every 3 seconds

## Slide 75: Latency Breakdown
RX Latency
TX Latency

## Slide 76: Questions?

## Slide 77: Fixed-Latency References
R. Giordano, V. Izzo and A. Aloisio, “High-speed Deterministic-Latency Serial IO” book chapter in the open access book “Field-Programmable Gate Array”, InTech, May 31, 2017, DOI: 10.5772/67012
R. Giordano and A. Aloisio, “Protocol-independent, Fixed-latency Links with FPGA-embedded SERDESes,” 2012 JINST 7 P05004, doi 10.1088/1748-0221/7/05/P05004
R. Giordano and A. Aloisio, “Fixed-Latency, Multi-Gigabit Serial Links with Xilinx FPGAs,” IEEE Trans. on Nucl. Sci., vol. 58, no. 1, pp. 194-201, Feb. 2011, doi: 10.1109/TNS.2010.2101083
A. Aloisio, R. Giordano et al., “High-Speed, Fixed-Latency Serial Links with FPGAs for Synchronous Transfers,” IEEE Trans. on Nucl. Sci, vol. 56, issue 5, pages 2864 to 2873, October 2009

## Slide 78: G-Link Emulation for the ATLAS Experiment

## Slide 79: The G-Link Chipset
A widely used chip-set in TDAQ Systems of Particle Physics
  Used by Alice, ATLAS, Babar, CDF, CMS, Nemo, and many others
Fixed-latency data transmission and clock recovery
3.3 V supply, low power dissipation
  590 mW Tx, 660 mW Rx
On-chip encode/decode using Conditional Inversion Master Transition (CIMT) protocol
Wide range serial rate 260-1400 MBaud (user selectable)
5V tolerant TTL interface 16 or 17 Bits wide
Discontinued since more than ten years
  Issue for experiments using it and needing spares or needing to upgrade the off-detector electronics
Agilent HDMP-1032/1034 Transmitter/Receiver Chip Set

## Slide 80: Emulation of G-Link for ATLAS
The Datapath is a synchronous pipeline clocked by the Timing, Trigger and Control system (40 MHz LHC clok)
Phase deskew feature on TTrx
FPGAs plus Serializer/Deserializer pair (G-Link) have fixed latency
Links run at 800 Mbps, encoded payload width is 20-bit, protocol is Conditional Inversion Master Transition
Let us supppose we want to do it by means of GTPs
Development of a replacement for ATLAS L1 muon barrel trigger links from the detector to the counting room
G-Link
Tx
G-Link
Rx
Trigger Data
Notes: Data from the detector is processed by an FPGA and then serialized. On the far end of the fiber, data is deserialized and transferred to another FPGA.

## Slide 81: Recommended Clocking Scheme
On Tx, user clock obtained dividing the reference clock with a Delay Locked Loop
On Rx, user clock obtained dividing the recovered clock (again with a DLL)
Issue: both the Tx and Rx logic clocks are out of phase with respect to the board clocks
Minimize latency => skip FIFOs and use phase align circuits
Minimize jitter => use dedicated clock resources
Data in
Data out
Clock in
(differential
80 MHz)
Clock in
(differential
80 MHz)
Serial connection
Notes: TXUSRCLK and TXUSRCLK2, as well as RXUSRCLK and RXUSRCLK2, must have a minimized skew

## Slide 82: An original clocking scheme
Clock in
(single ended
40 MHz)
Data in
Data out
Clock in
(single ended
40 MHz)
Serial connection
On both Tx and Rx:
  Same DLL used to generate the reference clock (at 80 MHz) from the board clock (at 40 MHz)
  user clocks are the board clocks (with a negligible skew (1 ns) )
The Programmable Delay Line emulates the propagation delay between Tx and Rx board clocks (like it actually is in the TTC system)
However there is an issue, see next slides

## Slide 83: GTP Configuration for G-Link Emulation
CIMT coding => No 8b10b
CLKIN
Shared
PLL
TX
Driver
PISO
FIFO
8b
/
10b
FPGA
Interface
TXDATA
TXUSRCLK
TXUSRCLK2
Parallel Clock
(XCLK)
Serial
Clock
Parallel Clock
(TXUSRCLK)
differential pair
Serial Section
Parallel Section
Phase Adjust
TXPHASE
REFCLKOUT
Dedicated
differential
clock input
(REFCLK)
FPGA fabric
X
X
Minimize latency => No FIFO, phase align instead
Transmitter

## Slide 84: GTP Configuration for G-Link Emulation
No FIFO and 8b10b decoder
Idle words are not commas => No Comma Detect and Align
RXRECCLK
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
RXDATA
RXUSRCLK2
Serial
Clock
Parallel Clock
(XCLK)
Parallel Clock
(RXUSRCLK)
Clock Divider
Parallel Section
Phase Adjust
RXPHASE
differential pair
Clock
Divider
X
X
X
RXUSRCLK
Receiver

## Slide 85: Implementing CIMT with the GTP
On Tx, Encoding performed by FPGA logic
On Rx, CIMT Decoder plus word align logic
  CIMT decoder asserts error if C-Field is not valid
  In case of a error the next incoming word is shifted by one bit with respect to the current
  Process repeated until a valid C-Field is received
Orange blocks are FPGA logic

## Slide 86: Design Layout
Resource Occupation:
LUTs 561 ( 2%)
Registers 408 ( 1%)
Slices 265 ( 3%)
DCMs 2 (16%)
GTP 1

## Slide 87: Latency Test
Two off-the-shelf boards with Virtex 5 FPGAs (w/ embedded GTPs) connected with two 8 ns, 50 W coaxial cables
60-hour tests resetting alternately transmitter and receiver: Latency remained fixed for some ranges of phase difference between transmitter and receiver board clocks (Probably due to phase align circuit limitations)
transmitted
pulse
received
pulse
latency

## Slide 88: A closer look to clock phases
Phase difference Df=f2-f1 depends on internal GTP delays, DLL, clock buffers and interconnections
By constraining DLL placement, it is possible to keep Df below a certain value
Board
clock
Recovered clock
Shared
PLL
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
Serial
Clock
Parallel Clock
(XCLK)
Parallel Clock
(RXUSRCLK)
differential pair
DLL
f2
f1
GTP RX
Clock
Divider
Phase Adjust

## Slide 89: A closer look to clock phases (2)
In addition to the previous case, Df=f2-f1 depends also on stream phase relative to the board clock, Df can be as high as half a period
Phase align circuit could be unable to resolve such a big phase difference for any clock period (our case 25 ns)
In ATLAS no problem: TTC de-skew feature
Board
clock
CLKIN
Shared
PLL
SIPO
CDR
FIFO
10b
/
8b
Comma
Detect
and
Align
FPGA
Interface
Serial
Clock
Parallel Clock
(RXUSRCLK)
differential pair
DLL
f2
f1
GTP RX
Parallel Clock
(XCLK)
Clock
Divider
Phase Adjust

## Slide 90: Hybrid configurations Tests
1 off-the-shelf board with a GTP connected to a custom board hosting a G-Link Tx/Rx pair via coaxial cables
Successfully trasmitted from GTP to G-Link and vice-versa at 800 Mbps
  Both CIMT modes have been tested
Higher jitter on GTP, clock source and configuration is not optimal

## Slide 91: Serial Transfers on a custom backplane
We developed a custom backplane (RODbus) for fast-communication of 5 adjacent VME64x boards
We embedded it in a standard VME crate
Deployed it for the ATLAS RPC Read Out Driver
LVDS busses on J0
5-slot backplane, integrated in a VME64x crate
TTL busses on J2, terminated as VME
Front view
Rear view
Embedded RODbus

## Slide 92: Running @ 2.5 Gbit/s
LVDS links have been tested successfully with Xilinx Virtex5 GTP transceivers @ 2.5 Gbit/s
The backplane would allow to sustain an aggregate bandwith of 65 Gbit/s (26 point-to-point pairs)

## Slide 93: G-Link Wrap Up
GTP transceivers:
  High-Speed, low-power serial transfers
  Reconfigurability and large number of configuration options
  Fixed latency achievable
Successfully implemented and tested an FPGA based fixed-latency link for DAQ/Trigger applications
Successful test for local data transfers on a custom backplane at 2.5 Gb/s
Data-rates up to 12.5 Gb/s with latest devices

## Slide 94: Questions?

## Slide 95: G-Link Emulation: Reference
A. Aloisio, F. Cevenini, R. Giordano, V. Izzo, “Emulating The G-Link Chip Set With FPGA Serial Transceivers In The ATLAS Level-1 Muon Trigger,” IEEE Trans. on Nucl. Sci., vol. 57, issue 2, pages 467-471, April 2010, doi: 10.1109/RTC.2009.5322105

## Slide 96: A lightweight JESD204B core for remote applications

## Slide 97: The JESD204B Protocol
High-speed interface for data converters (ADCs/DACs)
2006, JESD204, single serial lane (released by JEDEC)
2008, JESD204A, multiple lanes up to 3.125 Gbps
2011, JESD204B, multiple Serial Lanes up to 12.5 Gbps, depending on physical layer, adds deterministic latency (subclasses 1 and 2)
Aimed at links over distances of few 10cm, Rx and Tx on same board
Requires dedicated LVDS signals between Tx/Rx in addition to serial lanes

## Slide 98: JESD204B Protocol: Subclasses
Subclass 0
  No master timing reference defined, no fixed latency between converter and FPGA/ASIC
Subclass 1
  Common timing reference signal (SYSREF) for both JESD204B link ends
Subclass 2
  Multi-purpose signal (SYNC*) is used also as a common timing reference for JESD204B link ends

## Slide 99: JESD204B Subclass 1
JESD204B signals
  serial streams or lanes
  device clocks (i.e. serial transceivers reference clocks)
  SYNC* used for Code Group Synchronization (CGS), byte boundary alignment in data link
  SYSREF used for timing synchronization (unique marking of device clock edges)
    Synchronous to device clocks

## Slide 100: JESD204B : State Diagrams
CGS

## Slide 101: Synchronization

## Slide 102: JESD204B Intellectual Properties
Many JESD204B IPs available for FPGAs
  Xilinx, Altera, ComCores, Design&ReUse
  Support the protocol in its most general form: configurable data rate and number of lanes, synchronization of different lanes, dynamic reconfiguration
  Complex blocks
  Expensive (>10k$)
In this talk we do NOT use JESD204B IPs
I will show a simple implementation with a single lane
JESD204B IP Core, Xilinx Inc., San Jose, Calif. (USA), [Online]. Available: http://www.xilinx.com/products/intellectual-property/1-5so323.html
JESD204B IP Core User Guide, Altera Corp., San Jose, Calif. (USA), [Online]. Available: https://www.altera.com/en_US/pdfs/literature/ug/ug_jesd204b.pdf
JESD RX/TX IP CORE, ComCores ApS, Horsholm, DK, [Online]. Available: http://www.comcores.com/JESD.html
JEDEC JESD204B IP core, Desig&Reuse S.A, Grenoble, FR, [Online]. Available: http://www.design-reuse.com/sip/jesd204b-controllerip-28162/
Some JESD204B IPs

## Slide 103: JESD204B Link: Initialization
JESD data arranged in multi-frames (sequence of K frames)
K is configurable

## Slide 104: Demonstrator
Firmware in FPGA handles JESD protocol (i.e. CGS, ILAS, and alignment monitoring)
*R. Giordano and A. Aloisio, "Fixed-Latency, Multi-Gigabit Serial Links With Xilinx FPGAs," in IEEE Transactions on Nuclear Science, vol. 58, no. 1, pp. 194-201, Feb. 2011. doi: 10.1109/TNS.2010.2101083
Simplified implementation of the general architecture:
  single remote FPGA, single ADC, 1 conversion channel
Conversion running at 200 MSps, 16 bits per sample, TI High-speed ADC (ADC16DX370)
1 JESD lane at 4 Gbps
ADC and jitter cleaner configuration

## Slide 105: Texas Instruments ADC16DX370
TI ADC16DX370
2 channels
16-bit, up to 370 MSps
1 or 2 serial lanes per channel
JESD204B subclass 1 and 0
SPI slow control

## Slide 106: Texas Instruments LMK04828B
TI LMK04828B
Up to 14 differential outputs
Up to 3 reference clock inputs
VCOs
  0: 2370 MHz to 2630 MHz
  1: 2920 MHz to 3080 MHz
Integrated RMS jitter on output 100 fs
Designed to lock on recovered clocks from serial links

## Slide 107: Kintex-7 GTX Transceivers
REFCLK
1 GTX receiver used in the Demo
Data rate depends on speed-grade and package

## Slide 108: Demo Boards
Texas Instruments
ADC16DX370EVM
Xilinx KC705
Texas Instruments
TSW14J10 (pass-through)

## Slide 109: FPGA Firmware Architecture
GTX
RX
RX
JESD204B
FSM
ADC16DX370
DECODE
FEC
LINK
16
16
REFCLK (@100 MHz)
JESD STREAM (4 Gbps)
RX DATA (15:0)
CHARISK (1:0)
COMMADET_EN
SYSREF
SYNC*
DATA_VALID
2
Vivado ILA

## Slide 110: FPGA Implementation
Logic Resources | Used/Available | Percentage
Registers | 3901/407,600 | 1%
LUTs | 3263/203,800 | 2%
BlockRAM | 2/445 | 1%
BUFGs | 5/32 | 15%
BUFGDS_GTEs | 1/8 | 12%
GTXs | 1/16 | 16%
Overall logic footprint occupation for both JESD and FEC link is tiny (2% per JESD lane)
Small FPGA needed
Available transceivers and their supported data-rate are the actual limit
Xilinx Kintex-7 325T
JESD-Link (1 lane)

## Slide 111: Configuring ADC and Jitter Cleaner

## Slide 112: Enabling the Link on ADC16DX370

## Slide 113: Test setup
Xilinx KC705 demo board
TI eval board w/ ADC and jitter cleaner plugged on KC705, via FMC connector
ADC and Jitter cleaner configured via SPI over USB connection on TI board
Tested functionality
TI ADC16DX370
EVM
Xilinx
KC705
SYNC*
JESD @ 4 Gbps
4V Power Supply for ADC EVM
Test signal generator
SPI over USB
JTAG
over USB

## Slide 114: JESD204B Link: Test Results
ILAS
CGS
Data
JESD Link
  Hardware test with Xilinx Vivado Hardware manager, virtual input output + integrated logic analyser
  JESD data arranged in multiframes (sequence of K frames)
  ADC replaces last octet of a frame (Dn) if Dn=Dn-1 with /A/ or /F/ 8b10b K symbols
  In Rx, alignment monitor checks /A/ and /F/ at expected positions and restores data
JESD data waveform
CHARISK[1:0]
ADC DATA[15:0]
CHARISK[1:0]
JESD204B states
/F/ and /A/ symbols

## Slide 115: JESD204B Link: Lessons Learned
/F/ (K28.7) characters used for replacement on frame boundaries contain a comma
Comma detection must be disabled after CGS (which includes /K/ K28.5) otherwise misalignment might happen
Octects from ADC16DX370 are encoded (not scrambled!)
Decoding
Test signal:
1 MHz, 800mV
sine wave

## Slide 116: JESD204B: Conclusions
Developed simple and light JESD204B-compliant core
Tested with a single lane running at 4 Gbps (200 MSps 16-bit conversion)
JESD204B might be tricky (misalignment, device might require user data decoding)
This talk is given as part of the Scientific Independence of young Researchers (SIR) ROAL project funded by the Italian Ministry of Education, University and Research (MIUR) in 2014

## Slide 117: JESD204B References
R. Giordano, V. Izzo, S. Perrella and A. Aloisio “A JESD204B-compliant Architecture for Remote and Deterministic-Latency Operation,” IEEE Trans on Nucl. Sci., Vol. 64, no. 6, Jun. 2017, doi: 10.1109/TNS.2017.2655569 – Open Access

## Slide 118: Backup

## Slide 119: Macro
Option Explicit
Public Sub ChangeSpellCheckingLanguage()
Dim j As Integer, k As Integer, scount As Integer, fcount As Integer
scount = ActivePresentation.Slides.Count
For j = 1 To scount
fcount = ActivePresentation.Slides(j).Shapes.Count
For k = 1 To fcount
If ActivePresentation.Slides(j).Shapes(k).HasTextFrame Then
ActivePresentation.Slides(j).Shapes(k) _
.TextFrame.TextRange.LanguageID = msoLanguageIDEnglishUS
End If
Next k
Next j
End Sub

## Slide 120: Interpolator
shifter
+
x
x
DAC
filter
From the Local Oscillator
From the Phase Detector
Up-Down
Control
sin(a+b) = sina cosb+ cosa sinb