## Slide 1
HIB@LNS 2015
Catania 14-15 December 2015
L. Cosentino1 , E. V. Pagano1,2 , Alfio Pappalardo1
1INFN – Laboratori Nazionali del Sud
2Università di Catania
Diagnostics of FRIBs beam transport line

## Slide 2
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
One of the most important task for a beam facility is to maximize the efficiency of the beam transport from the accelerator to the experimental hall.
Current
Transverse profile of the beam
For Radioactive Ion Beams (103-105 pps) the characterisation of the beam properties requires dedicated diagnostic devices.
Easy task
  For stable beams@LNS (107-109 pps)
An optimal beam tuning procedure requires that the position, the shape and the intensity of the beam are continuously under control along all the beam line.
Notes: In general the observable are the current, the transverse profile of the beam and the emittance. With stable beam, where, the intensity of the beam is relatively high (107-109 pps) is quite simple to measure such observable, i.e. to current measurement it is possible to use a common farady cup, more in genera, it is possible to measure such observable using commercial instruments.

## Slide 3
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Movable production Target water cooled
Two 45° dipoles of the beam line allow for the fragments selection
Fragmentation beams at INFN-LNS - Catania
Reaction target and fragments detection

## Slide 4
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
There are 13 diagnostic points where we can measure the variables to optimize the transport of the beam.

## Slide 5
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Component along the beam line?
To measure the current of beams with low intensity (below 105 pps) we need to integrate in a proper time range the particles beam counting rate; and to do this, fast signals (15-20 ns) coming from plastic scintillators (NE111, NEXXX, BC404, BC408, Fibres, ecc) are needed.
BEAM COUNTING
Plastic scintillator (BC408) optically coupled to a small PMT, working in pulse counting mode
Current measurement

## Slide 6
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Component along the beam line?
Transverse profile measurement
Real time beam imaging based on fast acquisition system
Spatial resolution 1-2 mm
cm
cm
cm
cm
cm
cm
cm
cm

## Slide 7
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
What Next?
Possible systems to improve the beam transport along with the line
Goals:
Non destructive real time (on-line) diagnostic systems
Good compromise between radiation damage, cost and maintenance
Relatively simple to use
Possible solutions!

## Slide 8
proton beam 180 KeV
Intensity < 0.1 pA
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Microchannel Plate (MCP) for Beam Imaging and Ions tagging

## Slide 9
Plastic fibres and compact PMT for particle counting
Fibres diameter: 300 ÷ 500 µm
FIBBS (Fibre Based Beam Sensor)
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Light collection efficiency at one end: ≈3.5%
Plastic scintillator fibres
scanning a beam with scintillating fibres, in order to produce the 1D intensity distribution
beam profile (mm)
x profile
beam profile (mm)
y profile
8Li E = 16 MeV Ibeam= 7 x 103 pps
SiPM
μ-sensor
Notes: 9

## Slide 10
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
Conclusions and remarks
Thanks for the attention
A suitable diagnostics for In flight RIBs made by fast plastic scintillator and position sensitive silicon detectors is already available at LNS. However, It needs improvements in order to maximize the efficiency of the beam transport along with the line.
There are different ideas under developing and others could be taken into account with respect to new technology
Some experimental efforts are needed with some budget (consumable and man power)

## Slide 11
Catania, Italy
15 December, 2015
E. V. Pagano
Univ. of Catania & LNS-INFN
HIB@LNS 2015
Catania 14-15 December 2015
What Next?
Possible systems to improve the beam transport along with the line
Goals:
Non destructive real time (on-line) diagnostic systems
Good compromise between radiation damage, cost and maintenance
Relatively simple to use
Possible solutions!
beam
Tstart
TStop
MCP
MCP
Ions tagging by TOF measurement
TOF - 50 psec/channel
7Li tail
7Li peak @ channel 1926
8Li peak
Channel 2567
Selected events
On-line discrimination among ions having the same energy but different masses.