## Slide 1: Slow control architecture for the ECL endcap (… and BEAST)
R. Giordano
on behalf of the uSOP Team (*)
(*) A. Aloisio, F. Ameli, A. Anastasio, R.Giordano,
P. Scotto di Vetta and G. Tortone

## Slide 2: Overview
The uSOP platform
ECL: System Integration and Mechanics
Installation at BEAST2
Plans (and issues…) for 2016
Conclusions

## Slide 3: The Hardware platform

## Slide 4: uSOP
4 GB Flash eMMC
Single Board Computer for embedded applications
3U Eurocard form factor, stand alone
Running Linux OS (Debian)
Designed as a platform for Belle2 slow-controls
Derived-from and compatible-with BeagleBone open-source project
512 MB DDR3 RAM

## Slide 5: uSOP peripherals
2 x RS232 (*)
JTAG (*)
2 x SPI (*)
2 x I2C (*)
4 x AIN (**)
16 x GPIO
*= fully isolated
** = buffered 12-bit ADC
USB device
10/100 Ethernet
USB host
uSD
10/100 Ethernet (controls and managament only)

## Slide 6: System integration and Mechanics
Draft

## Slide 7: Aggregation scheme (4 sectors)
data
controls
Uplink to BELLE2 network (data)
Uplink to BELLE2 network (cntrls)

## Slide 8: Aggregation scheme (F/B wheel)
data
controls
Uplink to BELLE2 network (data)
Uplink to BELLE2 network (cntrls)
PC server + PDU

## Slide 9: Hardware Layout
6U Eurocard crate (per wheel)
Power supply
4 uSOP boards
Backplane
4 sectors per uSOP
Belle2 E-hut (Jun.2015)

## Slide 10: The uSOP Carrier
6U carrier board
One carrier prototype to be manufactured and to be tested @ INFN Na

## Slide 11: Rack Layout
1 crate per wheel (16 sectors)
2 patch panels
  16 cables each
Power supplies
Patch
panels

## Slide 12: Patch Panel

## Slide 13: Plug-in Units
Fully shielded (shield not shown in order not hide internals)

## Slide 14: uSOP @ BEAST

## Slide 15: Goals of uSOP at BEAST
6 boxes with 3 crystals each
uSOP monitors humidity and temperature in each box

## Slide 16: Sensors
Same sensors as Belle2 ECL (and same readout scheme)
0.1°C uncertainty on temperature
3% uncertainty on relative humidity
Thermistor
Semitec AT-2
10kohm
RH probe
Vaisala HMP60

## Slide 17: Sensor Installation
In each box, one thermistor per crystal (Lyso, pure CsI, CsI(Tl)) and a humidity probe
Cable adapter pcb on the box side
Sockets/plugs compatible with Belle2 ECL
Each box read via a 16-wire shielded cable routed to DAQ room
Thermistors
Sensor
wiring
Box hosting crystals
Humidity
probe
Close-up

## Slide 18: T/RH read-out
Cable Adapter (passive):
Selects grounding scheme
Filters the power to the VAISALA Rh probe
Sets 2, 3 or 4 wire (Kelvin) read-out
T-RH Controller
Adapter card
(LTC2983)
uSOP
40m 16-wire
cables
DAQ room
Each uSOP reads three boxes
Box #6
Box #5
Box #4
Interaction Region (backward)
SPI
SPI

## Slide 19: In the DAQ Room
Hosts 3 uSOP systems
2 uSOPs read 6 boxes
1 uSOP for FPGA readout
Each uSOP has a dedicated ethernet connection for remote power-on/off
Power supply
uSOP minicrate
BEAST Rack
3 cables
from IP
3 cables
from IP

## Slide 20: EPICS Process Variables
Each uSOP outputs PVs for relative humidity, crystal temperatures and corresponding dew points
Magnus-Tetens
Approximation
For dew point
measurement

## Slide 21: Temperature and RH logs
Logs for BOX #1, from 20/12/2015 5:35 JST to 22/12/2015 10:40 JST
Temp difference between crystals within 0.5°C
T (°C)
Time (a.u.)
Orange - Pure CSI
Grey - LYSO
Blue - CSI(Tl)
Time (a.u.)
RH (%)
1 day
1 day
Box is sealed and includes humidity absorber, RH varies mostly due to variation of temperature

## Slide 22: Irradiation of FPGAs at BEAST
FPGA board installed on the BEAST structure (behind TCP)
Designed for radiation effect studies, Kintex-7 325T and passives, no active components (almost)
Readout by uSOP for measuring bit upsets induced by radiation (JTAG over 40m CAT7 cables)
External power supplies (4-wire scheme)
uSOP+ADC(LTC2499) sense remote voltage
IR forward
On the back
of the strut

## Slide 23: Contribution to internal note
Writing a contribution to the Belle2 internal note on BEAST2
BEAST community plans to submit to NIM after publication as a note

## Slide 24: Plans (and issues) for 2016
Need to manufacture 8 carrier PCBs, uSOPs, T_Controller (spares ...?)
Buy connectors, buy/build cables
Software development
INFN purchases locked until end of march 2016 ?
  This sets a timing constraint on production and testing

## Slide 25: Conclusions
uSOP up and running at BEAST for reading crystal T and RH in boxes
EPICS compliance fully tested in the field
uSOP for ECL (BW+FW) designed, in 2016 production
  Mechanics designed and need to be produced
  Crate and board arrangement chosen
  Power supply boards designed
  PCB carrier designed
Installation at KEK foreseen for middle 2016 (around summer B2GM)

## Slide 26
Backup slides

## Slide 27: 3-wire Resistance Measurement

## Slide 28
New Linear ADC for slow-control

## Slide 29
uSOP: remote management
Lantronix XPort Pro
      Thumb-sized embedded uClinux module
      CPU Freescale Coldfire MCF5208 @160 MHz
      16 Mbyte RAM
      16 Mbyte FLASH
      Fast Ethernet 10/100 Mbps (1)
      UART (1)
      GPIO (3)
UART
RESET
POWER ctl
USD boot ctl
ETHERNET
LAN
µC

## Slide 30: Sensors Close-ups

## Slide 31: Plans (and issues…) for 2016

## Slide 32: BEAST - Ehut
Lorem ipsum

## Slide 33: BEAST - IP
Lorem ipsum
FPGA
(ROAL)
Slow controls
Cable Adapter