## Slide 1: Positron beam for PADME
Paolo Valente*, Bruno Buonomo, Luca Foggetta, Claudio Di Giulio
con lo staff del LINAC di DAFNE
INFN Laboratori Nazionali di Frascati
*INFN Sezione di Roma

## Slide 2
BTF
BTF
control room
Damping
Ring
transfer line
transfer line
Main rings
LINAC
Power supplies
The DAFNE complex

## Slide 3: BTF strong points …
Efficiency
  Taking out the linac down-time and the dead-time during the switch of the LINAC and the transfer lines from electron to positron mode, the fraction of time with beam available to BTF is >90%
  However during injections for DAFNE the number of bunches available to BTF goes down from 49 to 2 per second
Flexibility
  Beam parameters can be adjusted in fairly wide ranges, quickly and with a good reproducibility
User-friendly diagnostics
  Diagnostics has been continuously improved during the years, both from the point of view of performance and ease of use
  In particular GEM TPC and MediPix/FitPix detectors allows real-time adjustment and monitoring of the beam spot size and position
  Calorimeter particle counting and WCM intensity measurement
Wide range of services
  Network, DAQ, gas distribution
  Magnetic fields
  Remotely controlled x-y trolley, linear and rotation stages
  Vacuum and (with some limitation) cryogenics setups

## Slide 4: … and limitations
  In parasitic operations
    The duty cycle is limited, mainly by the switch between electrons and positrons, but more importantly the intensity of the beam on the BTF target (and thus downstream in the BTF line) changes by almost an order of magnitude in the two modes
    The maximum energy is limited to 500 MeV (in “single particle”, lower at high intensity)
    The bunch length is fixed at 10 ns
  Working with the BTF target
    The maximum intensity is limited to 103-104 particles/bunch only lowering the selected energy and opening the collimators, thus worsening the momentum resolution (up to 1-2%)
  The beam spot
    Is practically Gaussian, it’s not easy to have an uniform intensity over a large area even defocussing and working with the collimators
  The angular divergence
    It’s of the order of 1-2 mrad, essentially dominated by the Coulomb scattering on the exit window (500 mm thick Beryllium)
    The last dipole adds a significant dispersion when increasing the intensity: opening of the collimators the entrance angle in the energy selection dipole increases, thus spoiling the momentum resolution
  The diagnostics
    Intensity is measured well in the low multiplicity range (by calorimeters) and above 107 particles/bunch (without target, by Integrating Charge Toroid), but with less accuracy in the intermediate range
    MediPix/FitPix are imaging detectors, not really a tracking system
    The GEM TPC has a sub-mm resolution only in the drift coordinate
  Tagged photons
    Are available, but with a low rate and not uniform energy resolution
  Neutrons
    Can be produced, but with RP limitations on the repetition rate and run duration,
    Diagnostics has to be improved

## Slide 5: BTF improvements
In the last years we have been constantly working in order to improve:
  The efficiency in terms of beam availability and stability
  The ease of tuning of beam parameters, through a constant work on the diagnostics
We have also put forward a number of ideas in order to widen the range of beam parameters:
  2003-2004: Photon tagging
  2008-2010: n@BTF, optimized target for studying the photo-production of neutrons
  Upgrade of the shielding for high intensity operation
  Pulse length >40 ns
  Improved target for positron production
  Improved collimation (aiming at hundreds of mrad)
  Second beam line
  Improved photon tagging
  Dosimetry for irradiation
  Integrated facility for space characterization
  Energy upgrade
  …

## Slide 6: Bunch length
Diluting in time electrons/positrons in one linac bunch can be very useful for a number of applications (e.g. decreasing pile-up)
Assuming constant current from the gun cathode, a longer pulse will correspond to a larger beam charge
The main limitation comes from the RF pulse compression, needed to reach higher energy: SLac Energy Doubling system (SLED)
Outside flat top the accelerating field decreases rapidly, thus increasing the energy spread
We aim at extending from 40 to 200 ns in the first phase
SLAC LINAC successfully operated at 500 ns with multiple phase inversions
10 ns
40 ns
Planned purchase of new gun pulser, from 1 to 4500 ns. Hopefully by the end of the year

## Slide 7: SLED
90° phase shift:
Resonant
cavities
accelerator
-90°
Resonant
cavities
accelerator
-180°
0°
-180°
After 180° phase inversion:
-90°
90°
0°
-90°
-180°
-90°
-180°
-90°
3.7 ms
0.8 ms
Input power
90°
0°

## Slide 8: New target
Present Copper target optimized for the production of maximum number of secondaries
Three steps: 1.7, 2.0 e 2.3 x0
  Not the optimal solution for high-energy (E ≈ E0) positron production
  Optimize depth of Copper target
  On-going:
    Try different material(s)
    Optimize geometry
(no fit)
1.0 x0
0.5 x0
1.7 x0
Positron yield vs. thickness
electrons
positrons
W
Al

## Slide 9: BTF target assembly and shielding

## Slide 10: Improved collimation
60 mm of Tungsten collimator
≈ 0.15 mm gap
≈ 100 particles/bunch at 450 MeV
15 cm
6 cm
20 cm

## Slide 11: Possible PADME installation (present BTF)

## Slide 12: Access to the facility
90% of shifts for detector testing and calibration
The Beam-Test activity will be completely stopped running PADME in the present configuration

## Slide 13: Doubling of beam-line
New control room ready
AIDA 2020 WP 15.4.1
On-going design of the new lines
Request for funding to INFN MAC (Machine Advisory Committee)
Basic idea: extend the present experimental area using the present control room
New elements in red

## Slide 14: Possible PADME installation
beam-test area

## Slide 15: Energy upgrade
Approximately 15 m drift at the end of the linac: add 4 accelerating sections, fed by one or two RF stations (reaching 1 GeV for e-). It is also possible to double the RF power in the other 8 sections after the positron converter (now fed by modulators C and D, to reach 1.2 GeV for e-)
(Similar to what proposed in: R. Boni, arXiv:0402081 [physics])
Last accelerating section
BTF/spectrometer/injection three-way switchyard
+200 MeV
+310 MeV
E
E
F

## Slide 16: Planning
2017
2016
2018

## Slide 17: Conclusions
Choices of the lab/management
Sharing of the LINAC
  PADME luminosity in parasitic running with DAFNE as a collider is reduced at least by an order of magnitude:
    40 ns operation not possible: bunch length fixed to 10 ns for injecting into the damping ring (1/4 of the luminosity)
    Energy obviously limited to 510 MeV (reduction of cross section)
    No beam during electron/positron switch
    AND
    Intensity during positron injection almost an order of magnitude less
    Only electron mode out of injection practically useful (less than 40%)
  How long will be the KLOE run?
  What will come after?
To Do
Short-medium term
  Pulse length >40 ns (buying 1 to 4500 ns pulser by the end of 2015)
    Probably “something” has to be done on the phase inversion or on the low-level RF to extend to several hundreds ns
    Possibility of a half-energy (350-400 MeV), high-luminosity run (100× more positrons on target) without SLED compression
  Improved target for positron production
  Improved collimation (aiming at hundreds of mrad)
Longer term
  Second beam line
    PADME installation better to come right before the installation of additional beam-pipe and magnets
    PADME run without a second BTF line would impact the operation (essentially no beam-tests during PADME runs)
  Energy upgrade
    Implies a longer LINAC shutdown
    Requires a significant financial effort

## Slide 18
Looking forward for the fruits of our work

## Slide 19: Call and Schedule
Two calls/year, typically ending in November and May
Scheduled shifts from January to July and from September to December
1 week shifts from Monday to Monday
Beam request web form:
http://www.lnf.infn.it/acceleratori/btf/request.html
BTF running subject to regular linac operations
BTF planning strongly linked to the DAFNE one
BTF Users Committee helps for the assignment of beam shifts
1 in 5 or 6 shifts dedicated to maintenance, facility improvements
High intensity runs to be agreed with RP

## Slide 20: DAFNE timing
25 or 50 Hz repetition rate
Last bunch every second always to spectrometer line
Spectrometer
BTF line
Accumulator
Main rings
LINAC = LINAC shots are delivered at 25(50) pulses/s and dumped at the end of TL
LINAC+BTF = LINAC shots are delivered with a selectable duty cycle to BTF: 1 to 24(49) pulses/s. Remaining pulses are dumped at the end of the TL
GLOBAL = LINAC shots are delivered with a variable duty cycle to BTF according to injection parameter in ACCUMULATOR
  NO INJECTION = SELECTABLE from 1 to 24(49) pulse per second
  INJECTION = the injection needs are DAΦNE Control Room controlled. Typically injection pulses are at 2Hz, taking from 1 up to 7 LINAC bunches per sequence. BTF delivers 22 down to 10 bunches per second

## Slide 21
Adjustment of the number of particles can be achieved:
Without changing the momentum resolution:
  Modulating the LINAC current [not possible in ‘parasitic mode’, rough] (transport optics or modulators power/phase, etc.)
  Collimating the beam before the target, using the up-stream vertical slits [large range]
  Choosing one of the three target depths [step change, very reproducible]
  Collimating the beam after the dipole, using the down-stream vertical slits [fine, small range]
Also changing the momentum resolution:
  Closing/Opening the horizontal collimators [both upstream and downstream]
Beam intensity fine tuning

## Slide 22
Target
Pulsed dipoles 3°/6°
Accelerating section