## Slide 1
M. Bongi, S. Bottai , 12/11/2015
Simulazione:applicazione della tecnica del dual readout

## Slide 2
Fluka-based MC simulation
  3,6cm CsI Scintillating crystals Scintillation Light collection efficiency and PD quantum efficiency (BGO , PWO ………..)
  Photodiode Energy deposits in the photodiodes due to ionization are taken into account
  Carbon fiber support structure (filling the gaps between crystals)
  Number of crystals passed via parameter
  New dedicated versions for Cherenkov and Neutrons detection added recently (to be finalized and eventually ‘unificated’ with standard version)
THE SIMULATION & RECONSTRUCTION TOOL
C++ reconstruction tools
  Noise
  Shower axis reconstructed by fit
  Lateral and longitudinal profiles respect to axis
  Point of first interaction along axis
  Length from first interaction to end of calorimeter
  ............................................................................
No MC truth is needed
in the analysys

## Slide 3: Apply the C/S correction to CALOCUBE
Vertical protons E=100 GeV, interacting in the first layer
S/E
C/S
C/S
Scorrected/E
RMS=22%
RMS=20%
RESOLUTION IMPROVEMENT ~ 10%
C=cherenkov and S=scintillation signals properly normalized
DUAL READOUT IN CALOCUBE

## Slide 4
ACCESS CALORIMETER : THIN SAMPLING CALO
Vladimir Nagaslaev, Alan Sill, Richard Wigmans
~ 10%
IMPROVEMENT DUE TO DUAL REDOUT ~ 10%
TEST BEAM ANALYSIS

## Slide 5
E=Ee +Eh
Ee =E*fem Eh =E*(1-fem)
EE
Eh
Sem =Ee * ke
p+/-
Shad =Eh * kh
ke ~ 0,95
kh ~ 0,1-0,2
Typical values
in our calo
Nucl excit., neutrons, p leak. !
calorimeter
Sem =Ee * ke
Shad =Eh * kh
Energy lost in ionization by electromagnetic fraction
Energy lost in ionization by hadronic fraction
E

## Slide 6
With Scintillation only we see total contribution to energy loss
Erec=a Stot=a(Sem+Shad)=a (Ee * ke + Eh * kh )=a (fem * E * ke + (1-fem)*E * kh )
If ke ≠ kh the fluctuation of fem induce a fluctuation on Erec
If ke = kh Erec= a (fem * E * ke + (1-fem)*E * kh )= a ke E
the fluctuation of fem DOES NOT induce a fluctuation on Erec
BUT ALSO FLUCTUATIONS ON kh PLAY THE GAME

## Slide 7
s=20 %
Electromagnetic fraction (fem)
2,8 l I CSI calo – 10 TeV
s=38%
Kh=Had Energy dep/Had Energy
2,8 l I CSI calo – 10 TeV

## Slide 8
Scintillation + Cherenkov (or neutrons) give information separately on Sem and Shad (not on Eh)
Once we know Shad , to reconstruct Eh, E, fem we need to use the constant 1/<kh> which can be large and hence increase the fluctuations of kh term
With Scintillation only we see total contribution to energy loss
Erec=a S=a(Sem+Shad)=a (Ee * ke + Eh * kh )=a (fem * E * ke + (1-fem)*E * kh )
propagating errors with approx of gaussian independent distributions
THE 'IDEAL' DUAL READOUT ALLOWS TO PERFECTLY MEASURE Sem and Shad
ke ~ 0,95
kh ~ 0,1-0,2
Typical values
in our calo

## Slide 9
x 3
WE SELECT 8 DIFFERENT SET OF VERTICAL SHOWERS FAR FROM BORDERS.
IN EACH SET THE SHOWERS HAS FIRST INTERACTION IN THE SAME CSI LAYERS
IN EACH SET THE SHOWERS SEE THE SAME CALO LENGTH FROM FIRST INT. TO END
THE 8 SETS CORRESPONDS TO 8 DIFFERENT CALO DEPTH FROM 5,6 lI TO 1.6 lI
STUDY OF CHERENKOV CORRECTIONS METHODS VERSUS CALO DEPTH
NEW SIMULATION

## Slide 10
methods of energy reconstructions compared
Erec = a * S
(all showers see the same calo length, no length correction needed)
(S/E)
C/S
Use Cherenkov/S to correct S
(A. Para)
S=E [ fem+(1-fem) (<kh>/<ke>) ]
C=E [ fem+(1-fem) (<kh>/<ke>)c ]
R=[1 - (<kh>/<ke>)c ] / [1 - (<kh>/<ke>) ]
Cherenkov correction ‘DREAM’ like
Ideal ‘dual’ detector , Se and Sh taken separetely event by event from simulation truth
SCINTILLATION ALONE

## Slide 11
Scintillation alone
Cherenkov corr. C/S
Chrenkov corr. Dream
Ideal ‘dual’ detector
standard
Calocube
20x20
1,9 lI
s(Erec-E)/E (%)
CSI Calo length from 10 interaction to end (cm)
1,9 lI
5,7 lI
3 lI
10 TeV protons
The resolution gain is roughly equivalent to add ~3 CSI plane
RESULTS

## Slide 12
10 TeV protons
Scintillation alone
Cherenkov corr. C/S
5,7 lI
3 lI
1,9 lI
s(Erec-E)/E (%)
CSI Calo length from 10 interaction to end (cm)
standard
Calocube
20x20
1,9 lI
10 TeV protons
Scintillation alone
Cherenkov corr. C/S
Chrenkov corr. Dream
Ideal ‘dual’ detector
standard
Calocube
20x20
1,9 lI
s(Erec-E)/E (%)
CSI Calo length from 10 interaction to end (cm)
1,9 lI
5,7 lI
3 lI
10 TeV protons
Relative Resolution Gain
Relative Resolution Gain
CSI Calo length from 10 interaction to end (cm)
5,7 lI
3 lI
1,9 lI
Cherenkov corr. C/S
Relative Resolution Gain
Relative Resolution Gain
CSI Calo length from 10 interaction to end (cm)
5,7 lI
Ideal ‘dual’ detector
3 lI
1,9 lI
Resolution with Cherenkov corrections (gaussian fit to peaks)