## Slide 1: Structured parallel programming on multi-core wireless sensor networks
Nicoletta Triolo, Francesco Baldini,
Susanna Pelagatti, Stefano Chessa
University of Pisa, Italy

## Slide 2: Background: wireless sensor networks
Sink
Internet,
Satellite Networks,
etc..
User

## Slide 3: Wireless sensor networks (WSN)
Main tasks of a sensor:
  Sense
  (pre)-process
  Communicate
Models of computation
  Centralized (at the sink, a sensor can make some pre-processing)
  Distributed

## Slide 4: Wireless sensor network platforms
platforms for conventional (single-core) sensors:
  8 bits/8MHz microcontrollers (MicaZ, T-Mote)
  128 KB flash memory
  8 KB RAM
  IEEE 802.15.4
  TinyOS + NesC

## Slide 5: Trends in WSN
Architectural level:
Application level:
Example of Application Domains: Multimedia WSN and VSN
Single-core WSN
Multi-core WSN
Simple data acquisition + forwarding
in-network processing model compute-intensive applications +computation -communication

## Slide 6: Trends in WSN
Parallel architectures of the single sensor node
Distributed computations throughout the WSN
Need for high-level abstractions
to support
Parallel Distributed programming

## Slide 7: Example of multi-core WSN node
Raspberry PI 2 Model B
ARM Cortex-A7 CPU
900 MHz quad-core
1GB RAM
Linux-Like + C/C++/Java + Wi-Fi IEEE 802.11

## Slide 8: Wireless/Visual Sensor Networks (W/VSN)
Number of networked devices
Each device:
  Microsystem with processor/memory
  Camera
  Wireless/wired network interface
Constrained resources
  Processing, communications
  Energy
Often used for tracking applications
    Mix of video processing, distributed communications

## Slide 9: Tracking with W/VSN
A number of cameras cooperatively track a mobile target
Detection when a target is in the Field of View (FoV) of a camera
Each camera computes location information of the target
All location information from different cameras are fused together
  Improve localization accuracy
  Alert other cameras in advance

## Slide 10: Example of a tracking application (I)
A generic node ci runs an infinite loop.
In a generic iteration k:
1. Acquisition phase:
Acquires an image from own camera: sk

## Slide 11: Example of a tracking application (II)
2. Exchange phase:
ci receives the output mik from its logical neighbors in n(ci )
where each Nj in n(ci) shares (part) of the FOV with ci

## Slide 12: Example of an application: tracking (III)
3. Computation phase:
xk+1 = f (xk , m1k, m2k , … , mik, sk)
f is the aggregation function
xk+1 is the output of tracking (estimated position of the target) at step k+1
mik is the output of neighbor Ni at step k
sk is the local image acquired at step k

## Slide 13: Example of an application: tracking (IV)
4. Transmission phase:
Broadcasts xk+1 to its logical neighbors

## Slide 14: Iterative Neighbor Stencil (INS) skeleton
Stencil-like computation
computation on matrix data structure
Fits common patterns of tracking apps in W/VSN
  Local image acquisition
  Local processing
  Exchange processed data with physical/logical neighbors (cameras with intersection FOVs)

## Slide 15: Skeletons: programming abstractions
efficient, portable, reusable and parametric

## Slide 16: Modeling tracking applications with INS
Real time execution
τ : max. latency of each round
  At next round data of this round are outdated
ρ : max. fraction of packets lost in each round per node
  Packet loss affects the quality of tracking
Non-functional requirement
Maximize network lifetime by reducing cameras duty cycle.

## Slide 17: Modeling tracking applications with INS
Implications on the underlying MAC layer
Determine a communication pattern
Affects packet loss and latency
Affects energy consumption
Two MAC protocols: MACAW and T-MAC
Two extremes:
  MACAW keeps radio always on
  T-MAC schedules off-periods for the radio
Tuning of MACAW and T-MAC for INS

## Slide 18: T-MAC and MACAW parameters
T-MAC
Preamble sampling based
Fs: frame size
Ta: length of active time
Vl: contention interval
MACAW
CSMA/CA, exponential backoff, radio always on
Initial backoff length

## Slide 19: Simulations
Castalia simulator
CC2420 wireless radio (IEEE 802.15.4)
4,7,10 nodes in a single hop network
100 iterations of the INS skeleton
Round of 0.5 sec.
Camera processing time of 30 msec.
τ=470 msec. (max communication Latency)
ρ=0.1 (max packet loss)
Notes: Un nuovo frame ogni 0,5 sec.
Una camera elabora il dato in 30 msec.

## Slide 20: Results
T-MAC
Frame size (Fs)
vs
round latency (τ)
Notes: Frame size Fs è la lunghezza totale di un frame T-MAC che include un periodo attivo di durata Ta e un periodo inattivo di durata Fs-Ta
All’aumentare della lunghezza del frame aumenta il periodo ne quale la radio è spenta e dopo un po’ si supera il limite
Nel grafico si fissa Ta e Vl a 10 millisecondi

## Slide 21: Results
T-MAC
Frame size (Fs)
vs
packet received in time (r)
Notes: Nota che conferma i risultati precedenti, per N=10 il max frame size è 50 ms

## Slide 22: Results
T-MAC
packet received in time (r)
vs
Contention Interval (Vl)

## Slide 23: Results
T-MAC
Energy consumption for communications *
vs
Timeout (Ta)
*of the camera that spends more
Notes: Energy consumption of the camera that spends more!!!

## Slide 24: Results
T-MAC
Energy consumption for communications
vs
Frame size (Fs)
Active time Ta=10ms
Notes: Solo fino a Fs=100 si può usare con N=4, dopo (per N>100) inizia a perdere molti pacchetti ed è per questo che il consumo è simile per tutti gli N
All of this suggests how to configure the T-MAC parameters in order to optimize energy consumption vs latency and packet loss
Fs = t/N
Ta= vl

## Slide 25: Results
Energy consumption with T-MAC and MACAW
T-MAC configured according to the previous experiments

## Slide 26: Conclusions
INS Skeleton fits well processing & communication patterns of tracking applications of W/VSN
Knowledge of communication pattern allows for fine configuration of MAC paramseters
  to achieve energy efficiency
  to meet requirements on latency and packet loss

## Slide 27: Future works
Analyse the tracking accuracy w.r.t. energy behaviour of INS
Analyse the behaviour of INS in multihop W/VSN
  cameras with intersecting FOV may be far in the communication topology
Extend this study to other patterns (skeletons) for WSN