## Slide 1: Perspectives for detection of gamma-ray counterparts of gravitational wave sources
Lorenzo Natalucci*, Pietro Ubertini, Angela Bazzano, Sandro Mereghetti, Carlo Ferrigno, Erik Kuulkers, Volodymyr Savchenko
*Istituto di Astrofisica e Planetologia Spaziali, INAF, Rome, Italy
on behalf of the INTEGRAL GW Team
Ligo-Virgo MoU 5/4/2014
Cosmic Ray International Seminar 2016, Ischia 4-8 July 2016
Notes: Rapid development of collaborations, tools and resources for hunting of EM counterparts.
Talk is mostly based on soft-gamma ray searches

## Slide 2
Launched in 2002 by ESA, INTEGRAL is providing advanced spectral and imaging capabilities in the X-ray/soft γ-ray band
INTEGRAL has provided, so far, the tightest upper limits on the EM energy emission GW150914
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
The INTEGRAL Space Observatory
Savchenko et al. 2016

## Slide 3
INTEGRAL main features
3 keV-10 MeV energy range with unprecedented sensitivity
2.7 days uninterrupted observations
wide FOV: ~100-1000 deg2
120 μs time resolution
arc min angular and keV energy resolution and
unique polarimetric capability
INTEGRAL is the link between the soft X-ray and high energy γ-ray sky
So far ~1000 INTEGRAL papers published
102+7 on-going PhD thesis (15+1 Italy)
and 100+ press releases
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 5
IBIS
SPI
All INTEGRAL high energy instruments use coded aperture to provide sky images
Developed after the ’60s; this technique is based on multiplexing the FOV by measuring different source positions and fluxes on the same detector elements
The coded aperture technique
How is this obtained?
An aperture passive device called coded mask, made of an array of opaque and transparent elements is standing at some distance from a position sensitive detector
3.2m
1.8m
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Notes: Let’s see briefly how INTEGRAL works

## Slide 6
IBIS carries two stacked imaging detector arrays: ISGRI (0.02-1MeV) based on room temperature CdTe semiconductor detectors. PICsiT (0.2-10 MeV) based on CsI scintillator devices
SPI (0.02-10 MeV), Ge cooled detectors provide high resolution spectra
JEM-X (3-35 keV) based on two identical high pressure microstrip gas chambers is providing low energy extension and arcmin resolution images
The INTEGRAL high energy detectors
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
ISGRI (CdTe) and SPI (Ge) detectors
The JEM-X detector
PICsIT array module and CsI crystal glued to its photodiode

## Slide 7
Performance parameters, IBIS vs SPI
Energy range | 0.015-10 MeV | 0.018-8 MeV
FOV (F.C.) | 9x9 deg | 16 deg hexagonal
Energy resolution | 8% @100 keV | 2.2 keV @1.2MeV
Detection area | 2100 cm2 | 500 cm2
Angular Resolution | 12’ | 2.5 deg
Location accuracy | < 1’ (> 20σ source) | ~ 1deg
Timing accuracy | < 200 μs | < 200 μs
IBIS SPI
For details see Ubertini et al. (IBIS) and Roques et al. (SPI),
2003 A&A 411(special issue on INTEGRAL)
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 8
Now: hunting
Gravitational Wave astrophysical counterparts
August 1975
May 1983
April 1996
December 1999
October 2002
November 2004
April 2007
June 2008
From BeppoSAX increasing the energy range in the last 20 years  XMM  INTEGRAL  AGILE  and CTA to exploit very high energy gamma ray science
Italy, and Europe, has a worldwide 4 decades record of success in the field of high energy astrophysics

## Slide 9
The SPI/ACS detectors view ~4π solid angle of the sky.
E>75 keV, Tres=50ms
Effective area: up to 1m2
The sensitivity to a gamma-ray transient depends on sky position and its evaluation must take into account the payload and satellite masses distribution
The IBIS detectors ISGRI and PICsIT have max sensitivity to directions normal to SPI/ACS factor of 5 at least
Outside the IBIS FOV (~30x30 deg2) the ISGRI and PICsIT detectors also view ~4π in the ~0.25-2.6 MeV band.
PICsIT: T_res=15.6ms
Effective area up to ~900cm2
INTEGRAL is similar to BeppoSAX for GW counterpart search…
INTEGRAL to hunt γ-ray transients
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Notes: INTEGRAL is also a true all-sky transient monitor in gamma-rays. The thick BGO shielding around the SPI detector is routinely used to detect gamma-ray bursts and a burst alert system –IBAS- is running all the time. In addtion the 3cm thick PICsit detector array can be used to detect transients outside the IBIS FOV.

## Slide 10
Events observed during
LIGO/Virgo O1
Credit: LIGO/Virgo Collaboration
Three events observed: all consistent with Binary BH mergers: most followed is GW150914
One of them, LVT151012, has a statistical significance of ~98%.
GW151226 not covered by INTEGRAL (but see the very recent CALET results, Adriani+16, arXiv:1607.00233v1)
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 11
Main astrophysical sources of gravitational waves
BH-BH mergers ???
NS-BH and NS-NS mergers Short GRBs
Gravitational Collapse Long GRBs
Magnetars; Pulsar Glitches Soft γ-ray Flares
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Extending substantially the range of masses of visible black holes!
Notes: Why do we search for EM counterparts? What do we expect to observe?

## Slide 12
arxiv1602.08492
V. Savchenko et al., 2016 ApJL,820,L36
Abbott, B. P et al, 2016 ApJL
Notes: 25 observing teams have searched the astrophysical counterpart spanning the whole EM spectrum. Gamma

## Slide 13
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
The Real-time IBAS GRB trigger system has not been triggered by the GW event. Off-line analysys has then been performed.
The whole sky was covered by INTEGRAL in the range from 50KeV to 2MeV before and after the reported GW150914 event
Using the omni-directional view of the INTEGRAL/SPI-ACS and the IBIS-PICSIT side FoV we have obtained tight upper limits on
the hard X-ray/gamma-ray prompt emission
INTEGRAL, FERMI and SWIFT data strongly constrain the fraction of energy emitted in the high energy electromagnetic component from the full high-probability sky region of LIGO/Virgo trigger
GW 150914

## Slide 14
INTEGRAL UL on γ-ray emission from GW150914
DT= -3s
DT= 0.4s
http://arxiv.org/abs/1602.04180
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 15
PICSIT Spectral Timing data
260 keV – 2.6 MeV
16ms time resolution

## Slide 16
Localization by the LIGO/Virgo collaboration yields a very large region…
The SPI/ACS sensitivity in FOV vary up by a factor 5, but its optimal value applies to 75% of the sky
GW150914: U.L. range is 0.2-4.5x10-7 erg cm-2 for event durations of 0.05 to 10s, respectively (applies to 95% of the Adv. LIGO error region)
Savchenko et al., ApJ lett., 2016
INTEGRAL Upper Limits on the γ-ray emission of GW 150914
The ratio of e.m. to gravitational energy is Rγ/g= 0.2-5x10-6
In case of events in the ~300 sq.deg FOV of INTEGRAL, the search flux limits would decrease by a factor ~5 at least
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 17
Event with associated false alarm probability of 0.02
Location compatible to be within INTEGRAL FoV
Possible BBH merger, with initial masses
and redshift
Abbott+16, arXiv:1602.03844v3
LVT 151012
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016

## Slide 18
INTEGRAL operation was changed after GW150914 to IMMEDIATELY follow-up the NEXT GW trigger.
INTEGRAL has constrained the energy emitted in the high energy electromagnetic component from the full high-probability sky region of LIGO/Virgo trigger to:
Eg/EGW < 10-6
Liso ≤ 1046 erg/s
INTEGRAL has observed with the allsky monitor LVT 151012 and a large part of the LIGO/VIRGO error box is within the FoV!!! 
More stringent upper limit to come….
INTEGRAL Highlights Summary for O1

## Slide 19
Prospects for O2 and beyond
LIGO/Virgo O2 starting in the Fall of 2016; Virgo expected to begin ops near the end of the year
Starting from the next O2 campaign, aLIGO+Virgo will start to approach their design performance. The error region will decrease to <few 100s sq.degrees
3-100 BBH events expected in O2 (see arXiv:1602.03842)
Different timescales for follow-up to be considered: from real-time (prompt) to hours-days (delayed emission)
INTEGRAL, Swift, Fermi are best candidates for follow-up
In case of events in the ~300 sq. deg FOV of INTEGRAL the flux limits would decrease by a factor ~5 at least
INTEGRAL can characterize the prompt and also the delayed emission using dedicated TOO programs.
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Notes: The fluence limit is ~1.5x10-7 erg cm-2 for 1s burst
O2: factor of a few in sensitivity better than O1;
Rates degli eventi previsti sono 5-500/campagna, dipende dai modelli

## Slide 20
Lobster eye X-Ray
+ gamma-ray trigger
10-50 High-Z GRBs
10y development Cost 100-500M€
Cubesat sworm constellation arcsec positioning
Short turnaround
Moderate cost, modularity: 100cubesat
INTEGRAL-SWIFT
Large Observatories
>10 years operations
Low cost!..
The HERMES mission High Energy Rapid Modular
Experiment Satellites
LOBSTER (NASA)
Theseus (ESA)
What’s next
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Notes: Cubesats con Gps fino 10ns di ris.temporale

## Slide 21
L. Natalucci – Cosmic Ray International Seminar, Ischia 4-8 July 2016
Backup slides

## Slide 22
L. Natalucci, Rome Tor Vergata, 2013
IBIS IN FRONT OF THE MeV: THE COMPTON MODE
Crab, Compton mode, 300ks (Forot et al. 2007)
ISGRI and PICsIT are also operated in signal coincidence, allowing to exploit the Compton kinematics for each event in the time coincidence window.
This allows to extend the energy range well into the MeV region,and to exploit polarization measurements.

## Slide 23: INTEGRAL vs Fermi/GBM
 | SPI/ACS | PICsIT | GBM | GBM
Detector | BGO | CsI | BGO | NaI
Energy range | >75 keV | 0.2-2.6 MeV Compton Mode 0.3-10MeV | 0.15-30 MeV | 8-1000 keV
Effective area | Up to ~1m2 | Up to ~900cm2 | Up to ~400cm2 | Up to ~150 cm2
Time resolution | 50ms | 15.6ms | 5μs | 
IBIS/PiCsIT
The SPI/ACS and GBM have quite different energy coverage and effective area
Assuming the Fermi/GBM spectral model, INTEGRAL would have detected a signal of significance in the range 5-15 sigma. The higher value is for the southern (most probable) direction