## Slide 1: Crystal structures in geant4
Enrico Bagli

## Slide 2: Introduction

## Slide 3: Crystals
A lattice is a discrete but infinite regular arrangement of points in a vector space
A crystal is defined as a lattice with a basis added to each lattice site.
Usually the basis consists of an atom, a group of atoms or a molecule.

## Slide 4: Crystals
Periodicity of the crystal structure is fundamental for many physical processes.
Important physical values can be calculated for each crystal structure.
For example the electron density in the crystal, the band structure, the dispersion relation for the phonon group velocity evolution.

## Slide 5: Crystals
The crystal lattice has an orientation in space.
The lattice orientation determines if some physics processes happen.
As an example X-ray diffraction strongly depends on the lattice orientation with respect to the incoming beam direction.

## Slide 6: Solid-state detectors
Semiconductor based detectors are used for astrophysics and high-energy physics, for X-rays detection in medical imaging and diagnostic, for particle counters in nuclear phyisic.
Ionizing particle produces a current pulse in the semiconductor, generating pairs of electron-holes transported by an electric-field, amplified, collected and digitalized.

## Slide 7: Dark matter search
  Measurement of the recoil energy imparted to a nucleus due to collisions with WIMPs is done employing detectors highly sensitive to the ionization and phonon signals that results from a WIMP-nucleus collision (Cryogenic Dark Matter Search experiment)

## Slide 8: Diffraction from periodical lattice
Bragg diffraction is the consequence of the interference between waves reflecting from different crystal planes coherently .
Field of applications are accelerator (synchrotrons), nuclear reactors (neutron diffraction), crystalline material analysis (diffractometry), astrophysics (laue lens), medicine (DNA, RNA macromolecules analysis).

## Slide 9: Channeling in crystals
Particle trajectories and penetration depth into crystal are altered by the presence of periodic structures.
Material analysis by ion channeling allows to examining the density of defects and the contaminants of the crystal.
At GeV energies channeling in bent crystals is used for the extraction, collimation and focusing of charged particles beams.

## Slide 10: Crystals in Geant4

## Slide 11: Geant4 + Crystals
Now:
Geant4 provides two examples with crystals, with two versions of support for crystal structures
  Phonon propagation in ultra-cold Ge
    examples/extended/exotic/phonon
  Channeling at high-energy in Si/Ge
    examples/extended/exotic/channeling
Near Future
General support for crystal structures in Geant4 (2016)
Physics list (from 2017):
  Channeling
  Phonon

## Slide 12: Geant4 Crystal Objects
Physical Volume
Crystal Data
Crystal Material
Logical Crystal Volume
Crystal Lattice
Atoms
A crystal is an ordered structure of atoms, ions or molecules.
G4MaterialCrystal is a class derived from the G4Material class.
G4MaterialCrystal collects the description of the unit cell, the base and the lattice.

## Slide 13: Geant4 Crystal Objects
Physical Volume
Crystal Data
Crystal Material
Logical Crystal Volume
Crystal Lattice
Atoms
G4LogicalCrystalVolume is a class derived from the G4LogicalVolume class.
G4LogicalCrystalVolume collects
  Crystal data (band structure, electron density, etc…);
  Lattice orientation with respect to the solid.

## Slide 14: Existing solid-state codes
Crystallographic Information File
Crystallographic Information File
  the standard for crystallographic data exchange prescribed by the International Union of Crystallography since 1991.
Crystallography Open Database:
  open-access database in which users are able to contribute with published and unpublished structures of small molecules and small to medium sized unit cell crystals to the database.
Solid State Software (GPL)
Geant4 is devoted to the simulation the propagation of particles (pseudo-particles) in matter.
The physical quantities of interest in crystals, e.g., electrons distributions, potential, electronic band structure, are needed by the Geant4 crystal processes.
The compatibility of input with existing codes is fundamental in the first version of the Geant4 support to crystal structures.

## Slide 15: Geant4 Crystal Objects
A Geant4 crystal object is instantiated as:
G4MaterialCrystal* SiCrystal =
new G4MaterialCrystal(Si);
SiCrystal->AddCrystalLattice(14,
new G4CrystalLatticeDiamond());
G4LogicalVolume* fXtalLogic =
new G4LogicalCrystalVolume(fXtalSolid,SiCrystal,"Target");
((G4LogicalCrystalVolume*)fXtalLogic)->AddCrystalData(
new G4CrystalProcessData());
Instantiate a crystalline material instead of a standard material
Preliminary

## Slide 16: Geant4 Crystal Objects
A Geant4 crystal object is instantiated as:
G4MaterialCrystal* SiCrystal =
new G4MaterialCrystal(Si);
SiCrystal->AddCrystalLattice(14,
new G4CrystalLatticeDiamond());
G4LogicalVolume* fXtalLogic =
new G4LogicalCrystalVolume(fXtalSolid,SiCrystal,"Target");
((G4LogicalCrystalVolume*)fXtalLogic)->AddCrystalData(
new G4CrystalProcessData());
Add a lattice to the base (the Si element)
Preliminary

## Slide 17: Geant4 Crystal Objects
A Geant4 crystal object is instantiated as:
G4MaterialCrystal* SiCrystal =
new G4MaterialCrystal(Si);
SiCrystal->AddCrystalLattice(14,
new G4CrystalLatticeDiamond());
G4LogicalVolume* fXtalLogic =
new G4LogicalCrystalVolume(fXtalSolid,SiCrystal,"Target");
((G4LogicalCrystalVolume*)fXtalLogic)->AddCrystalData(
new G4CrystalProcessData());
Instantiate a crystalline logical volume with the crystalline material
Preliminary

## Slide 18: Geant4 Crystal Objects
A Geant4 crystal object is instantiated as:
G4MaterialCrystal* SiCrystal =
new G4MaterialCrystal(Si);
SiCrystal->AddCrystalLattice(14,
new G4CrystalLatticeDiamond());
G4LogicalVolume* fXtalLogic =
new G4LogicalCrystalVolume(fXtalSolid,SiCrystal,"Target");
((G4LogicalCrystalVolume*)fXtalLogic)->AddCrystalData(
new G4CrystalProcessData());
Add crystal data to the logical crystal volume
G4CrystalProcessData is a derived class of G4CrystalData
Preliminary

## Slide 19: Geant4 Crystal Objects
Standard material
G4Material* Si =
G4NistManager::Instance()-> FindOrBuildMaterial("G4_Si");
Crystal material
G4MaterialCrystal* SiCrystal =
new G4MaterialCrystal(Si);
SiCrystal->AddCrystalLattice(14,
new G4CrystalLatticeDiamond());
G4LogicalVolume* fXtalLogic = new G4LogicalVolume(fXtalSolid,Si,
"Target");
G4LogicalVolume* fXtalLogic = new G4LogicalCrystalVolume(fXtalSolid,
SiCrystal,"Target");
((G4LogicalCrystalVolume*)
fXtalLogic)->AddCrystalData(
new G4CrystalProcessData());
Preliminary

## Slide 20: Geant4 Crystal Objects
In a Geant4 process, you can ask if the logical volume is a crystal and get the crystal data:
if(G4CrystalManager::GetManager()->Has(logVolume)){
G4LogicalCrystalVolume* logCrystal =
(G4LogicalCrystalVolume*) logVolume;
if(savedIndex == -1){
savedIndex = logCrystal
->GetCrystalDataIndex("someCrystalData");
if(savedIndex > -1){
G4CrystalProcessData* crystalData = (G4CrystalProcessData*) logCrystal
->GetCrystalData(savedIndex );
G4double aValue = crystalData->GetValue();
...
}
}
Ask the crystal manager if a logical volume is a crystal
Preliminary

## Slide 21: Geant4 Crystal Objects
In a Geant4 process, you can ask if the logical volume is a crystal and get the crystal data:
if(G4CrystalManager::GetManager()->Has(logVolume)){
G4LogicalCrystalVolume* logCrystal =
(G4LogicalCrystalVolume*) logVolume;
if(savedIndex == -1){
savedIndex = logCrystal
->GetCrystalDataIndex("someCrystalData");
if(savedIndex > -1){
G4CrystalProcessData* crystalData = (G4CrystalProcessData*) logCrystal
->GetCrystalData(savedIndex );
G4double aValue = crystalData->GetValue();
...
}
}
Ask the logical crystal volume the index of the data “someCrystalData”
Preliminary

## Slide 22: Geant4 Crystal Objects
In a Geant4 process, you can ask if the logical volume is a crystal and get the crystal data:
if(G4CrystalManager::GetManager()->Has(logVolume)){
G4LogicalCrystalVolume* logCrystal =
(G4LogicalCrystalVolume*) logVolume;
if(savedIndex == -1){
savedIndex = logCrystal
->GetCrystalDataIndex("someCrystalData");
if(savedIndex > -1){
G4CrystalProcessData* crystalData = (G4CrystalProcessData*) logCrystal
->GetCrystalData(savedIndex );
G4double aValue = crystalData->GetValue();
...
}
}
Get the data using the stored index
Preliminary

## Slide 23: Phonon Propagation
Phonon example in extended/exotic

## Slide 24: Phonons
Phonons are collective oscillations of a crystal lattice (wave-particle duality)
Two types of phonons:
  acoustic phonons:
    coherent movements of atoms of the lattice
  optical phonons
    out-of-phase movements of the atoms in the lattice

## Slide 25: Phonons
Oscillations of acoustic and optical phonons may have three modes:
  Longitudinal waves: the displacement and the travel of the wave are in the same/opposite direction
  Transverse waves: oscillations are perpendicular to the direction of energy transfer (slow and fast)

## Slide 26: Geant4 Phonons
CDMS experiment
The goal of the CDMS experiment is to detect CDMS the WIMPs (Weakly Interacting Massive Particles), i.e. the Dark Matter.
The experiment aims to measure the recoil energy imparted to a nucleus due to collisions with WIMPs.
The employed detectors are highly sensitive to the ionization and phonon signals that results from a WIMP-nucleus collision.
The CDMS detectors are cylindrical Ge crystals approximately 75 mm in diameter with a height of 25 mm, cooled to approximately 60 mK
Nuclear Recoil

## Slide 27: Geant4 Phonons
CDMS experiment
The goal of the CDMS experiment is to detect CDMS the WIMPs (Weakly Interacting Massive Particles), i.e. the Dark Matter.
The experiment aims to measure the recoil energy imparted to a nucleus due to collisions with WIMPs.
The employed detectors are highly sensitive to the ionization and phonon signals that results from a WIMP-nucleus collision.
The CDMS detectors are cylindrical Ge crystals approximately 75 mm in diameter with a height of 25 mm, cooled to approximately 60 mK
Geant4 Phonon Types
The phonon transport code described is intended for temperatures T < 1K
Scattering of thermally excited background phonons is ignored
Only acoustic phonons in cubic lattices are treated.
Three types of phonons are implemented:
  Longitudinal
  “slow” and “fast” transverse

## Slide 28: Geant4 Phonons Processes
Processes implemented
Anisotropic propagation
Isotope Scattering
Mode Mixing
Downconversion
Anisotropic propagation
Phonon propagation in the absorber crystal is governed by the three-dimensional wave equation
By solving it for a phonon of given wave vector k, three eigenvalues ω and three eigenvectors e can be found, corresponding to the three discrete polarization states Longitudinal , Fast and Slow Transverse.

## Slide 29: Geant4 Phonons Processes
Processes implemented
Anisotropic propagation
Isotope Scattering
Mode Mixing
Downconversion
Anisotropic propagation
Energy transport occurs along the group velocity vector, which can be found from the three-dimensional wave equation as
There are two key aspects to the solution of the wave equation:
  The momentum vector is not generally parallel to the vector of energy transport.
  Phonons at frequencies characteristic of quasi diffusion are non-dispersive.

## Slide 30: Geant4 Phonons Processes
Processes implemented
Anisotropic propagation
Isotope Scattering
Mode Mixing
Downconversion
Isotope Scattering & Mode Mixing
Isotope scattering occurs when a phonon interacts with an isotopic substitution site in the lattice.
During the elastic scattering the phonon momentum vector is randomized, and the phonon polarization state can change freely between the three states (mode mixing)

## Slide 31: Geant4 Phonons Processes
Processes implemented
Anisotropic propagation
Isotope Scattering
Mode Mixing
Downconversion
Downconversion
In anharmonic inelastic scattering events, energetic phonons spontaneously decay into pairs of less energetic phonons
The wave vector directions of the daughter phonons are determined by assuming that the group velocity is isotropic and requiring that energy and momentum are conserved.
k
k'
k''

## Slide 32: Phonon physics list
void XPhysicsList::ConstructParticle() {
G4PhononLong::PhononDefinition();
G4PhononTransFast::PhononDefinition();
G4PhononTransSlow::PhononDefinition();
}
void XPhysicsList::ConstructProcess() {
AddTransportation();
// Only make processes once
G4VProcess* phScat = new G4PhononScattering;
G4VProcess* phRefl = new G4PhononReflection;
G4VProcess* phDown = new G4PhononDownconversion;
theParticleIterator->reset();
while( (*theParticleIterator)() ){
G4ParticleDefinition* particle = theParticleIterator->value();
G4ProcessManager* pmanager = particle->GetProcessManager();
if (phScat->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phScat);
if (phDown->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phDown);
if (phRefl->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phRefl);
}
}

## Slide 33: Phonon physics list
void XPhysicsList::ConstructParticle() {
G4PhononLong::PhononDefinition();
G4PhononTransFast::PhononDefinition();
G4PhononTransSlow::PhononDefinition();
}
void XPhysicsList::ConstructProcess() {
AddTransportation();
// Only make processes once
G4VProcess* phScat = new G4PhononScattering;
G4VProcess* phRefl = new G4PhononReflection;
G4VProcess* phDown = new G4PhononDownconversion;
theParticleIterator->reset();
while( (*theParticleIterator)() ){
G4ParticleDefinition* particle = theParticleIterator->value();
G4ProcessManager* pmanager = particle->GetProcessManager();
if (phScat->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phScat);
if (phDown->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phDown);
if (phRefl->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phRefl);
}
}
Longitudinal, fast and slow transverse phonons are constructred

## Slide 34: Phonon physics list
void XPhysicsList::ConstructParticle() {
G4PhononLong::PhononDefinition();
G4PhononTransFast::PhononDefinition();
G4PhononTransSlow::PhononDefinition();
}
void XPhysicsList::ConstructProcess() {
AddTransportation();
// Only make processes once
G4VProcess* phScat = new G4PhononScattering;
G4VProcess* phRefl = new G4PhononReflection;
G4VProcess* phDown = new G4PhononDownconversion;
theParticleIterator->reset();
while( (*theParticleIterator)() ){
G4ParticleDefinition* particle = theParticleIterator->value();
G4ProcessManager* pmanager = particle->GetProcessManager();
if (phScat->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phScat);
if (phDown->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phDown);
if (phRefl->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phRefl);
}
}
Create one instance of each process, since they are the same for the three phonons

## Slide 35: Phonon physics list
void XPhysicsList::ConstructParticle() {
G4PhononLong::PhononDefinition();
G4PhononTransFast::PhononDefinition();
G4PhononTransSlow::PhononDefinition();
}
void XPhysicsList::ConstructProcess() {
AddTransportation();
// Only make processes once
G4VProcess* phScat = new G4PhononScattering;
G4VProcess* phRefl = new G4PhononReflection;
G4VProcess* phDown = new G4PhononDownconversion;
theParticleIterator->reset();
while( (*theParticleIterator)() ){
G4ParticleDefinition* particle = theParticleIterator->value();
G4ProcessManager* pmanager = particle->GetProcessManager();
if (phScat->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phScat);
if (phDown->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phDown);
if (phRefl->IsApplicable(*particle)) pmanager->AddDiscreteProcess(phRefl);
}
}
Add the processes to the manager only if they are applicable to the particle

## Slide 36: Scattering process
G4double G4PhononScattering::GetMeanFreePath(const G4Track& aTrack,
G4double /*previousStepSize*/,
G4ForceCondition* condition) {
//Dynamical constants retrieved from PhysicalLattice
G4double B = theLattice->GetScatteringConstant();
G4double Eoverh = aTrack.GetKineticEnergy()/h_Planck;
//Calculate mean free path
G4double mfp = aTrack.GetVelocity()/(Eoverh*Eoverh*Eoverh*Eoverh*B);
if (verboseLevel > 1)
G4cout << "G4PhononScattering::GetMeanFreePath = " << mfp << G4endl;
*condition = NotForced;
return mfp;
}

## Slide 37: Scattering process
G4double G4PhononScattering::GetMeanFreePath(const G4Track& aTrack,
G4double /*previousStepSize*/,
G4ForceCondition* condition) {
//Dynamical constants retrieved from PhysicalLattice
G4double B = theLattice->GetScatteringConstant();
G4double Eoverh = aTrack.GetKineticEnergy()/h_Planck;
//Calculate mean free path
G4double mfp = aTrack.GetVelocity()/(Eoverh*Eoverh*Eoverh*Eoverh*B);
if (verboseLevel > 1)
G4cout << "G4PhononScattering::GetMeanFreePath = " << mfp << G4endl;
*condition = NotForced;
return mfp;
}
The mean free path scales as E-4

## Slide 38: Scattering process
G4VParticleChange* G4PhononScattering::PostStepDoIt( const G4Track& aTrack, G4Step& aStep) {
G4StepPoint* postStepPoint = aStep.GetPostStepPoint();
if (postStepPoint->GetStepStatus()==fGeomBoundary) {
return G4VDiscreteProcess::PostStepDoIt(aTrack,aStep);
}
aParticleChange.Initialize(aTrack);
G4ThreeVector newDir = G4RandomDirection();
G4int polarization = ChoosePolarization(theLattice->GetLDOS(),
theLattice->GetSTDOS(),
theLattice->GetFTDOS());
G4Track* sec = CreateSecondary(polarization, newDir, aTrack.GetKineticEnergy());
aParticleChange.SetNumberOfSecondaries(1);
aParticleChange.AddSecondary(sec);
aParticleChange.ProposeEnergy(0.);
aParticleChange.ProposeTrackStatus(fStopAndKill);
return &aParticleChange;

## Slide 39: Scattering process
G4VParticleChange* G4PhononScattering::PostStepDoIt( const G4Track& aTrack, G4Step& aStep) {
G4StepPoint* postStepPoint = aStep.GetPostStepPoint();
if (postStepPoint->GetStepStatus()==fGeomBoundary) {
return G4VDiscreteProcess::PostStepDoIt(aTrack,aStep);
}
aParticleChange.Initialize(aTrack);
G4ThreeVector newDir = G4RandomDirection();
G4int polarization = ChoosePolarization(theLattice->GetLDOS(),
theLattice->GetSTDOS(),
theLattice->GetFTDOS());
G4Track* sec = CreateSecondary(polarization, newDir, aTrack.GetKineticEnergy());
aParticleChange.SetNumberOfSecondaries(1);
aParticleChange.AddSecondary(sec);
aParticleChange.ProposeEnergy(0.);
aParticleChange.ProposeTrackStatus(fStopAndKill);
return &aParticleChange;
Only works if the particles is not at boundary

## Slide 40: Scattering process
G4VParticleChange* G4PhononScattering::PostStepDoIt( const G4Track& aTrack, G4Step& aStep) {
G4StepPoint* postStepPoint = aStep.GetPostStepPoint();
if (postStepPoint->GetStepStatus()==fGeomBoundary) {
return G4VDiscreteProcess::PostStepDoIt(aTrack,aStep);
}
aParticleChange.Initialize(aTrack);
G4ThreeVector newDir = G4RandomDirection();
G4int polarization = ChoosePolarization(theLattice->GetLDOS(),
theLattice->GetSTDOS(),
theLattice->GetFTDOS());
G4Track* sec = CreateSecondary(polarization, newDir, aTrack.GetKineticEnergy());
aParticleChange.SetNumberOfSecondaries(1);
aParticleChange.AddSecondary(sec);
aParticleChange.ProposeEnergy(0.);
aParticleChange.ProposeTrackStatus(fStopAndKill);
return &aParticleChange;
Randomly choose the direction and the polarization of the new phonon

## Slide 41: Scattering process
G4VParticleChange* G4PhononScattering::PostStepDoIt( const G4Track& aTrack, G4Step& aStep) {
G4StepPoint* postStepPoint = aStep.GetPostStepPoint();
if (postStepPoint->GetStepStatus()==fGeomBoundary) {
return G4VDiscreteProcess::PostStepDoIt(aTrack,aStep);
}
aParticleChange.Initialize(aTrack);
G4ThreeVector newDir = G4RandomDirection();
G4int polarization = ChoosePolarization(theLattice->GetLDOS(),
theLattice->GetSTDOS(),
theLattice->GetFTDOS());
G4Track* sec = CreateSecondary(polarization, newDir, aTrack.GetKineticEnergy());
aParticleChange.SetNumberOfSecondaries(1);
aParticleChange.AddSecondary(sec);
aParticleChange.ProposeEnergy(0.);
aParticleChange.ProposeTrackStatus(fStopAndKill);
return &aParticleChange;
Create the ”secondary” particle and add to the stack

## Slide 42: Scattering process
G4VParticleChange* G4PhononScattering::PostStepDoIt( const G4Track& aTrack, G4Step& aStep) {
G4StepPoint* postStepPoint = aStep.GetPostStepPoint();
if (postStepPoint->GetStepStatus()==fGeomBoundary) {
return G4VDiscreteProcess::PostStepDoIt(aTrack,aStep);
}
aParticleChange.Initialize(aTrack);
G4ThreeVector newDir = G4RandomDirection();
G4int polarization = ChoosePolarization(theLattice->GetLDOS(),
theLattice->GetSTDOS(),
theLattice->GetFTDOS());
G4Track* sec = CreateSecondary(polarization, newDir, aTrack.GetKineticEnergy());
aParticleChange.SetNumberOfSecondaries(1);
aParticleChange.AddSecondary(sec);
aParticleChange.ProposeEnergy(0.);
aParticleChange.ProposeTrackStatus(fStopAndKill);
return &aParticleChange;
Kill the primary particle, which is “substituted” by the secondary

## Slide 43: Simulated transport processes
Downconversion
Isotope Scattering +
Mode Mixing
Downconversion + Isotope Scattering +
Mode Mixing

## Slide 44: Phonon Focusing
Experimental
Geant4
Phonon flux intensity on a Ge crystal face resulting from a point source at the crystal center.
Northrop and Wolfe PRL 19, 1424 (1979)
Notes: Anisotropies in the elasticity tensor lead to phonon focusing into complicated intensity patterns.
Three phonon processes are currently available, though may not be fully functional.
•G4PhononScattering Treats scattering of phonons off of isotopic impurities or lattice defects, changing direction and
randomizing the polarization state (mode mixing)
•G4PhononDownconversion Longitudinal phonons split in two,
either L ➔ L’T or L ➔TT
The processes developed so far support acoustic phonons, which are relevant for low-temperature (tens of mK) crystals.
Three polarization states are recognized
Longitudinal (G4PhononLong)
Transverse “slow speed” (G4PhononTransFast)
Transverse “fast speed” (G4PhononTransSlow)

## Slide 45: Channeling
ExExCh example in extended/exotic

## Slide 46: Particle interaction with aligned crystals
Condition for coherent effects: particle direction of motion nearly aligned with crystal planes or axes.

## Slide 47: Crystal
Ordered pattern of atoms.
Ki-Bum Kim, SPIE Newsroom, DOI: 10.1117/2.1200812.1396

## Slide 48: Crystal
Ordered pattern of atoms.
Aligned atoms can be seen as planes or axes.
Ki-Bum Kim, SPIE Newsroom, DOI: 10.1117/2.1200812.1396

## Slide 49: Charged Particle Interaction
Crystal
Amorphous

## Slide 50: Bent crystal
Channeled particles follows the crystal curvature and are deflected (1.).
Particle whose trajectories is tangent to crystalline planes are “reflected” by the potential barrier (3.)
1.
2.
3.
Impact Position
Penetration Depth

## Slide 51: Modified density
Positive particles oscillate between atomic planes; negative particles repeatedly cross them.

## Slide 52: Modified density
Positive particles oscillate between atomic planes; negative particles repeatedly cross them.
Depending on the transverse energy of the particle, the density of nuclei and electron “seen” by a channeled particle is different
Positive
Negative

## Slide 53: Orientational phenomena in bent crystals
Transverse Energy
Impact Position

## Slide 54: Bent crystal
Varying the crystal orientation with respect to the beam direction orientational effects are observed:
No effect
Channeling
Dechanneling
Volume reflection
Volume capture
No effect
Notes: CERN H8 experiment:
Beam
  Protons
  400 GeV/c
Si crystal
  Plane (110)
  Length 3.0 mm
  Radius 18.5 m

## Slide 55: Bent crystal
Varying the crystal orientation with respect to the beam direction orientational effects are observed:
No effect
Channeling
Dechanneling
Volume reflection
Volume capture
No effect
W. Scandale et al., PRL 98, 154801 (2007)
A
B
C
A
B
C
Notes: CERN H8 experiment:
Beam
  Protons
  400 GeV/c
Si crystal
  Plane (110)
  Length 3.0 mm
  Radius 18.5 m

## Slide 56: Collimation with bent crystals
UA9 experiment
Crystal can be used as a primary collimator to deflect particles of the halo toward a secondary collimator.
Main advantage is the possibility to deflect the beam out and reduce the beam losses.
Experimental Setup
W. Scandale et al. PLB 692, 72 (2010)
standard collimation system
crystal collimation system

## Slide 57: Beam loss reduction
Two bent Si crystals were mounted on the LHC on February 2014. Measurement in the CERN LHC ring with 6.5 TeV/c protons and Si (110) crystal varying the crystal orientation with respect to beam direction showed a of the ratio of the beam loss.
W. Scandale et al., Physics Letters B 758 (2016) 129–133

## Slide 58: Channeling process
Features
Working from MeV (or hundreds of KeV) to GeV particle energies.
Exact information on position and momentum within one step.
On-the-fly average nuclei density per step.
Interface to Geant4 processes managed by biasing classes.
Scheme

## Slide 59: Channeling process
G4double ExExChProcessChanneling::
GetMeanFreePath(const G4Track& aTrack,
G4double, // previousStepSize
G4ForceCondition* condition){
//----------------------------------------
// the condition is forced to check if
// the volume has a lattice at each step.
// if it hasn't, return DBL_MAX
//----------------------------------------
*condition = Forced;
if(HasLattice(aTrack)){
GetInfo(aTrack)->SetInTheCrystal(true);
return GetChannelingMeanFreePath(aTrack);
}
else{
GetInfo(aTrack)->SetInTheCrystal(false);
return DBL_MAX;
}
}

## Slide 60: Channeling process
G4double ExExChProcessChanneling::
GetMeanFreePath(const G4Track& aTrack,
G4double, // previousStepSize
G4ForceCondition* condition){
//----------------------------------------
// the condition is forced to check if
// the volume has a lattice at each step.
// if it hasn't, return DBL_MAX
//----------------------------------------
*condition = Forced;
if(HasLattice(aTrack)){
GetInfo(aTrack)->SetInTheCrystal(true);
return GetChannelingMeanFreePath(aTrack);
}
else{
GetInfo(aTrack)->SetInTheCrystal(false);
return DBL_MAX;
}
}
Check if the volume traversed by the particle has a lattice

## Slide 61: Channeling process
G4double ExExChProcessChanneling::
GetMeanFreePath(const G4Track& aTrack,
G4double, // previousStepSize
G4ForceCondition* condition){
//----------------------------------------
// the condition is forced to check if
// the volume has a lattice at each step.
// if it hasn't, return DBL_MAX
//----------------------------------------
*condition = Forced;
if(HasLattice(aTrack)){
GetInfo(aTrack)->SetInTheCrystal(true);
return GetChannelingMeanFreePath(aTrack);
}
else{
GetInfo(aTrack)->SetInTheCrystal(false);
return DBL_MAX;
}
}
If TRUE, limits the step and set TRUE the flag “InTheCrystal” for the other processes

## Slide 62: Channeling process
G4double ExExChProcessChanneling::
GetMeanFreePath(const G4Track& aTrack,
G4double, // previousStepSize
G4ForceCondition* condition){
//----------------------------------------
// the condition is forced to check if
// the volume has a lattice at each step.
// if it hasn't, return DBL_MAX
//----------------------------------------
*condition = Forced;
if(HasLattice(aTrack)){
GetInfo(aTrack)->SetInTheCrystal(true);
return GetChannelingMeanFreePath(aTrack);
}
else{
GetInfo(aTrack)->SetInTheCrystal(false);
return DBL_MAX;
}
}
If FALSE, do NOT limit the step and set FALSE the flag “InTheCrystal”

## Slide 63: Channeling process
G4VParticleChange* ExExChProcessChanneling::
PostStepDoIt(const G4Track& aTrack,
const G4Step&){
aParticleChange.Initialize(aTrack);
GetInfo(aTrack)->StoreDensityPreviousStep();
if((HasLattice(aTrack) == true) &&
(HasLatticeOnBoundaryPost(aTrack) == false)){
UpdateParameters(aTrack);
G4ThreeVector vMomentum =
GetInfo(aTrack)->GetMomentumChanneled().unit();
G4ThreeVector vPosition;
vPosition =
ComputePositionInTheCrystal(aTrack.GetStep()->GetPostStepPoint(),
aTrack);
GetXPL(aTrack)->ProjectMomentumVectorFromLatticeToWorld(vMomentum,
vPosition);
aParticleChange.ProposeMomentumDirection(vMomentum.unit());
}
Check if the volume traversed by the particle has a lattice

## Slide 64: Channeling process
G4VParticleChange* ExExChProcessChanneling::
PostStepDoIt(const G4Track& aTrack,
const G4Step&){
aParticleChange.Initialize(aTrack);
GetInfo(aTrack)->StoreDensityPreviousStep();
if((HasLattice(aTrack) == true) &&
(HasLatticeOnBoundaryPost(aTrack) == false)){
UpdateParameters(aTrack);
G4ThreeVector vMomentum =
GetInfo(aTrack)->GetMomentumChanneled().unit();
G4ThreeVector vPosition;
vPosition =
ComputePositionInTheCrystal(aTrack.GetStep()->GetPostStepPoint(),
aTrack);
GetXPL(aTrack)->ProjectMomentumVectorFromLatticeToWorld(vMomentum,
vPosition);
aParticleChange.ProposeMomentumDirection(vMomentum.unit());
}
Update position and momentum in the channel and the density ratio

## Slide 65: Channeling process
G4VParticleChange* ExExChProcessChanneling::
PostStepDoIt(const G4Track& aTrack,
const G4Step&){
aParticleChange.Initialize(aTrack);
GetInfo(aTrack)->StoreDensityPreviousStep();
if((HasLattice(aTrack) == true) &&
(HasLatticeOnBoundaryPost(aTrack) == false)){
UpdateParameters(aTrack);
G4ThreeVector vMomentum =
GetInfo(aTrack)->GetMomentumChanneled().unit();
G4ThreeVector vPosition;
vPosition =
ComputePositionInTheCrystal(aTrack.GetStep()->GetPostStepPoint(),
aTrack);
GetXPL(aTrack)->ProjectMomentumVectorFromLatticeToWorld(vMomentum,
vPosition);
aParticleChange.ProposeMomentumDirection(vMomentum.unit());
}
Propose a new direction of the particle, i.e. rotate the particle momentum

## Slide 66: Channeling process
else{
// if the volume has no lattice it resets the density factors
ResetDensity(aTrack);
GetInfo(aTrack)->SetMomentumChanneled(G4ThreeVector(DBL_MAX,
DBL_MAX,
DBL_MAX));
GetInfo(aTrack)->SetPositionChanneled(G4ThreeVector(DBL_MAX,
DBL_MAX,
DBL_MAX));
}
return &aParticleChange;
}
If the volume does is not a crystal, reset the stored position in the channel, the stored transverse momentum and set to 1 de density ratio of nuclei and electrons

## Slide 67: Process Wrapper
G4double XWrapperDiscreteProcess::
PostStepGetPhysicalInteractionLength (const G4Track &aTrack,
G4double previousStepSize,
G4ForceCondition *condition){
[...]
if ( (previousStepSize < 0.0) || (theNumberOfInteractionLengthLeft<=0.0))
ResetNumberOfInteractionLengthLeft();
} else if ( previousStepSize > 0.0) {
SubtractNumberOfInteractionLengthLeft(previousStepSize*vDensityPreviousStep);
} else {}
G4double regIntLength =
fRegisteredProcess->PostStepGetPhysicalInteractionLength(aTrack,
previousStepSize*vDensityPreviousStep,
[...]
currentInteractionLength = regIntLength;
[...]
if(vDensity == 0.) return DBL_MAX;
currentInteractionLength /= vDensity;
return currentInteractionLength;

## Slide 68: Process Wrapper
G4double XWrapperDiscreteProcess::
PostStepGetPhysicalInteractionLength (const G4Track &aTrack,
G4double previousStepSize,
G4ForceCondition *condition){
[...]
if ( (previousStepSize < 0.0) || (theNumberOfInteractionLengthLeft<=0.0))
ResetNumberOfInteractionLengthLeft();
} else if ( previousStepSize > 0.0) {
SubtractNumberOfInteractionLengthLeft(previousStepSize*vDensityPreviousStep);
} else {}
G4double regIntLength =
fRegisteredProcess->PostStepGetPhysicalInteractionLength(aTrack,
previousStepSize*vDensityPreviousStep,
[...]
currentInteractionLength = regIntLength;
[...]
if(vDensity == 0.) return DBL_MAX;
currentInteractionLength /= vDensity;
return currentInteractionLength;
Divide the current interaction length by the density ratio. If the density is higher than 1, the step is shorter than the standard one and vice versa for density lower than 1

## Slide 69: Process Wrapper
G4double XWrapperDiscreteProcess::
PostStepGetPhysicalInteractionLength (const G4Track &aTrack,
G4double previousStepSize,
G4ForceCondition *condition){
[...]
if ( (previousStepSize < 0.0) || (theNumberOfInteractionLengthLeft<=0.0))
ResetNumberOfInteractionLengthLeft();
} else if ( previousStepSize > 0.0) {
SubtractNumberOfInteractionLengthLeft(previousStepSize*vDensityPreviousStep);
} else {}
G4double regIntLength =
fRegisteredProcess->PostStepGetPhysicalInteractionLength(aTrack,
previousStepSize*vDensityPreviousStep,
[...]
currentInteractionLength = regIntLength;
[...]
if(vDensity == 0.) return DBL_MAX;
currentInteractionLength /= vDensity;
return currentInteractionLength;
Subtract to the number of interaction length left the previous real step size multiplied by the density ratio of the previous step

## Slide 70: Process Wrapper
G4double XWrapperDiscreteProcess::
PostStepGetPhysicalInteractionLength (const G4Track &aTrack,
G4double previousStepSize,
G4ForceCondition *condition){
[...]
if ( (previousStepSize < 0.0) || (theNumberOfInteractionLengthLeft<=0.0))
ResetNumberOfInteractionLengthLeft();
} else if ( previousStepSize > 0.0) {
SubtractNumberOfInteractionLengthLeft(previousStepSize*vDensityPreviousStep);
} else {}
G4double regIntLength =
fRegisteredProcess->PostStepGetPhysicalInteractionLength(aTrack,
previousStepSize*vDensityPreviousStep,
[...]
currentInteractionLength = regIntLength;
[...]
if(vDensity == 0.) return DBL_MAX;
currentInteractionLength /= vDensity;
return currentInteractionLength;
Modify the physical interaction length with the density ratio of the previous step

## Slide 71: Channeling Example in Geant4
Beam Deflection
Experimental Setup
Channeling
Volume Reflection
Not Aligned
Bent Crystal
Beam
The example simulates the channeling of 400 GeV/c protons in bent Si crystal.
The example provides the physical model for planar channeling and volume reflection in bent crystals.
Physical model published in:
  E. Bagli, M. Asai, D. Brandt, A. Dotti, V. Guidi, D. H. Wright, “A model for the interaction of high-energy particles in straight and bent crystals implemented in Geant4”, European Physics Journal C 74, 2996 (2014)

## Slide 72: Deflection Angle Distribution
Data
Geant4
Channeling
Dechanneling
Volume Reflection
Not aligned
1.
2.
3.
4.
1.
2.
3.
4.

## Slide 73: Deflection Angle Distribution
Outgoing Particles/Incoming Particles = (98.8 +/- 0.9) %
dechanneling due to elastic collision
Some particles are lost due to inelastic collisions
Geant4 model for elastic scattering

## Slide 74: Temperature Dependence (G4)
Channeling Population
Dechanneling Population

## Slide 75: Conclusions
General support for crystal structure in Geant4 is under development (release for the end of 2016).
Thanks to this implementation, each user would be able to take information of crystal structures and use them for its own processes/purposes.
Geant4 already provides support for the channeling process and the phonon transportation at low temperature in the extended/exotic examples.

## Slide 76: Thank you for your attention