## Slide 1: Development of Optical Resonant Cavities for laser-Compton Scattering
Tohru Takahashi
Hiroshima University
September 29 2016
Channeling2016@Desenzano del Garda, Italy
for
Y.Hosaka, Y. Uesugi，Y. Honda, A. Kosuge，T. Omori，T. Takahashi，J. Urakawa，M. Washio
KEK-Waseda-Hiroshima University

## Slide 2: Contents
Status and Issues of the Optical Resonant Cavity
An idea of the feedback-free cavity
Status of the R&D
  Continuous Wave -> Pulsed Oscillation

## Slide 3: Introduction
Photons by Laser-Compton Scattering
  Lower electron energy
  Polarized photons
Issue
Intensity of photons
x ray
Polarized gamma ray:
M.Fukuda. et. al, Phys. Rev. Letts. 91, 164801 (2003)
Polarized e+ ;
T.Omori, et. al, Phys. Rev. Letts 96, 114801(2006)

## Slide 4: Enhancing laser pulse energy using an Optical Resonant Cavity
O(10pm) or less

## Slide 5
29th Mar 2013
detector
Laser cavity
ATF parameter
1.3GeV
1×1010 electron/bunch
Up to 10 bunch/train
2.16×106 turn/s
Setup at the KEK-ATF

## Slide 6: 4 mirror cavities at the KEK-ATF
KEK-Hiroshima
installed 2011
LAL-Orsay
installed summer 2010
relatively simple control system
employs new feed back scheme
sophisticated control
digital PDH feedback

## Slide 7
The KEK-Hiroshima Cavity
IP
Plane Mirror
Concave Mirror
Plane Mirror
Concave Mirror
Main Parameters
Circumference: Lcav=1.68m
Finesse: F=4040(Measured)
Power Enhansement: 1230

## Slide 8: Stored Laser Power in the cavity
Stored Power [w]
Right pol
Left pol
Sotred power
Laser Power: 2.6kW
w/ 38W fluctuation
14th Sep 2012
Must be
achieved

## Slide 9: Toward High Power Storage
High reflective mirrors
  99.999%
  very low power loss O(ppm) to prevent thermal effect
  sophisticated control system
  sophisticated mirror treatment and leaning
  A Feedback free cavity
(currently ~16pm)

## Slide 10: Self- Resonating Mechanism (KEK,Waseda,Hiroshima)
Laser medium
An Optical cavity is embedded in the laser oscillation
Start laser oscillating with a wavelength selected by the cavity (positive feedback)
If the cavity length changes, the system continue or resume to oscillation with a new wavelength selected by the cavity
Cavity

## Slide 11: The optical setup
Pump LD
YDF
WDM
Coupler1
Coupler2
PBS2
QWP3
QWP2
PBS1
HWP
QWP1
FP cavity
FI1
FI2
L1
L2
PD2
PD1
PD3
M1
M2
to SP
to SP
W1
W2
FC1
FC2
Reflectivity of the cavity mirror > 99.999%
Cavity has an intrinsic finesse of 640,000
Fiber amp.
Cavity

## Slide 12: It looks,,,
Cavity
Pump LD
WDM
YDF

## Slide 13: High Finesse Oscillation (CW)
Incident power 13.5 mW
Transmitted power 4.8m W
Reflected power 2.8 mW
PD1
PD3
PD2
to SP
Cavity
Amplifier
σ ~ 1.7 %
  The Effective Finesse inc. stability of the system
  = 324,000
  Power enhancement 187,000
APL Photonics 1, 026103 (2016);

## Slide 14: Toward the mode locked pulse Oscillation
Seeding mode locked pulses with
Nonlinear Polarization Rotation (NPR) optics
NPR fiber optics

## Slide 15: Pulse Oscillation
Mode locked pulsed oscillation requires overlap of laser pulses in the
inner loop (cavity ) and the outer loop
We chose,,,,,

## Slide 16: Demonstration of the pulse oscillation

## Slide 17: Model locked pulse oscillation
After adjustment of Lloop
by hand:
requirement for pulse overlap
automatic:
requirement for
Current issue
not stable enough
the oscillation lasts a few second
but resumes by itself !

## Slide 18: Summary
R&D of optical cavities for laser-Compton light source is on going with a collaboration of KEK-Waseda-Hiroshima
Toward the High power storage in the cavity
  Precise cavity control by the feedback sysyem
  New idea to avoid precise control of high finesse is on going.
Feedback scheme
  Fineese of 4040 -> 40,000 is planed
Feeback free mechamism
  Successfully demonstrated
  High finesse oscillation with continuous wave
  mode locked pulse oscillation
  Stability and higher frequency is planned towared the Compton experiment

## Slide 19: Performance of the cavity (alone)
Finesse: F = 2πcτ / L (L: cavity length)
☆ Measured finesse:
F = 650,000 which corresponds to R = 99.99952 %
ΔL must be less than 1.6 pm to keep this cavity on resonance
Transmitted power [a.u.]
Switch OFF
Laser
1047 nm
PD
Triger signal
Decay time constant
τ = 142.5±0.1 [us]
Time [us]
Cavity

## Slide 20: Schematic
Output
Input
Isolator
Pump LD
Yb fiber amp.
Cavity

## Slide 21: Power and enhancements
Power Inside the cavity 4.2W
Incident power 0.111W
Power Enhancement 38

## Slide 22: Model locked pulse oscillation
After adjustment of Lloop
Intensity [arb. unit]
CW
Mode-Locked
Pulse

## Slide 23
Miyoshi PosiPol2010
dL∝l/enhancement ~0.01nm
for enhancement ~1000
l
Lcav