Characterisation and Comparison of Event Generators for Pair Conversion: A Crucial Step for Future Low Energy Gamma Telescopes
Philippe Gros
LLR, Ecole Polytechnique
SciNeGHE, Pisa 2016-10-18

---
- Motivation
- Conversion kinematics
- exact 5D generator validation
- Comparison of generators
  - Angular resolution
  - Polarimetry
- Conclusions

---
Telescope projects
Gaseous
HARPO
AdEPT
Emulsion
GRAINE
Silicon
e-ASTROGAM
ComPair
PANGU
- Improvement on angular resolution of tracks
  - Light (low scattering) + (very) fine point resolution
  - Better angular resolution for photon
  - Access to polarisation

---
Kinematics
- q recoil momentum
- θ+- opening angle
- x+ = E+/Eγ
- ϕ = (φ- + φ+)/2
         azimuthal angle
y
φ+
z
φ-
x
θ+-
q
γ

---
5D exact generator
- Home made generator (D. Bernard)
- Models of 5D cross-section:
  - full Feynman diagram calculation with HELAS
  - Bethe-Heitler formula
- P.d.f. generation with SPRING/BASE

---
Cross-Validation
q distributions compared to analytic formula by Jost

---
Remark:
Angular resolution vs q
- High energy approximation
  - tranverse recoil
  - small angles
  θ = q/E
- Valid within 10% above 1 MeV

---
Form factors
- Nature of conversion nuclei taken into account with form factors
- Negligible at low E
- Clear above 100 MeV

---
Available generators
- EGS5 (v1.0.6)
  - IPRDST=0
    θ+=θ-=m/E
  - IPRDST=2
    θ+,θ- independent (Schiff)
  - no conservation of energy-momentum
- Geant4 (v10.02.01)
  - emstandard G4BetheHeitler
    coplanar (φ- - φ+=π)
  - penelope G4PenelopeGammaConversion
    θ+,θ- independent (no conservation of E-p)
  - livermorepola G4LivermorePolarizedGammaConversion
    high energy approximation
    from Depaola, polarised

---
Comparison
The distribution vary between models
  - especially q, and therefore the angular resolution
  - EGS0 and emstandard are most inaccurate, as expected
  - regime changes around 200keV and 1MeV for livermorepola

---
Angular resolution
- Tracking resolution from multiple scattering
  - approximation of homogeneous tracker σ=(p/p1)-3/4
  - model differences disappear for p1=1MeV (~Fermi-LAT)
  - accurate models necessary for high resolution (e.g. gaseous tracker)

---
Momentum resolution
- Track momentum used in estimation of photon direction
- Bisector gives worse resolution at high energy (factor 3 at 100MeV)
- Rough momentum estimation (<50%) recovers most of it

---
Polarimetry
- Azimuthal angle distributions
  - Apparently consistent at high energy
  - No asymmetry in livermorepola at low energy

---
Polarimetry
dN/dϕ ∝ 1+Acos(2(ϕ-ϕ0))
- Asymmetry A is underestimated in livermorepola, especially below 50MeV (regime change)
- Phase ϕ0 varies below 50MeV;
  strange offset above

---
Remark on
Azimuthal angle
- Azimuthal angle ill defined
  - recoil angle φr
  - pair plane angle ω
  - pair bisector ϕ
- Angle ω used in previous publications underestimates A at low energy
- ϕ appears in Bethe-Heitler formula, agrees with asymptotic values

---
Conclusion
- Exact 5D generator fully validated
- Detailed kinematics of pair conversion poorly described by available generators
- Important for new generation telescopes with fine resolution/low multiple scattering
  (gas, Si only or emulsions)
- Polarisation rarely taken into account
  - only Geant4, but poorly described < 50MeV
  Be careful which generator you use!

---
Backup

---
Comparison θ+-
- EGS0 with fixed value
         θ+-E=2m
- Other models qualitatively similar
- 2 regime changes in livermorepola

---
Comparison x+
- All models consistent
- small offset around 1MeV for emstandard and livermorepola models

---
Comparison q
- Very different results from generators
- No FF in Geant4 and EGS5
- EGS (IPRDST=0) and emstandard inappropriate