## Slide 1: LCLS Injector Improvements & Plans
Feng Zhou
SLAC
Presented at HBB, Havana, Cuba, March 29, 2016

## Slide 2: What are the major impacts on 24/7 LCLS injector performance?
LCLS injector routine projected emittance for hard x-ray FEL (2014-2016)
24/7 LCLS injector emittance is mainly impacted by:
Drifting of laser location on Cu photocathode
Changing of UV drive laser spatial performance

## Slide 3: LCLS injector improvements
Boosted QE by 25-30 times w/ laser cleaning on the LCLS Cu cathode, which has operated for 5 yrs.
Improved emittance and better understood injector emittance measurements:
  Applied truncated-Gaussian laser for emittance reduction
  Developed laser profile tolerances for maintaining ultra-low emittance
  Lengthened laser pulse for emittance reduction
  Reliably characterized injector emittance
What is the next?
  Shaping laser with spatial filter
  Shaping e-beam with transversely circular collimator

## Slide 4: LCLS laser cleaning in 2011: QE/emittance evolution
QE increased by 25-30 times compared with original 5e-6:
  QE was increased by ~8 times upon the laser cleaning
  QE was further increased by 3-4 times in the first 6 months following laser cleaning
Emittance recovery took 2-3 wks:
  High-power RF conditioning may improve e- emission profile
Provided a very simple but a very robust way for XFEL application
OTR emittance

## Slide 5: We can do better w/ laser cleaning …
  Improved laser cleaning procedures at the gun test bed resulting in much better QE and emittance evolution.
Next day after cleaning
Immediately after cleaning
F. Zhou et al., NIM A 783 (2015)
~3 wks QE ~1e-4

## Slide 6: After ~5 years 24/7 operations
electron/ion back bombardment effect
2 mm
1.2 mm laser size
QE: 1.5e-4 of QE
2 mm
Optimized projected x ~0.4 µm @250pC

## Slide 7: Truncated-Gaussian laser for operations
  Implemented truncated-Gaussian laser profile for the routine operations:
    Improved injector emittance
  Laser power needed from laser systems is reduced by about 3 times with truncated-Gaussian laser on the cathode compared with the one with pseudo-uniform laser:
    Relaxed laser system significantly
F. Zhou et al., PRST-AB 15, 090701 (2012)
150 pC

## Slide 8: Spatial laser profile tolerances: w/ lineout method
How to define/maintain the desired laser profile for 24/7 operations??
Spatial laser tolerances can be characterized with simple lineout method when the laser is reasonably clean
Laser profile tolerances, such as g/h, a1/a2, are strongly required for maintaining good laser profiles.
simulated lineout profiles

## Slide 9: Laser profile tolerance: w/ lineout method
For <5% of emittance growth, the spatial laser requirements:
    g/h: 1±0.25
    a1/a2: 1±0.3
Simulation
a2
a1

## Slide 10: General method: w/ Zernike modes
  Zernike functions are orthogonal over the unit circle:
  where
  The coefficients for Zernike modes
Actual laser profile is represented:
    Symmetry power Psymmetry:
(n0)
    Asymmetry power Pasymmetry:
(m0)
Example: 21 Zernike modes Znm
F. Zhou et al FEL15

## Slide 11: Zernike method: measurements Requirements: Psymmetry 0.025-0.04; and Pasymmetry <0.015
Psymmetry: 0.025-0.04
Pasymmetry: <0.015
(a)
(c)
(b)
(a): pseudo-uniform
(c): truncated Gaussian
(b): truncated Gaussian
measurements
measurements

## Slide 12: Laser temporal requirement: stacking 2ps lasers with 1.5-2ps separation
  LCLS typical laser pulse ~2ps FWHM of Gaussian
  Pulse stacking with s- and p-polarization with 1.5-2ps separation to lengthen the pulse length
  Compromise RF emittance w/ space charge emittance
simulations
measurements
simulations
measurements

## Slide 13: Better understanding LCLS Injector emittance measurement
OTR light for different quad settings
Laser heater chicane ON
Laser heater chicane OFF
OTR light fir different quad settings
  Injector emittance measured with an OTR screen (downstream of laser heater chicane) is underestimated:
    -bunching through the small laser heater chicane makes core beam brighter resulting in smaller beam size
F. Zhou et al., PRST-AB, May 2015

## Slide 14: Crosscheck slice-emittance measurement w/ BC1 collimator
  Measured projected emittance for the sliced beam in the non-bending plane  injector emittance.
  Measured projected emittance for slice beams in the bending plane is 25% larger than the injector emittance:
    it includes CSR effect – cannot be used for slice emittance measurement for the bending plane
F. Zhou et al., PRST-AB 18, 050702 (2015)

## Slide 15: What is the next? - clean spatial laser w/ spatial filter
Studying 4 major issues before implementing it to LCLS drive laser system:
  Damage issues
  Beam loss
  Pointing stability
  Reliability
Alan Fisher

## Slide 16: What is the next? - clean e-beam w/ circular collimator
With circular collimator, only dipole wake contributes to emittance growth:
  25m tolerance is required to control emittance growth <1% for 0.3mm aperture (Bane).
40% emittance reduction is expected from simulations
Study is planned before implementing it to LCLS:
  Full simulation for FEL with circularly collimated beam
  Reliability of controlling 25um transverse tolerance
40% reduction
Candidate collimator location

## Slide 17: Summary
QE is increased by 25-30 times with laser cleaning. The cathode has operated for 5 yrs.
Optimized projected emittance is ~0.4m for 250pC:
  With truncated Gaussian spatial laser; defined/controlled spatial laser profile
  With stacking of 2-ps pulses lengthening temporal laser
Reliably characterized injector emittance measurements
Near-term plans:
  Shaping laser with spatial filter and
  Shaping e-beam with circular collimation