## Slide 1
EuroGammaS Association
Physics and Applications of High Brightness Beams – Havana, Cuba – March 28th/April 1st 2016
EuroGammaS Gamma Characterisation System for ELI-NP: The Nuclear Resonance Scattering Technique
Maria Grazia Pellegriti
INFN-Sezione di Catania- Italy

## Slide 2
Outlook
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
Magurele, Romania
See talks of A. Variola and G. Palumbo
 | Eg (MeV) | DEg (%) | Ibw (ph/sec)
ELI-NP | 0.2-19.5 | 0.5 (rms) | 8.3∙108 (FWHM)
Eli-np facility
The accelerator and the Gamma characterization system
Compton System, Calorimeter, Imager
Nuclear Resonant Scattering System

## Slide 3
Photoinjector
Low Energy Line
High Energy Line
High Energy
Laser
Interaction
Chamber
Linac
Low Energy
Laser
Interaction
Chamber
For the two beam-lines (high and low energy), two identical complete systems for collimation and characterisation of the gamma beam will be delivered, each one optimized for the corresponding energy range.
Machine layout
Low energy
collimation and
characterisation system
High energy
collimation and
characterisation system
Measurement of the gamma beam energy distribution
Measurement of the number of photons per pulse
Measurement of the size and spatial distribution of the gamma beam
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy

## Slide 4
Gamma beam characterization system
Compton
Spectrometer
Nuclear resonant
scattering System
Profile
imager
Calorimeter
    Compton Scattering Spectrometer
high–precision measurements of single Compton scattering from thin target
    Absorption Calorimeter
    calorimetric, total absorption technique
    Profile Imager
    Nuclear Resonant Scattering calibration System
high-precision energy measurement at selected energy values for absolute energy calibration
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
g-beam

## Slide 5
Compton Spectrometer
Micrometric target is micrometric (1-2 µm) and low-Z material
High resolution electron detectors -> HPGe (energy) + Si-strip (position)
Measure also the scattered gamma in coincidence for background reduction
Energy detector
Position detector
Cu collimator
Be-window
300 µm thick n-type silicon
25.5 µm/66.5 µm pitch for the X/Y side
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
g
g’
e-
f
Gamma energy is obtained by measuring Compton scattered electron energy
g-beam

## Slide 6
Gamma calorimeter
Plastic converters
Si detectors
Longitudinally segmented calorimeter
Stack of 25 plastic converters (low Z) interleaved by Si detectors
For increasing gamma energy the cross-section decreases -> shower depth increases
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy

## Slide 7
Profile Imager
The gamma profile Imager is is composed by a cross vacuum chamber in which scintillator targets intercept the gamma beam at 45°.
The light emitted by the scintillator is acquired using a mirror and lens system to focus onto a CCD camera.
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
Gamma beam
Scintillator targets
vacuum chamber
CCD

## Slide 8
Nuclear Resonant Scattering System – Concept
Task: Provide an absolute energy scale calibration for other detectors
Working principle: detection of the gamma decays of properly selected nuclear levels of a given nucleus X when resonant condition with the beam energy is achieved
Performing a scan of the beam energy
Er
Eg
the resonant energy Er can be matched through the detection of the corresponding
decay photons Eg
Eg
X
CROSS-SECTION
ƛ2
Level total width
Ground state spin
excited level spin
width for gamma transition to ground state
width for transition
to a specific channel
Metzger F.R., Progress in Nuclear Physics 7 (1959) 53
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
Examples: 26Al: 2.982 MeV; 2.212 MeV
12C: 4.439 MeV; 15.11 MeV
9Be: 2.429 MeV
6Li: 3.563 MeV

## Slide 9
Electron energy tuning
Beam steps
Beam steps
NRSS counts
Photon density
dE < DE 0.3%
DE
Nuclear Resonant Scattering System – Concept
 < DE
Perform an energy scan of the beam and precisely identify the resonant energies, by detecting the corresponding characteristic gamma emissions
  Very narrow lines!!!! (43.6 eV for the 15.11 MeV C12 line)
   Very accurate calibration
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy

## Slide 10
Gamma
beam
Gamma
counters
Gamma
spectrometer
Target
Set of thin targets made of materials with precisely known gamma de-excitation emission spectra.
Detector:
Gamma counter, for fast energy scan to provide a prompt information on the established resonant condition; good energy resolution not required, high overall efficiency needed.
Gamma spectrometer, aimed to precisely identify resonant excited levels, in particular when a complex decay pattern is expected.
Nuclear Resonant Scattering System – Design
135°
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
n.1 central LYSO
n. 4 BaF2 counters
g-beam
Pb shields
Target
shifter

## Slide 11
Fast Counting Mode and timing
10 ns
BaF2 coupled with
the R2078 PMT
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
Pulse to pulse separation=16 ns
16+16=32 pulses
MACRO-PULSE
Pulse lenght= 0.91 ps
Macro-pulse
repetition rate =100 Hz
Fast component: 0.88ns; Slow component: 600ns

## Slide 12
Simulation: efficiency
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
BaF2
LYSO

## Slide 13: Thanks for the attention!
PAHBB - Havana, March 29th 2016
Maria Grazia Pellegriti - INFN, Sezione di Catania - Italy
13

## Slide 14
EuroGammaS Association
Physics and Applications of High Brightness Beams – Havana, Cuba – March 28th/April 1st 2016
WP09-Collaboration
M. Gambaccini , P. Cardarelli, M. Andreotti, E. Consoli, F. Evangelisti , G. Di Domenico , M. Marziani , M. Statera
INFN – Ferrara
M. Veltri, O. Adriani , G. Graziani , G. Passaleva, R. Borgheresi, M. Lenzi, A. Serban , O. Starodubtsev
INFN – Firenze
S. Albergo , G. Cappello, A. Tricomi , M.G. Pellegriti, B. Zerbo
INFN - Catania