## Slide 1
O
E
S
VOXES, a new high resolution X-ray spectrometer for low yield measurements in high background environments
Alessandro Scordo
Laboratori Nazionali di Frascati, INFN
Workoshop “Developement of novel detectors at LNF”, Frascati, 14-06-2016
X

## Slide 2
Project’s goal
VOXES’s goal: to develop, test and qualify the first prototype
of ultra-high resolution and high efficiency X-ray spectrometer in
the range of energies 2 - 20 keV using HAPG bent crystals in the
von Hamos configuration able to work in high background environments
Ultra high resolution (few eV) measurements of the X rays (2-20 keV) emitted in various processes is strongly demanded in: particle and nuclear physics, fundamental science, astrophysics, biology, medical and industrial applications
Additionally, the realisation of such X-ray detector systems able to work in high background environments is badly needed.
Grant Giovani CSN-5 (INFN) n. 17367 (2015)

## Slide 3
An example: the K- mass puzzle
K- mass is a fundamental quantity in physics
to reduce the electron screening effect
Needs precision below 0.1 eV!

## Slide 4
The solid state detectors have intrinsic resolution (FWHM ~ 120 eV at 6 keV) given by the electronic noise and the Fano Factor
Commonly used detectors for X-rays in the range 1-20 keV are the Solid State Detectors (CCD, SDD, etc…)
However…
Presently, to achieve ~ 1 eV resolution, two options are available:
Transition Edge Sensors (TES)
Crystals and CCDs (Bragg spectrometers)

## Slide 5
TC ~ 50 mK !!!
Transition Edge Sensors (TES).
Excellent energy resolution (few eV at 6 keV)
LIMITATIONS:
not optimised for E < 5 keV
very small active area
prohibitively high costs
rather laborious use (complex cryogenic system needed)

## Slide 6
High resolution can be achieved depending on the quality of the crystal and the dimensions of the detectors
Geometry of the detector determines also the energy range of the spectrometer
Limitation in efficiencies
But….
Crystals response may not be uniform (shape, impurities, ecc.)
Lineshapes are difficult to be measured within few eV precision (surface scan)
In accelerator environments particles may hit the detector
Background reduction capability is mandatory

## Slide 7
VOXES: the 3 pillars
Integrate :
(1) focusing properties of the von Hamos scheme with the
(2) high efficiency and resolution of HAPG mosaic crystals and
(3) use triggerable detectors to dramatically reduce
background in a new detector system capable to perform

## Slide 8
Mosaic crystal consist in a large number of nearly perfect small crystallites.
Mosaicity makes it possible that even for a fixed incidence angle on the crystal surface, an energetic distribution of photons can be reflected
Increase of efficiency
(focusing) ~ 50
Loss in resolution
Pyrolitic Graphite mosaic crystals (d = 3.354 Å):
Highly Oriented Pyroliltic Graphite (HOPG)
Highly Annealed Pyrolitic Graphite (HAPG)
flexible HAPG has twice higher spectral resolution, while flexible HOPG – approximately twice higher reflectivity
Resolution of E/∆E=7000 for (004) reflection at 15 µm HAPG film @ 8 keV (1,1 eV)

## Slide 9
Production
Thermo cracking of CH4
on heated substrate at T=2100oC
Pyrocarbon d002=3,44Å, mosaicity 30o
Annealing under pressure at T>2800oC
Pyrographite:
HOPG d002=3,356-3,358Å, mosaicity <1o
HAPG d002=3,354-3,356Å, mosaicity <0.1o

## Slide 11
Bending does not influence resolution and intensity
Mosaic spread down to 0.05 degree
Integral reflectivity ~ 102 higher than for other crystals
Variable thickness (efficiency)
Excellent thermal and radiation stability
Von Hamos configuration: Cylindrically bent crystal combines mosaic focusing in diffraction plane with sagittal focusing.
E/∆E & efficiency are one order of magnitude better than expected from the crystal mosaicity only
Already tested with 500 m slits
VOXES wants to go further

## Slide 12
In accelerators (and not only) environment experiments, X-rays have to be discrimated from charged particles on the detector
CCD:
Background reduction with an algorithm based of the number of fired pixels
SDD:
Background reduction thanks to trigger capability
Already used in the SIDDHARTA experiment giving a factor 105 reduction factor
Even better

## Slide 13
HAPG optics in VH geometry allows:
To reach energy resolution at the level of eV in a broad X rays energy range (2 – 20 keV)
To get efficiencies ~102 than for any other crystal in the flat geometry
To develop a compact spectometer, with moderate cost, which could be easy moved and installed at a new place
The von-Hamos focusing geometry gives high collection efficiency:
evH/eflat ~ Rθ/a
radius of curvature angular aperture source size
Source size can be increased playing with the R of the crystal allowing high efficiency for larger sources

## Slide 14
The research activity aims to the construction of an X-ray spectrometer, consisting in three von Hamos spectrometers (VH units), each optimised for a specific energy range, E1<E<E2 and it will be realised in two phases:
First phase:
R&D on HAPG and optimisation
Detailed Monte Carlo simulations
Single VH unit design and construction
System debug and characterisation in the
laboratory, using targets activated by an
X-ray tube
AIM: optimize the acceptance (source size) and energy resolution
Second phase:
Mcarlo simul. design, and construction of the final VOXES system prototype: 3 VH units
Use of SDDs
Final Slow Control & DAQ software
Debug, test and calibration @ LNF
Pionic helium measurement at PSI
AIM: VOXES qualification by the measurement of the pionic helium X-ray lines @ PSI with:
FWHM < 5 eV
efficiencies ~102 than for previous
measurements (VH, HAPG, SDD)
Additionally:
Implement a strategy for the kaonic helium and kaon mass measurements at DAFNE or at JPARC using SDDs.
Organise a dedicated workshop where to invite representatives of the potentially interested companies/industries and other interested users

## Slide 15
E ~ 16 keV
B~ 7 ° (n=1)
B~ 13 ° (n=2)
HAPG
CCD / SDD
Signal X-Rays
Reflected X-Rays
Target
Rails
E ~ 4 keV
B~ 27 ° (n=1)
B~ 67 ° (n=2)
E ~ 10.6 keV
B~ 10 ° (n=1)
B~ 20 ° (n=2)
The VOXES final prototype will consist in 3 VH units:
10.6 keV -> He
4.5 keV -> Ti (calib)
15.8 keV -> Zr (calib)
Target:
Ti, Cu, Br, Zr foils + X-ray
tube (calibration and test)
Cryogenic targets for He
circular rail to collect the different Bragg angles
HAPG-SDD/CCD unit rotate on its central axis to optimise the X-ray collection and focusing.

## Slide 16
He is particularly interesting because the helium nucleus is small and the nucleons are tightly bound
Few (and old) precision measurements of pionic transitions in light elements showed that the experimentally determined energy shifts and widths of the 1s level due to strong interaction effects do not agree with theoretical models
Useful to understand low energy QCD (non-perturbative region)
Old Si(Li) experiment (Batty, 1979)

## Slide 17
Kaonic helium is formed when a K- is captured in the electron orbit
It down cascades toward the lowes levels emitting X-rays
To test the influence of the strong interaction the energy a precise measurement of the line shift and width of the 3d->2p transition is needed
The discrepancies between different theoretical models and approaches could be eliminated with ~ 1eV precision measurement
Best measurements (SIDDHARTA):
 
4He +5 ±3 (stat.) ±4 (syst.) 14 ±8 (stat.) ± 5 (syst.)
3He −2 ±2 (stat.) ±4 (syst.) 6 ±6 (stat.) ±7 (syst.)
New measurements are needed

## Slide 18
http://pdg.lbl.gov/2015/reviews/rpp2014-rev-charged-kaon-mass.pdf
(6→5) kaonic nitrogen transition: 7560± 32 eV,
(7→6) kaonic nitrogen transition: 4589± 37 eV.
Exploratory test with DEAR @ DANE
Not yet performed
Calculated efficiency ~ 400 times less than @ DAFNE
Un-efficient background reduction (statistics loss)

## Slide 19
High precision values for the hadronic shift
and width of the 1s ground state of pionic hydrogen
high pion flux in E5 at PSI
p=112 MeV/c, ~ 109 -/s
Light weight cryogenic target
for wide density range
spherically bent Bragg crystals (Silicon)
position sensitive X-ray detection with CCD array:
CCD-22 (600x600 pixel) in 2x3 matrix,
background reduction by shielding and pixel analysis
calibration lines (pionic oxygen) measured in parallel
Goal:
 ~ 7 eV
 ~ 1 eV
Problems in the measurement:
Too low rate to obtain results on the response lineshape of the spectrometer !

## Slide 20
O
X
E
S
HAPG technology development
Medical Applications
(Mammography)
Foundations:Quantum Mechanics
Industry, art and Safety: Elemental Mapping
Particle and Nuclear Physics
X-ray spectroscopy (DANE-Luce)
JPARC
(K-atoms)
PSI
(-atoms)
DANE
(K-atoms)
LNGS
(PEP)
FAIR
(exotic atoms)

## Slide 21
Crystals optimization and construction
Mechanical setup &
SlowControl & DAQ
Vacuum and cryogenic for target and detectors
Detectors & electronics assembly
Single VH unit
Pionic atoms measurement at PSI
Final VOXES prototype
Laboratory tests
LNF
OPTIGRAPH
LNF
SMI
LNF
POLIMI&FBK
DATA analysis and publications
LNF
DATA analysis
LNF
SMI
SMI
Coordinating Unit: LNF-INFN
Duties: DAQ, detector assembly and tests
SMI-Vienna
Duties: cryogenic and vacuum systems, mechanics design and realisation, detector assembly and tests
Optigraph
Duties: HAPG design (MC) & production
Politecnico Milano & FBK
Duties: Detectors & electronics

## Slide 22
Starting VOXES:
first tests with HAPG crystals
First stage measurements (efficiency):
Ti, Cu, Br, Zr (activated with X-Ray tube)
Direct detection with a XR-100CR Si-PIN X-Ray Detector
Different r crystals (10.6 mm & 206.7 mm)  efficiency
Different thickness (20,40,100 mm)  efficiency
r = 10.6 mm
100 mm
r = 206.7 mm
100 mm
r = 206.7 mm
40 mm
r = 206.7 mm
20 mm

## Slide 23
Starting VOXES: test Setup
Designed by Nicola Intaglietta
LNF services

## Slide 24
Starting VOXES: test Setup
Printed with the 3D printer @ LNF

## Slide 25
Location for VOXES development
Laboratory equipped with optical bank @LNF
Bunker for radioactive sources @LNF
Inside the bunker

## Slide 26
VOXES develops an innovative ultra-high resolution X-ray spectrometer
prototype, badly needed in various fields of research and technological
applications
VOXES will realise a feasibility demonstration through a preliminary measurement with high scientific impact (pionic helium at PSI)
Thank you for the attention
To achieve its goal VOXES sets up a highly qualified multi-disciplinary international network, with contacts with the world-leader producer of HAPG (Optigraph)
VOXES introduces a new technology in INFN, having high potential for
applications inside INFN (DANE-Luce, SIDDHARTA, VIP@LNGS) and in
external facilities (JPARC, PSI, FAIR), in strong contact with world-leader
institutes (PoliMi, SMI, FBK) and crystals producer (Optigraph)