## Slide 1: APSEL6D Architecture, simulations and results
SuperB Meeting – Perugia, 6/16/2009
Filippo Giorgi - INFN Bologna

## Slide 2: Outline
Expected Target Conditions
Matrix Architecture
Readout architecture
Simulations
Efficiencies
Summary

## Slide 3: Target Conditions
100 MHz/cm2 hit rate:
    25 MHz/cm2 track rate (includes x5 security factor)
    4 MHz/cm2 cluster factor
160 Mhit/s chip bandwidth
0.25 – 2.0 µs BCO clock:
    Time Counter clock, represents the time granularity of the events.
60-100 MHz Matrix Read Clock

## Slide 4: The Matrix Architecture
Common Pixel Data Bus – Active 1 column of pixel at a time
Pixel Matrix
Active Column

## Slide 5: The Matrix 320x256 (40µm pitch)
256 pxl
4 horizontal parallel scans for the Active Column
80 x 256 pxl, 40 microns pitch
4 independent
Submatrix
AC
AC
AC
AC
80K pixel matrix
Total area ~ 1.3 cm2
130 Mhit/s
80 x 4 = 320 pxl
1 000 pixels analyzed in 1 CLK cycle

## Slide 6: Submatrix Scan Policy
Column scan time oriented: 1 scan for each Time Stamp
 The hits are time sorted

## Slide 7: The Macro Pixels
Matrix divided into MPs: group of pixels (2x8)
  MP global lines:
    Fast-OR line: (output) inclusive OR of all pixels.
    Freeze line: (input) disable the reception of new hits.
  On BCO clock edge all MPs with active fast-OR :
    Gets frozen
    Are associated to the current value of BCO counter (Time Stamp)
    Waits to be scanned and reset
Active Fast-OR
MP gets frozen
BC edge
Time
MP reset after read
TIME STAMP

## Slide 8: Zone sparsification of the Active Column
TS
The 256 pixels of the Active Column are divided into 32 vertical zones (1x8 pixels each)
Every HIT stored contains the information of a zone, not of a single pixel:
  HIT= (Zone address+ Zone pattern)
    X zone address = Column address : 80 columns 7 bit
    Y zone address : 32 vertical zones  5 bit
    Zone pattern: 8-pixel zone  8 bit
Time Stamp: since the hits are time sorted, the relative TS word is stored at the beginning of each hit sequence
Zone 0
Zone 1
Active Column
Active
Column

## Slide 9: The sparsifiers and barrels
ACTIVE COLUMN
64 PXL
64 PXL
64 PXL
64 PXL
Barrel: an asymmetric FIFO with variable input width:
  from 1 to 8 hits stored per clk cycle.
N Hit to write
8-hit wide BUS
1 Hit BUS
8 zones
8 zones
8 zones
8 zones

## Slide 10: Sparsification and barrel trees
80
80
80
80
Common output stage
Each submatrix scan has its own readout – all working in parallel

## Slide 11: Output stage
FULL resolution Hit + time stamp
  8 bit TS (modulo 256 BCO counter)
  9 bit X address (320 pixels)
  8 bit Y address (256 pixels)
  TOT 25 bit
   expected rate 130 MHit/s per chip = 130MHz x 25bit = 3.2 Gbps
Zone sparsification & time sorting of the hits (TS heading the relative hits) lead to:
  2 bit Barrel L2 address (1/4 of submatrix: 80x64 pxl)
  2 bit Barrel L1 address (1 submatrix: 80x256 pxl)
  7 bit X address (80 pixels)
  3 bit zone Y address (8 vertical zones for each L2 barrel)
  8 bit zone pattern
  TOT 22 bit
   expected rate: 130 (+1 TS) * 22 = 2.8 Gbps
   [(22*2)* 0.875 + (22*4)*0.125 ] *25 Mtrack s-1 cm-2 * 1.3 cm2
    Weighted average ~ 1.6 Gbps
BUT: Considering the cluster factor x4 of the expected rate in the form 2x2:
in 87.5% of cases 2 hits only & in 12.5% are required 4 hits

## Slide 12: The components simulated:
Sub Matrix
Scan Control
Freezer
Scan Buffer
TS + MP pattern
2nd layer barrels (B2)
1st layer barrel (B1)
Concentrator
Sparsifiers
All the models are described using synthesizable VHDL
NB: Full B1 output bandwidth supposed available (1 hit/clk cycle)

## Slide 13: Study on Barrel optimal Depth:
Expected rate @B2: 8,2 MPxl/s
Expected rate @B1: 32,8 MPxl/s
B2
A
B
B counts/
A counts
Barrel depth
Barrel clock 40 MHz
Forbidden region
Mean input rate > ouput throughput
Barrel inefficiencies due to fluctuation over the mean rate

## Slide 14: Frozen Efficiency @ 100 MHz/cm2
frozen effi. |  |  |  |  |  | 
 |  |  |  | BCO (us) |  | 
 |  | 0,25 | 0,5 | 1 | 1,5 | 2
 | 100 | 99.7 | 99,5 | 99,3 | 99,2 | 99,0
Rd_clk (MHz) | 80 | 99,6 | 99,4 | 99,1 | 99,1 | 98,8
 | 60 | 97,5 | 98,9 | 98,8 | 98,8 | 98,4
Chart: 
| 0.25 | 0.5 | 1 | 1.5 | 2
60 | 97.5 | 98.904 | 98.832 | 98.776 | 98.42
80 | 99.6 | 99.385 | 99.095 | 99.05 | 98.808
100 | 99.7 | 99.528 | 99.25 | 99.23 | 99.035
BCO period (us)
%
Fast read clock and narrow BC edges
Barrels efficiency 100%
No barrel overflow
(B2 and B1)
Readout efficiency not
100% :
Scan buffer overflow
NB: for 200 MHz/cm2 minimum Rdclk 80MHz and efficiency with BC=1 us is 97.6%

## Slide 15: Slow Control : I2C-like system
slave
slave
slave
slave
slave
slave
½ Modulo:
6 APSEL 6D
I²C : two bidirectional open-drain lines.
Serial Data (SDA)
Serial Clock (SCL), pulled up with resistors.
SDA
SCL
VDD
001
010
011
100
101
110
Hard Wired Addresses
DAQ
BUS master
Registers R/W access communication type

## Slide 16: Conclusions
Study conducted to point out the optimal readout policy and architecture.
A parametrized model has been coded with synthesizable VHDL.
Simulations perfomed allowed a fine adjustment of the free parameters, and showed for a “typical” configuration a global readout efficiency: above 98,4%
Works in progress:
  Realization of the final output stage
  I2C like interface for slow control
To Do
  Service infrastructure (killmask, MP mask, calib facilities…)
  Selection of the elements to be implemented in the sett 09 chip

## Slide 17: BackUp Slides

## Slide 18: Macro Pixel Cycle

## Slide 19: 2D scan BCO vs RDclk @ 1MHz/mm2
RN | sim DURATION (us) | RDclk (MHz) | BCO (us) | Mean Sweeping time (us) | global hit rate (MHz) | rate on area (MHz/mm2) | B2 depth | B1 depth | B1 max fill | B1 mean fill | BC lost | Already hit effi (%) | frozen effi (%) | ro effi B2 (%) | ro effi B1 (%)
107 | 1 | 60 | 0,5 | 0,45 | 33,8 | 1.03 | 8 | 32 | 5 | 1 | 0 | 99,96 | 98,90 | 100 | 100
108 | 1 | 80 | 0,5 | 0,34 | 33,8 | 1.03 | 8 | 32 | 5 | 1 | 0 | 99,95 | 99,39 | 100 | 100
109 | 1 | 100 | 0,5 | 0,27 | 33,8 | 1.03 | 8 | 32 | 5 | 0 | 0 | 99,96 | 99,53 | 100 | 100
110 | 1 | 60 | 1 | 0,75 | 33,8 | 1.03 | 8 | 32 | 8 | 1 | 0 | 99,91 | 98,83 | 100 | 100
111 | 1 | 80 | 1 | 0,56 | 33,8 | 1.03 | 8 | 32 | 9 | 1 | 0 | 99,91 | 99,10 | 100 | 100
112 | 1 | 100 | 1 | 0,45 | 33,8 | 1.03 | 8 | 32 | 9 | 1 | 0 | 99,91 | 99,25 | 100 | 100
113 | 1 | 60 | 1,5 | 0,95 | 33,8 | 1.03 | 8 | 32 | 19 | 1 | 0 | 99,86 | 98,78 | 100 | 100
114 | 1 | 80 | 1,5 | 0,71 | 33,8 | 1.03 | 8 | 32 | 18 | 1 | 0 | 99,86 | 99,05 | 100 | 100
115 | 1 | 100 | 1,5 | 0,57 | 33,8 | 1.03 | 8 | 32 | 18 | 1 | 0 | 99,86 | 99,23 | 100 | 100
116 | 1 | 60 | 2 | 1,08 | 33,8 | 1.03 | 8 | 32 | 24 | 3 | 0 | 99,84 | 98,42 | 100 | 100
117 | 1 | 80 | 2 | 0,81 | 33,8 | 1.03 | 8 | 32 | 23 | 2 | 0 | 99,83 | 98,81 | 100 | 100
118 | 1 | 100 | 2 | 0,65 | 33,8 | 1.03 | 8 | 32 | 23 | 2 | 0 | 99,83 | 99,04 | 100 | 100