## Slide 1: Beam test facility (BTF)
Paolo Valente*, Bruno Buonomo, Luca Foggetta, Claudio Di Giulio
*INFN Roma
LINAC technical staff
Maurizio Belli, Riccardo Ceccarelli, Alberto Cecchinelli, Renato Clementi, Graziano Piermarini, Serena Strabioli, Luis Antonio Rossi, Raffaele Zarlenga
BTF support team
Francesca Casarin, Maria Rita Ferrazza, Manuela Giabbai

## Slide 2: BTF & DAFNE
BTF
BTF
Control room
Damping
Ring
Transfer line
Transfer line
LINAC
Power supplies
The complex:
Started mid ’90
Commissioning of KLOE 1999
Collisions at the F (1020 MeV/c2)
Beam-test facility (2004)
Synchrotron radiation lines
Main rings
Notes: La BTF nel complesso DAFNE e’ situata alla fine del LINAC. Questo permette di estrarre fasci di elettroni e positroni prima dell’iniezione nel ring attraverso una linea di trasferimento dedicata.

## Slide 4: DAFNE LINAC
 | Progetto | Prestazioni
Energia Finale fascio e- | 800 MeV | 510 MeV
Energia Finale fascio e+ | 550 MeV | 510 MeV
Radio Frequenza | 2856 MHz | 
Energia Conversione e+ | 250 MeV | 220 MeV
Freq. ripetizione impulso | 1 to 50 Hz | 1 to 50 Hz
Lunghezza impulso | 10 ns | 1.4 to 40 ns
Corrente del gun | 8 A | 8 A
Dimensioni del fascio sul convertitore e+ | 1 mm | 1 mm
Emittanza Normalizzata (mm mrad) | 1 (e-) 10 (e+) | < 1.5
RMS Energia | 0.5% (e-) 1.0% (e+) | 0.5% (e-) 1.0% (e+)
Corrente elettronica sul converitore e+ | 5 A | 5.2 A
Massima corrente per e- | >150 mA | 500 mA
Massima corrente per e+ | 36 mA | 85 mA
Efficienza di trasporto dalla conversione alla fine del LINAC | 90% | 90%
Strutture acceleranti | SLAC-type, CG, 2π/3 | 
Sorgenti and amplificazione Radio Frequenza | 4 x 45 MWp SLED-ed klystrons TH2128C | 
TITAN Beta (Ca,USA) 1995
S-band, 60 m long, 3,05 m long SLAC-type, TW, CG, 2/3π sections
High current thermo-ionic gun, four RF stations, 45 MWp klystrons (Thales) with SLED compression.
Strong consolidation and upgrade activity started in 2012
10 ns pulses delivered to collider
Notes: Il LINAC di DAFNE è un acceleratore lineare costruito dalla TITAN Beta (Ca,USA) ed installato alla fine del 1995.
L’ acceleratore lineare e’ lungo ~60 m ed e’ in banda S-band.
E’ composto di un gun termoionico, quattro klystrons da 45 MW con l’amplificazione fornita dagli SLED, e da 15 guide d’onda di tipo 2/3π di tipo SLAC con sezioni acceleranti lunghe 3 m.
L’energia finale raggiungibile dagli elettroni e’ 800 MeV dai positroni 550 MeV la duranta dell’impulso microbunchato va da 1.4 a 40 ns.

## Slide 5: The Beam-Test Facility (BTF)
Starting from 1010(109) electrons (positrons) from the linac, it operates mainly in two different intensity regimes:
  High intensity primary beam driven to the experimental hall, between 250 MeV and Emax, tuned with collimators
  Single particle/bunch (Poisson distribution) between few tens of MeV and Emax, created intercepting the beam with a variable depth copper target, selecting the energy and collimating.
Intermediate intensity (<105 particles/bunch) is possible
Primary beam fixed to E=510 MeV and Dt=10 ns during operations of DAFNE collider (“parasitic” operation)
Wider range can be covered (higher energy, longer pulses, etc.) in dedicated operation (no injections)

## Slide 6
Copper target≈2x0, collimation and magnetic momentum selection
< 4 mrad
Maximum input divergence:
Energy resolution:
d≈0.25 mm
D=60 mm
Out of target
10-1
10-3
10-5
10-7
10-7
10-6
10-5
10-8
10-7
10-6
10-5
10-8
1 (E0)
0.8
0.6
0.4
0.2
0
1 (E0)
0.8
0.6
0.4
0.2
0
1 (E0)
0.8
0.6
0.4
0.2
0
Target
Energy spread (LYSO)

## Slide 7: Low intensity tuning
Tuning the number of particles can be achieved:
Without changing the momentum resolution:
  Modulating the LINAC current [not possible in ‘parasitic mode’, rough] (transport optics or modulators power/phase, etc.)
  Collimating the beam before the target, using the up-stream vertical slits [large range]
  Choosing one of the three target depths [step change, very reproducible]
  Collimating the beam after the dipole, using the down-stream vertical slits [fine, small range]
Also changing the momentum resolution:
  Closing/Opening the horizontal collimators [both upstream and downstream]

## Slide 8: “High” intensity
Primary beam focused, scrapered and transported to the BTF hall
Radio-protection limit: 3.125 ×1010 particle/s
Photo-production of neutrons on dedicated target

## Slide 9
Improved shielding in BTF hall
Dismantling of existing shielding blocks on Jul. 13th
Complete refurbishing of the experimental hall (ducts, cabling, electricity, safety systems…)
Sep. 7th: start new block-house installation

## Slide 10: High intensity/high energy electrons
Typical charge to damping ring with 10 ns pulses at 50 Hz:
  1 to 2 nC/pulse for e-
  0.7-0.8 nC/pulse for e+
But…
  Much higher charge is driven onto the converter during positron production
  Indeed up to 8 A (12 A) can be drawn from the gun cathode
ICT readout (e+ injection)
Extracted charge can be increased:
At constant current (no saturation), by simply increasing the pulse duration to the gun
Increasing the pulse height of applied voltage
Decreasing the stopping voltage applied to grid
0.5 to 40 ns
300 to 750 V

## Slide 11: n@BTF
Viene fatto collidere con un bersaglio di Tungsteno.
Gli elettroni di alta energia producono uno spettro continuo di fotoni per bremsstrhalung. Questi possono generare neutroni attraverso reazioni foto-nucleari se la loro energia è almeno uguale all’energia di legame dei neutroni nel bersaglio.
Il numero di neutroni dipende dalla potenza rilasciata nel bersaglio:
  P = rate×energia =[N×f]×E
    N = numero di particelle per bunch (1×1010)
    f = frequenza (1-49 Hz)
    E = Energia dle fascio (510-800 MeV)
  Potenza massima: 40 W a 510 MeV
Swanson: 1011n per W, 8.8×108 n/cm2/s

## Slide 12: Neutron electro-production
Evaporation peak + fast neutrons shoulder
Tungsten target
At full linac power: 1013 e/s
  to be compared e.g. with nELBE, N=6·1015 e/s
Swanson estimate
  9.3·1010 Z(0.73±0.05) n/s kW-1
  2.15 ·1012 n/s kW-1 for Tungsten
Optimizing the target configuration can (slightly) improve the yield:
  n@BTF optimized target: 2.75 ·1012 n/s kW-1
  0.218 n/pr (over 4p and all spectrum)
In our case the main limitation will always be the intensity delivered onto the target

## Slide 13: Tagged photons
dipole magnet
silicon tagging
target
silicon detectors
Be window
Incoming electron
Progettato e costruito in collaborazione con il team del satellite AGILE il cui scopo era la calibrazione del payload tracciatore+calorimetro.
I fotoni sono “taggati” in energia utilizzando il dipolo le cui pareti interne sono ricoperte da 10 moduli Si micro-strip.
A seconda della perdita di energia nella produzione di fotoni, gli elettroni urtano una striscia diversa una volta impostato il valore di corrente di dipolo.
La correlazione tra la posizione dell’elettrone sulla camera di silicio e la posizione di impatto all’interno delle strip nel magnete permettono la “taggatura” dei fotoni.
γ
E

## Slide 14
Beam parameters
Different ranges of beam parameters can be achieved in the different modes: dedicated running or parasitic operation / with or without attenuating target
Parameter | Parasitic mode |  | Dedicated mode | 
 | With target | Without target | With target | Without target
Particle species | e+ or e- Selectable by user | e+ or e- Depending on DAFNE mode | e+ or e- Selectable by user | 
Energy (MeV) | 25–500 | 510 | 25–700 (e-) 25–500 (e+) | 250–730 (e-) 250–530 (e+)
Energy spread | 1% at 500 MeV | 0.5% | 0.5% | 
Repetition rate (Hz) | Variable between 10 and 49 Depending on DAFNE mode |  | 1–49 Selectable by user | 
Pulse duration (ns) | 10 |  | 1.5–40 Selectable by user | 
Intensity (particles/bunch) | 1–105 | 107–1.5 1010 | 1–105 | 103–3 1010
Maximum average flux | 3.125 1010 particles/s |  |  | 
Spot size (mm) | 1–25 (y) × 1–55 (x) |  |  | 
Divergence (mrad) | 1–2 |  |  | 
With target
Without target

## Slide 15: Strong points
Efficiency
  Al netto del down-time del linac e del tempo morto dovuto allo switch del linac tra modalità elettroni e modalità positroni, l’efficienza complessiva è >90%
  Naturalmente durante le iniezioni, il numero di bunch disponibili scende da 49 al secondo a 49 – n dove n è il numero di bunch ineiettati
Flexibility
  I parametri fondamentali del fascio sono modificabili in range piuttosto ampi, ma soprattutto in modo veloce e riproducibile
  Lo spot è molto riproducibile e il fuoco può essere facilmente modificato
User-friendly diagnostics
  In questi anni la diagnostica del fascio è stata continuamente migliorata, sia dal punto di vista delle prestazioni, sia da quello della facilità d’uso
  In particolare i rivelatori di tipo MediPix/FitPix permettono di aggiustare lo spot del fascio in tempo reale e garantiscono una misura molto accurata delle dimensioni e posizione del fascio

## Slide 16: Access & Schedule
Two calls/year typically in november and may, for planning a long period before summer and one short after Aug. shutdown
Strongly epending on DAFNE operations
Operators 24/7, of course, but also technical services
Strong support from Administration for heavy load (150-200 users/year)

## Slide 17: Users statistics
90% detector testing and calibration
10% high intensity
Average 150% of requested/available time

## Slide 18: BTF 2016
Jan
Mar
Apr
May
Jun
Jul
Not approved
Cancelled/Maintenance
January-July:
2 development shifts
1 safety qualification +
1 maintenance weeks
1 CHAOS-BTF joint shift
18 users slots/22 requested
138 users (with repetitions…)
Feb

## Slide 19: Schedule
2 pre-booked shifts (startup, teacher’s week)
1 safety qualification week
1 development shift
16 weeks new requests
Considering already booked or not available weeks, we will accept not more than 8 out of 20 new requests for the last part of the year
Projected overall 2016: 38 requests/26 available
[But we are not even at the end of May]
Inline with usual 150% request level

## Slide 20: Future
1991
2016
arXiv:1603.05651 [physics.acc-ph]

## Slide 21
WP1: LINAC modulators consolidation
WP2: Increase energy to 1 GeV
WP3: second BTF beam-line

## Slide 22: BTF line doubling
DHSTS01
DHSTB01
QUATB01-03
DHPTB102
DHPTB101
DHPTS01
QUATB101-102
DHSTB02
DHSTB03
DHSTB04
QUATB06-07
QUATB08-09
QUATB04
QUATB05
BTF new beam-lines:
Existing elements
New elements
PADME experiment approved for searching dark photon/ALPs and other light dark matter mediators using positron annihilations on target at the BTF line: needs a couple of years at full rate running
Recently included in ASI/ESA facilities for electron irradiation
1013 positrons on target

## Slide 23: PADME detector
Dipole 0.55 Tm
Diamond target
50-100 mm
Electron veto
1 cm scintillators with SiPM readout
Calorimeter
BGO crystals 20×20x220 mm3
Positron veto
1 cm scintillators with SiPM readout
Small Angle Calorimeter
Positron beam
High Energy Positron veto
1 cm scintillators with SiPM readout

## Slide 24: PADME experiment status
CSN I full approval for 1,350 kEuro for 2016-2018
Magnet from CERN (OK, being measured now)
600 BGO crystals from former L3 experiment
Calorimeter construction starting in summer 2016
Thin diamond, full Carbon, large area active target developed in Lecce
Scintillating bars positron veto being developed in Bulgaria
Interest from Hungarian group
Collaboration with Cornell starting this summer

## Slide 25: PADME main backgrounds
Signal e+e-->gA’
BG SM annih. e+e-->gg(g)
BG SM Brems.: e+N->e+Ng
g
g
g
P4g,t
P4e+,t
g
Mmiss=MA’
1 lost g
1 lost e+
e+
e+
e+

## Slide 26: PADME-invisible decay sensitivity
PADME can explore in a model-independent way the favourite by (g-2)m band up to M2A’ = 2meEe+
Ee+=550 MeV: MA’ < 23.7 MeV/c2
Ee+=1 GeV: MA’ < 32 MeV/c2
PADME 2 years of data taking at 50% efficiency with bunch length of 40 ns
1013 EOT = 6000 e+/bunch × 3.1107s  49 Hz
Based on 2.5x1010 fully GEANT4 simulated 550MeV e+ on target events
  Number of BG events is extrapolated to 1x1013 electrons on target
  Using N(A’g)=s(NBG)
  d enhancement factor d(MA’) = s(A’g)/s(gg) with e=1
  New estimate with optimized detector layout public by the summer!

## Slide 28: BTF upgrade(s): pulse width extension
10 ns pulse
New pulser for the LINAC gun ordered at end of 2015. Delivery due in these days
Adds to 1.5 – 40 ns (0.5 ns steps) the capability of producing 50-1000 ns pulses (50 ns steps)
Fully compatible with existing hardware and only minor modifications to software
Installation during summer shutdown, tests at restart of the LINAC in September
Crucial for PADME! Luminosity increases linearly with pulse duration, since it increases the number of positrons in the beam while keeping the pile-up probability in the detector constant
Indication that time and phase differences among the four modulators produces a good accelerating field in the 200 ns range already in the presente configuration, without any modification to the RF system.

## Slide 29: LINAC energy upgrade
LINAC energy upgrade:
add 4 accelerating sections
+ 1 klystron/modulator

## Slide 30: Thank you
LIMADOU: China-INFN g satellite
Cherenkov quartz detector for
crystal channeling
Negative ion TPC
pALPIDE chip for ALICE ITS upgrade
… and many others

## Slide 31: BTF layout
Pulsed dipole 3°
Pulsed dipole 6°
3-way beam pipe
LINAC spectrometer
BTF line
To/from damping ring
BTF dipole
Target
Target

## Slide 32: Beam spot
Beam spot at the exit of the vacuum pipe suffers from
  Beam divergence ≈1 mrad
  Multiple scattering on the Beryllium window
    0.5 mm thickness/352.8 mm = 1.4 10-3 X0
    ≈1 mrad at 500 MeV
Best spot: 0.6×0.5 mm2 (at 450 MeV)
Imaged by Medipix (FITpix) detector
  Si pixel, 55 mm pitch, 15×15 mm2 area
Beam spot centroid stability at the level of 200 mm

## Slide 33: Irradiation: beam spot
The “natural” beam spot in the transverse plane has a Gaussian shape
Generally, aiming at a “pencil” beam at low multiplicity
450 MeV electrons: 540×480 mm2 (s)
50 MeV electrons: 8.6×3.5 mm2 (s)
6 103/pulse
50 MeV electrons: 9.3×6.1 mm2 (s)
3.5 103/pulse
Irradiation requirement is the opposite: uniform intensity on a ≈cm2 area (±10%)
50 MeV electrons: 3.2×3.4 mm2 (s)
1 103/pulse
FitPIX detector:
2.25 cm2 area

## Slide 34: Irradiation: dosimetry
Planned acquisitions:
Diamond detector:
  It gives flux measurement without relying on calorimetry with no saturation effects
Faraday cup:
  The “standard” charge absolute reference measurement
F. Burkart et al.
CIVIDEC diamond detector
With target
Without target

## Slide 35: A possible beam-dump
A new thin vacuum chamber for DHPTT01 with double exit
  Exactly the same design of existing DHPTT02
A straight beam-line to the inside of the cavity hosting the dump target (to be optimized, designed, cooled, etc.)
Possibly, use DR pumps hall for dump experiments
Additional shielding all around the area, to be carefully calculated
DR pumps hall

## Slide 36: A possible beam-dump
DR pumps hall

## Slide 37: Projects
BTF additional line
  Approved AIDA-2020, Task 15.4.1
Refurbished photon tagging
  Approved AIDA-2020, Task 15.4.2
SATELLES
  Proposed: large overlap with additional line project
Long linac pulse
  From 40 to about 150 ns
  Above 150 ns up to 500 ns
Thin BTF target
  High energy positron production for PADME
Micro-divergence beam
Electron irradiation facility
Energy upgrade of the linac
  Submitted to INFN
  Includes matching funds for BTF additional line
  Includes consolidation of linac modulators power supplies
Dump for high-intensity
  BDX, PADME
  Neutron/pion/muon production

## Slide 38: DAFNE timing
25 or 50 Hz repetition rate
Last bunch every second always to spectrometer line
Spectrometer
BTF line
Accumulator
Main rings
LINAC = LINAC shots are delivered at 25(50) pulses/s and dumped at the end of TL
LINAC+BTF = LINAC shots are delivered with a selectable duty cycle to BTF: 1 to 24(49) pulses/s. Remaining pulses are dumped at the end of the TL
GLOBAL = LINAC shots are delivered with a variable duty cycle to BTF according to injection parameter in ACCUMULATOR
  NO INJECTION = SELECTABLE from 1 to 24(49) pulse per second
  INJECTION = the injection needs are DAΦNE Control Room controlled. Typically injection pulses are at 2Hz, taking from 1 up to 7 LINAC bunches per sequence. BTF delivers 22 down to 10 bunches per second