## Slide 1: PET reconstruction software test
Giovanni Pirrone
INSIDE meeting, 14/06/2016, Roma

## Slide 2: MLEM algorithm: iterative method for Tomographic Image Reconstruction
Why iterative?
  Can handle complex acquisition geometries
  Do not need complete projection data
  Can account for the type of measurement statistics
  Can model both the geometry and the physics of the acquisition system
From continuous to discrete
  The image is discretised: fj=1,…,N with N as the number of voxels/pixels
  The data is discretised: pi=1,…,M with M as the number of measured projection
  The imaging system is modeled vie the system matrix A Є RM X N . System matrix entry expresses the contribution of image pixel j to detector bin i.

## Slide 3: Basic concepts: how to recover the image
Imaging process is expressed as linear system of equations
but A might not be invertible! i.e. not square or bad conditioned
More practical approach: search for the solution f iteratively by guessing f and improving it iteratively using only A and AT:
Where k is the iteration number, and the system matrix A is used in the «correction term»

## Slide 4: Basic concepts: how to recover the image
Image (fk)
‘artificial’ projection data
Project
A
Correction data
Measurement data (p)
compare
Correction data
Backproject
AT
For k=1 start
with a guess
Compute next
image (k=k+1)
Loop notation
Operator notation
Divide by the sensitivity

## Slide 5: INSIDE 5x2 System matrix
System matrix informations
Head-to-Head distance (mm): 500
FOV dimension (in voxels): 140,70,165
FOV spacing (mm): 1.6
Crystals size (mm2): 3 x 3
Crystals pitch (mm): 3.2
Detector size (mm): 51.2
Detector pitch (mm): 54.5
Model size (Mb): 458
X
Y
Z
Reference system
PET 1
PET 2

## Slide 6: Sensitivity image
Sensitivity evaluation
  Lines Of Response (LORs) backprojection into the Field Of View (FOV)
  For each image voxel a value is assigned. This value is given by LORs that are crossing the voxel
  If the voxel is crossed by j LORs, the value for that voxel is computed by a weighted sum of j terms
  The weights Wj are given by the lines length within the voxel
LOR1
LOR2

## Slide 7: Sensitivity image
Y
Z
Z
X
Y
X
Sensitivity image orthogonal views (central slices)

## Slide 8: Sensitivity image: symmetry
Y
Y
Z
Z
Horizontal flip
Vertical flip
No visible pattern.
Image values ~ 10-9 ÷ 10-10.
No visible pattern.
Image values ~ 10-9 ÷ 10-10.

## Slide 9: Sensitivity profiles
Z
Y

## Slide 10: Sensitivity: computed VS simulated
Gate simulations
  F-18 point source (cube of 500 μm) within a PMMA phantom (cube of 10 mm side)
  Activity: 100 μCi (3700000 Bq)
  Simulation time: 120 s
  The source was positioned in different points of the FOV along the x, y and z directions

## Slide 11: Point source reconstruction
Gate simulations
  A ROI was selected for each slice along all the orthogonal planes and the arrays of the average counts values were calculated
  Profile plot and gaussian fit were performed to determine the reconstructed position as a function of the nominal position
Z
Z
X
X
Y
Y

## Slide 12: Point source reconstruction Profiles along Y (plane YZ)
Gate simulations
  F-18 point source (cube of 500 μm) within a PMMA phantom (cube of 10 mm side)
  Activity: 100 μCi (3700000 Bq)
  Simulation time: 120 s
  Source positions: 0, 10, 20, 30, 40 mm along the Y direction (with the coordinates X and Z equal to 0)
  The std of the profiles gaussian fit goes from 0.9 mm to 1.3 mm for the positions y=0 mm and y=40 mm respectively
Same behaviour along the Z direction

## Slide 13: Point source reconstruction Profiles along X (plane XY)
Gate simulations
  F-18 point source (cube of 500 μm) within a PMMA phantom (cube of 10 mm side)
  Activity: 100 μCi (3700000 Bq)
  Simulation time: 120 s
  Source positions: 0, 25, 50, 75, 100 mm along the Y direction (with the coordinates X and Z equal to 0)
  The std of the profiles gaussian fit goes from 4.3 mm to 6.2 mm for the positions x=0 mm and x=100 mm respectively.
  Worst results (but satisfying) on the position reconstruction

## Slide 14: Limits of our system…

## Slide 15: CNAO data reconstruction Single spot, 124 MeV (111 mm in H2O), high statistic
Z
Y
X
Y

## Slide 16: PET-CT image fusion
Rando CT
PET image
fusion
Treatment plan information | 
Radiation type | Proton
Target prescription dose | 55.8 Gy
Number of fraction planned | 31
Fraction dose | 1.8 Gy
Number of beam | 2 (B1, B2)
Measurements information | 
Beam | B1
Dose delivered | 0.9 Gy
Nominal beam energy range | 73.93 ÷ 134.12 MeV