## Slide 1
SINGLE PARTICLE
LONGITUDINAL DYNAMICS
INTRODUCTION
LONGITUDINAL DYNAMICS IN LINAC
LONGITUDINAL DYNAMICS IN SYNCROTRONS AND STORAGE RINGS
Alessandro Gallo and David Alesini
INFN-LNF

## Slide 2
1) INTRODUCTION
Fundamental relations of the relativistic dynamics

## Slide 3
Fundamental relations of the relativistic dynamics
To change the energy of a charged particle a longitudinal E-field component is necessary:
In most existing accelerators leptons are fully relativistic particles (Wk>>W0, with the exception of the very first acceleration phase) while protons and ions are weakly relativistic particles (Wk<W0, with the exception of large high energy colliders - such as Tevatron, LHC, …- ).
Bending radius
To bend a particle trajectory the B-field is preferably used, being a factor “v” more efficient (v = particle velocity – see Lorentz force) of the E-field:
Lorentz force

## Slide 4
Proton
source
AC
voltage
1) LONGITUDINAL DYNAMICS IN LINACs
A Linac consits in a linear sequence of accelerating structures;
They can be Drift Tubes, SW cavities, TW structures, or a combination of them;
Whatever the accelerating structures are, the particles gain energy and velocity while travelling through each of them, and need to arrive at right time to the next one to get the proper kick and continue the acceleration process;
Particles and accelerating fields need to be synchronized. If they are not, the acceleration process will result to be perturbed. The longitudinal dynamics describes the particle motion in the longitudinal phase space, whose coordinates are the particle time (or RF phase) error and energy deviation.

## Slide 5
Energy gain of a particle moving along the axis of a standing wave RF cavity:
Let’s consider a LINAC designed to provide an energy kick qVk any time that a particle travels along the axis of a SW cavity:
A particle which is injected in the Linac with the design phase s and proper initial energy will get the design energy kick and will arrive perfectly in time at the following gaps. We define s as the synchronous phase and the particle as the synchronous particle.
It’s easy to demonstrate that if s 0 a generic particle with phase and energy values close to the synchronous particle ones is accelerated in similar way with small energy and phase oscillations around the synchronous values.
In fact, since the synchronous phase preceeds the peak, any particle crossing the gap before the synchronous particle will get a smaller energy kick, will gain less velocity and its time of flight to next gap will be longer, compensating the initial error.
Any particle arriving late at the gap with respect to the synchronous particle will get a larger energy kick, will gain more velocity and will arrive to next gap with a smaller error.
The choice fs<0 provides longitudinal focusing of the beam (phase stability principle for linear accelerators). The opposite choice leads to longitudinal instability.
Relying on particle velocity variations, longitudinal focusing does not work for fully relativistic beams. In this case acceleration “on crest” is more convenient.
LONGITUDINAL DYNAMICS IN LINACs – non relativistic particles
2.1 Synchronous Particle and phase stability
fs
Vk
VRF
average accelerating
gradient

## Slide 6
In order to study the longitudinal dynamics in a LINAC, the following variables are used, which describe particle position and energy with respect to the synchronous particle:
Average accelarting gradient, as seen by the generic particle and by the synchronous particle in a portion of the trajectory of length L:
Energy gain per unit length of a generic particle and of a synchronous particle:
From previous expressions one gets:
Phase-energy equations
Let’s also define:

## Slide 7
The longitudinal motion is governed by a non-linear system of two coupled differential equations:
In case of small oscillations around the synchronous particle ( << 1 rad) and neglecting the particle energy and speed variation along the LINAC (adiabaticity), we get:
The condition to have stable longitudinal oscillations and acceleration at the same time is:
Synchrotron oscillations in the longitudinal phase space
harmonic oscillator equation
w

The trajectory of a a generic particle in the longitudinal phase space is an ellipse.
The maximum energy deviation is reached at  = 0 while the maximum phase excursion corresponds to w=0.
It is easy to show that:
Numerical
example:
Protons (W0 = 938 MeV) @ 100 MeV; E0 = 2,5 MV/m; fs = -30°; fRF = 600 MHz; Llinac= 40 m

## Slide 8
According to Liouville’s theorem, under the action of conservative forces, the ellipse area in phase space is constant.
The amplitude of the synchrotron oscillations remains rigorously constant only at constant energy (which is not the case in accelerators!), while in case of slow acceleration (low gradients) the oscillation amplitudes will smoothly change to satisfy the Liouville’s theorem. In fact:
The result is that during acceleration the bunch gets shorter and its relative energy spread is reduced.
Bunch length and energy spread along a LINAC
ADIABATIC DAMPING

## Slide 9
To study the longitudinal dynamics at large oscillations, we have to consider the non linear system of differential equations without approximations. By neglecting particle energy and speed variations along the LINAC we obtain:
The restoring force F can not be considered purely elastic anymore and may by derived from a potential function according to the usual definition:
At large oscillations:
the phase space trajectories are not ellipses anymore;
the oscillations are stable within a region bounded by a special curve called separatrix. The maximum phase excursion is equal to 2s ;
the region inside the separatrix is called RF bucket. The dimensions of the bucket shrinks to zero if s=0.
points outside the buckets belong to unstable trajectories.
Large oscillations
With few simple passages we obtain an “energy conservation”–like law:

## Slide 10
Synchronous particle and phase
dipole bending radius, invariant during the whole acceleration process
dipole magnetic field at turn # n
The synchronous particle is the particle that undergoes the ideal acceleration process, gaining a constant amount of energy W per turn remaining all the time on the design orbit. While running the nth turn, the synchronous particle has to have the proper energy to perfectly satisfy the following condition:
Accelerator Length
2) LONGITUDINAL DYNAMICS IN SYNCROTRONS
The particle velocity increases turn by turn during acceleration (and tends asyntotically to the speed of light at high energies), and so it does the revolution frequency (Frev). As a consequence the frequency of the RF system (fRF) must change to be synchronous with the beam motion.
Energy gain of the synchronous particle due to the nth passage in the RF cavity
synchronous phase
(invariant)
harmonic number
Corresponds to the number of time-separated synchronous particles that can be accelerated in the synchrotron
Synchronization between acce-lerating field and synchronous particle requires:
Synchrotrons are circular accelerators. Particles are bended by dipolar magnets, while acceleration is provided by standing wave RF cavities.
Differently from LINACs, in synchrotrons the particles run over closed orbits so that they are accelerated by the RF cavities in a very large number of turns.
Since the beam energy and momentum increase turn by turn, the bending magnetic field has to be increased proportionally to the momentum, in order to keep invariant the bending radii and the orbit. The revolution frequency also increases with energy, which requires variation of the RF frequency to maintain the synchronization between beam and accelerating field.

## Slide 11
Turn-by-turn energy increase:
B-field increase to keep the synchronous particle on a constant orbit
fRF asyntotically tends to hc/L as B becomes much larger than m0c/q , i.e. when the particle becomes ultra-relativistic and v→c
B and fRF variations during acceleration
Frev variation
fRF has to be continouosly changed to keep synchronized the accelerating field and the synchronous particle passages
Turn-by-turn energy increase:
B has to grow linearly with time
t
fRF
hc/L
t
B
Bin

## Slide 12
Exercise : let’s design a synchrotron!
RF
Diagnostics
Injection
Extraction
Bending
radius r
Bending
Magnets
Particle | Protons
Rest energy | W0 = 938 MeV
Injection energy | Win = 10 MeV gin ≈ 1.01 bin ≈ 0.14
Extraction energy | Wout = 400 MeV gout ≈ 1.43 bout ≈ 0.71
B field @ extraction | Bmax = 1.0 T
Bending radius | r ≈ 3.2 m
B field @ inction | Bin = 0.14 T
Total length | L= 40 m (2pr + 4d)
RF kick Voltage | V·cos(fs) ≈ 1 kV
Magnetic field slope | dB/dt = 7.81 T/s
Energy ramp duration | Tramp ≈ 110 ms
Number of turns | Nturna ≈ 390000
Revolution frequency | frev ≈ 1.7 MHz in ≈ 5.0 MHz out
RF frequency | fRF = frev (h=1)
?
?
?
?
?

## Slide 13
Exercise : let’s design a synchrotron!
Extraction
RF
Diagnostics
Injection
Bending
radius r
Bending
Magnets
Particle | Protons
Rest energy | W0 = 938 MeV
Injection energy | Win = 10 MeV gin ≈ 1.01 bin ≈ 0.14
Extraction energy | Wout = 400 MeV gout ≈ 1.43 bout ≈ 0.71
B field @ extraction | Bmax = 1.0 T
Bending radius | r ≈ 3.2 m
B field @ inction | Bin = 0.14 T
Total length | L= 40 m (2pr + 4d)
RF kick Voltage | V·cos(fs) ≈ 1 kV
Magnetic field slope | dB/dt = 7.81 T/s
Energy ramp duration | Tramp ≈ 110 ms
Number of turns | Nturna ≈ 390000
Revolution frequency | frev ≈ 1.7 MHz in ≈ 5.0 MHz out
RF frequency | fRF = frev (h=1)

## Slide 14
Transition energy is defined as:
Momentum compation factors are usually positive (>0) in circular accelerators, so that below transition energy particle revolution frequency increases with energy (the velocity increase dominates the orbit length increase). On the contrary, beyond transition energy revolution frequency decreases while energy increases (since vc and orbit length variation dominates in this case).
“Momentum compaction” and transition energy
while the relative revolution frequency variation for a given relative particle momentum variation is called “slippage factor” h :
The relative orbit length variation for a given relative particle momentum variation in a circular, transversely focused accelerator is property of ring magnetic guide called “momentum compaction” factor a :

## Slide 15
For a non-synchronous particle we may define the following quantities to measure the deviation respect to the synchronous particle at the nth turn:
Non-synchronous particles: phase-energy equations
Deviations of revolution frequency, phase , energy, etc., respect to the synchronous particle:
Turn-by-turn evolution of energy and phase of non-synchronous particle is described by the following equations:

## Slide 16
If we consider small oscillations around the synchronous phase and slow variations of Ps, Frev_s and , we easily obtain the equation of an harmonic oscillator whose frequency fs is called again synchrotron frequency.
To get stable oscillations the following condition have to be fulfilled:
Synchrotron oscillations
If during acceleration the transition energy is crossed, the RF cavity phase has to be rapidly changed in order to preserve the beam longitudinal stability.

## Slide 17
Similarly to the already shown result for the longitudinal dynamics of LINACs, particles oscillate around the synchronous one with the frequency fs and the trajectories of their motion in the longitudinal phase space are ellipses.
However, differently from the LINAC case, the synchrotron frequency shows a rather complex scaling law with energy:
Synchrotron oscillations
w

Adiabatic damping
Previous results concerning small oscillations are rigorously valid under the assumption of very slow beam energy Ws variation with time compared to those of the variable w and . Again, a more correct result obtained applying the Liouville’s theorem reveals that the amplitude of energy and phase oscillations changes during the acceleration process. In particular, since oscillation amplitudes of both phase and relative energy deviation of the particles are reduced during the acceleration, this effect is called adiabatic damping.

## Slide 18
Adiabatic damping
Please note:
accordingly with these expressions it may appear that near transition energy the phase oscillation amplitude goes to zero while that of the energy spread goes to infinity. This is not actually the case since in this particular regime linear approximations are not valid anymore. A more rigorous approach shows that the oscillations can be made stable also in this case.
w/Ws

Energy ramp
start
Energy ramp stop

## Slide 19
As already discussed in the LINAC case, at large oscillations the non-linearity in the phase – energy differential equations can not be neglected, and the particle trajectories in the longitudinal phase space are deformed (not ellipses anymore). A potential U for the non linear restoring force can be introduced again, just as in the LINAC case, and a separatrix line divides the stable and unstable regions in the longitudinal phase space (RF bucket). In particular the RF acceptance is defined as one half of the bucket total height and is given by:
Large oscillations and energy acceptance
the RF acceptance can be also expressed as:
and being the synchronous phase identified by the relation:
that for large values of the overvoltage factor is reduced to:
2 x RF acceptance

## Slide 20
Lepton rings
This phenomenon cause a turn-by-turn beam energy loss which has to be compensated by the RF system.
The emission strongly depends on the particle energy, which produces a damping effect on the synchrotron oscillation amplitude.
On the other hand the synchrotron radiation emission is a stochastic quantum process which drives the longitudinal oscillations acting as a noise excitation term.
Radiation damping and quantum excitation are two counteracting processes that lead to an equilibrium state characterized by a particle distribution in the longitudinal phase space.
particle are ultra-relativistic at relatively low energies already (>10 MeV) and their speed is almost constant and equal to c all over the acceleration process;
while traveling through bending dipole magnets the beam emits radiation in a wide spectrum range (synchrotron radiation).
The RF system is much simpler since frequency change is not necessary.
The power emitted in the form of synchrotron radiation is given by:
emission is completely negligible for heavy particle up to very high energies. On the contrary, it is a very important effect in electron rings.
Rings for light particles (electrons) present two peculiar aspects that deeply impact the longitudinal dynamics:
The energy radiated in a single turn is given by:
A particle with an energy deviation w with respect to the synchronous particle energy Ws will radiate more, with a radiated energy excess urad given by:

## Slide 21
Equilibrium distributions in lepton rings
In light particle (such as electrons) synchrotrons the equilibrium final distribution is given by the two contributions of the radiation damping ,which reduces the oscillation amplitude (of both phase and energy deviation), and of the quantum emission noise which sthoastically excites the oscillations. The equilibrium distributions fully depend on these processes while the memory of the particle initial condition is completely lost in few damping times.
It may be demonstrated that the final equilibrium distribution of the bunch particles in the longitudinal phase space is a bi-dimensional gaussian:
The 2 standard deviations are related by:
depends on radiation process, may be calculated from the ring linear optics functions

w
The linearized differential equation of the particle longitudinal motion for a storage ring of constant energy has the following form:
Damping term:
responsible of the exponential decay of the oscillations amplitude (radiation damping) with a damping time:
Quantum excitation term

## Slide 22
SPARE
SLIDES

## Slide 23
From previous formulae it is clear that there is no motion in the longitudinal phase space for ultrarelativistic particles (>>1), that typically get to the LINAC end before executing a single complete synchrotron oscillation.
It is interesting to analyze the conditions that allow to inject and capture an electron beam produced by a cathode directly in a TW structure with phase velocity equal to c, or equivalently in a SW structure designed to accelerate ultrarelativistic particles.
In this case particles enter the structure with velocity v<c and, at least initially, they are not synchronous with the accelerating field.
Light particle capture by TW sections (no synchrotron motion) (1/2)
Is this the case of electrons whose velocity is always close to speed of light c even at low energies. Accelerating structures are designed to provide an accelerating field synchronous with particles moving at v=c. One possible choice is to use traveling wave structures with phase velocity equal to c.
E0
z
c

## Slide 24
Let’s consider the phase f between field and particle, i.e. the phase of the wave computed at the position z occupied by the particle at the instant t. After an elementary time increment dt the phase variation df can be computed according to:
From Newton’s 2nd law we have:
Let’s introduce the variable  defined by:
From previous
equations:
By integrating the equation between t0 and t, that means between β=β0 e β =1 one gets:
Since this quantity can never exceed the value of 2, we got a condition which sets a minimum value of the accelerating field below which no particle can be captured:
Light particle capture by TW sections (no synchrotron motion) (2/2)
c
v<c
v=c
negative if z > 0,
i.e. particle ahead the wavefront
integral:

## Slide 25
Numbers!
e- beam, W0 = 510 keV
Win = 100 keV, (kinetic energy) -> g ≈ 1.2; b ≈ 0.55
fRF= 2856 MHz -> lRF≈ 10.5 cm
E0min = ?
How is the capture if E0 =2 E0min ?
E0 = 16.4 MV/m

## Slide 26
RF Compression
The curve of the capture phase vs the injection phase contains an important information. The derivative of the plot indicates – to the 1st order – how a bunch injected at a certain phase will be shortened or elongated after being captured.
Ex: SPARC
Win≈ 5 MeV, gin ≈ 10.8, bin ≈ .996
Eacc ≈ 15 MV/m => Eacc / Emin ≈ 20
Compression is always maximum for bunches injected at –90° (at the accelerating field zero crossing);
Bunches injected at > -90° are less compressed (and accelerated more);
Bunches injected at < -90° are overcompressed, which means that head and tail are reversed after capture;
This model describes single particles, i.e. does not take into account space charge which might be relevant in high compression regimes.

## Slide 27
In order to increase the capture efficiency of a traveling wave section, pre-bunchers are often used. They are standing wave cavities aimed at pre-forming particle bunches gathering particles continuously emitted by a source.
Gun
Thermionic
Buncher
(SW Cavity)
Capture section
(SW or TW)
I
t
I
t
T
RF
I
t
T
RF
L
drift length
Continuous
beam
Continuous beam
velocity modulation
Bunched
beam
Bunched and captured
beam
Bunching is obtained by modulating the energy (and therefore the velocity) of a continuous beam using the longitudinal E-field of a SW cavity. After a certain drift space the velocity modulation is converted in a density (and charge) modulation. A TW accelerating stucture (capture section) is placed at an optimal distance from the pre-buncher, to capture a large fraction of the charge and accelerate it till relativistic energies. The density modulation deplates the regions corresponding to injection phase values incompatible with the capture process. The amount of charge lost is drastically reduced, while the capture section provide also further beam bunching.
2.7 pre-buncher
Once the capture condition is fulfilled the fundamental equation:
sets the ranges of the injection phases f0 actually accepted. Clearly, there will always be a range of values around f0 =p /2 corresponding to sin f ≥ 1. Particles whose injection phases are within this range cannot be captured and are lost.

## Slide 28
4) LONGITUDINAL DYNAMICS IN CYCLOTRONS
In cyclotrons the acceleration is provided by an alternate electric field between two or more electrodes immersed in a uniform dipolar magnetic field.
The particle gains energy at each passage in the gap between the 2 electrodes.
The bending radius of the beam trajectory changes turn-by-turn with the particle momentum and is given by:
The synchronization between accelerating field and particles is preserved provided that the following condition is fulfilled:
Standard cyclotrons have constant fRF so that synchronization is guaranteed only in non relativistic particle case (m=m0=constant)
Spiral trajectory
Synchronization between particles and accelerating field

## Slide 29
In the ideal case the phase of the RF should increase of exactly 2 in one turn. The phase advance error is given by (if h=1):
Phase and energy evolution with time
Concerning the energy we got:
(remember that every turn the beam passes twice across the accelerating gap):
These equations allows studying the energy and phase evolution in time of a particle of given initial conditions.

## Slide 30
By elaborating the previous equations we obtain:
By integrating both sides of the equations between initial and final instants:
Phase-energy diagram
Initial phase
Rest energy
Starting from this expression it is possible to plot sinf as a function of the final kinetic energy for different initial phase values. The plots make sense only in the [1,-1] interval of the vertical coordinate. The maximum energy is obtained for a specific optimal phase that depends on the accelerator parameters and on the characteristics of the particle.
Unless the B-field and/or the electrode shape are properly profiled to correct the revolution frequency dependence on the particle energy, it can be easily shown that the maximum kinetic energy of the accelerated particle is limited to:

## Slide 31
References:
All the particle accelerator physics @ CERN Accelerator School Proceedings
http://cdsweb.cern.ch/search.py?sc=1&p=CERN+Accelerator+School&f=&cc=CERN+Yellow+Reports
In particular, longitudinal dynamics @
http://cdsweb.cern.ch/record/235242/files/CERN-94-01-V1.pdf
Joel Le Duff, “Dynamics and acceleration in linear structures”, p. 253
Joel Le Duff, “Longitudinal beam dynamics in circular accelerators”, p. 289
All abour RF, cavities, power sources , … @
CERN Accelerator School: RF for Accelerators - Ebeltoft, Denmark, 8 - 17 Jun 2010
http://arxiv.org/html/1201.4648v2
Storage rings
http://www.slac.stanford.edu/cgi-wrap/getdoc/slac-r-121.pdf
Matthew Sands, “The physics of electron storage rings. An introduction”