## Slide 1: Medical Image Processing
Alessandra Retico
Istituto Nazionale di Fisica Nucleare - Sezione di Pisa
alessandra.retico@pi.infn.it
Image Processing Meeting (FTK-IAPP)
Pisa, July 5, 2016

## Slide 2: Outline
Diagnostic Imaging
Medical Image Processing:
  Visualization
  Segmentation of anatomical/functional/pathological structures
  Quantification
  Identification of Biomarkers

## Slide 3: Diagnostic imaging modalities

## Slide 4: Image processing and machine learning
Post-processing of raw data:
  Visualization
Quantification:
  Image segmentation
  Volumetric assessment of regions of interest (ROIs), lesions, etc.
Follow up of pathological conditions:
  Grow rate of lesions; assessment of treatment efficiency
Fusing information:
  Inter/intra-modality acquisitions (deformations, registration algorithms)
The aim is to assist clinicians in their tasks, not to replace them.

## Slide 5: Measuring structure and function of the brain
Non-invasive methods
Structure
Structural Magnetic Resonance imaging
MRI
Diffusion Tensor Imaging
DTI
Function
Functional Magnetic Resonance Imaging
fMRI
Computed Tomography
CT
Positron Emission Tomography
PET
Ionizing
radiation
Ionizing
radiation

## Slide 6: Structural MRI (sMRI) T1-w images
3D array of data:
The voxel is the “volume element”
“High resolution” MRI T1-w images: vx × vy × vz ≈ 1 × 1 × 1 mm3
Sagittal
Coronal
Axial or transaxial
e.g. Nx x Ny x Nz = 256 x 256 x 128
16 bit 16 MB

## Slide 7: Functional MRI (fMRI)
BOLD Response: blood-oxygen-level-dependent (BOLD) contrast
1 volume per second (3x3x3mm3), for 4-5 min:~ 320 MB
  Stimuli (visual, auditory, tactile, …) are presented during the scan
Analysis of data time series to look for up-and-down signals that match the stimulus time series
Functional connectivity
Resting state rs-fMRI: study of temporal correlations between spatially remote neurophysiological events

## Slide 8: Diffusion weighted imaging
Water molecules diffuse around during the imaging readout window
Diffusive movement of water in brain is not isotropic
  In white matter (WM) diffusion along axonal fiber orientation is faster
Imaging can be made sensitive to this diffusive motion
Isotropic diffusion
Anisotropic diffusion
Structural connectivity: Fiber tractography
The orientation of axon fibers is reconstructed in vivo

## Slide 9: T1-weighted brain images
Axial slices of a human head with spatial resolution of 1 mm3
Grey Matter (GM) cortex can by followed and cortical thickness can be evaluated to investigate GM involvement in pathological conditions.
White Matter (WM)
Grey Matter (GM)
Cerebrospinal fluid (CSF)

## Slide 10: Segmentation of brain components
Grey matter
White matter
Cerebrospinal fluid
Tissue probability maps (TPMs) in SPM8
Tissue segmentation in SPM8
In a simple MOG, the probability of obtaining a voxel with intensity yi given that it belongs to the kth cluster, i.e. Gaussian (ci = k), and that the kth Gaussian is parameterized by mk and sk2 is:
Mixture of Gaussian Model (MOG)
The prior probability of any voxel, irrespective of its intensity, belonging to the kth is:
Sum over K clusters, accounting for each voxel and maximize with respect to the unknowns (m, s)
Using Bayes rule, the joint probability of cluster k and intensity yi is:
www.fil.ion.ucl.ac.uk/spm/

## Slide 11: Brain parcellation
http://freesurfer.net/
http://www.loni.usc.edu/
Notes: FRONTAL LOBE
Concerned with reasoning, planning, parts of speech and movement (motor cortex), emotions, and problem-solving.
PARIETAL LOBE
Concerned with perception of stimuli such as touch, pressure, temperature and pain.
TEMPORAL LOBE
Concerned with perception and recognition of auditory stimuli (hearing) and memory (hippocampus).
OCCIPITAL LOBE
Concerned with many aspects of vision.

## Slide 12: Group comparison (voxel/regional level)
Patients (group 1) vs. Controls (group 2):
  Pathology specific brain alterations
Longitudinal studies (same group after a time delay)
  Effect of aging
  Effect of treatments
Group 2
Voxel-wise statistical analysis
Group 1
Comparison between groups
Multivariate techniques, machine learning,
predictive models.

## Slide 13: The Alzheimer’s Disease Neuroimaging Initiative (ADNI)
http://adni.loni.ucla.edu/
> thousands of cases: baseline, follow up; AD, MCI, Controls; MRI, PET
~ 800 cases with genetic data

## Slide 14: Dataset available in this study
  The Alzheimer’s Disease Neuroimaging Initiative (ADNI)
Train & test: 144 AD + 189 age-matched Controls (CTRL)
Trial on 302 MCI subjects: 136 converters (MCI-C) + 166 non converters (MCI-NC)
This dataset was selected with the requirement of having at least 2-year information in addition to the baseline scan:
  the AD/CTRL subjects were confirmed to be healthy controls/AD at the follow-up assessment;
  MCI-C subjects converted to AD in a time-frame of 2 years from the baseline scan.
Dataset used in this study:
http://adni.loni.ucla.edu/
The mission of the ADNI is to define the progression of Alzheimer’s Disease. A major goal of the ADNI study has been to collect and validate data such as MRI and PET images, cerebral spinal fluid, and blood biomarkers as predictors of the disease. Data from Alzheimer’s Disease patients, Mild Cognitive Impairment subjects, and elderly controls are available to download.
TOT 635

## Slide 15: Example of MTL atrophy visibility on MRI structural data
AD
CTRL
Healthy younger subject

## Slide 16: Voxel-Based Morphometry (VBM) analysis with SPM8
The VBM whole-brain analysis provides statistical parametric maps (SPM) of regions where GM significantly differs among groups of subjects
A mask is derived from the SPM map
GM
WM
CSF
Gaussian smoothing with s=3 mm;
Covariates: Age, Gender and TIV
VBM preprocessing:
  SPM tissue segmentation of GM, WM and CSF
  DARTEL registration and study specific template
  Alignment to MNI space
VBM analysis (voxel-wise t-test) to identify the regions where AD and CTRL differ (Gaussian smoothing with s=3mm; i>0.1; covariates: Age, Gender and TIV)
  The amount of GM in AD is significantly lower than in CTRL, especially in the Temporal and Limbic Lobes

## Slide 17: VBM results: Structural abnormalities in AD subjects vs. Controls
Regions where GM in AD < than GM in Controls are displayed: significant SPM blobs are overlaid to a representative T1-w image
(s=3 mm, covariates: age, gender and TIV)

## Slide 18: Limitation of the VBM approach
VBM allows localizing brain regions where GM (WM) significantly differs among groups of subjects.
VBM limitations:
  VBM allows for comparisons between groups of subjects, not for single subject analysis.
  The inference on new cases is not possible.

## Slide 19: Why using machine-learning techniques?
Some tasks cannot be defined well, except by examples.
Relationships and correlations can be hidden within large amounts of data.
  Machine Learning/Data Mining may be able to find these relationships.
The amount of knowledge available about certain tasks might be too large for explicit encoding by humans (e.g., medical diagnostic).
  Learning from examples
Vocabulary:
  Training set: a subset of items, with known classification
  Training: allowing the algorithm to set weights and “learn” how to classify your data, using the training set
  This produces classifier, i.e. a quantitative mapping from features to class.
  Classification: using these training-set weights to classify data of previously unknown category
Notes: Some tasks cannot be defined well, except by examples (e.g., recognizing people).
Training a decision-making system
  Defining a criterion for success [What is the error that needs to be minimized?]
  Choose an algorithm capable of finding weights of a linear function that minimize that error [e.g. the Least Mean Square (LMS) training rule].

## Slide 20: Pattern classification in MRI data of Alzheimer’s disease
Automatic classification of subjects into the Alzheimer’s Disease (AD) and the Healthy Control (HC) categories
The predictive value of structural MRI can be investigated to:
  classify newly acquired subjects;
  infer on the outcome of Mild Cognitive Impairment (MCI) subjects.
A. Retico - INFN Pisa

## Slide 21: Support Vector Machine (SVM) classification
AD subjects
Healthy Controls
Trained SVM
Training on known cases
SVM OUTPUT
AD subject
Healthy Control
New subject
Prediction on MCI outcome

## Slide 22: Support Vector Machine (SVM) classification
Binary classification
VBM preprocessed data:
segmented, normalized, modulated and smoothed GM for each subject
Notes: Only distinguishes
between two different
classes (+1/-1)

## Slide 23: Support Vector Machines (SVM)
Find w and b such that
Φ(w) = ½ wtw is minimized;
and for all {(xi ,yi)}: yi (wTxi + b) ≥ 1
Quadratic optimization problems are a well-known class of mathematical programming problems, and many (rather intricate) algorithms exist for solving them.
The solution involves constructing a dual problem where a Lagrange multiplier αi is associated with every constraint in the primary problem.
-

## Slide 24: SVM Recursive Feature Elimination (SVM-RFE)
Features/voxels are iteratively removed from the data set with the aim of retaining only those voxels that carry discriminative information
  The weight magnitude |wi| is used as ranking criterion:
    features/voxels with low |wi| are removed from the dataset,
    features/voxels with high |wi| are retained.
  A new SVM is trained at each iteration.
  The SVM classification performance (AUC) is evaluated at each iteration (i.e. as a function of the number of retained GM voxels)
3 105 voxels
6 103 voxels
8 104 voxels
2 104 voxels
The SVM-RFE discrimination maps can be compared to the VBM maps.
[Guyon et al, Mach Learn (2002)]
Notes:   Features/voxels with low |wi| are removed from the dataset, while retaining those encoding the discriminative information (high |wi|).
We are interested both in reducing the large number of voxels to classify and in the visual information contained in the discrimination maps

## Slide 25: Local vs. global approach
The average values obtained over 10 repetitions of 20f-CV are shown; the bands around the average curves correspond to two standard deviations.
6000 voxels
AUC=(87.1±0.6)%
AUC=(70.7±0.9)%
A. Retico et al., J Neuroimaging (2015)

## Slide 26: Advantages of SVM analysis
In contrast to VBM, SVM is a multivariate approach thus automatically takes into account interregional correlations.
  Identification of patterns of brain alterations
In addition SVM offers a predictive value
  Once the decision function is learned from the training data (AD vs. CTRL) it can be used to predict the class membership of new test examples (MCI prediction of conversion).

## Slide 27: Where this pipeline can be improved?

## Slide 28: Deep learning
An algorithm to make ANN learn in multiple levels of representation, corresponding to different levels of abstraction.
Convolutional neural networks (CNNs) represent mid-level and high-level abstractions obtained from raw data.
Neural networks with 6-9 hidden layers

## Slide 29: The tissue border enhancement (TBE) sequence
TBE acquisition technique provides images with enhanced visualization of borders between two tissues of interest without any post-processing.
TBE is an Inversion Recovery sequence (FSE-IR) with appropriate TI
Accurate assessment of the GM-WM interface is important in the classification of cortical malformations
MWM
MCGM

## Slide 30: 7T MRI in Polymicrogyria
TBE imaging depicted a hypointense line corresponding to GM-WM interface, improving detection of the polymicrogyric cortex
  Potential relevant implications for diagnosis, genetic studies, and surgical treatment of associated epilepsy.
De Ciantis et al,. AJNR (2015)
SWAN
SWAN minIP
TBE