## Slide 1
Gruppo di Napoli
A. Aleksandrov, G. De Lellis, A. Di Crescenzo, M. Fioranelli,
A. Iacomino, A. Lauria, J. Lotti, M.C. Montesi, V. Tioukov
1. Detector structure and construction
2. Set up for the measurement
3. Calibration run
Emulsion Cloud Chamber
for the FOOT experiment

## Slide 2
The ECC is made of three sections:
  Section 1: alternated layers of emulsions and target (C/CH2)
    vertex detector
    tracking of all charged particles produced
  Section 2: made of emulsion films only
    charge identification for low Z fragments (H, He, Li)
  Section 3: alternated layers of emulsions and lead
    Momentum measurement by range
Beam
Emulsion layer
Pb layer
1 mm
300 μm
1 mm
C or CH2 layer
1. Detector structure
Section 1
vertexing
Section 2
Charge identification
Section 3
momentum

## Slide 3
Alternate target layers of C or CH2 (1 mm) and emulsion (300 μm)
Vertex detector and particle tracking
Chamber thickness defined by the interaction length  obtain a sufficiently high number of interactions
20% of Carbon ions interacting in 3 cm Lexan
Total length ∼ 30 cells = 39mm
1. Section 1: vertex detector
1 mm
300 μm
C or CH2
∗
Beam
C or CH2
C or CH2

## Slide 4
Charge identification for low Z fragments (H, He, Li)
Emulsion were differently treated after the exposure and before the chemical treatment according to their position in the elementary cell (0, 1, 2)
R0:
    Not refreshed
    Developed soon after the exposure
    Sensitive to m.i.p.
R1:
    Appropriate refreshing for protons
    Insensitive to m.i.p.
    Sensitive to protons
R2:
    Appropriate refreshing for He
    Sensitive to He
Incident particles
from vertex
∗
R0
R1
elementary cell
R2
m.i.p.
p
    He
1. Section 2: structure charge analyzer

## Slide 5
The standard deviation for the separation of pair of nuclei, as function of number of elementary cells, is reported in the table.
1 cell = 0.9 mm length. A 3σ He-Li separation with 9 cells (8.1 mm)
1. Section 2: how many elementary cells for charge separation?
Cells | 3 | 9 | 13 | 20
H-He | 3.3 | 4.5 | 6.5 | 
He-Li | 2.6 | 3.9 | 4.3 | 5.0
Li-Be | 1.7 | 2.7 | 3.1 | 3.5

## Slide 6
Emulsion films interleaved with 1mm thick lead plates
Lead plates from ∼10 to ∼50 according to the incident beam energy
1. Section 3: momentum measurement
Emulsion layer
Lead layer
1 mm
300 μm
Pb
Pb
Pb
Pb
Pb

## Slide 7
∗
C/O beam
Counter
Beam
monitor
Emulsion
spectrometer
2. Set up for the measurement
To monitor the incident beam:
spatial distribution with ~ 1mm resolution: drift chamber
Scintillator counter for flux monitor
Depending on the rates, ECC may be moved by a motorised 2D stage
motorised
stage

## Slide 8
3. Calibration (+Physics?) run
p, C beam
Counter
Beam
monitor
Emulsion
H
He
Journal of Instrumentation 2 (2007) P06004
Exposure of ECC made of ∼30 emulsions in order to measure the sensitivity to p, alpha and cosmic rays
we need:
  proton source
  Ideally He/Li

## Slide 9
back up slides

## Slide 10
 | ECC (C or CH2) |  |  | TOT
 | Section 1 (em+C) | Section 2 (em) | Section 3 (em+Pb) | 
Emulsion films | 30 | 30 | 20-50 | 80-110
C or CH2 layers | 30 | 0 | 0 | 30
Pb plates | 0 | 0 | 20-50 | 20-50
At least 2 ECC (C or CH2) for each energy exposure
3. Detector construction: material
4. Detector construction: material